## Slide 1
Achievable bunch profile
The quality of our bunch profile measurement is limited by our spectrum bandwidth.
Longitudinal bunch profile diagnostics for EPAC
Kirill Fedorov1, Jamie Watts 1,2, Phillip Bradford1, Chris Armstrong 1, Rajeev Pattathil1, Alex Koala3, Ettore Pedretti3, Elin McCormack3, Peter Huggard3
1 Central Laser Facility, STFC Rutherford Appleton Laboratory, Didcot, OX11 0QX, UK 2University of Bath, Bath, BA2 7AY, UK
3 RAL Space, STFC Rutherford Appleton Laboratory, Didcot, OX11 0QX, UK
References
[1] Bajlekov S. I., Heigoldt M., Popp A., Wenz J., Khrennikov K., Karsch S. and Hooker S. M., "Longitudinal electron bunch profile reconstruction by performing phase retrieval on coherent transition radiation spectra", (23 April 2013) Phys. Rev. ST Accel. Beams :16 : 040701.
[2] Dogeun Jang, Hanran Jin, and Ki-Yong Kim, "Single-shot terahertz spectrometer using a microbolometer camera", (31 August 2020) Appl. Phys. Lett. :117 (9): 091105.
[3] Guo-Qian Liao, Yu-Tong Li, Xiao-Hui Yuan, “Relativistic Laser-Driven Table-top Intense Terahertz Transition Radiation Sources” [Internet] [cited: 27 November 2023] Available from: http://www.2physics.com/2016/07/relativistic-laser-driven-table-top.html
2D and 1D (2D averaged) taken with blackbody source. Background have been removed. The measured spectra have been normalised for the camera sensitivity.
Interference between the beams creates fringes on both cameras
Introduction
The electron bunch length, s, is related to the coherence and intensity of the emitted radiation.
Acknowledgements
This work is supported by,
CFI funding: Single-shot THz spectroscopy
Royal Society: Dorothy Hodgkin fellowship
Strategic Priorities Fund
Ultrashort (≈50fs) relativistic electron bunches, such as those produced by a laser wakefield accelerator, can be reliably and non-invasively inferred from spectral measurements of Coherent Transition Radiation (CTR). At the Extreme Photonics Applications Centre (EPAC), we are planning to use the CTR emitted when electrons cross the boundary between two different media to measure electron bunch properties. The CTR spectrum will be detected single-shot in the region ≈20µm – 2µm.
Here the path difference varies across the camera sensor ⇒ we can use it in single-shot mode
From the coherent part of the THz spectrum, we can:
  Measure the bunch duration,
  Determine the bunch profile (i.e. microbunching)
When two coherent beams superpose at an angle, φ, an interference pattern with a period of, Λ, arises.
Instrument Resolution:
Maximum detectable frequency:
Thorlabs SLS303 blackbody [0.6-15µm]
[500-20THz]
Xeva-FPA 640 InGaAs
[1.0-1.7µm]
[300-180THz]
PV320 pyroelectric
[1.7-20µm]
[180-15THz]
INO microbolometer
[3-14µm]
[100-21THz]
where L is the length of the detector and d is the pixel pitch
The Kramers-Kronig minimal phase retrieval algorithm can be used to restore phase information which is lost during interferometry.
Our spectrometer is designed to have a resolution of 1.3 THz and spectral bandwidth of 15 – 300 THz.
As a result, we will be able to resolve complex bunch structure in a range of 900 fs with resolution of 1.7 fs.
Pushing the limit:
Additional spectral information can be obtained using a VIS-light grating spectrometer.
The temporal resolution can be increased to 0.5 fs.
Single-shot THz spectroscopy
Electron bunch reconstruction from THz spectrum
Phase retrieval:
Profile retrieval:
Resolution:
Bandwidth:
fs
fs
Coherent THz/MIR radiation emitted by EPAC
PIC Sim of EPAC Bunch Profile
Corresponding CTR emission in frequency space