## Slide 1
Flavour programme at colliders
Dr. Harry Cliff
Cavendish Laboratory, University of Cambridge
PPAP Community Meeting
University of Birmingham
Tuesday 25th June 2024

## Slide 2: Flavour physics
What explains the pattern of mixing between generations?
What drives the hierarchy of fermion masses?
Why six quarks and six leptons?
CP violation?
Are quarks and leptons connected?
All these questions can be probed by studying beauty and charm quarks

## Slide 3: Flavour as a probe of new physics
studying heavy flavour decays gives sensitivity to BSM quantum fields in the loops
sensitive to energy scales above direct reach of LHC (up to 100 TeV in FCNC b decays)
Standard Model
New Physics
?

## Slide 4: Flavour physics at the LHC
Nature Phys. 18 (2022) 1
B oscillations
CP violation in charm
Phys. Rev. Lett. 122 (2019) 211803
CKM triangle
Exotic hadrons

## Slide 5: Flavour physics at the LHC
Bs → μ+μ-
Nature 522 (2015), 68-72
FCNC angular
Eluned Smith @LHCP
Parrott, Bouchard, Davies: Phys. Rev. D 107, 014511 (2023)
FCNC branching fractions

## Slide 6: The LHCb Upgrade I
Major upgrade to LHCb now in operation:
Almost all-new detector to allow readout at 30 MHz
Removal of hardware trigger
Full software trigger
Unprecedented beauty samples:
Targeting 50fb-1 by end of Run 4
Significant increase in trigger efficiencies for many modes
New silicon pixel vertex locator
New silicon upstream tracker
New scintillating fibre tracking system
New data centre and all-software trigger
New ring-imaging Cherenkov detectors

## Slide 7: LHCb Upgrade I
Notes: Not the final gradient

## Slide 8: LHC Schedule
High-Luminosity LHC
European Strategy Update 2020: “The full potential of the LHC and
the HL-LHC, including the study of flavour physics, should be exploited”
LHCb Upgrade II

## Slide 9: LHCb Upgrade II
Detector for the HL-LHC era
Most physics statistically rather than systematically or theoretically limited motivates high luminosity experiment.
Aim to record 300fb–1 by end of HL-LHC.
LHCb-TDR-023
Global changes:
Fast timing to reduce backgrounds
Radiation hardness
Removal of HCAL, introduction of TORCH and magnet tracking stations
PicoCal

## Slide 10: LHCb Upgrade II - Physics
Targeting huge improvements in precision on key flavour observables
LHCb-TDR-023

## Slide 11: LHCb Upgrade II – Luminosity
The challenge of luminosity
Instantaneous luminosity increase from 2 × 1033 cm−2 s−1 to 1.5 × 1034 cm−2s−1
42 interactions per bunch crossing
2000 charged particles within LHCb acceptance
Design challenges:
Higher granularity, non-uniform detectors to cope with busier events
Radiation-hard detectors to survive intense conditions
Introduce fast timing to separate overlapping pp interactions
Run 3: pile-up ~6
Upgrade II: pile-up ~42
LHCb-TDR-023

## Slide 12: LHCb Upgrade II –Timing
No timing
20 ps window
LHCb-TDR-023
Fast timing crucial to reduce backgrounds in high luminosity environment
LHC bunches are long (50mm) and pp interactions occur over 0.2 ns.
Timing with a few tens of ps resolution per particle allows charged tracks and photons to be associated to the correct primary vertex.
VELO, RICH, TORCH and ECAL will be fast timing detectors:
Adds new dimension to information exchanged between sub-detectors
New potential for data suppression in front-end hardware and software trigger
Sets challenging R&D requirements, particularly for sensors and front-end ASICs.
Notes: UK involvement in VELO, RICH TORCH

## Slide 13: LHCb Upgrade II –Tracking
LHCb-TDR-023
Tracking system comprised:
Vertex Locator (VELO)
Upstream Tracker (UT)
Magnet Stations (new addition)
Mighty Tracker (SciFi + inner silicon)
Higher occupancies require higher granularity.
Mismatch rate between upstream and downstream track segments needs to be minimised.
Shift from strip to pixel technology and add fast timing.

## Slide 14: LHCb Upgrade II –VELO
LHCb-TDR-023
Candidate sensors:
thin planar, 3D sensors
Candidate ASICs (28 nm technology)
VeloPix2, IGNITE
Mechanical design challenges:
cooling, module replacement, minimisation of material (RF foil), vacuum compatibility
Timing
Improvements in spatial resolution not sufficient
Require track time resolution of ~20ps and hence hit time resolution of 50 ps for the 4D pixels.
Notes: Low Gain Avalanche Diodes – degredation at high fluences

## Slide 15: LHCb Upgrade II –MAPS Trackers
LHCb-TDR-023
Mighty Tracker
Replace central region of of SciFi tracking stations with silicon detecors
Use Monolithic Active Pixel Sensors (MAPS) for both Mighty Tracker and UT
First large-scale tracking detector with this technology
Meets radiation requirement (3 × 1015 neq/cm2 at UT)
Building on experience from STAR, ALICE, ATLAS and mu3e

## Slide 16: LHCb Upgrade II –Particle Identification
LHCb-TDR-023
Ring-Imaging Cherenkov detectors (RICHs) perform charged hadron ID from 3 GeV/c (veto mode) to 65 GeV/c using C4F10 in RICH 1 and 15-100 GeV/c using CF4 in RICH 2.
New TORCH (Time of internally reflected Cherenkov light) will cover the lower momentum range from 2-10 GeV/c by combining the time-of-flight and time-of-propagation techniques.
The electromagnetic calorimeter (ECAL) performs photon, electron and π0 identification - separated from the muon detectors by a 1.7 m-thick iron shield.
Notes: Greenhouse gases – R&D into alternative radiators and RICH gas-tight boxes

## Slide 17: LHCb Upgrade II –RICH
LHCb-TDR-023
RICH:
Reduced footprint vs current detector
Improved granularity to 1.0 x 1.0 mm2 pixels avoids peak photon occupancy exceeding 100%
Sensors under study: SiPMs, MCP-based detectors, next gen MaPMTs
Using reconstructed parameters in the RICH algorithms and the PV t-zero, can predict the detector hit times to within 10 ps.
Time gate around the predicted time significantly reduces combinatorial background and helps to recover the Run 3 particle ID performance.
Faster detectors are better, as in practice the photon detector resolution will dominate the width of the time gate. Aiming for a resolution better than 100 ps.

## Slide 18: LHCb Upgrade II –TORCH
LHCb-TDR-023
TORCH (Time Of internally Reflected CHerenkov light):
Innovative ToF detector providing pion/kaon (kaon/proton) separation up to momenta of 10 (20) GeV.
Highly-polished 1 cm thick quartz plate used as radiator
Photons internally reflected and focussed onto photon detectors.
Arrival time of photons measured precisely.
At 10 metres from collision point require per track resolution of 15 ps for 3σ K/π separation
Per photon resolution of 70 ps.
“Start time” t0 determined from timing of other tracks from primary vertex

## Slide 19: BESIII
LHCb-TDR-023
Beijing Spectrometer III (BESIII) runs at Beijing Electron-Positron Collider
Variable beam energy between 2 and 4.6 GeV, luminosity 1033 cm–2s–1
Charm physics with D0/D+: dataset 7 x larger than before now available
Very clean e+e– environment. Semi-leptonic/leptonic decays for Vcd and Vcs
Work here forms important input to LHCb (and Belle2)
Driven by UK groups (there are 3 on BESIII)
Also other datasets for exotic charm spectroscopy, Λc physics
Future: Super Charm-τ Facility (STCF) -> 100 x larger dataset!
Nano-beam scheme: 40 x increase in luminosity
Asymmetric collisions at sqrt(s) = m(Υ(4S))
Advantages for final states with π0, γ, KS, KL and neutrinos
Higher tagging power and electron reconstruction efficiency
Wide programme to explore e+e-  τ+τ-
D0 decays are quantum correlated.
Without entanglement these plots would look identical!

## Slide 20: SuperKEKB and Belle II
LHCb-TDR-023
Major upgrade of KEKB e+e- collider
Nano-beam scheme: 40 x increase in luminosity
Asymmetric collisions at sqrt(s) = m(Υ(4S))
Advantages for final states with π0, γ, KS, KL and neutrinos
Higher tagging power and electron reconstruction efficiency
Wide programme to explore e+e-  τ+τ-

## Slide 21: SuperKEKB and Belle II
LHCb-TDR-023
During phase I (2019-2022) recorded 400 fb-1  targeting 50 ab-1 by end of experiment.
Things to look forward to:
Lepton flavour violating τ decays
Searches for bsνν decays
Time dependent CPV in bsg
Modes with neutrals, allowing flavour symmetries to be exploited
… and many more

## Slide 22: Exciting times ahead
LHCb-TDR-023
Despite all the great results that will flow from LHCb Upgrade I, most observables will still be statistically limited by the end of Run 4
LHCb Upgrade II will make it possible to fully exploit the HL-LHC for flavour physics
UK leadership at all levels, now in exciting R&D phase
Also strong flavour programme at ATLAS and CMS, particularly in beauty decays to muons
Despite challenges, Belle II will provide crucial cross-checks of LHCb results and complementary sensitivity in final states that are hard to access at LHCb
In longer term, beauty samples from 5x1012 Z boson decays at FCC-ee offer opportunities in specific final states (neutrinos and taus) that complement HL-LHC programme
Belle II
LHCb
To FCC-ee

## Slide 23: Backup
LHCb-TDR-023

## Slide 24: LHCb Upgrade II –ECAL
LHCb-TDR-023
LHCb Electromagnetic Calorimeter not replaced (except electronics) in Upgrade I
During Run 3 will operate at 25x its design luminosity!
Main challenges for Upgrade II:
Achieving same energy resolution and reconstruction efficiency as original detector at significantly higher pile-up and occupancy
Radiation hard to accumulated 300 fb-1
Proposal: crystal fibres (SpaCal) in central region and Shashlik (outer region)
20 ps timing information to supress background