## Slide 1: Accelerator R&D
Stewart Boogert
PPAP Community Meeting Birmingham
26th June 2024

## Slide 2: Introduction
Far too much accelerator R&D work in the UK to cover in a 20-minute talk
Rather personal view presented and intended for discussion and preparation for our “strategy year”
Projects omitted (EIC, AWAKE…) as focus on HEP energy frontier machines
20 years has seen a divergence of accelerator and HEP communities
  Frequency of applied sciences accelerators vs HEP projects
Summary of existing national and international scale accelerator projects
  Currently wide range of national scale projects in the plans
  Whistle stop tour of the current projects

## Slide 3: Project landscape
Important national scale projects (non-HEP)
  EPAC (1-10 GeV e-)
  Diamond 2 (3.5 GeV e-)
  RUEDI (10s MeV e-)
  CLARA/FEBE (250 MeV e-)
  ISIS2 (1.2 GeV p → Neutrons)
  UK XFEL (8 GeV e-)
  LhARA/ITRF (10-15 MeV p)
International HEP projects
  Electron Ion Collider (EIC)
  International Linear Collider (ILC)
  Compact linear Collider (CLIC)
  International Muon Collider (IMC)
  Future Circular Collider (FCC-ee, -hh)

## Slide 4: Topics and theme landscape
Areas with strong interest from UK accelerator institutes
  Particle beam therapy (Protons, VHEE, Ions)
  FLASH particle beam therapy (> 40 Gy/s)
  Sustainability of accelerators
  Advanced acceleration (PWFA, LWFA)
Areas of UK strength in conventional accelerators
  Machine detector interface
  Beam instrumentation
  Sustainability and energy efficiency
  Beam dynamics
  Positron production
  Radio-frequency
  Advanced acceleration

## Slide 5: Extreme Photonics Applications Centre (EPAC)
New RAL based user facility
  Due to come online in 2025
  10 Hz Petawatt laser
  Two experimental areas
  1-10 GeV electron beams

## Slide 6: Diamond II
Upgrade to UK synchrotron source
  ~£500 M investment
  Increase energy from 3 GeV to 3.5 GeV
  New lattice based on double triple bend achromats
  Reduce horizontal emittance by factor 20
  Up to 3 orders of magnitude gain for harder end of the X-ray spectrum
  24 straight sections for potential insertion devices
https://www.diamond.ac.uk/Home/About/Vision/Diamond-II.html

## Slide 7: RUEDI
Relativistic Ultrafast Electron Diffraction & Imaging
  Single shot time-resolved with MeV electrons
  Ultra-fast electron diffraction down to 10 fs
  Current designs split the imagine and diffraction
  £124 M approved from infrastructure fund
  User facility at Daresbury Lab
Recent designs split accelerator for imaging and diffraction
https://ruedi.uk

## Slide 8: UK X-ray free electron laser
8 GeV superconducting, 1 MHz electron linac
  Multiple different colour X-ray beam-lines
  Focus on scientific throughput and flexibility
Funding from infrastructure fund
https://xfel.ac.uk

## Slide 9: CLARA/FEBE
In preparation for UK XFEL there is the CLARA facility
  Test system for FEL technologies
  100 Hz, 250 MeV FEL quality beam
Full energy beam exploitation (FEBE)
  Experimental area to test PWFA and LWFA
  FEL beam combined with 130 TeV laser system
Phys. Rev. Accel. Beams 27, 041602

## Slide 10: LhARA/ITRF
Laser driven source to accelerate protons and ions for radiobiology
Laser solid interaction to accelerate protons and/or ions
Two stage project
FFAG to reach higher energies
https://indico.stfc.ac.uk/event/986/
Phase 1
Phase 2

## Slide 11: ISIS2
Replacement for the current ISIS neutron spallation source
  High power proton beam
  Target stations to >MW
Accelerator options
  Low energy linac → rapid cycling synchrotron to 1.2 GeV
  Full energy linac to 1.2 GeV → accumulator ring to bunch compress
  Low energy linac → fixed field alternating gradient to accelerate 1.2 GeV and compress
https://www.isis.stfc.ac.uk/Pages/ISIS-II-webinar-13-March-2024.aspx
RCS
FFA
AR

## Slide 12: UK accelerator community
STFC and community has been successful in obtaining UKRI infrastructure funding
Securing funding for UK XFEL or ISIS2 will absorb significant (human) resources for decades
Depth of capability within the accelerator community could make significant contributions to a future HEP collider
There is a desire to engage more significantly with HEP projects
Strong steer from PP community and STFC required for accelerator institutes and ASTeC to engage more fully

## Slide 13: National facilities and relevance to HEP
Are there credible HEP uses of planned UK accelerator infrastructure?
UK XFEL
  Single electron dump experiment light dark matter
  Strong field Quantum Electrodynamics
  Unruh radiation? Kaons?
ISIS 2
  Muon/flavour physics (a la PSI)
CLARA/FEBE
  Testing of staging plasma accelerator beams
  Manipulation of beams for injection into plasma
EPAC
  Real photon collision cross section measurement
  Strong field QED (again)

## Slide 14: FCC-ee
FCC-ee is many machines over time
  Low energy Z-pole ~ B-factory or DAΦNE (36 MeV/turn)
  High energy tt threshold (9.2 GeV/turn)
  Significantly increase the RF power delivered to beam as the CoM energy is increased
STFC/ASTeC/Cockcroft is investing significantly in SCRF technologies
https://www.isis.stfc.ac.uk/Pages/ISIS-II-webinar-13-March-2024.aspx

## Slide 15: International Muon Collider
Potential to reach multi TeV lepton collisions
Challenges are manifold
  Production target, cooling and acceleration
In general, an important requirement is high RF gradients in the presence of large magnetic fields
Collider ring magnet technology
https://iopscience.iop.org/article/10.1088/1748-0221/19/02/T02015/pdf

## Slide 16: HALHF
Hybrid, asymmetric, linear Higgs factory
  Plasma-wakefield for electrons and conventional RF for positrons
  Staging multiple plasma accelerators to reach 100s GeV is far from a solved problem
  Beam power handing is a significant issue
  Reduction in overall collider length and cost saving potentially substantial
https://iopscience.iop.org/article/10.1088/1367-2630/acf395

## Slide 17: Sustainability
B Sheppard Talk at IoP PAB meeting 2024

## Slide 18: SCRF efficiency
Look at the SC RF system efficiency
  Creating the RF power (klystrons)
  Delivering the RF power to the accelerating structures (FRTs)
  SC Material and Tc speaks to the cryogenic systems
B Burt Talk at IoP PAB meeting 2024
High efficiency Klystrons can halve this
Fast reactive tuners can reduce this by 10
Thin film SRF can halve this

## Slide 19: Thin super conducting films
Replace bulk Niobium e.g copper with thin SC film
Higher Tc material (Nb3Sn, V3Si, NbN, NbTiN, MgB2)
Reduce cyrogenic power consummation
Improve accelerator performance (gradient, quality factor)
B Sheppard Talk at IoP PAB meeting 2024
Deposit
Fundamental
measurements
Acc structure
measurements

## Slide 20: Mapping research onto projects (incomplete)
Research area | IMC | FCC-ee | FCC-hh | HALHF | UK XFEL | ISIS2
SCRF (RF efficiency) | Proton linac High-B and RF | Replace SR losses |  | 200 GeV Electron linac | 8 GeV linac | 1.2 GeV p linac
High field magnets | Collider ring |  | Collider ring |  |  | 
RCAs/FFAs | Rapid acc |  |  |  |  | High power
Advanced acceleration |  |  |  | Plasma staging |  | 
Machine detector interface | Complex IR | Significant IR radiation |  | See ILC issues |  | 
Beam instrumentation |  |  |  |  |  | 
Beam dynamics |  |  |  |  |  | 

## Slide 21: Summary
UK community is comparatively rich with non-HEP accelerator projects
ASTeC and STFC is rightly focused on national facilities
Cockcroft and John Adams Institutes have the expertise to made meaningful contributions to FCC-ee, IMC, HALHF (insert HEP collider project of your choice here) etc.
  ASTeC and STFC will also play an important role if construction of a new project is approved
Sustainability will and should play a significant part of the R&D considerations.
Mapping current UK expertise onto planned HEP collider projects is probably a worthy exercise in preparation for STFC strategy development, ECFA visit and ESPPU