WP5 Milestones
ITRF Milestone 16
- Automated cell dish handling and environmental system design complete (LhARA M5.1)
- End-station user-community consultation complete (LhARA M5.2),
- End-station component testing at Birmingham complete (LhARA M5.3),
- kGy/s tests at Birmingham complete (LhARA M5.7).
  ITRF Milestone 17
- Specification of LhARA beam monitoring technology complete (LhARA M5.5).
  - Report produced on existing technologies with limitations on these for low energy / very intense beams

---
Automated cell dish handling and environmental system design complete (LhARA M5.1)
- Cell dish handling for SCAPA / MC40 underway.
- Env system has two options
  - Modified env. Chamber such as at The Christie
  - Small env. Chambers that are transported to the beam
- Shared properties
  - Thinned window to seal the chambers due to low energy
  - Real time none destructive dosimetry (e.g. gas profiler)
  - Motors / robots to move multiple samples around
  - Feedback to accelerator for shot to shot delivery.

---
End-station user-community consultation complete (LhARA M5.2)

---
End-station user-community consultation complete (LhARA M5.2)

---
End-station component testing at Birmingham complete (LhARA M5.3)
- Supported work for WP2, WP4, WP5 experimental campaigns at UoB
- Monte Carlo studies underway to support these activities
- RCF measurements started to assess feasibility of EBT-XD and HD-V2
- Existing silicon detectors at UoB studied to extrapolate performance requirements
- Energy loss and scattering studied and verified through thin materials in Geant4 physics verified.

---
kGy/s tests at Birmingham complete (LhARA M5.7)
- Working with NPL using developmental Transcal and SSCal (Secondary standard calorimeter)
- Dose rates and repeatability studied
- SSCal should be dose rate independant
- Dose rate of 2.5 kG/s achieved in the SSCal
- Results of Transcal and SSCal are under review

---
Any questions?