## Slide 1: FLASH Radiotherapy Research at QUB
Prof Karl Butterworth
Advanced Radiotherapy Group
LhARA collaboration meeting
Monday 2nd September, 2024
Notes: Good morning, thank organisers
Rapid period of development in flash research over the past 18 months or sos
Received funding from MRC to implement a program of photon flash RT research using a novel preclinical platform - the FLASH SARRP -

## Slide 2
Radiotherapy Research at PGJCCR
Prostate Cancer Centre (PCC)
Advanced Radiotherapy Group (ARG)
Johnston Cancer Centre
(PGJCCR)
Northern Ireland Cancer Centre (NICC)
LhARA Collaboration Meeting, 2024.
Notes: Give you a brief overview of RT at the PGJCCR.
The Advanced Radiotherapy Group (ARG) is a multidisciplinary team of clinicians, physicists, radiation biologists, radiographers and physiologists whose remit is to research, initiate and develop new and advanced radiation treatments encompassing basic laboratory research, preclinical studies and clinical delivery.

## Slide 3
Radiotherapy Research at PGJCCR
Prostate Cancer Centre (PCC)
Advanced Radiotherapy Group (ARG)
Johnston Cancer Centre
(PGJCCR)
Northern Ireland Cancer Centre (NICC)
LhARA Collaboration Meeting, 2024.
Notes: Workflow encompassing radiobiology, physics and clinical oncology
Example of both forward translation early phase studies in SABRT, radionuclide and drug RT combinations
Reverse translation, some excellent examples of this recently in the area of radiation induced cardiac toxicity and subvolume effects

## Slide 4
ARG Research Themes
Precision Radiotherapy
Radiotherapy Combinations
Clinical Trials
Advanced delivery modalities including radionuclides
Genomic signatures
Imaging biomarkers
Mechanistic modelling
RBE treatment planning
DDRI’s
HDAC’s
Radiation protectors
Nanoparticle radiosensitizers
Tumour metabolism
PACE-NODES, SABRE, SPORT, ADDRAD
CONCORDE
PARABLE
CENTRE
LhARA Collaboration Meeting, 2024.
Notes: Research crosses a number of central themes

## Slide 5
Preclinical Infrastructure
Precision Radiotherapy
Radiotherapy Combinations
Advanced delivery modalities including radionuclides
Genomic signatures
Imaging biomarkers
Mechanistic modelling
RBE treatment planning
DDRI’s
HDAC’s
Radiation protectors
Nanoparticle radiosensitizers
Tumour metabolism
LhARA Collaboration Meeting, 2024.
Preclinical radiotherapy technologies
Small animal radiotherapy research platform (SARRP)
Ultra-high dose rate (FLASH- SARRP)
Notes: Support by key enabling preclinical infrastructure.
Example of how we are using these platforms to drive innovation in precliinical RT studies
Describe infrastructure

## Slide 6
Preclinical infrastructure
Small animal radiotherapy research platform (SARRP)
CBCT image guidance, TPS, > 0.5 mm beam size.
Conventional dose rates (0.5 Gy/min).
Dedicated TPS, collimation etc.
LhARA Collaboration Meeting, 2024.
Notes: SARRP
Onboard CBCT, enabling previously unimaginable capabilities for radiological experimentation
Enbale normal tissue radiobiology developments
2014, grant from friends, develop by john wong

## Slide 7
Preclinical infrastructure
Small animal radiotherapy research platform (SARRP)
CBCT image guidance, TPS, > 0.5 mm beam size.
Conventional dose rates (0.5 Gy/min).
Dedicated TPS, collimation etc.
FLASH-SARRP
Conventional dose rates: 0.05 – 0.5 Gy/s
FLASH dose rates (<200 Gy/sec), exposures 50 – 500 ms
On board μCT capability (40 μm voxel size).
LhARA Collaboration Meeting, 2024.
Notes: More recently flash sarrp
Enabled rapid development of flash RT program within QUB – define specifically at does rates < 200 Gy/sec
Also developed by john wong and commercialised by xtrshal
Rotating anode fluoroscopic xray tubes

## Slide 8
Modern Era of FLASH Research
LhARA Collaboration Meeting, 2024.
Favaudon et al, 2014.
Notes: Followed by pioneering studies for example by Jolyen studies be Hendry and colleague reporting sparing of radionecrosis in a mouse tail studies.
Innovation trigger for the modern era FLASH research from Vincent Favuadon and MCat Vozenin., seminar study demonstrating

## Slide 9
Preclinical models & mechanisms of FLASH sparing
LhARA Collaboration Meeting, 2024.
Limoli & Vozenin, 2023.
Notes: No consensus on biological mechanism.

## Slide 10
Development of FLASH-RT Research at QUB
LhARA Collaboration Meeting, 2024.
NCI Workshop
2018
Collaborations with K Petersson & G Adrain, Lund University.
2019-2021
FLASH SARRP ERA
2022-
UK Preclinical Photon-FLASH Radiotherapy Facility
Notes: A FLASH effect appearing at low doses under normoxic conditions for several cell lines in vitro. The magnitude of the FLASH effect differed between the cell lines, suggesting inherited biological susceptibilities for FLASH irradiation.
Models of oxygen kinetics during irradiation were used to develop a time-dependent model of the oxygen enhancement ratio in mammalian cells that incorporates oxygen depletion.

## Slide 11
FLASH systems (<2022)
Proton Cyclotron
230 MeV, 40-100 Gy/s
Singletron Accelerator
4.5 MeV, <1000 Gy/s
Electron Accelerator
5.6 MeV,< 300 Gy/s
Modified Linac
6 MeV,<150Gy/s
6 MeV electrons
150 kV X-ray
FLASH studies require complex beamlines not initially designed for purpose.
Majority of studies have used H+ or e- sources.
  >85% of treatments & radiobiology studies use photons.
  Different macro- and micro-scale energy deposition patterns - Dosimetry & RBE challenges.
  Need for accessible photon sources to leverage pre-existing knowledge.
LhARA Collaboration Meeting, 2024.
Notes: Up to this point, very little evidence for the FLASH effect reported using photons, major of studies using e- and p+
Complicates the interpretation of much of the published data on FLASH-RT and its translation to clinical settings
Low penetration
Only a small fraction of the energy fluence of electrons is transferred to photons, with the majority of the energy fluence dissipated through various phenomena, including heat.
This means that a FLASH photon accelerator must have a source capable of producing many more electrons (by a factor of 1000) than is achievable with currently available devices
No compact, labor

## Slide 12
X-ray FLASH
LhARA Collaboration Meeting, 2024.
Gao et al, 2022.
High energy x-rays generated using PARTER (platform for advanced radiotherapy research) at the CTFEL (Chengdu THz Free Electron Laser facility, China).
Superconducting linac, 6–8 MeV electrons with an adjustable mean current of up to 10 mA.
Maximum dose rate of 1000 Gy/s.
CONV doses using a 6 MV beam Elekta Precise linac.

## Slide 13
FLASH SARRP
Rezaee et al 2021, Phys. Med. Biol. 66 095006 (2021)
First commercial photon FLASH system for preclinical studies.
Developed by JHU and commercialised by XStrahl.
Opposing-pair rotating anode x-ray tubes provide > 100 Gy/s over 2 cm thick medium.
Key enabling technology for FLASH-RT research.
  150 kVp x-ray sources at 100 kW.
  Vertical motion of tubes for SSD adjustment.
  Rotational motion to reduce high entrance/exit dose.
  Mirrored beams to compensate heel effects.
LhARA Collaboration Meeting, 2024.
Notes: The target rotates rapidly during X-ray generation, allowing for more efficient heat dissipation and increased X-ray output.

## Slide 14
FLASH SARRP
LhARA Collaboration Meeting, 2024.

## Slide 15
First implementation of the FLASH SARRP
LhARA Collaboration Meeting, 2024.
Miles et al, Int J Radiat Oncol Biol Phys, (2023).
Notes: A custom 3-dimensionally printed immobilization and positioning tool was developed for reproducible irradiation of a mouse hind limb.

## Slide 16
Commissioning & implementation challenges
LhARA Collaboration Meeting, 2024.
Alignment and firing of 2 tubes.
Defining mechanical and radiation isocentres.
Filtration, dosimetry & QA
Tube conditioning & warmup.
Stage control & Mouse positioning.
Target localisation and CBCT integration.
Integration of TPS.
Define workflows for different targets.

## Slide 17
Beamline characterisation
LhARA Collaboration Meeting, 2024.
Depth dose measurements & field uniformity using SARRP phantom & EBT3.
Distances measured from flange exit.
Notes: -dose rates > 60 Gy sec at 5 mm depth
-upper and lower tubes have similar outputs
-Heel effects are observed for single tube orientations (top, middle), but combining two tubes at equal distances gives a relatively uniform dose distribution (bottom).

## Slide 18
Beamline characterisation
LhARA Collaboration Meeting, 2024.
Ionisation Chamber outputs.
HVL measurements -150 kV (Anna Subiel, NPL).
Notes: -correction factors for flash dose rates
-reliable HVL measurements at different currents and temperatures.
Technical characteristics, development of the program

## Slide 19
QUB FLASH-RT Program
Aim: To support the safe & robust translation of photon FLASH-RT.
Establish the technical infrastructure of a UK photon FLASH-RT Facility (partnered with ICR).
Develop the evidence base for photon FLASH.
  Define key physical & radiobiological variables (Dose, dose-rate, beam structure, fx, hypoxia).
  Develop a mechanistic understanding of the photon FLASH effect (genetic, epigenetic, metabolic & immune effects).
Enable collaborative, cross-centre studies including other FLASH modalities.
Support clinical translation of FLASH towards UK led trials.
LhARA Collaboration Meeting, 2024.

## Slide 20
Program Development
2024
2025
Investigating the impact of photon FLASH in primary glioblastoma
Brainwaves NI Studentship: 1/10/23 - 30/9/26
Beamline validation & biological characterisation of the FLASH-SARRP. MRC CAST Studentship 1/10/24 - 30/9/27
Investigating the basis of photon FLASH in tumours & normal tissues. MRC Project: 1/6/24 – 31/5/27
ProFLASH - photon FLASH in prostate cancer.
Prostate Cancer UK. 1/2/24 -31/7/26
Spatio-temporal dependenc of radiotherapy induced cardiac toxicity MRC Project: 1/10/2021 - 30/9/24
QUB Agility fund
LhARA Collaboration Meeting, 2024.

## Slide 21
FLASH in primary GBM
Investigating the impact of photon FLASH radiotherapy on therapeutic index in primary glioblastoma (October 2023-26).
Aim 1: Development of in vitro system to investigate responses to photon FLASH-RT.
Aim 2: Assessment of GBM tumour responses to photon FLASH-RT.
Aim 3: Development of an in vivo model of radiation-induced normal tissue injury.
Malachy McIvor
LhARA Collaboration Meeting, 2024.

## Slide 22
In vitro FLASH studies in GBM cell models
LhARA Collaboration Meeting, 2024.
Assembly
Inverted JHU flange adaptor & collimator.
Surface 100% PLA, infill 40%/60% PLA/air.
Lower tube, dose rate = 86 Gy/s
Adaptable for hypoxic in vitro irradiations – nBIONIX Cell culture kit.

## Slide 23
Photon FLASH in tumours & NTs
WP1: Characterising the photon FLASH effect in normal tissues.
Lung, skin, gut & radiation-induced lymphopenia.
WP2: Characterising the photon FLASH effect in lung tumour models.
Subcutaneous lung tumour models (LL3 & KP).
Orthotopic lung tumour model.
KP inducible tumour model.
WP3: Defining the biological mechanisms of tumour and normal tissue responses to FLASH-RT
Integration of gene expression, metabolomics and immune-cell phenotypes
Preclinical radiomics.
Quantitative radiobiological modelling.
Mihaela Ghita
Kathryn Brown
LhARA Collaboration Meeting, 2024.
Notes: Started June 2024.

## Slide 24
Single tube setups – skin & subQ tumour
Assembly
JHU flange adaptor & leg holder.
Upper tube, dose rate = 87 Gy/s.
Assembly
JHU flange adaptor, pedestal, tumour collimator & bed.
LhARA Collaboration Meeting, 2024.

## Slide 25
FLASH-SARRP is a complex, early-stage system.
Working to establish best practices for tube conditioning & warmup – narrow operational window.
Potential limitations of the tubes for comparative studies at conventional dose-rates – may have to use conventional SARRP.
Non-trivial hardware & software upgrades are required.
Method of anesthesia is critical.
What have we learnt so far?
LhARA Collaboration Meeting, 2024.
Notes: required to reach full potential

## Slide 26
LhARA Collaboration Meeting, 2024.
Summary
UKRI funded FLASH research program at dose rates < 200 Gy sec, enabled by the FLASH-SARRP.
QUB facility operational since March 2024.
  Dosimetry and beamline characterisation.
  Initiated in vivo studies June 2024.
  Initial parameter mapping – dose, dose rate thresholds, beam structure, fractionation.
Preclinical models linking tissue function & molecular mechanisms.
Notes: Hype cycle for flash-RT
Use the system to expand the evidence base for photon flash

## Slide 27
Acknowledgements
PGJCCR, QUB
Kevin Prise
Stephen McMahon
Mihaela Ghita
Kathryn Brown
Brianna Kerr
Malachy McIvor
Gerard Walls
Clinical Physics, NICC
Alan Hounsell
Conor McGarry
Owen McLaughlin
Johns Hopkins University
John Wong
Mohammed Rezaee
Daniel Sforza
National Physical Laboratory
Giuseppe Schettino
Anna Subiel
University of Pennsylvania
Yiannis Verginadis
LhARA Collaboration Meeting, 2024.
Oxford University
Kristoffer Petersson
Lund University
Gabriel Adrian

## Slide 29
The dose-rate spectrum
LhARA Collaboration Meeting, 2024.
Hall E, BJR 1972.
‘At ultra-high dose-rates (pulses of micro or nanoseconds) a clear dose-rate effect has been demonstrated for bacteria, but is less certain for mammalian cells; these dose rates have no certain application in radiotherapy at the present time’.
‘These results have been explained in terms of local oxygen depletion: the rapid deposition of radiant energy causes oxygen to be consumed too quickly for diffusion to maintain an adequate level of Oxygenation’.
Notes: Pres

## Slide 30
Preclinical models & mechanisms of FLASH sparing
LhARA Collaboration Meeting, 2024.

## Slide 31
FLASH SARRP
SARRP FLASH early adopter supported by UKRI MRC October 2022.
UK delivery April & System install May 2023.
High priority – Beamline validation, tumour & NT responses to photon FLASH.
Medium-term – Biophysical mechanisms of FLASH-RT.
Long-term – Integrating the FLASH-SARRP across QUB radiobiology research.
LhARA Collaboration Meeting, 2024.