## Slide 1: Lessons from laser electron studies
Conor McAnespie
LhARA, September 2024

## Slide 2
LhARA, September 2024
Conor McAnespie
Introduction to electrons in radiobiology
Very High Energy Electrons (VHEE)
Laser-driven sources of electrons for radiobiology research
  Direct laser acceleration
  Laser-wakefield acceleration
Cell irradiations with laser-driven sources
Contents

## Slide 3
LhARA, September 2024
Conor McAnespie
Introduction

## Slide 4: Electrons sources for radiobiology
LhARA, September 2024
Conor McAnespie
∽fs
fs-ps
ps-s
s-hr
hr-d
Physical step
Ionisations and excitations
Physio-chemical step
Molecular dissociations
Chemical step
Reactions and diffusions
Biochemical step
DNA repair Enzymatic
Biological step
Cellular and tissue response
Conventional
Laser-Driven
Flash
Current electron beam energies in clinical settings are limited to a few MeV.
Used to treat surface or near-surface tumours.
Proposed to increase the energy to 100’s of MeV to target deep-seated tumours.

## Slide 5: Very High Energy Electron RT
LhARA, September 2024
Conor McAnespie
First proposed in the early 2000’s VHEE describes the use of 100-250MeV electrons to reach deep-seated tumours.
Relatively low cost to develop accelerators to reach these high energies.
Possible to reach high-dose per pulse and ultra-short pulse durations for the studies of dose-rate effects (FLASH and beyond).
Source | Electron energy [MeV] | Change [pc] | Duration [ps]
CLEAR [1] | 60-220 | 10-1500 | 0.1-10
CLARA [2] | 250 | 250 | 2-10
[1] https://clear.cern/content/welcome-clear
[2] D. Angal-Kalinin et al. Phys. Rev. Accel. Beams 23, 044801

## Slide 6: Advanced techniques
LhARA, September 2024
Conor McAnespie
Whitmore, L. et. al. Scientific Reports, 11(1), p.14013.
Current x-ray based RT techniques include shaping the beam and multiple irradiation angles to reduce normal tissue dose.
Due to their charge, it is possible to manipulate electron bunches to produce Bragg-like peaks, comparable to that proposed with ion sources.
Notes: Here only the final quadrupole strength was changed to vary the dose distribution: Electron energy 250MeV

## Slide 7
LhARA, September 2024
Conor McAnespie
Laser driven electron sources

## Slide 8: Laser-driven electron sources
LhARA, September 2024
Conor McAnespie
Electron acceleration from the interaction of a laser pulse with an under-dense plasma (gas targets).
Laser wakefield acceleration (LWFA)
Direct laser acceleration (DLA)
Electron and proton acceleration from the interaction of a laser pulse with an over-dense plasma (solid targets).

## Slide 9: Beam properties from DLA
LhARA, September 2024
Conor McAnespie
1.5cm
2cm
2.5cm
3cm
Electron energies in the range of few – 10MeV, scaling up to <100MeV
High divergence (~30 degrees)
C.A. McAnespie, et. al.- arXiv:2309.06870, 2023
Simulated electron duration ~10’s of picoseconds.
Dose-rates on the order of 1011 Gy/s

## Slide 10: Beam properties from LWFA
LhARA, September 2024
Conor McAnespie
C.A. McAnespie, et. al.- Submitted 2024
Electron profile at the cell plane, reaching >1Gy over cm-scales areas
Electron energies >100MeV
Low divergence (<0.1 degrees)
Expected duration <50 femtoseconds

## Slide 11
LhARA, September 2024
Conor McAnespie
Electron experiments at QUB
(With help from many others)

## Slide 12: Laser-driven electron sources
LhARA, September 2024
Conor McAnespie
Parameter | TARANIS | Gemini
e- energy [MeV] | 0 - 12 | 100-1000
e- divergence [mrad] | 0.49 | 0.002
e- duration [ps] | 10 - 20 | 0.045
dose [Gy] | 0.5 – 6 | 0.5 - 3
Gemini – LWFA
TARANIS – DLA

## Slide 13: Studying biological effectiveness
LhARA, September 2024
Conor McAnespie
DNA DSB repair kinetics
20% O2
<0.5% O2
0.5hr
24hr
Cell survival assay

## Slide 14: Cell lines used
LhARA, September 2024
Conor McAnespie
Performed reference x-ray irradiations at 0.49 Gy/min dose-rate (PGJCCR).
AG01522 D Human skin fibroblast cells (Coriell Institute).
E2 Patient-derived glioblastoma stem-like cells.
Used for comparison with laser-driven studies.

## Slide 15
LhARA, September 2024
Conor McAnespie
Taranis – Picosecond scale irradiations

## Slide 16: Picosecond-scale irradiations
LhARA, September 2024
Conor McAnespie
24hrs after irradiation, no significant difference measured between picosecond-scale and conventional irradiations.

## Slide 17: Picosecond-scale irradiations
LhARA, September 2024
Conor McAnespie
AGO - Skin
E2 - Cancerous
Cell line | source | ⍺ (Gy-1) | Β (Gy-2)
AGO | X-ray | 0.370.03 | 0.130.01
 | e- | 0.680.08 | 0.010.01
E2 | X-ray | 0.320.01 | 0.090.01
 | e- | 0.510.14 | 0.010.03
Cell line | source | ⍺ (Gy-1) | Β (Gy-2)
AGO | X-ray |  | 
 | e- |  | 
E2 | X-ray |  | 
 | e- |  | 
High alpha, low beta!

## Slide 18
LhARA, September 2024
Conor McAnespie
Gemini – Femtosecond scale irradiations

## Slide 19: Femtosecond-scale irradiations
LhARA, September 2024
Conor McAnespie
Cell line | source | Foci at 24hr | RFI at 24hrs
AGO | x-ray | 0.9 0.4 | 1.44 0.92
 | e- | 1.3 0.6 | 
E2 | x-ray | 1.3 0.4 | 1.46 0.70
 | e- | 1.90.7 | 
Cell line | source | Foci at 24hr | RFI at 24hrs
AGO | x-ray |  | 
 | e- |  | 
E2 | x-ray |  | 
 | e- |  | 

## Slide 20: Further foci analysis
LhARA, September 2024
Conor McAnespie
Subpopulation of 53BP1 foci at 24 hours after irradiation highlight a trend for more damages from VHEE electrons.
Size of the induced foci also indicated a more complex damage site.

## Slide 21: Femtosecond-scale irradiations
LhARA, September 2024
Conor McAnespie
AGO - Skin
E2 - Cancerous
Cell line | RBE at 50% survival
AGO 1522D | 1.41 0.08
E2 | 1.40 0.08
Cell line | RBE at 50% survival
AGO 1522D | 
E2 | 
C.A. McAnespie, et. al.- Submitted 2024

## Slide 22: Limitations
LhARA, September 2024
Conor McAnespie
Shot-to-shot fluctuations in position and level of dose
  Laser energy / pointing
  Target misalignment / imperfections
Regimented access to facilities to perform detailed experiments with multiple repeats.

## Slide 23: Conclusions
LhARA, September 2024
Conor McAnespie
Performed successful irradiations of biological samples at picosecond and femtosecond level with laser driven sources.
Measured increased biological effectiveness at the femtosecond level in both healthy and cancerous tissue.

## Slide 24: Collaborators
LhARA, September 2024
Conor McAnespie
CLMI
H. Maguire
L. Calvin
K. Fleck
M. Streeter
E. Gerstmayr
J. Sarma
G. Sarri
B. Kettle
S. Mangles
J. Mill
D. Jaroszynski
PGJCCR
C. McDonnell
S. McMahon
K. Prise
N. Bourgeois
O. Finlay
S. Needham
S. Botchway
P. Chaudhary
G. Schettino

## Slide 25
LhARA, September 2024
Conor McAnespie
Thanks for your attention!