## Slide 1
Exploring the use and delivery of laser-driven proton beams for ultra-high dose rate radiobiology at the BELLA Center
Jared De Chant*, J. L. Inman, L. Obst-Huebl, A. McIlvenny, K. Nakamura, S. Hakimi, J. H. Bin, C. G. R. Geddes,
L. Geulig, A. J. Gonsalves, S. Kidd, J.-H. Mao, C. Palmer, C. Y. Ralston, C. B. Schroeder, B. Simmons,
B. Stassel, S. Subramanian, J. van Tilborg, A. M. Snijders, E. Esarey
Lawrence Berkeley National Laboratory
*Also at Michigan State University
ITRF/LhARA Collaboration Meeting #6
Belfast, UK, Sep 3, 2024
Work supported by the U.S. DOE Office of Science, Offices of FES and HEP, and LaserNetUS under Contract No. DE-AC02-05CH11231 and Laboratory Directed Research and Development Grant, PI A. M. Snijders

## Slide 2: Outline
Investigating FLASH Radiotherapy with laser-driven ion acceleration at the BELLA Center
The challenges of delivering laser-driven ions for radiobiological applications
  Beam transport
  Dosimetry
Initial in vitro radiobiological experiments at the long focal length (LFL) beamline with an active plasma lens (APL)
Design and implementation of permanent magnet-based beam transports for 10 & 30 MeV protons
Recent LaserNetUS radiobiological experiments:
  irradiation of in vivo samples with laser-driven ions (~7 MeV) and
  irradiation of peptides in solution with laser-driven ions (7-30 MeV)

## Slide 3: BELLA (Berkeley Lab Laser Accelerator) Center houses multiple laser systems enabling a wide range of applications[1]
BELLA-PW (iP1)
40 Joule in 40fs (1 PW)
GeV acceleration, Staging
Proton & ion acceleration
BELLA-HTT
3 Joule in 30fs (100 TW)
Mono-chromatic gamma rays
BELLA-HTU
3 Joule in 30fs (100 TW)
X-ray laser
BELLA-iP2 at BELLA-PW
40 Joule in 40fs (1 PW)
Proton & ion acceleration
BELLA-KHz
A few mJ in 5fs (TW)
MeV Acceleration
[1] K. Nakamura et al., Journal of the Particle Accelerator Society of Japan 19, 205 (2023)
BELLA FIBER
100s mJ in <100fs (>1kHz)
Laser R&D
Light sources at >1kHz

## Slide 4: Recent upgrades of the BELLA PW Laser facility enable groundbreaking research on laser plasma-based particle acceleration (e- & p+)
comp1
OAP1
DM 1&2
iP1
OAP3
Sf-OAP
comp2
OAP2
2BL focus
BS
Main Amplifier table
GAIA pump lasers (x12)
Control room
Gowning room
1BL focus
Diagnostic room
Laser room
Shielded room
5 m
iP2
- Two interaction regions iP1 (LFL, f/65) and iP2 (SFL, f/2.5)
- Second beamline (2BL) enables multiple LPA stages
- iP2 enables high-intensity laser plasma interactions
On target | Value
Rep-rate | 1 [Hz]
Energy | 40 [J]
Peak Power | 1 [PW] (for 40 fs)
Peak Intensity (iP1) | 1.5 [1019 W/cm2] (for w0 53 μm)
Peak Intensity (iP2) | > 1 [1021 W/cm2] (for w0 2.7 μm)

## Slide 5: The laser-driven ion accelerator at BELLA is a good platform for studying ultra-high dose rate radiobiology due to its short pulse and high intensity
Time
Log(amplitude)
Laser-driven
protons
Conventional
Protons
MHz
Hz
Mean dose rate 1800 Gy/min
Laser-driven protons:
instantaneous dose rate >107 Gy/min
High rep rate (1 Hz) tape drive target
13 µm Kapton tape
Target Normal
Sheath Acceleration
1013 ions/shot
~ps pulse duration at source
High intensity laser
>1021 W/cm2
2.7 µm focal spot
40 J
Target
TPS*
Short focal length F/2.5 OAP
iP2 target chamber
*Thompson parabola spectrometer

## Slide 6: Recently achieved proton energies up to 45 MeV with ~22 J laser energy; enables the irradiation of thicker samples
TPS/RCF measured proton spectra at source
TPS measured proton spectra
Waterfall plot of proton spectra measured by TPS with varying target z positions relative to laser focus
Particles will deposit their energy at different depths according to their Bragg peak
Sample proton spectra measured by TPS scaled to match particle number measured with radiochromic film (RCF) placed 10 cm from the laser target

## Slide 7: Outline
Investigating FLASH Radiotherapy with laser-driven ion acceleration at the BELLA Center
The challenges of delivering laser-driven ions for radiobiological applications
  Beam transport
  Dosimetry
Initial in vitro radiobiological experiments at the long focal length (LFL) beamline with an active plasma lens (APL)
Design and implementation of permanent magnet-based beam transports for 10 & 30 MeV protons
Recent LaserNetUS radiobiological experiments:
  irradiation of in vivo samples with laser-driven ions (~7 MeV) and
  irradiation of peptides in solution with laser-driven ions (7-30 MeV)

## Slide 8: Delivering laser-driven ions to biological samples is challenging due to their high divergence, broad energy spread, and shot-to-shot variability
A beam transport system is required to:
            collimate the highly divergent beam,
            select the desired energy,
  and deliver a high dose rate with a uniform profile.
On-shot dosimetry is required to:
            account for shot-to-shot fluctuations
            and ensure uniform dose deposition.
Beam divergence 10-30°
Measured proton spectrum (iP2)
Proton profile stability measurement
Plastic scintillator (EJ-260) 10 cm from source with 300 μm Cu attenuator to block proton energies < 10 MeV

## Slide 9: BELLA and other groups have attempted to address the challenges with transporting laser-driven ions by using advanced beam optics
*Not demonstrated in LDA experiments
Active plasma lens
Strong focusing field
Small bore  low capture efficiency
Axially symmetric focusing
HZDR DRACO
  Large energy acceptance and collection efficiency
  Strong possibility of quenching (laser or ions)
Superconducting achromats*
Pulsed solenoid
Strong focusing field
Low rep rate
Large bore  high collection efficiency
BELLA PW iP1
F. Kroll, et al.. Nat Phys. 2022 doi:10.1038/s41567-022-01520-3
J. H. Bin, L. Obst-Huebl, et al., Sci. Rep. 2022
W. Wan, L. Brouwer, et al.. Phys. Rev. ST Accel. Beams 2015 doi:10.1103/PhysRevSTAB.18.103501
Notes: Add citations
Make table of pros and cons

## Slide 10: Long focal length (F/65) BELLA PW beamline (iP1) allows for acceleration of low divergence, high charge, < 10 MeV proton beams
BELLA laser beam
Ion beam
TPS
Tape drive target
Steinke et al., PRAB 23, 021302 (2020),
J.H. Bin et al., Rev. Sci. Instrum. 90, 053301 (2019)

## Slide 11: Capture and transport of fraction of proton beam with active plasma lens (APL)
11
J. van Tilborg et al., PRL 115 (2015) 184802.
APL provides strong, compact focusing
- Compact strong B-field (1mmD, 33 mm unit)
- Radially symmetric focus
- Tunable via current (timing)
- ~20 years of experience and infrastructure ready
Neutral particles, X-rays
Protons, ions
For radbio experiment at iP1,
APL + Dipole was chosen to fulfill requirements.
Limitation 
Small bore (1 mm D) limits ion capture and transport and is not easily scalable

## Slide 12: Outline
Investigating FLASH Radiotherapy with laser-driven ion acceleration at the BELLA Center
The challenges of delivering laser-driven ions for radiobiological applications
  Beam transport
  Dosimetry
Initial in vitro radiobiological experiments at the long focal length (LFL) beamline with an active plasma lens (APL)
Design and implementation of permanent magnet-based beam transports for 10 & 30 MeV protons
Recent LaserNetUS radiobiological experiments:
  irradiation of in vivo samples with laser-driven ions (~7 MeV) and
  irradiation of peptides in solution with laser-driven ions (7-30 MeV)

## Slide 13: Active plasma lens transport: Experiment/Simulation showed good agreement, providing ~1 cm beam for in vitro cell studies
J.H. Bin et al., Rev. Sci. Instrum. 90, 053301 (2019)
L. Geulig et al., Rev. Sci. Instrum., 93, 103301 (2022)
RCF
Simulation
1cm2
RCF Stack
On-sample spectrum

## Slide 14: Cell holder design and automation drains sample solution during irradiation allowing for low energy protons to pass through
14
Design for cell culture holder with following characteristics:
1 cm irradiation field
Stretched 3.6 um thick mylar membrane windows
Rubber leak proof seals
Remove culture media during irradiation
After radiation move media back onto cells
Successfully proton-irradiated 56 cell samples in two days with a total of 1000 PW-laser shots

## Slide 15: Offline/absolute (RCF) and online/relative (ICT) diagnostics are used to determine the dose applied to every irradiated cell sample
1 cm
Dose on cells:
1 Gy per shot
Variation across sample: 20 % due to beam profile non-uniformity
Integrating current transformer (ICT)
fielded for online dosimetry
L. Geulig et al., Rev. Sci. Instrum., 93, 103301 (2022)
J.H. Bin et al., Rev. Sci. Instrum. 90, 053301 (2019)
10 shots
16 shots
20 shots
Proton pulse length ~30 ns  instantaneous dose rate of 4×107 Gy/s
mean dose rate: 0.5 Gy/s (pulse separation 5 s)

## Slide 16: Laser accelerated ions delivered by active plasma lens to cell sample -differential sparing between normal and tumor cells observed
1 cm
Dose on cells:
1 Gy per shot
- PC3 prostate tumor cells
- RWPE1 normal prostate cells
J. H. Bin et al., Sci. Rep. 12 1585 (2022)
LD protons: ultra-high instantaneous dose rate
X-rays: clinical dose rate
Limitations:
Dose homogeneity and shot to shot fluctuations
Clinical proton dose rate reference is missing (X-ray radiobiological effectiveness is different)  influence of LET?
Oxygen tension is unknown
More cell types needed
In vivo study needed

## Slide 17: Outline
Investigating FLASH Radiotherapy with laser-driven ion acceleration at the BELLA Center
The challenges of delivering laser-driven ions for radiobiological applications
  Beam transport
  Dosimetry
Initial in vitro radiobiological experiments at the long focal length (LFL) beamline with an active plasma lens (APL)
Design and implementation of permanent magnet-based beam transports for 10 & 30 MeV protons
Recent LaserNetUS radiobiological experiments:
  irradiation of in vivo samples with laser-driven ions (~7 MeV) and
  irradiation of peptides in solution with laser-driven ions (7-30 MeV)

## Slide 18: Permanent magnet quadrupoles (PMQs) are compact, high field gradient focusing elements with a large bore, necessary for maximum charge collection
Permanent magnets can be arranged in a Halbach configuration to produce a strong focusing gradient (100s T/m) with a large bore (10-50 mm)
K. Halbach, Nucl. Instrum. Methods. 1980
A. Ghaith et al. Instruments 2019 https://doi.org/10.3390/instruments3020027
LMU Munich PMQ
T. Rösch, PhD dissertation, LMU Munich 2022
D. Margarone et al. ELIMAIA: A Laser-Driven Ion Accelerator for Multidisciplinary Applications. Quantum Beam Sci. 2018 https://doi.org/10.3390/qubs2020008
ELIMAIA: ELIMED beamline
Notes: Talk about other beamlines (lucas Brouwers work)

## Slide 19: Permanent magnet quadrupoles (PMQs) are compact, high field gradient focusing elements with a large bore, necessary for maximum charge collection
Purchased from Radiabeam and Radial Magnets
NdFeB
Permanent magnets can be arranged in a Halbach configuration to produce a strong focusing gradient (100s T/m) with a large bore (10-50 mm)
Compact transversely and longitudinally and radiation resistant
Not easily tunable but simple to construct and commercially available
iP2 magnet parameters | M1 | M2 | M3 | M4
Inner radius (mm) | 5 | 15 | 20 | 25
Gradient (T/m) | 219.5 | 59.7 | 37.3 | 29.0
Effective length (mm) | 50.25 | 50.10 | 57.9 | 60.1
Strength (T) | 11.03 | 2.99 | 2.40 | 1.92
iP2 magnet parameters | M1 | M2 | M3 | M4
Inner radius (mm) | 5 | 15 | 20 | 25
 | 219.5 | 59.7 | 37.3 | 29.0
 | 50.25 | 50.10 | 57.9 | 60.1
 | 11.03 | 2.99 | 2.40 | 1.92
Designed in Radia
(mm)
Notes: Talk about other beamlines (lucas Brouwers work)

## Slide 20: Transports were modeled and optimized using COSY Infinity while performance was estimated based on high order particle tracking
COSY Infinity
Software package for the simulation of particle optical systems
Uses differential algebra (DA) techniques to compute Taylor transfer maps to high order
3rd order maps and above are necessary due to the large energy spread of the beam
Monte Carlo Particle Tracking
Performed in MATLAB by passing a large number of particles (>107) through the COSY-generated map
Models the effect of the beam passing through matter (Kapton window, air, RCF, etc.) and estimates the dose deposited in the sample

## Slide 21: Permanent magnet-based beam transports for 10 & 30 MeV protons were installed in the BELLA iP2 beamline and used for RadBio experiments
Two configurations were implemented, designed to collimate protons with energies of 10 MeV and 30 MeV. The PMQs are mounted on motorized stages to easily switch between configurations.
After collimation, the beam is deflected with the dipole to separate the co-propagating neutrals and electrons and for spectrum manipulation.
On-shot dosimetry was performed with radio chromic films (RCFs) and an online integrating current transformer (ICT).

## Slide 22: Permanent magnet-based beam transports for 10 & 30 MeV protons were installed in the BELLA iP2 beamline and used for RadBio experiments
Two configurations were implemented, designed to collimate protons with energies of 10 MeV and 30 MeV. The PMQs are mounted on motorized stages to easily switch between configurations.
After collimation, the beam is deflected separation from co-propagating neutrals and electrons and for spectrum manipulation.
On-shot dosimetry was performed with radio chromic films (RCFs) and an online integrating current transformer (ICT).

## Slide 23: Beam transport system successfully delivered over 1 Gy/shot to the samples while maintaining a uniform dose profile
Chart: Target z from focus / µm
| -150 | -100 | 50 | 0 | 50 | 100 | 150
10 MeV transport | 548.7986 | 487.1534 | 199.6654 | 135.7121 | 450.6434 | 480.5938 | 231.0838
30 MeV transport | 106.8955 | 128.9371 | 82.5856 | 51.5081 | 113.8272 | 142.8334 | 64.2904
No transport | 32.8131 | 49.092 | 19.5488 | 14.4978 | 44.8389 | 29.6944 | 30.0768
Simulated profile
Measured profile
After 8 mm D collimation
Transport boosted the charge delivered to the sample by at least x5
Notes: Need to rotate, crop

## Slide 24: Online dosimetry performed by correlating the charge measured by the ICT to the dose measured by in situ RCF
Chart: Summed* ICT charge / nC
| 0.54400000000000004 | 0.999 | 0.54500000000000004 | 0.95 | 0.31480000000000002 | 0.65500000000000003 | 1.75
 | 5.3559 | 10.4458 | 6.6327 | 8.8865 | 4.3956 | 7.3712 | 16.7315
Dose-charge correlation
Raw ICT Signal
145 pC
L. D. Geulig et al., Rev Sci Instrum 2022
Modeling the measured beam spectrum through the beamline, the dose values measured by the RCFs were scaled to account for their LET-dependent response.
Schollmeier et al. Rev. Sci. Instrum. 2014
*Accumulated over multiple shots

## Slide 25: Outline
Investigating FLASH Radiotherapy with laser-driven ion acceleration at the BELLA Center
The challenges of delivering laser-driven ions for radiobiological applications
  Beam transport
  Dosimetry
Initial in vitro radiobiological experiments at the long focal length (LFL) beamline with an active plasma lens (APL)
Design and implementation of permanent magnet-based beam transports for 10 & 30 MeV protons
Recent LaserNetUS radiobiological experiments:
  irradiation of in vivo samples with laser-driven ions (~7 MeV) and
  irradiation of peptides in solution with laser-driven ions (7-30 MeV)

## Slide 26: First animal irradiation at BELLA with ~7 MeV laser-driven protons to investigate radiation damage to mouse ear tissue in vivo shows sparing compared to x-rays
7 mm
Preliminary data
36 Gy +/- 1.1 Gy
4 shot days, total of 1220 shots & 60 irradiated animals with prescribed doses of 10 – 40 Gy
Bio endpoints: ear thickness and reddening
L. Geulig et al., Rev. Sci. Instruments 93 (2022) 103301.
J. De Chant et al., Journ. of Acc. Conferences, IPAC'24 MOPR72 (2024)
7 J

## Slide 27: First animal irradiation at BELLA with ~7 MeV laser-driven protons to investigate radiation damage to mouse ear tissue in vivo shows sparing compared to x-rays
7 J
Ongoing:
Biological tissue staining methods and transcript sequencing
Is RBE (proton/x-ray) = 1.1 valid?  Seeking proton reference irradiation opportunities
36 Gy BELLA prt
36 Gy X-rays
40 Gy X-rays
7 mm
Preliminary data
L. Obst-Huebl, J. Inman, et al., in preparation

## Slide 28: Outline
Investigating FLASH Radiotherapy with laser-driven ion acceleration at the BELLA Center
The challenges of delivering laser-driven ions for radiobiological applications
  Beam transport
  Dosimetry
Initial in vitro radiobiological experiments at the long focal length (LFL) beamline with an active plasma lens (APL)
Design and implementation of permanent magnet-based beam transports for 10 & 30 MeV protons
Recent LaserNetUS radiobiological experiments:
  irradiation of in vivo samples with laser-driven ions (~7 MeV) and
  irradiation of peptides in solution with laser-driven ions (7-30 MeV)

## Slide 29: First peptide experiments at BELLA iP2 with ~7-30 MeV protons were conducted in April 2024
29
“Flat” spectrum  uniform dose deposition
Sample Volume
20 J

## Slide 30: The stability of the higher energy TNSA source needs further improvement for systematic radbio studies
20 J
Cumulated dose / Gy
Cumulated ICT charge / nC
30
~1 Gy/shot
“Flat” spectrum  uniform dose deposition
Proton dose and spectrum declined over the course of sample irradiations due to a drift in the system when shooting the laser continuously
 Finding the source of this drift + implementing online spectral measurements are work in progress
time
Sample #
1
2
3
4
5
6
Sample Volume

## Slide 31: Outlook: explore physico-chemical step of FLASH effect with ultra-short electron bunches from laser plasma accelerator
“Very high energy electrons” (VHEE) ~150-250 MeV range, can penetrate large samples
Few 10 fs bunch length
  ultra-high instantaneous dose rate ~ 1012 Gy/s
  ultrafast access to the very early (physico-chemical) step of FLASH
Synchronized measurements with pulsed optical (incl. higher harmonics) & betatron x-ray beams
BELLA HTT LPA spectrum
Chappuis Physica Medica 110 (2023) 102601
LPA VHEE are increasingly recognized as a tool for radiobiology research/potential future radiotherapy: Laschinsky Radiat. Res. 53:395-403 (2012), Kokurewicz SPIE: Bellingham WA, USA (2017), Labate Sci. Rep. 10:17307 (2020), Cavallone Appl. Phys. B 127:57 (2021), Svendsen Sci. Rep. 11:5844 (2021),
+ startup company in Israel ebeam4therapy, …

## Slide 32: Outlook: explore physico-chemical step of FLASH effect with ultra-short electron bunches from laser plasma accelerator
“Very high energy electrons” (VHEE) ~150-250 MeV range, can penetrate large samples
Few 10 fs bunch length
  ultra-high instantaneous dose rate ~ 1012 Gy/s
  ultrafast access to the very early (physico-chemical) step of FLASH
Synchronized measurements with pulsed optical (incl. higher harmonics) & betatron x-ray beams
BELLA HTT LPA spectrum
1) Simulations with OpenTOPAS-nbio
A. Lu, J. De Chant
2) Build setup at BELLA HTT for in vitro/in vivo sample irradiations
Chappuis Physica Medica 110 (2023) 102601

## Slide 33: Summary
The laser-driven ion accelerator at BELLA iP2 is a good platform for investigating ultra-high dose rate radiobiology and was used in recent LaserNetUS experiments to explore the FLASH effect.
Permanent magnet-based beam transports for 10 & 30 MeV protons were installed in the BELLA iP2 beamline to improve the overall dose rate and uniformity of the dose delivered.
Experiments have explored:
  differential sparing of normal versus tumor tissue in both in vitro and in vivo (analysis ongoing) samples when irradiated with ultra-high instantaneous dose rate laser-driven protons and
  first peptide irradiation experiments at BELLA iP2 with ~7-30 MeV protons conducted in April 2024 (analysis ongoing).
Online dosimetry performed by correlating the charge measured by the ICT to the dose measured by in situ RCF.
Plan to explore physico-chemical step of FLASH effect with ultra-short electron bunches on the HTT beamline at BELLA.

## Slide 34
Kei Nakamura
Lieselotte Obst-Huebl
Aodhán McIlvenny
Sahel Hakimi
Antoine Snijders
Jian-Hua Mao
Jamie Inman
Laura Geulig
Jianhui Bin
Stepan Bulanov
Savannah Kidd
Anthony J. Gonsalves
Qing Ji
Carl B. Schroeder
Cameron G.R. Geddes
Brendan Stassel
Corie Ralston
Sayan Gupta
Brandon Russell
Charlotte Palmer
Simruthi Subramanian
Sven Steinke
Jeroen van Tilborg
Thomas Schenkel
Blake Simmons
Eric Esarey
Acknowledgements
We gratefully acknowledge the contributions of:
Zac Eisentraut, Mark Kirkpatrick, Tyler Sipla, Teo Maldonado, Art Magana, Joe Riley, Mackinley Kath, Wim Leemans, Eleanor Blakely, Samuel Barber, Csaba Toth, Jonathan Bradford, Greg Mannino and Nathan Ybarrolaza
Supported by the U.S. Department of Energy Office of Science Offices of High Energy Physics and Fusion Energy Sciences, under Contract No. DE-AC02-05CH11231 and by LaserNetUS

## Slide 35: The use of ultra-high dose rates in radiotherapy is recognized as a promising breakthrough in radiation oncology, but further research is needed
Radiotherapy is the current standard of care for > 50% of all cancer patients but its use is limited by access to facilities and healthy tissue toxicity.
FLASH effect: the differential sparing of healthy tissue under irradiation at ultra-high dose rates (historically >40 Gy/s)
M. Vozenin et al., Nature Rev Clin Onc, 2022, 10.1038/s41571-022-00697-z
S. Boucher et al., Snowmass 2021 White Paper, arXiv:2203.11047
Ion therapy center
Heidelberg
(1 Gy of dose equals the absorption of 1J of radiation energy per kilogram of matter)
?
Weeks after irradiation
Normal Tissue Damage (%)
Electrons
Durante et al., Br Radiol 2018 10.1259/bjr.20170628.,
Favaudon et al: Sci Transl Med. 2014 10.1126/scitranslmed.aba4525

## Slide 36
A peptide irradiation platform was established at the Advanced Light Source (ALS) to study dose rate effects on oxidative damage to peptides
X-ray footprinting mass spectrometry used with a reductionist approach (peptides in vitro) to isolate individual components of the FLASH effect
+16 Dalton
oxidative modification
Liquid Chromatography
Mass Spectrometry (LC-MS)
S. Gupta et al., Radiation Research 200(6), 523-530 (2023)
Ecrit = 3.1 keV
36

## Slide 37
S. Gupta et al., Radiation Research 200(6), 523-530 (2023)
A peptide irradiation platform was established at the Advanced Light Source (ALS) to study dose rate effects on oxidative damage to peptides
Dosimetry was conducted with radiochromic film
(Exposure time is determined by sample speed)
37

## Slide 38
S. Gupta et al., Radiation Research 200(6), 523-530 (2023)
The dose rate and oxygen dependent modification of peptides is confirmed in x-ray irradiations at the ALS versus at a conventional x-ray tube
Less damage after ultra-high dose rate than conventional dose rate irradiations
Less damage at low than atmospheric oxygen content
X-rays
38

## Slide 39
S. Gupta et al., Radiation Research 200(6), 523-530 (2023)
The dose rate and oxygen dependent modification of peptides is confirmed in x-ray irradiations at the ALS versus at a conventional x-ray tube
Less damage after ultra-high dose rate than conventional dose rate irradiations
Less damage at low than atmospheric oxygen content
6 MeV pulsed electron beam (linac)
39

## Slide 40
S. Gupta et al., Radiation Research 200(6), 523-530 (2023)
The dose rate and oxygen dependent modification of peptides is confirmed in x-ray irradiations at the ALS versus at a conventional x-ray tube
Less damage after ultra-high dose rate than conventional dose rate irradiations
Less damage at low than atmospheric oxygen content
6 MeV pulsed electron beam (linac)
Result: peptides can be used in a reductionist approach to study the damage by OH radicals under different radiation regimes and sample conditions
40

## Slide 41: BELLA iP2: Short focal length setup to achieve >2 orders higher intensity on target for ion acceleration and HEDS studies
iP2: New short focal length F/2.5
Focal spot measurements indicate >5x1021 W/cm2 for 40 J pulse energy
OAP
Option for double plasma mirror in PL1 →
Ultra high contrast and advanced ion acceleration mechanisms for iP2
Available for user experiments through LaserNetUS
41
L. Obst-Huebl et al., Proc. SPIE Optics and Optoelectronics (2023) submitted.

## Slide 42: Back reflections limited iP2 operation at higher laser pulse energies
1-10 mJ back reflected energy measured in rejected beam
μs HV pulse
Faraday rotation isolator and saturable absorber on selected shots were not able to prevent damage in Booster amplifier (focused geometry) ---- downstream 1 Hz PC did not function to specs (1μs HV pulse instead of 10 ns) --- now fixed
Safe operation up to 12 J on plastic foil target
1 cm diameter Ti:Sa crystal
L. Obst-Huebl et al., Proc. SPIE Optics and Optoelectronics (2023) submitted.

## Slide 43
Mechanism of FLASH effect is not well understood
Laser-driven radiation sources provide uniquely high intra-pulse (“instantaneous”) dose rates and are increasingly available in university-scale laser labs
They can contribute to FLASH research by complementing conventional accelerator facilities
Time
Log(amplitude)
Laser-driven
protons
Conventional
Protons
MHz
Hz
FLASH effect: the differential sparing of healthy tissue under irradiation at ultra-high dose rates
In-vivo study on mice irradiated with electrons
Constant total dose but different (mean) dose rates (blue vs. red)
(reminder: 1 Gy of dose equals the absorption of 1J of radiation energy per kilogram of matter)
Mean dose rate might be low but
instantaneous dose rate >107 Gy/min
Mean dose rate 1800 Gy/min
Weeks after irradiation
Pulmonary fibrosis (%)
Continuous growth of radiobiological research with laser-driven proton beams: A. Yogo et al., Appl. Phys. Lett. 94:181502 (2009), S. Kraft et al., New J. Phys. 12:085003 (2010), D. Doria et al., AIP Advances 2:011209, E. Bayart et al., Sci. Rep. 9:10132 (2019), F. Hanton et al., Sci Rep. 9:1-10 (2019), F. Kroll et al., Nat. Phys. 18:316-322 (2022), J. Metzkes, et al., Sci. Rep. 13:20611 (2023), Snowmass/Journal article: R. Schulte et al., Transformative Technology for FLASH Radiation Therapy, Appl. Sciences 13:5021 (2023)
Laser-driven proton pulses are uniquely short and intense and are therefore of interest to study radiobiological/radiotherapeutical effects induced by ultra-high dose rates
Notes: FLASH effect: several pre-clinical studies have shown that irradiation at dose rates far exceeding those currently used in clinical contexts reduce radiation-induced cell damage of healthy tissue
whilst maintaining an equivalent tumor response
  Pulmonary fibrosis (radiation induced lung tissue damage) substantially reduced when going to ultra-high dose rates of 60 Gy/s as can be achieved with conventional accelerators
  This differential effect could be even further enhanced when going for laser-driven protons with 10^7 Gy/s
unique time structure resulting in ultra-high instantaneous dose rates
Mice exposed to total 17 Gy with 4.5 MeV electrons

## Slide 44: In general, the literature recognizes that oxygen concentration may play an important role in the FLASH effect
Wilson et al. Frontiers in Oncology 2020 10.3389/fonc.2019.01563
44
Notes: Wilson: Some researchers have suggested that the differential response between FLASH-RT and CONVRT may be due to the radiochemical depletion of oxygen at ultra-high dose rates and subsequent radioresistance conferred to the irradiated tissue (32, 38, 39). It is widely accepted that hypoxic tissues are more radioresistant than well-oxygenated tissues. This is because in the presence of molecular oxygen there is fixation of indirect radiation-induced DNA damage. Indirect damage, the predominant mechanism by which low linear energy transfer (LET) radiation induces DNA damage, occurs when radiation results in the radiolysis of water molecules and the subsequent generation of free radicals. Free radicals are then incorporated into DNA, causing damage—yet this can be easily resolved. However, if a free radical reacts with molecular oxygen, this yields a peroxyl radical. Peroxyl radicals have the potential to induce permanent damage, and are therefore a more efficacious DNA damaging agent. Hence, a lack of oxygen in the immediate environment of a cell limits the extent of radiation-induced DNA damage (40).
The authors hypothesized at the time that this response was a consequence of oxygen depletion following a large dose of radiation in such a short timeframe; the time for which the bacteria were irradiated for was shorter than the time required for oxygen to diffuse and restore the oxygen that had been depleted. Given that molecular oxygen is depleted as it reacts with free radicals generated from the radiolysis of water, irradiation at ultra-high dose rates is able to significantly deplete oxygen before it can replenish. This gives rise to a small window of radiobiological hypoxia.
Adrian [2020]: Besides local and transient oxygen depletion, radical–radical interaction is another hypothesized reason for the FLASH effect. FLASH irradiation results in a high local radical concentration, leading to radical–radical interactions and less free radicals available to interact with DNA.17 Biological damage produced by X-ray/electron radiation is dominated by indirect action, i.e. free radicals interacting with DNA.18 Furthermore, radical-induced DNA damage can be permanently 'fixed' by molecular oxygen, rendering DNA damage irreparable. Consequently, lower oxygen concentration is recognized to cause radio-resistance.19

## Slide 45
1 cm
Dose on cells:
1 Gy per shot
RNA sequencing of cell samples suggests a possible role of different responses of normal versus tumor cells to oxidative stress
- PC3 prostate tumor cells
- RWPE1 normal prostate cells
J. H. Bin et al., Sci. Rep. 12 1585 (2022)
45
Cell samples were sealed off from air 24 hrs prior and 24 hrs after irradiation
Artificially reducing oxygen concentration to be more similar to in vivo conditions
RNA sequencing of cell samples showed differential expression of genes responsible for dealing with oxidative stress.
 E.g., down/up regulated in RWPE1/PC3:
  ATF3: responsive to reactive oxygen species (ROS), which induce permanent damage in cells
Notes: Dose estimation error:
Sample to sample fluctuations including shot to shot variation dominates the accumulated dose error per data point.
We are currently working on online dose diagnostics to ensure that the prescribed dose is applied.
- In vivo response may be very different from in vitro (you would not expect 99% killing):
  Immuno response
  3D effects in vivo different  usually more resistant than in vitro,
  only one cell type  different cell types interact to repair damage,
  individual cell sensitivity in the presence of oxygen differs between cell types
  wide range of oxygen concentrations in different cell types
  In irradiation setting: damage to cells is measured e.g. via reddening and blistering of the skin
why lower tumor survival for ref. x-rays, should be inverse (tumors hypoxic so less radiation damage)
  because this is in-vitro, no surrounding living organism that would result in hypoxic conditions
  needs to be studied in vivo
Is this in agreement with previous FLASH studies?
  This is the first study observing diff. sparing w/ ld protons, so no “prev data” to compare to
  For comparison of FLASH vs. CONV, where proton FLASH achieved with conv. Acc., so ~ 1000Gy/s: FLASH/CONV (for relevant endpoint for healthy tissues) is ~ -50-90% (Friedl et al 2021) at 10 Gy total dose.
Why FLASH effect observed in vitro in the first place? Normally not observed in vitro
  Adrian (2020): sparing effect depends on Oxygen concentration and we reduced oxygen by sealing cells off 24 hrs before irradiation.
    But this was done to both healthy and cancer cells, so both should be equally spared
      So the observed difference might be a result of different metabolic pathways involved in the response of normal and tumor cells. We observe indication of this in our RNA sequencing results