## Slide 1
Next 20 years: CLARA/FEBE
An informal, fun, and speculative view
Tom Pacey
ASTeC, Daresbury Laboratory
Cockcroft Institute 20th Anniversary 20/09/24
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 2: Outline
CLARA and FEBE
5 years of Awesome Experiments at FEBE
Legal Obligation: Diagnostics
10-20 years into future of CLARA

## Slide 3: My background
Undergrad at Manchester, project with Hywel Owen and James Jones, Storage Ring beam dynamics
First came to Daresbury 10 years ago for a tour with Hywel…a lot has changed!
PhD with Yuri Saveliev, Dielectric Wakefield Accelerators
  Bunch length measurements, tunable THz sources, Wakefield Dechirpers
Since 2019: CLARA Operation, User Exploitation (BA1), Diagnostics Development, FEBE Design…
BA1 Martin-Puplett interferometer, 2018

## Slide 4: Health warning
This is our (Daresbury Lab) flagship facility
CLARA vision changed from 10 years ago…
But we do have a strategy…
CLARA/FEBE over next 5 years is relatively clear
Truth is talking about facility/area in 15 years post 2029…
Everything presented is my own personal view and does not reflect the views of:
Diagnostics Group, ASTeC Senior Management, STFC, UKRI, or DSIT
All comments to be addressed to: rob.smith@stfc.ac.uk
Notes: Feeling pressure
Bring out the CDR
Bring out strategy

## Slide 5: CLARA layout

## Slide 6: FEBE Beamline & Hutch
Up to 250 MeV
250 MeV – 2 GeV
250 – 600 MeV
Highly instrumented beamline supports
- Setup & characterisation
- Feedback systems
PARS Design: G. Xia, O. Mete et. al. NIMA 2014
FEBE Design: E. Snedden et. al., PRAB 2024

## Slide 7
Tom Pacey, CI 20th Celebration, Sept 24

## Slide 8: Things we will do in the next 5 years
Finish CLARA
Finish FEBE
What does ‘Finish’ mean to me?
Spatio-temporal alignment & synchronisation of 120 TW laser with 250 MeV electrons:
Compressed pulses, <50um, <10fs in FEC1
…
Complete several competitive access exploitation periods
What would those periods look like?
Notes: Rather than list all of the many commissioning milestones along the way, boil it down to one specific technical achievement

## Slide 9: Some ways of doing FEBE experiments
Beam Driven wakefields: Staging
Flash Irradiation
External Injection Laser Wakefield Acceleration
Plasma wakefield: Advanced Diagnostics

## Slide 10: Aspirations for Awesome Experiments at FEBE
These are because I have:
  been involved in design of FEBE since 2019
  been in discussions with previous and prospective users over plans
  some ideas of what facility is design capable of
“Awesome” = what would be challenging/impactful/exciting
  Presented in no particular order
Suggesting some extra challenges, impactful areas
  Some experiments/goals will take multi-run iteration & development

## Slide 11: Awesome Experiments I would love to see at FEBE
Dielectric Wakefield: Beam Break Up suppression
  Structures across 2 FEBE chambers
  1.5m of wakefield structure, 100 MeV drive beam energy extraction
Beam driven PWFA experiments
  Support R&D EUPRAXIA @ SPARC
  Or R&D for HALHF
  Plasma optics, staging, plasma dynamics
Energy doubling of CLARA beam to 500 MeV using ex-injection LWFA
  Beam stabilised and held for 8 hours in the FEBE dump
Combined THz manipulation – plasma acceleration experiment
  Otherwise unreachable beam-laser optimisation
  (diagnostics, compression, shaping, sync.)
FLASH VHEE therapy on biological samples (cells)
FLASH VHEE diagnostics (dosimetry, beam shaping)
  Reliability Robustness, deployable in clinical setting
Single shot diagnostics for emittance & bunch length
  ‘RF Free’ & ‘EM Quad Free’
ML driven, ‘high dimension’ virtual diagnostics
  Optimise/provide high-order correction for CLARA beam,
  Measure the otherwise unobservable
Photon production from electrons
  Compton backscatter, undulator

## Slide 12: Awesome Experiments I would love to see at FEBE
If fully completed would be a very impressive science programme; broad, impactful
All of these experiment would be in led by, or in collaboration with Cockcroft Institute partners
To keep up with this programme need to average:
~2 “Awesomes” per year over 5 years…

## Slide 13
Legal Obligation:
Diagnostics are very important
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 14: Novel Accelerators as ‘THE FUTURE’
“We can make a GeV beam in only a few centimetres”
“We can simulate that quality is preserved under ABC scheme to X TeV”
Need to validate the models to scale to a FEL/Collider
Challenging experiments, not many places in world to do them
Precision diagnostics needed for models to be validated

## Slide 15: Challenge: Diagnostics for ‘Novel Accelerators’
Space = limited
Beam = rigid
Stability = variable
‘RF Free’
  CLF/EPAC don’t want to buy RF modulators etc. etc.!
Need: high precision, single shot diagnostics
Bunch profiles, emittances, longitudinal phase spaces…etc.
ML is a tool, not a catch all solution. We need to validate models
Need creativity, ‘new diagnostics’, and a test bed for experiments
FEBE can deliver these types of experiments

## Slide 16
CLARA/FEBE
in 10-20 years…
Speculating…
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.

## Slide 17: Bring back GeV Beams to Daresbury Lab
NINA 4.5 GeV, SRS 2 GeV
ALICE 30 MeV,
CLARA Ph.1 50 MeV, Phase 2 250 MeV
GeV technologies for CLARA:
  Lasers – FEBE laser 5 Hz…10 years R&D
  Beam driven, 40% transfer efficiency Drive - witness
  X band RF
Need to consider…Beam brightness, characterisation, stability, etc. etc. etc.
laser
High-tech. Flexible Compact Interesting
Powerful Fast Optimised Exciting

## Slide 18: CLARA – ‘Original Phase 3’
≈20m Undulators
≈ 10m Afterburner
≈ 10m e- Diagnostics
Modulator
≈ 40m space budget

## Slide 19: CLARA 1 GeV Booster Concept: Deliver within ~10 years
≈ 10m e- Diagnostics
Thanks Neil T for discussion on photons & scaling
0.25 → 1 GeV booster module
10 m (i.e. FEBE hutch)
~kA current bunch
e.g. SC Helical,
RF,
Halbach ‘comb’
Novel short period undulator section
10m sat. length
~5 keV Photons
~1 GW peak power
What could the booster look like?
FEBE prototyping?
FEL provides ‘proof of quality’
Phased Build?
Notes: I will present 4 boosters, in order of increasing Awesome and technical difficulty/risk

## Slide 20: CLARA 1 GeV Booster Concept: XARA (2019)
≈ 10m e- Diagnostics
Undulator section
15m
~0.5 keV Photons
100 uJ, ~4 GW
D. J. Dunning , L. S. Cowie1 , J. K. Jones ,
XARA: X-BAND ACCELERATOR FOR RESEARCH AND APPLICATIONS ,
THP066, FEL2019
Modulator
Add 3
X-band cavities
@ 70 MV/m
1 GeV

## Slide 21: CLARA 1 GeV Booster Concept: Collinear DWA Booster
≈ 10m e- Diagnostics
Novel short period undulator section
10m
~5 keV Photons
~1 GW peak power
500pC Drive (shaped)
50 pC Witness
Both at 250 MeV
5m long DWA structure
Modular construction
<1mm gap, BBU suppression
50 MV/m decelerating field
TR ≈ 3 Produces ~1 GeV witness
40-50% energy transfer, Fully passive.
CLARA creates and shapes
Drive + witness beams

## Slide 22: CLARA 1 GeV Booster Concept: Laser Wakefield Booster
≈ 10m e- Diagnostics
Novel short period undulator section
10m
~5 keV Photons
>1 GW peak power
≈ 20 pC Bunch
Highly Compressed >3kA
Low Emittance
≈ 10cm plasma cell
Transverse Matching Section
Post acceleration beam conditioning
CLARA creates high quality witness
Accelerated by FEBE laser
Notes: I will present 4 boosters, in order of increasing Awesome and technical difficulty/risk

## Slide 23
A 1 GeV Beam Driven Plasma Booster stage for CLARA…
(Not a copy of EuPRAXIA@SPARC)
…which could also be a test module for HALHF
Notes: EUPRAXIA@ SPARC – 1 GeV x band linac, configure for 500 MeV with a 500 MeV plasma booster stage
Shouldn’t copy that…but could as a 250 MeV – 500 MeV booster.
But they will beat us ont ime scales and energy, so why bother

## Slide 24: What is HALHF?
Hybrid Asymmetric Linear Higgs Factory: 250 GeV e+ e- c.o.m.
B Foster, R D'Arcy, and C A Lindstrøm, New J Phys, 2023
Beam driven plasma linac, 5 GeV → 500 GeV, 32 Stages, 500m
“Serious plasma collider”

## Slide 25: CLARA 1 GeV Booster Concept: PWFA Module Booster
≈ 10m e- Diagnostics
Novel short period undulator section
10m
~5 keV Photons
~1 GW peak power
Drive Beam:
250 pC (shaped)
250 MeV
Recipe:
HALHF: 32 GeV Drive, 5 GeV Witness → 37 GeV Witness
CLARA: 250 MeV Drive, 50 MeV Witness → 1 GeV Witness
≈40% Drive – Witness energy transfer
Compression and
matching line
5-10m
0.5 m plasma cell
0.5 GV/m gradient on drive
TR of > 4, (shown at PITZ)
≈2GV/m witness
Build accelerator next to CLARA!
(VELA will get jealous)
25 pC, 50 MeV in <5m
See CLARA Phase 1

## Slide 26: Incredibly preliminary simulation
Wake-T (as in HALHF paper)
Adopt shaping as in Loisch, PRL 2018
Drive bunch length 0.7ps
Plasma density 2 x 1016 cm-3
Non-optimised loading of witness
(Produced yesterday…)
Credit: Toby Overton
0.5 GV/m gradient on drive
≈2GV/m witness

## Slide 27: CLARA & FEBE next 20 years
We (CI) have the potential to carry out a very exciting and impactful experiments at CLARA on FEBE
We should develop high precision diagnostics for novel accelerators
We should bring GeV beams back to Daresbury
We could build a (really) novel energy booster to get to 1 GeV
Such a booster could be relevant to HEP Colliders

## Slide 28
Happy Birthday CI!
20 Years Old!
Thank you for listening
Notes: The abstract pattern can be removed or repositioned if required. Be careful to ‘Send to Back’ so that it does not obscure any important information.