## Slide 1: CMS: L1 Trigger Vertex Reconstruction using ML
By Walter Taylor
Acknowledgements: Dr Emmanuel Olaiya, CMS group
Notes: ML model ready for the L1 trigger upgrade 2026
CMS detector upgrade in 2026 – data collection rates are higher
In the upgrade, we can generate tracks and from tracks - identify the primary vertex of the event.
Previously used Application Specific Integrated Circuits - fast. Downside – no flexibility.

## Slide 2: Motivation and Aim
Predict the primary vertex using a neural network.
Lightweight enough to fit on a FPGA
Robust enough to be trained on a mixed data set and still perform on individual decay types.
Notes: Be able to design an NN that can identify a pv using track information – needs to be light low parameters – fast enough low latency that fits within time budget – also accurate – programmed to a fpga.

## Slide 3
https://youtube.com/watch?v=YKtPqh-P8lo

## Slide 4: Field Programmable Gate Arrays
Configurable integrated circuit that can be repeatedly programmed after manufacturing.
High signal speed
Low resource capability
Notes: Application Specific Integrated Circuits – can’t be reprogrammed after manufacturing
Benefit of an fpga – not waiting to the next cms upgrade to change the update the model.

## Slide 5: Data Processing
Simulated data root file processed into numpy arrays of track data.
TT̄ and QCD decay
Notes: Ttbar – high energy leptons. QCD – not many jets or high energy leptons hard to reconstruct vertex

## Slide 6: Timeline
Multi-layer Perceptrons
Notes: MLP – Multiple layers of neurons
Nonlinear activation functions to learn complex patterns in data
Feedforward propagation

## Slide 7: Timeline
Convolutional neural network
Notes: CNN identifies features in the dataset and uses that to learn patterns

## Slide 8: Timeline
Recurrent Neural Networks
  GRU
  SimpleRNN
Notes: RNN – Hidden layer can remember and use previous inputs for future predictions
Useful for sequential data

## Slide 9: Improving performance
Model types
Loss function
Model architecture
Notes: Loss func – how a model minimizes the error in prediction
Model architecture – how varying node number and layer number effects performance

## Slide 10: Improving performance: model types
TT̄
Notes: Kernel density estimate plot – show the difference at tails
Log y axis

## Slide 11: Improving performance: model types
TT̄
Notes: Zoomed in between errors of -1 and 1

## Slide 12: Improving performance: model types
TT̄
Notes: Integration of kde plot – easier to compare performance

## Slide 13: Improving performance: losses
TT̄
Notes: MAE – minimise average loss – works well for small errors
MSE – minimise squared loss – works well to reduce large errors
Huber – combination of the two – crossover defined by delta defined by delta

## Slide 14: Improving performance: model architecture
Mixed
Notes: Mixed data set by increasing layers and reducing number of nodes – increased performance

## Slide 15: Identifying individual decays
Mixed

## Slide 16: Restructuring data set
Find the probability of the primary vertex being in a certain bin.
Test the model using track data from the bin with the highest probability.
In preparation for the new CMS trigger where live data will come one bin at a time.
Focusing on TT̄.
Notes: Calc pv in each in calc prob of being a pile up or pv
Latency – we need a decision by a certain time – rnn has the latency benefits as rnn can make the calc as soon as you see the first tracks coming in.

## Slide 17: Performance
Simple RNN:
1321 parameters
Able to predict the correct bin 91.11% of the time for a bin size of 2
GRU:
4041 parameters
Able to predict the correct bin 91.72% of the time for a bin size of 2
TT̄
20
20
Input
RNN Layer 1
RNN Layer 1
Output
Notes: GRU has more ‘memory’

## Slide 18: Performance
TT̄

## Slide 19: Performance
TT̄

## Slide 20: Summary
Models trained on a mixed decay dataset can pick out individual decays.
Able to predict the primary vertex within a tolerance of 0.15cm 96% of the time on TT̄ decay.
Able to predict the correct bin 91% of the time.
Promising for implementation on an FPGA.

## Slide 21: Future work
Investigate the effects of overlapping the binned tracks on performance.
Look into hyperparameters in more detail to improve model performance e.g learning rate, batch number etc.
Include more decays in the dataset to see if the model can distinguish between different decays.
Implement model into FPGA.

## Slide 22: Thanks for listening Any questions