## Slide 1
Preparing for
Experiments at FEBE
Thomas Pacey
On behalf of the CLARA Team
ASTeC & TD, STFC Daresbury Laboratory
4th CLARA User Meeting,
December 3rd 2024
Notes: Welcome

## Slide 2: Outline
CLARA & FEBE Beamlines
FEBE Chambers
Electron Beam Parameters & Delivery
Summary

## Slide 3
CLARA &
FEBE Beamline

## Slide 4: CLARA
High brightness beam
Flexible & optimised parameters
Thoroughly instrumented beamline
Delivered to a shielded hutch

## Slide 5: FEBE Beamline & Energy Sectors
Up to 250 MeV
250 MeV – 2 GeV
250 – 600 MeV
All accelerated beam experiments subject to:
Experimental Risk Assessment
Shielding power limits
Radiation survey under experimental conditions
Further detail on FEBE beamline design can be found in
Snedden, E. W., et al. "Specification and design for full energy beam exploitation of the compact linear accelerator for research and applications." PRAB 27.4 (2024): 041602.
https://doi.org/10.1103/PhysRevAccelBeams.27.041602
BAM
ICT &
CTR
ICT

## Slide 6
FEBE Hutch and
Experiment Chambers

## Slide 7: FEBE Hutch Beamline: viewed on orientation similar to previous schematic
CLARA
250 MeV e-
Laser from roof
FEC1
FEC2
IP2
IP1
FEC = FEBE Experiment Chamber
IP = Interaction Point (e- foci)
More images at end of presentation

## Slide 8: FEBE Hutch – Viewed as one enters
CLARA
250 MeV e-
Laser from roof
FEC = FEBE Experiment Chamber
IP = Interaction Point (e- foci)
More images at end of presentation
FEC1
FEC2
IP2
IP1

## Slide 9: FEBE Hutch Plan
Shield wall
Dipole
Internal ~0.9m
Distance between nominal IPs
Distance last IP to dipole straight on port
Straight on port
e-
FEC1
4.9m
6.5m
FEC2
IP1
IP2
FEC = FEBE Experiment Chamber
IP = Interaction Point (e- foci)
Internal ~0.9m
Internal ~0.9m
Internal ~0.9m

## Slide 10: FEC1&2 Plan view – sectioned on beam axis
Base breadboard
e-
Slide door
Slide door
Slide door
Slide door
1.5 m
1 m

## Slide 11: FEC1&2 Side, sectioned on beam axis
Base breadboard
Feeds
Feeds
Feeds
e-
Internal 1.1M
Internal 1.8M
Beam height off base board 0.2515M

## Slide 12: FEC Chamber Doors
Design for FEC2 large doors to be confirmed. Circular ports all ISO flanges – see end of slides for sizes
CLARA
250 MeV e-
CLARA
250 MeV e-
FEC2
FEC1

## Slide 13: FEC Chamber Doors Annotated
Design for FEC2 large doors to be confirmed. Circular ports all ISO flanges – see end of slides for sizes
CLARA
250 MeV e-
CLARA
250 MeV e-
Large transparent viewport
Can be used for feedthroughs
Can be used as viewport or feedthrough
Centred on beam axis
Can be used as viewport or feedthrough;
Centred on beam axis
Can be used for feedthroughs
FEC2
FEC1
Centred over IP1

## Slide 14: Notes on chambers - Doors
Doors will be on ½ - 2/3 split as shown, and slide open.
  A clear access path to the centre of the chamber (IP1/2) is possible from either side.
Additional space is availible on the ‘north side’ of the chambers for tables and other breadboards
  Discuss us your requirements with us.
The final of design of the doors with large rectangular viewports is TBC early 2025
South
North

## Slide 15: FEC1 Top
CLARA
250 MeV e-
Viewport over IP1 or 2 (both) is possible from the top
Turbo pump locations cannot be changed

## Slide 16: FEC1&2 Plan view
e-
Slide door
Slide door
Slide door
Slide door
Turbo
Turbo
Port Line
Port Cluster
Port Cluster
Port Cluster
Port Cluster
Port Line
Port Cluster
Internal ~ 1.1m
Internal ~ 1.8m
Port Cluster
These port clusters are on interchangeable panels if required. Alternate panels to be provided by users.
Technical drawing on slide 27
Can be used as viewport or feedthrough
Centred on beam axis

## Slide 17: In Air Experiments
Experiments can be performed in air in either FEC1 or 2
There is an operational preference for FEC2 so that beam scatter and excess radiation is delivered to FEH back wall and not to other components
  If required by beam parameters, FEC1 can be used
There is an ICT before FEC2, providing on-shot absolute charge measurement for irradiation experiments
Internal flange mount for vacuum isolation window

## Slide 18: Gas delivery
Gas delivery will be possible to FEC1 , from a manifold outside of the hutch
  Upgraded version of BA1 system
We will be able to deliver: hydrogen, inerts, and premixed cylinders
  Gas delivery in absolute pressures.
  Remote control of backing line pressure regulators possible.
All gas delivery parameters subject to vacuum limitations and in-situ experimental verification of pumping performance.
  Specific limits will vary based on the geometry of gas target used.
For experiments with high gas load differential pumping may be required.
  Different requirements for the FEBE laser & for CLARA beam
  A conceptual design has been prepared for diff. pumping.
Schematic for H2 delivery system

## Slide 19
Photos of chambers
As Installed Dec 24

## Slide 20: FEC Chambers
FEC 1 from North, e- right to left
FEC1 narrow door w/ x2 ISO200 flanges
Bottom is on axis with e-
Slide door motion & safety system

## Slide 21: FEC Chamber Top
Some feedthroughs will be reserved for diagnostics

## Slide 22: Hutch
FEC1 from North Side
Narrow south side
Space will be used for commissioning diagnostics & search route

## Slide 23
Electron Beam Delivery

## Slide 24: Day 1 Electron Beam Parameters
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5
RMS t [fs] | 100 | 50
σE/E [%] | <5 | <1
RMS x [µm] | 100 | 20
RMS y [µm] | 100 | 20
εN x [µm] | 5 | 2
εN y [µm] | 5 | 2
Further detail on FEBE beam parameters can be found in
Snedden, E. W., et al. "Specification and design for full energy beam exploitation of the compact linear accelerator for research and applications." PRAB 27.4 (2024): 041602.
https://doi.org/10.1103/PhysRevAccelBeams.27.041602
To be delivered at either FEC1 or FEC2 IP
These parameters are for short beams.
If longitudinally compressed beam is not required, emittance will be reduced and transverse focus also reduced in size.

## Slide 25
Technical Systems Commissioning
All RF / diagnostics / magnets / controls ready for beam
Injector & Emittance
Characterise and optimise injector emittance and transverse properties
CLARA LPS measurements
Measure (TDC) CLARA long. phase space (LPS) and optimise to meet goals
CLARA Longitudinal Setup
Achieve required compression in CLARA and characterise beam
CLARA Longitudinal Dynamics Optimisation
Optimise CLARA LPS for multiple beam modes (Q, E, t, E etc.)
FEBE Standard Setups + Characterization
Optimise CLARA+FEBE for multiple beam modes (Q, E, t, E etc.)
0
1
2
3
4
5
COMMISSIONING COMPLETE
FEBE Technical Systems Commissioning
FEBE Advanced Technical Systems Commissioning
>x5 increase in all sub-components from CLARA front-end to CLARA Phase 2 + FEBE

## Slide 26: How Day 1 parameters will be verified
Parameter | High charge | Diagnostic | Low charge | Diagnostic
Energy [MeV] | 250 | FED Spec | 250 | FED Spec
Charge [pC] | 250 | FED FCUP & FEH ICT | 5 | FED FCUP & FEH ICT
RMS t [fs] | 100 | Wakefield Streaker + TDC & Modelling of FEBE Arc | 50 | TDC & Modelling FEBE Arc
σE/E [%] | <5 | FED Spec | <1 | FED Spec
RMS x [µm] | 100 | FEC Imaging | 20 | FEC Imaging
RMS y [µm] | 100 | FEC Imaging | 20 | FEC Imaging
εN x [µm] | 5 | FEBE Quad Scan | 2 | FEBE Quad Scan
εN y [µm] | 5 | FEBE Quad Scan | 2 | FEBE Quad Scan

## Slide 27: How you should use ‘Day 1’ Parameters
Please do use in simulations of experiments
  Where possible support proposals with simulations using day 1 parameters
Please do not submit proposals which are strongly contingent on R&D parameters for the first run
Consider how your requested beam parameters will be validated and make allowances for this in your plans
  We will support integration of our existing diagnostics systems into your experiments
  There will be constraints & resolution will be limited; performanceTBC in commissioning
If significant beam changes are needed, please discuss with us
  Short discussions will be offered in first instance
  We will have limited performance knowledge until we complete beam commissioning

## Slide 28: Flexibility of Delivery: Electron Parameters
Users must allow for beam time to tune to a beam setup when requesting time in a proposal
  Especially for first run(s)
  Please discuss any requests for setups with CLARA team in advance of proposal submission. We can advise an estimate of time required to tune, based on commissioning experience.
  Over time our number of quickly repeatable setups will evolve and increase.
We will strive to provide the beam most suited to experimental requirements; performance restrictions and time permitting.

## Slide 29: Tuning beam setups
In order of easiest to tune away from a ‘working point’ machine setup:
Electron focal position and size :
  Focus can be moved up- or downstream in either FEC
  This will compromise quality, best optics match is for IP1/2
  Laser focus is always centre of FEC1 at IP1 for first run.
Charge:
  Can be varied between 5 and 250 pC
  Tighter requirements on bunch length or size will require more tuning and optimisation time for a given charge
  If no requirements on length, and with relaxed focusing requirements, charge is more readily tunable.
Bunch Length and energy spread/chirp
  These are both tunable, but initial setups will be at fixed working points
  Delivering specific combinations of length or chirp will require dedicated modelling and setup time.

## Slide 30: The R&D Parameters
Also presented in PRAB:
  Snedden, E. W., et al. "Specification and design for full energy beam exploitation of the compact linear accelerator for research and applications." PRAB 27.4 (2024):
These are looking to the future
  Later runs we will publicize the 'actual' modes
Parameter | High charge | Low charge
Energy [MeV] | 250 | 250
Charge [pC] | 250 | 5 → <5
RMS t [fs] | 100 → 50 | 50 → <50
σE/E [%] | <5 → 1 | <1
RMS x [µm] | 100 → 50 | 20 → ~1
RMS y [µm] | 100 → 50 | 20 → ~1
εN x [µm] | 5 → <5 | 2 → 1
εN y [µm] | 5 → <1 | 2 → <1
  R&D: Verifying these parameters will require upgraded and/or new diagnostics

## Slide 31: Summary
There is a huge potential to exploit the full flexibility and performance of the CLARA Beam & the FEBE Hutch.
Our Vision: Maximising the potential of CLARA for its users
It will take us time to get there.
We will take input from you, our community, on what directions to explore and prioritise.
We will build up the complexity of experiments we can support.
Please work with us and discuss with us throughout the proposal call and experiment process.

## Slide 32
Backup slide
Appendix
& technical
Drawings

## Slide 33: 2D Plan View
South
North
CLARA
250 MeV e-
Laser from roof
Dims

## Slide 34: View from South
CLARA
250 MeV e-
Laser from roof

## Slide 35: View from North
CLARA
250 MeV e-
Laser from roof

## Slide 36: FEC1- Some additional Details; view from south
Internal Cage for Experiment support mounting
Usable internal dimensions will be slightly less than indicated in slides above because of internal cage, end plates and differential pumping baffles.

## Slide 37: FEC1 Top
CLARA
250 MeV e-

## Slide 38: FEC1 Plan: Section on Beam Axis
CLARA
250 MeV e-
Internal breadboard holes span across whole chamber

## Slide 39: FEC1&2 Side – Section on Beam axis
CLARA
250 MeV e-

## Slide 40: FMBOX1 – FMBOX2 Section on Beam Axis
CLARA
250 MeV e-
Laser from roof

## Slide 41
North Side
FLANGE | QTY | Colour | Designation | System Flange | Notes
ISO100 | 5 | Green | Free | N | 
ISO200 | 4 | Bright Yellow | Free | N | 

## Slide 42
Top
FLANGE | QTY | Colour | Designation | System Flange | Notes
ISO63 | 16 | Light Blue | Free | N | 
ISO80 | 12 | Turquoise | Free | N | 
ISO160 | 3 | Red | Free | N | 
ISO250 | 2 | Purple | TMP | Y | Bespoke adaptor designed – non-standard bolt pattern