## Slide 1: Radiation from a plasma undulator based on a plasma wakefield
Claudia Cobo, Louis Forrester, Adam Hughes, Runfeng Luo and Zulfikar Najmudin
CLARA User Meeting
3rd December 2024

## Slide 2: Introduction
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Electron bunch in the blowout regime
        Need nb > n
Uniform ion channel is associated with strong transverse fields
        Field varies linearly with x in a non-linear wakefield
Electrons undergo betatron oscillations and emit radiation
E. Esarey et al. Phys. Rev. E 65 056505 (2002)
Notes: NL regime – field varies linearly with x

## Slide 3: Plasma Undulator
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Wakefield generation
FBPIC simulations of wakefield driven by the CLARA beam
Beam density= 2 × 1022 m −3
Bubble size is appropriate for the CLARA beam size at plasma electron density 2×1021 m−3
n0 = 5×1022 m−3 at 3.2 ps
n0 = 2×1021 m−3 at 15.9 ps
Drive Beam Parameter | Value
Energy (MeV) | 250
Charge (pC) | 250
RMS duration (fs) | 50
Simulations by R. Luo
Notes: Linear field needs full cavitation (strongly driven regime) --> exploring if CLARA can drive this.
Coherent? Looking into that (Genesis + pIC) but challenging

## Slide 4: Plasma Undulator
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Witness beam timing
ekrgerhkj
Witness beam at position of zero accelerating field produces a nonevolving-energy beam over a long interaction distance
Energy change of witness beam minimised at 175 µm separation
Witness Beam Parameter | Value
Energy (MeV) | 250
Charge (pC) | 150
Duration (fs) | 50
Focal spot size (µm) | 13
Equilibrium spot size (µm) | 6
145 µm separation
175 µm separation
Drive beam position
Witness beam position
Simulations by R. Luo
Notes: alpha_twiss2=1.7482124925208413
beta_twiss2=0.01566260984793899
Zero accelerating field to make beam stable, extend interaction distance, minimise energy gain or lose

## Slide 5: Plasma Undulator
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Full Simulation Results
Energy gain/loss of witness beam could be improved by tailoring the beam current profile
Simulation Parameter | Value
Plasma density (1021 m−3) | 2
Interaction length (mm) | 300
Drive – witness separation (µm) | 175
Initial witness transverse offset (µm) | 10
Simulations by R. Luo

## Slide 6: Plasma Undulator
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Particle Trajectories and Energy Progression
Plasma Properties
ne= 2x1021 m-3
Lplasma = 0.3 m
K = 1.316 for 10 µm offset
λ = 91 nm
Notes: Drive 250pC

## Slide 7: Plasma Undulator
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Radiation Spectrum
Peak photon fluence of 105 photons/mrad2/0.1% BW
Broad synchrotron-like spectrum with critical energy of ~ 1keV
Total yield of 4x1011 photons above 0.01 keV in modelled radiation beam
Temporal Intensity Profiles
FWHM duration of 100 fs
Beam has a FWHM divergence of approximately 6 mrad along x-axis
The modelled x-ray beam has a peak brightness of 1021-1022 photons/s/mrad2/mm2/0.1% BW
Radiation Outputs (Radiation Computation Code)
Analysis by A. Hughes

## Slide 8: Plasma Formation in Experiment
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Plasma Properties
ne= 2×1021 m-3
Lplasma = 0.3 m
Simulated plasma parameters can be achieved with a discharge plasma source
Discharge Plasma Source
Parameter | Value
Tube length (m) | 1
Diameter (mm) | 19.5
Gas pressure (mbar) | 0.01 – 1.5
Discharge current (A) | ~ 400
Discharge time (us) | 1 - 100
Plasma electron density (1020 m-3) | 1 – 20

## Slide 9: Compton Scattering
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
Electron beam
250 pC = 1.56 × 109 electrons
Laser
2.5 J = 1019 photons
Laser volume ~ 3 × 10 15 m
Photon density = 3 × 1033 m − 3
Compton scattering cross-section
Photon energy 1.5 eV upshifted to 4γ2 hc/λ0 (a0 < 1): λC = 1.5 MeV
At high photon energies, approximate the total cross section as = 6.65 × 10 −35 m
Electron – photon collisions
Electron MFP = 1/photon density x = 5 m
Probability of collision in ~10 μm interaction length = 0.000002
Number of interactions = 3120 photons
Useful to probe radiation reaction
Preliminary Calculations
J. Cole et al. Phys. Rev. X 8 011020 (2018)

## Slide 10: Conclusions
Claudia Cobo c.cobo@imperial.ac.uk 4th CLARA User Meeting
We have modelled possible configurations of the CLARA electron beam propagating in a plasma channel, forming a plasma undulator
We offset the witness beam’s axis of propagation from that of the drive beam by 10 µm for enhanced radiation generation
We can produce a collimated, ultrashort, high brightness, broadband radiation beam comprising photon energies up to 10 keV
        100 fs FWHM duration
        6mrad FWHM divergence
        1021-1022 photons/s/mrad2/mm2/0.1% BW peak brightness

## Slide 11: Plasma Undulator
Witness beam matching