## Slide 1: Closed Shell Charge Breeding of Radioactive Fission Products with an Electron Beam Ion Source
September 10, 2025
Richard vondrasek
ICIS 2025
Science and Technology Facilities Council (STFC)
Oxford, England

## Slide 2
The work of many people made these results possible
nuCARIBU
G. Savard, R. Pardo, J. McLain, R. Scott, D. Santiago-Gonzalez, J. Nolen, J. Song, J. Clark
EBIS development
P.N. Ostroumov, C. Dickerson, S.A. Kondrashev, G. Zinkann, A. Barcikowski, G. Cherry, S. Sharamentov, J. Alessi, E. Beebe, A. Pikin
Helpful conversations
E. Beebe, A. Lapierre, B. Schultz, F. Wenander
This work was supported by the U.S. Department of Energy, Office of Nuclear Physics, under Contract No. DE-AC02-06CH11357. This research used resources of ANL’s ATLAS facility, which is a DOE Office of Science User Facility.
Acknowledgements

## Slide 3: Outline
The ATLAS facility
nuCARIBU
  Source of radioactive ion beams (1+ and 2+)
  An upgrade of the Californium Rare Ion Breeder Upgrade
EBIS charge breeder
  Raises 1+ and 2+ ions to n+ for post-acceleration
  Past performance
  Closed shell breeding
Current status

## Slide 4: atlas
Argonne Tandem Linac Accelerator System
ATLAS is primarily a stable beam facility for nuclear physics
  Beam current typically <500 pnA, energy <20 MeV/u
20-25% of beams are radioactive
  nuCARIBU - Heavy neutron-rich beams
  RAISOR - Light in-flight beams close to stability
Deliver ~6000 hours of accelerated beam each year
  Plus 2000 hrs/yr of CARIBU stopped beam
  24 hours a day / 7 days a week / 93% availability
  300-400 users per year

## Slide 5: Atlas
nuCARIBU – n-rich beams
EBIS – charge breeder
ECR2 – stable beams
ECR3 – C-14, stable
Surface Ionization Source - lithium
Ion sources

## Slide 6: nuCARIBU
Radioactive beams produced via neutron-induced fission
  6 MeV, 0.5 mA protons
  p-7Li reaction for neutron production
    1010 n/cm2
  Moderator
  Actinide target – 235U
    109 fissions/s
Fission fragments are thermalized in large volume helium gas catcher
Extracted as 1+ or 2+ ions
  Energy spread - 1 eV
  Emittance – 3 π·mm·mrad
Isobar separator - 1:20,000 resolution
Upgrade of CARIBU (2025)

## Slide 7: nuCARIBU
Lithium target
Design Parameters | 
Enriched Li-7 target | 4 cm x 0.1 cm
Beam power | 3 kW
Peak flux | 1 kW/cm2
Target temp | 170 °C
HX body temp | 130 °C
Water temp | 81 °C
Water velocity | 3 m/s
Design Parameters | 
Enriched Li-7 target | 
Beam power | 3 kW
Peak flux | 1 kW/cm2
Target temp | 170 °C
HX body temp | 130 °C
Water temp | 81 °C
Water velocity | 3 m/s
Al6063 HX
25 µm Mo
1 mm Li
p+

## Slide 8: nuCARIBU
RFQ cooler/buncher
Capacity: 105 ions/bunch Accumulation: 30-100 ms
Transmission: 70% (2+), 50% (1+)
Pulse width: 100 ns
MR-TOF
Capacity: 104 ions/bunch
Resolution: 1:100,000 Transmission: <50%
Hold-up time: 15 ms
EBIS
Frequency: 10 Hz
Breeding time: 30-90 ms
Efficiency: 10-70%
Stopped beam experimental area
Elevator
Beam energy
2 keV  25 keV
Isobar Separator
Resolution: 1:14,000
Transmission: 100%
Resolution: 1:20,000
Transmission: 60%
HIGH VOLTAGE PLATFORMS AND ECR3 ARE NOT SHOWN IN THIS VIEW
Gas catcher
1+ and 2+ ions
RFQ
Room temperature
60.625 MHz
A/q < 7
PII Linac
Superconducting
Cyclotron
6 MeV, 0.5 mA
Protons
ECR2
AECR-U type
14 GHz
Charge breeding cycle

## Slide 9
Warm bore
11 drift tubes
3 for trap
Electrostatic transport line
Injection/extraction cycle
Electron gun
3.9E-10 torr
20 kW Collector
7.3E-10 torr
1+
n+
EBIS Operating Parameters | 
Solenoid field | 5.5 T
Magnetic field on cathode | 0.15 T
Cathode diameter | 4.2 mm
Drift tube diameter | 20 mm
Electron energy in trap | 6300 eV
Electron current | 0.32 A
Effective electron current density in trap | 190 A/cm2
Trap length | 50 cm
Charge capacity | 2.2x1010
Injection time | 50 µs
Repetition rate | 10 Hz
Duty cycle | 50 %
EBIS bias | 20 kV
Pressure | 1x10-10 torr
Drift tube number
Voltage (kV)
Barrier drift tube
Trap drift tubes
EBIS Charge breeder
High-energy electron beam

## Slide 10
Ebis charge breeder
Breeding efficiency, EBIS only
Gun+trap: 6265 V
E-beam: 317 mA
Time: 49 ms
Cs+: 13.5 pA
86 epA
23%
Absolute efficiency
  Ratio of n+ particles out in a single charge state (SCS) to 1+ particles in
Stable Cs-133 from surface ionization source
  Pulsed deflector
    50 µs, ~10 epA
Radioactive beams from CARIBU
  All beams from Cf-252 (2017-2020)
High electron beam energies (>3 keV)
Moderate breeding times (<100 ms)
Broad charge state distributions (CSD) for the mid-mass species
Limits how many particles can populate a single charge state

## Slide 11: Closed shell breeding
Target large gaps in ionization energy at shell closures
  Narrow charge state distribution
  Enhance single charge state abundance
Set electron beam energy slightly below ionization energy of last electron in a shell
  Ionization of this charge state is inhibited
  Its relative abundance is enhanced
    R. E. Marrs, M. A. Levine, D. A. Knapp, J. R. Henderson, Phys. Rev. Lett. 60, 17, 1715-1718 (1988)
    R. Becker, "EBIS/EBIT: Electron Beam Ion Source/Trap," Handbook of Ion Sources, B. Wolf, Ed., Boca Raton, NY, London, Tokyo, CRC-Press, 157-182 (1995)
  Ba46+, 5.69-8.20 keV, continuous mode (EBIT)
    R. E. Marrs et al.
  Na9+, K9+,17+, Cu19+, 35-40% SCS efficiency
    F. Wenander, JINST 5, C10004 (2010)
  Ar16+, 4.95 keV and 1000 ms (EBIT)
    S. Geyer, A. Sokolov, A. Thorn, G. Vorobyev, h. Stohlker, O. Kester, JINST, vol. 5, no. C10003, (2010)
Improve single charge state efficiency
Cesium ionization energies. A. Kramida, Y. Ralchenko, J. Reader and NIST ASD Team (2023), NIST Atomic Spectra Database (ver. 5.11)
[Ar]3d10
[Ar]3d104s

## Slide 12: Closed shell breeding
Constraints
Desired charge state dictates electron beam energy
  Linac acceptance A/q < 7
  Ionization/radiative recombination > 1
Beam energy affects electron beam intensity
  Lower energy  less electron beam propagated
  Lower current density  longer breeding time
Shell Ionization Energy
+25 [Ar]3d104s2 875 eV
+26 [Ar]3d104s 916.1
+27 [Ar]3d10 1592
+28 [Ar]3d9 1672
NIST Atomic Spectra Database (ver. 5.11)
Cesium
R. Becker; O. Brinzanescu; Th. Stöhlker, AIP Conf. Proc. 572, 119–125 (2001)
Breeding window
  RFQ-C/B 10 Hz rep rate  100 ms window

## Slide 13: Closed shell breeding
Implementation
Selected 133Cs27+
  Electron beam energy in trap < 1592 eV
  Electron current limited to < 200 mA
  Electron current density ~ 50 A/cm2
Slowly lowered electron gun and trap voltages
  Lowered electron current to avoid virtual cathode
  Increased breeding time to stay on 27+ peak
Gun+trap: 6265 V
E-beam: 317 mA
Time: 49 ms
Cs+: 13.5 pA
Gun+trap: 2736 V
E-beam: 174 mA
Time: 79 ms
Cs+: 10 pA
Gun+trap: 2033 V
E-beam: 171 mA
Time: 89 ms
Cs+: 5.2 pA
87 epA
62%
86 epA
23%
10 charge states
7 charge states
4 charge states

## Slide 14: Closed shell breeding
EBIS Operating Parameters | 
Solenoid field | 5.5 T
Magnetic field on cathode | 0.15 T
Cathode diameter | 4.2 mm
Drift tube diameter | 20 mm
Electron energy (est.) | 1610 eV
Electron current | 0.172 A
Effective electron current density in trap (est.) | 280 A/cm2
Trap length | 50 cm
Charge capacity | 2.4x1010
Injection time | 50 µs
Repetition rate | 10 Hz
Duty cycle | 90 %
EBIS bias | 20 kV
Pressure | <1x10-10 torr
Low-energy electron beam
Cesium - measured absolute efficiencies (EBIS only).
Measured absolute efficiency and EBIS total efficiency versus breeding time. No tuning between data points.
Vgun: -890 V, Vtrap: 1141 V (applied voltage: 2031 V)
Effective electron current density estimated with EBISIM

## Slide 15: Closed shell breeding
Current density discrepancy
EBISIM best CSD fit for 89 ms breeding time
  Beam energy: 1610 eV
  Effective current density: 280 A/cm2
Observed by MSU and REXEBIS groups as well
  A. Gunnarsson et al., 2025, JINST 20 C03053
Mode | Beam energy (eV) | Expected current density (A/cm2) | Effective current density (A/cm2) | Breeding time (ms) | SCS eff. (%)
High energy | 6000 | 83 | 190 | 49 | 23
Medium energy | 2000 | 46 | 185 | 78 | 28
Low energy | 1610 | 43 | 280 | 89 | 72
Gas (xenon) | 6000 | 71 | 125 | 130 | ---

## Slide 16: Closed shell breeding
28+ presence
Suspect portion of 28+ is created during trap emptying cycle
  Breeding voltage: 1953 V
  Emptying voltage: 2913 V
  IE(27+): 1592 eV, IE(28+): 1672 eV
Trap cycle consists of two waveforms
  “Close to emptying” ramp
  “Emptying” ramp
Extended duration of ramp cycle 1  4 ms
  Held “emptying” ramp at 0.8 ms

## Slide 17: Closed shell breeding
Operational space assuming 100 ms breeding window
2p/3s transition
  Large energy differential
  Unrealistic current density?
3p/3d transition
  Realistic current density
  Moderate energy differential
    Limits effectiveness
3d/4s transition
  Large energy differential
  Realistic current density
    Need to explore lower Z region
      Zirconium, Z=40
60 A/cm2
1000 A/cm2
Compiled from NIST ionization energies. A. Kramida, Y. Ralchenko, J. Reader and NIST ASD Team (2023), NIST Atomic Spectra Database (ver. 5.11)
15+
22+
30+
27+
Zr
Cs

## Slide 18: Closed shell breeding
Zirconium
EBISIM
  Determine optimum beam energy
  Corresponding effective current density
    Constrained by Bursian limit
  Assume 80% device efficiency
Charge state | A/q | Beam energy (eV) | Effective current density (A/cm2) | Breeding time (ms) | Absolute SCS efficiency (%)
15+ | 6.67 | 573 | 59 | 89 | 72
22+ | 4.54 | 1160 | 171 | 89 | 43
30+ | 3.33 | 3788 | 1010 | 89 | 68

## Slide 19: nuCARIBU
First RIB out of gas catcher– June 18, 2025
  Proton current: 15 mA
    Limited by radiation levels
  142Cs1+, T1/2 = 1.687 s
First charge bred RIB – July 9
  Normal mode
  Proton current: 50 mA
    More shielding but still limited by radiation
Worked on closed shell mode with RIB – July 14
  Exceedingly difficult
Shifted to 100Zr2+ high energy mode – July 16
  Tested machine-learning-based tuning of injection line
  Started tuning beam through linac to target
Current status
~10 mA
~15 mA

## Slide 20: nuCARIBU
Lithium target failure – July 18, 00:45
  Breach between cooling circuit and vacuum
  Only 135 hours of beam on target
  Investigating failure mode
Current status

## Slide 21: summary
nuCARIBU
  First fission products (Cs-142, Ba-144, Zr-100) extracted from gas catcher
  Failure analysis of lithium target underway
Closed shell breeding with Cs-133 has been very effective
  72% single charge state efficiency
Need to establish closed shell breeding of RIBs
  Matching stable beam into EBIS is challenging in closed shell mode
  Doing this with RIBs is especially difficult
Investigating electron current density discrepancy