## Slide 2
Overview of the Heavy Ion Physics Programme at CERN Current and Future Ion Source Requirements and Challenges
D. Küchler, R. Alemany Fernández, G. Bellodi, B.S. Bhaskar, E. Mahner, R. Scrivens, M. Slupecki (CERN)

## Slide 3: Contents
Ion injector complex at CERN
Accelerators and users
GTS-LHC ion source
Operation
New Ion types
Requests from the users
Challenges and upgrade proposals
Summary and Outlook

## Slide 4: Accelerator complex at CERN

## Slide 5: A long history with ions
Ion front end with a duoplasmatron and an ECR type ion source on the Linac1 linear accelerator in the 80s
Study of ion beam transport through the CERN accelerator chain and first ion experiments using oxygen and sulphur ion beams
Design and construction of Linac3 (dedicated linear accelerator for ions with an ECR4 type ion source) at the beginning of the 90s
A new ion source (GTS-LHC) and the Low Energy Ion Ring (LEIR) designed and constructed at the beginning of the 2000s as part of the LHC ion injector complex upgrade to overcome brightness limitations
Linac1 front end with two sources

## Slide 6: Ion injector complex at CERN
2.5 keV/u
4.2 MeV/u
72.2 MeV/u
5.9 GeV/u
5.36 TeV/u
177 GeV/u

## Slide 7
Linac3 linear accelerator and GTS-LHC ion source

## Slide 8: Collider experiments

## Slide 9
Event displays of the collider experiments during lead-lead collisions

## Slide 10: Fixed target experiments

## Slide 11
Fixed target experiments
NA61/Shine in the North Area of SPS
HEARTS in the East Area of PS

## Slide 12: The GTS-LHC ion source
GTS-LHC ion source is an ECR type ion source based on the Grenoble Test Source, installed at Linac3 in 2005
14.5 GHz up to 2.2 kW, 10 Hz repetition rate, 50 ms microwave pulse
Operation in afterglow mode
Two operational micro-ovens
Pulsed bias disk up to 800 V
Three electrode extraction system with voltage up to 25 kV
PLC based controls integrated in the CERN controls network
Main ion type: 208Pb29+

## Slide 13: Source operation and beam performance
Ion @ Src | I / eµA | Ion @ Linac3 | I / eµA
40Ar11+ | 140 | 40Ar11+ | 60
129Xe22+ | 175 | 129Xe39+ | 34
86Kr22+ | 130 | - | -
24Mg7+ | 50 | 24Mg7+ | 19
16O4+ | 239 | 16O4+ | 93
20Ne5+ | 181 | 20Ne5+ | 59
208Pb29+ | 182 | 208Pb54+ | 31
Source extraction matched to 2.5 keV/u for RFQ injection
Stable part of the source pulse ~ 300 µs for LEIR injection
Some for the beams are stripped at the end of the linac
Transmission in the linac and stripper efficiency vary for the different ion types
Past short ion runs or tests
2015: Argon run up to SPS → for NA61
2017: Xenon run → for NA61 & LHC
2023: Krypton test → input for injector model & LHC Run 5
2023: Oxygen test → validation of LHC oxygen run in 2025
2024: Magnesium test → validation for NA61++ (Run 4, 2030+)
2025: Oxygen run → for LHC & NA61
2025: one day Neon run → for LHC (Nuclear imaging)

## Slide 14: Ion beam operation in the complex
300 µs of flat beam pulse from the linac with up to 5 Hz repetition rate
High pulse and pulse-to-pulse stability required (~ 5%)
Beam delivery during working hours from the source for the setup of all the machines in the ion accelerator chain followed by beam delivery 24/7 during the physics period of the different users
Operation periods of several weeks up to several months
Due to the long setup periods only two ion types per year possible
O
O
Pb
2025

## Slide 15: LHC Long-term schedule

## Slide 16: Motivation for new ion types
Physics
  Explore different regions of the phase diagram of quark-gluon plasma → ALICE, NA61/SHINE, NA60+
  Measure high-energy cross-sections for astroparticle physics models
  Enrich nuclear shape models (traditionally based on low-energy measurements)
Facilities
  Irradiation using wide range of linear energy transfer (LET) beams → HEARTS – facility for irradiation of space and accelerator electronic components and boards
  Gamma factory
    Using principle of resonant absorption and gamma boosted emission of photons
    Better intensity and higher energy of photons than traditionally used methods (inverse Compton scattering)
    Spin-off: possibly enable high-brilliance Ca beams and high-rate collisions (Use the same principle to cool the beam by emitting gammas)

## Slide 17: Future ion beam requests
These projects are not approved yet

## Slide 18: Status and Challenges Fixed target SPS North Area
NA61++ / SHINE (Run 4, 2030+)
  Beam test with magnesium done in 2024
    Sufficient intensity for LEIR injection
    Bottleneck found, to be retested
  2nd magnesium test planned for 2026
    Validation of mitigation against short oven lifetime Reduction of magnesium consumption by adding a tantalum hot screen in the plasma chamber
Beam test with boron planned for 2027
  At the source and Linac3
  Validation of decaborane (B10H14) delivered with the MIVOC setup
  Goal: Stability and beam intensity reach
NA60+
  Ongoing beam tests with lead

## Slide 19: Status and Challenges Fixed target PS East Area
  HEARTS – most demanding request for Run 4 (2031+)
    Provide: O, Ar, Kr, Xe, Pb
      No specific ions required, but rather a menu consisting of ions covering a wide mass range
    Every operational day, with switching times between species of maximum 15 minutes
    The experiment decides the order in which the species are delivered
    Switch between ions at will
    Impossible with present injectors: switching between ions takes days to weeks
    Cocktail beams to be tested at the source (not scheduled yet)

## Slide 20: Status and Challenges LHC
LHC experiments in Run 5
  One ion species to be selected to maximize nucleon-nucleon luminosity
  Need inputs from source operational tests with new ions for beam transport simulations along the accelerator chain
  Beam tests with krypton up to Linac3 done in 2023
  2nd krypton test possibly in Run 4
Nuclear physics at the LHC
  Many ideas, e.g. this years short LHC neon run
Gamma factory
  Proof of principle in the SPS is being prepared
Possible ions for LHC Run 5 and 6
All Linac3 currents are experimental values as known
in 2024, except for Ca, which has never been tested
One month integrated ion-ion luminosity
One month integrated nucleon-nucleon luminosity

## Slide 21
Ion Complex Upgrade study (ICU) Low-energy region of Linac3 – present limitations
  One ion source, fully committed to operation from Run 4
    Limited time for any tests (new ions, automation)
    Only up to two ion species (mixtures) can be operated per year
  Beam-destructive instrumentation located far away from the source extraction
    Minimal feedback while tuning parameters, especially when the source is unstable
    Source tuning based more on experience than measurements
    Time-consuming new beam development with trial-and-error
    Limited feedback for automation
    Beam dynamics model improvements limited
  CSD scans time consuming

## Slide 22
Ion Complex Upgrade study (ICU) 2nd source & new low-energy beam diagnostics
Specifications and caveats
  Position and connection of the new source is under discussion
    Need thorough study to select an optimal source type to fulfil the requests
    Need extensive beam dynamics study to select an optimal LEBT
    Most LEBT components need to be pulsed to monitor and optimize the performance of both sources when coupled with the RFQ concurrently
  Every beam pulse unused by downstream accelerators could be redirected to the beam diagnostic line
    Continuously measure charge-state distribution (2 min per full scan)
    On demand 2D beam profile measurement, emittance and energy distribution

## Slide 23: Summary and outlook
CERN has a long and rich history of ion beam acceleration and ion physics
Until the end of Run4 (2033) mainly lead will be operated for the collider physics at the LHC
    Ongoing studies to identify the optimal ion species for maximizing nucleon-nucleon luminosity in Run 5 Krypton is one candidate and a first test at the source was done
    There is growing interest in short LHC runs with lighter ions
Several new ion species have recently been tested (Kr, Mg) and operated (O, Ne)
    More tests have to be performed for validation and tests of the accelerator chain with these ions
    2nd magnesium test, boron, cocktail beams for HEARTS
A second source and an upgrade of the Linac3 front-end will be needed if some of the proposed projects would be approved and funded
A schedule cannot be given as it depends on the approval of the related projects and the availability of resources

## Slide 25
Operation with ions at CERN Past experience
In21+ from source >70 𝛍A
Stripped at the end of Linac3 to In37+, ~ 25 𝛍A
Stripped to In49+ before SPS
No attempt at LEIR NOMINAL beam
Ref: CERN-PS-2002-058-PP
115In 2003 (fixed target)
40Ar 2015 (fixed target)
129Xe 2017 (fixed target & LHC pilot run)
Xe22+ from source ~160 𝛍A
Stripped to Xe39+ at the end of Linac3, ~ 30 A
Stripped to Xe54+ before SPS
Attempted LEIR NOMINAL beam
Not stripped; at the end of Linac3: ~60 µA
Stripped to Ar18+ before SPS
No attempt at LEIR NOMINAL beam

## Slide 26
Operation with ions at CERN 2023: Pb, O, Kr