## Slide 1
A gasdynamic ECR ion source developed at IMP
and its preliminary results
Huanyu Zhao, Yuting Lu
Institute of Modern Physics, Chinese Academy of Sciences

## Slide 2: Outline
Motivation
Introduction to the gasdynamic ECR ion source
Preliminary results of the source
  The first ion beams
  Electron diagnostics of the plasma
Summary and outlook

## Slide 3: HIAF
High Intensity heavy-ion Accelerator Facility- HIAF
T1
iLinac
SECR
HFRS
SRing
BRing: Booster Ring
C: 569 m
Bρ: 34 Tm
SRing: Spectrometer ring
C: 278m
Bρ: 15Tm
iLinac: Superconducting linac
E: 17 MeV/u( 238U35+)
I : 1 emA
iLinac-2 (reserved)
E: 100 MeV/u U46+
Requirements for injector
Phase I (2018-2025)
~1 emA U35+ (1-5 Hz, 0.2-2 ms) from SECR
Phase II
2-10 emA U4n+ from pre-injector

## Slide 4: An alternative for front-end of HIAF

## Slide 5: Gasdynamic ECR ion source @ IMP
Operation mode | Pulsed (1 Hz, 5-10 ms width)
Microwave power | up to 20 kW
Microwave transmission | TE01 mode, circular waveguide (φ32.54 mm)
Magnetic field | Pulsed simple mirror trap (L=40 cm, R=3.3, Bmax up to 3.0 T)
Plasma chamber diameter | 45 mm
Extraction | 2-electrode system, φ1 mm aperture

## Slide 6: Magnetic confinement field- simple mirror
Axial B field distribution with different coil current
Typical waveform of exciting current
10 ms

## Slide 7: Microwave coupling module
Electric field norm (V/m)
Electric field distribution (10 kW) :
Transmission efficiency for TE01 mode
ECR zone outside the trap
Location of Bmax
Gas feeding
Waveguide
To avoid discharge outside the chamber
To protect the microwave window from the plasma

## Slide 8: The first beams- Nitrogen
Φ-plasma=1 mm
Current density reaches 128.0 mA/cm2 at 19 kV and 1.2×10-4 mbar in space-charge-limited mode.
Higher current can be obtained by moving the extraction system closer to the mirror plug.
RF power: 20 kW

## Slide 9: The first beams- Hydrogen
Typical waveforms with different pressure
Peak current density reaches 305.6 mA/cm2 at 19 kV and 4.1×10-4 mbar.
Compared with nitrogen, the working pressure is much higher for hydrogen.

## Slide 10: Electron diagnostics of the plasma
Leaking electron current measurement
Electron energy distribution
EUV spectroscopy of the plasma
Electron temperature
Relative electron density
Electron density

## Slide 11: Measurement of leaking electron current
Amplitude of current @ FC (mA)
Waveform of negative current @ FC
Current @ FC vs negatively biased voltage

## Slide 12: Fitting of electron energy distribution
Electron energy distribution can be obtained by fitting the curve of Ie vs Vbias

## Slide 13: Influence of microwave power on Te & ne
Both Te and ne tend to saturate with the increasing PMW, even decline for further increasing power.
Relatively low pressure is favorable for electron heating.
The Te of 100 eV can be obtained.

## Slide 14: Influence of gas pressure on Te & ne
Electron temperature decreases with gas pressure.
Electron density increases with pressure at first, then decreases with pressure.

## Slide 15: Influence of Bz on ne
Electron density increases with magnetic field.
No obvious pattern for electron temperature.
Pchamber=2.8×10-4 mbar

## Slide 16: Spectroscopy @ EUV
EUV Spectrometer
Range: 1-5 nm and 5-20 nm
Groove density: 2400 grooves/mm and 1200 grooves/mm
Resolution: 0.042 nm @ 15.15 nm

## Slide 17: Electron temperature diagnostics
Cross-section data from: Itikawa Y, Hara S, Kato T, et al. Atomic Data and Nuclear Data Tables, 1985, 33: 149-193.
The 5p-2s transition (12.46 nm) cannot be observed at low power or high gas pressure.

## Slide 18: Influence of microwave power and pressure on Te
The results are consistent with those from the leaking current measurements in terms of the value and trend of Te

## Slide 19: Electron density diagnostics
Kato T, Lang J, Berrington K E. Atomic Data and Nuclear Data Tables, 1990, 44(1): 133–187.
Dependence of ne on gas pressure is similar to the result of the leaking current measurement.
The electron density approaches to 1013 cm-3 at medium pressure.
O4+
20 eV
40 eV
100 eV
100 eV

## Slide 20: Te, ne dependence on PMW, pressure and B
Te
ne

## Slide 21: Summary and outlook
To meet the future requirements of HIAF on intense heavy ion beams, a gasdynamic ECR ion source has been being developed at IMP.
The beam intensity of hundreds of mA/cm2 was obtained.
The electron temperature and density of the plasma were diagnosed with the measurements of the leaking current and EUV spectra.
The microwave transmission and feeding system and the extraction system need further optimizing to explore the capability of the ion source.
To get higher charge states, the electron temperature need increasing.

## Slide 22
Thanks for your attention!