## Slide 1
Ion Sources in Alternative Fusion
Shadrach Hepner
Ion beam lead
Avalanche Energy
Shadrach Hepner1, Samantha Valenteen1, Scott Schipmann1, Siamak Rahmanian1, Robert Welton2, Robin Langtry1
1Avalanche Energy
2Oak Ridge National Laboratory
International Conference on Ion Sources
September 8, 2025
Oxford, England
Notes: Shadrach Hepner, representing Avalanche Energy, where we are using ion beams to pursue our goals of compact nuclear fusion.
Interest in fusion has surged recently, likely in part due to…

## Slide 2: The fusion reaction
H
X
n
David Moiraf, “The use of Plasma Mirror for Relativistic Electron Generation Relevant to Fast Ignition in Inertial Confinement Fusion”
~64 keV
High energy particle
(hydrogen isotope)
Target
High energy product (neutrons)
Ion sources are a great way to provide initial energy
Notes: Many ways to achieve these high energies – ion sources are certainly one of them. But this talk is about “alternative” sources- what does that mean?

## Slide 3: The Fusion Scene
Fusion
Tokamak
Stellarator
Laser-based inertial confinement
“Alternative”
Ion source
No Ion Source
Neutron generation
Energy production
How does the private sector use ion sources for these goals?
Notes: Shorten reactions- “Commonly hydrogen reactions for the purpose of high energy neutrons”
Maybe make the reactions their own slide
While publicity around private fusion focuses around energy production, the market for neutrons is significant and growing as well
First 3: ITER, Wendelstein-7X, NIF
(for reference): Public beam-related concepts:
Gamma10 tandem mirror (NBI)

## Slide 4
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
Notes: Mention that I have visited all but tae

## Slide 5
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
Notes: Mention that I have visited all but tae

## Slide 6: ECR beam-target fusion
Microwave power
Electron cyclotron resonance
High energy acceleration
Fusion Target
Solid target
Gas target

## Slide 7: SHINE Technologies
300 kV
100 mA D+
Gaseous tritium target
Differential pumping
Magnetic focusing
…
2.45 GHz
ECR
Ion source
5e13 n/s
R. Radel and L. Jacobson, “Characterization of SHINE’s High‑Flux DT Neutron Source,” presented at the Workshop for Applied Nuclear Data Activities (WANDA), Lawrence Berkeley National Laboratory, Feb. 2024.
Neutron Target
Irradiation Cavity
Notes: Mechanism:
(Permanent or electromagnets- could not find that information)
ECR ion source at 300 kV, produces ~100 mA
Magnetic focusing through multiple differential pumping stages
Focused through a gaseous tritium target to produce 5e13 n/s (continuous up to 132 hours)
Irradiation cavity houses target, surrounded by water for radiation suppression and water cooling’
Progression towards a potential plasma target to further increase neutron generation rate

## Slide 8: Adelphi Technology ECR neutron source
https://www.adelphitech.com
J. H. Vainionpaa et. Al., “Technology and Applications of Neutron Generators Developed by Adelphi Technology, Inc,” Physics Procedia, vol. 60, pp. 203–211, 2014, doi: 10.1016/j.phpro.2014.11.029.
Actively pumped: ~20 mA
Deuterium only, 1e10 n/s
“Sealed”: ~2 mA
Tritium enabled, 2e10 n/s
Notes: Portable, often shipped out of house
Can be found on all continents except Antarctica
Make this slide quick
Add something for scale (labelled line?)
Ask about permanent vs electro magnets
Tweak words here
Electro vs permanent magnets
Picture with scale (also scale of ECR chamber if available)

## Slide 9: Miniaturization
Miniaturizing the ion source
~1 cm scale plasma
<1 W power
Ion source having a magnetic field translatable along an axis of the source, U.S. Patent No. 11,574,788 B1, filed October 8, 2021, issued February 7, 2023

## Slide 10
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
300 kV, 100 mA
Gas target
5e13 n/s
100 kV, 2-20 mA
Solid target
2e10 n/s
Benchtop device
Notes: Mention that I have visited all but tae

## Slide 11
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
300 kV, 100 mA
Gas target
5e13 n/s
100 kV, 2-20 mA
Solid target
2e10 n/s
Benchtop device
Notes: Mention that I have visited all but tae

## Slide 12: Neutral beam injection (NBI)
I. Shikhovtsev et al., “Overview of neutral beam injectors for plasma heating and diagnostics developed at Budker INP,” J. Plasma Phys., vol. 90, no. 1, p. 155900301, Feb. 2024, doi: 10.1017/S0022377824000278.
Target plasma
Strong field
High energy ion deposition
Notes: Add bonus slide on negative sources for NBI (energy cutoff)
Generally kW-MW class neutral beam
Commonly used in traditional fusion to heat a plasma

## Slide 13: Magnetic Bottles
Magnetic bottle baseline geometry
Seed plasma
Neutral beam injection

## Slide 14: Magnetic Bottles
NBI directly heats and fuels the plasma
Ions go into diamagnetic orbits
External systems maintain stability

## Slide 15: Magnetic Bottles
NBI directly heats and fuels the plasma
Ions go into diamagnetic orbits
External systems maintain stability
Plasma generates closed field geometry

## Slide 16: Realta
Wisconsin high-temperature superconductor axisymmetric mirror experiment (WHAM)
1 NBI system, space for a second
D. Endrizzi et al., “Physics basis for the Wisconsin HTS Axisymmetric Mirror (WHAM),” J. Plasma Phys., vol. 89, no. 5, p. 975890501, Oct. 2023, doi: 10.1017/S0022377823000806.
Notes: NBI system from TAE- RF plasma version
https://arxiv.org/abs/2411.06644 - Hammir might use negative ion sources
WHAM vs Hammir vs Anvil?
Do a double check for published results since first plasma- if not mention that we have not seen any results publications

## Slide 17: Realta NBI system
25 keV, 40 A
Developed at Budker INP  TAE  WHAM
Heritage system from TAE architecture (C-2)
D. Endrizzi et al., “Physics basis for the Wisconsin HTS Axisymmetric Mirror (WHAM),” J. Plasma Phys., vol. 89, no. 5, p. 975890501, Oct. 2023, doi: 10.1017/S0022377823000806.
A. Sorokin et al., “Characterization of 1 MW, 40 keV, 1 s neutral beam for plasma heating,” Review of Scientific Instruments, vol. 81, no. 2, p. 02B108, Feb. 2010, doi: 10.1063/1.3266141.
L/s, cryogenic
25 keV, 40 A
Neutralizer (80 cm)
Notes: Realta achieved their first plasma in 2024 and are already in the planning phase for their higher power systems, which will require 1 MeV neutral beams for energy production (Hammir- this will be a negative source)
4 MHz, 10 mTorr
https://arxiv.org/abs/2411.06644 - Hammir might use negative ion sources

## Slide 18: Realta NBI system
25 keV, 40 A
Developed at Budker INP  TAE  WHAM
Heritage system from TAE architecture (C-2)
D. Endrizzi et al., “Physics basis for the Wisconsin HTS Axisymmetric Mirror (WHAM),” J. Plasma Phys., vol. 89, no. 5, p. 975890501, Oct. 2023, doi: 10.1017/S0022377823000806.
A. Sorokin et al., “Characterization of 1 MW, 40 keV, 1 s neutral beam for plasma heating,” Review of Scientific Instruments, vol. 81, no. 2, p. 02B108, Feb. 2010, doi: 10.1063/1.3266141.
L/s, cryogenic
25 keV, 40 A
Neutralizer (80 cm)
Beam deflector
Gas puff
RF coil
Triode optics
Permanent magnets
Future: 1 MeV NBI
S. Frank et al., “Confinement performance predictions for a high field axisymmetric tandem mirror,” J. Plasma Phys.
Notes: Realta achieved their first plasma in 2024 and are already in the planning phase for their higher power systems, which will require 1 MeV neutral beams for energy production (Hammir- this will be a negative source)
4 MHz, 10 mTorr
https://arxiv.org/abs/2411.06644 - Hammir might use negative ion sources

## Slide 19: TAE NBI
H. Gota et al., “Formation of hot, stable, long-lived field-reversed configuration plasmas on the C-2W device,” Nucl. Fusion, vol. 59, no. 11, p. 112009, Nov. 2019
Neutral beam injectors
8 NB Injectors, ~150 A each:
  4x tunable (15-40 keV) beams
  4x static (15 keV) beams
>20 MW of deposited power

## Slide 20: Budker Ion Source
Arc-discharge plasma source (x4)
40x35 cm expander chamber
Multiaperture Spherical optics
P. Deichuli et al., “Low energy, high power hydrogen neutral beam for plasma heating,” Review of Scientific Instruments, vol. 86, no. 11, p. 113509, Nov. 2015, doi: 10.1063/1.4936292.
4x 15 keV H+ beam
Multi-aperture triode optical system
Cusped magnetic field
Notes: BLOW UP OF ARC DISCHARGE HERE
What benefit did they gain going from RF to arc?
What did they gain by going to ti getter instead of cryos?
Find some more info on the arc discharge- hollow anode? Something else?
- Ion sources with arc-discharge plasma box driven by directly heated LaB6 electron emitter or cold cathode „invited...
Limiting factor is grid overheating
Add image of optics if it can be found- or just some details (number of slits? Etc.)
Diameter of expander=40 cm, length=35 cm
[Expander is surrounded by] 48 rows of small ceramic Nd–Fe–B magnets (9 mm × 12 mm × 240 mm each) with the alternating magnetization directions, which form a longitudinal line-cusp plasma trap

## Slide 21: Budker Ion Source
Arc-discharge plasma source (x4)
40x35 cm expander chamber
Multiaperture Spherical optics
P. Deichuli et al., “Low energy, high power hydrogen neutral beam for plasma heating,” Review of Scientific Instruments, vol. 86, no. 11, p. 113509, Nov. 2015, doi: 10.1063/1.4936292.
4x 15 keV H+ beam
175 A pulsed
Multi-aperture triode optical system
Magnetic coils
Arc plasma
Cusped magnetic field
Notes: BLOW UP OF ARC DISCHARGE HERE
What benefit did they gain going from RF to arc?
What did they gain by going to ti getter instead of cryos?
Find some more info on the arc discharge- hollow anode? Something else?
- Ion sources with arc-discharge plasma box driven by directly heated LaB6 electron emitter or cold cathode „invited...
Limiting factor is grid overheating
Add image of optics if it can be found- or just some details (number of slits? Etc.)
Diameter of expander=40 cm, length=35 cm
[Expander is surrounded by] 48 rows of small ceramic Nd–Fe–B magnets (9 mm × 12 mm × 240 mm each) with the alternating magnetization directions, which form a longitudinal line-cusp plasma trap

## Slide 22: Injector
Multislit optics
Converging neutral beam
Titanium getter pumping
1e5 L/s
Plasma chamber
A. V. Brul et al., “High-Power Neutral Beam Injector with Tunable Beam Energy for Plasma Heating and Stabilization,” Plasma Phys. Rep., vol. 47, no. 6, pp. 518–525, June 2021
Notes: Additional gas puff into the neutralizer- total between plasma source and neutralizer is 50 torr l/s = 4000 sccm

## Slide 23: Tunable Beam Optics
Variable energy required for higher temperatures  higher B field
Tetrode allows constant current at varying beam energy
A. V. Brul et al., “High-Power Neutral Beam Injector with Tunable Beam Energy for Plasma Heating and Stabilization,” Plasma Phys. Rep., vol. 47, no. 6, pp. 518–525, June 2021, doi: 10.1134/S1063780X21060040.

## Slide 24: 2025: FRC formation by NBI alone
Variable NBI system enabled full FRC
FRC
T. Roche et al., “Generation of field-reversed configurations via neutral beam injection,” Nat Commun, vol. 16, no. 1, p. 3487, Apr. 2025, doi: 10.1038/s41467-025-58849-5.

## Slide 25
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
300 kV, 100 mA
Gas target
5e13 n/s
100 kV, 2-20 mA
Solid target
2e10 n/s
Benchtop device
20 MW NBI
8 injectors
15-40 keV (variable)
1 MW
1 injector, space for 2
25 keV
Notes: Mention that I have visited all but tae

## Slide 26
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
300 kV, 100 mA
Gas target
5e13 n/s
100 kV, 2-20 mA
Solid target
2e10 n/s
Benchtop device
20 MW NBI
8 injectors
15-40 keV (variable)
1 MW
1 injector, space for 2
25 keV
Notes: Mention that I have visited all but tae

## Slide 27: Orbitron: 10’s kW hybrid
M. Affolter et al., “The Orbitron: A Crossed-Field Device for Co-Confinement of High Energy Ions and Electrons,” AIP Advances, vol. 14, no. 8, p. 085025, Aug. 2024.
Magnets
Cathode
(-100-300 kV)
Anode (ground)
D+ beam injection
~12 cm
Notes: The orbitron is a 10’s of kW class fusion reactor based on a hybrid electric-magnetic densification approach. We have a strong electric field in (r, z) generated by a negative cathode that, when ions are injected, can maintain ions in a long duration orbit. This is similar to an orbitrap.
The magnets that you see enable simultaneous electron confinement, which allows us to push past the space charge limits imposed by an ion-only trap.

## Slide 28: Avalanche Beamline
Ion source
Differential Pumping
Deceleration, focusing, steering
Orbitron entrance

## Slide 29: Ion sources
Veeco Mark 1 (1 mA)
D-Pace ISVF (2 mA)
D-Pace ECR (10 mA goal)
Repurposed broad beam source
Positive/negative source
30 mA generated at 50 kV
Development ongoing
Notes: Progressive densification requires an increase in beam current to match
As the company has grown rapidly over the last few years, we have had multiple different goals and projects to achieve them
1 mA vs 6 mA? What’s going on here
Justify beam current levels

## Slide 30: Ion beam simulations
Python-wrapped IBSimu (“pybsimu”)
  Publicly available!
Wrapped in surrogate optimization techniques (pySOT)
Amazon Web Services used to host computations

## Slide 31
Beam-target
(ECR)
Magnetic Bottle
(NBI)
Inertial electrostatic confinement
(Multiple)
300 kV, 100 mA
Gas target
5e13 n/s
100 kV, 2-20 mA
Solid target
2e10 n/s
Benchtop device
20 MW NBI
8 injectors
15-40 keV (variable)
1 MW
1 injector, space for 2
25 keV
10 mA
DC, ECR positive beams
Notes: Mention that I have visited all but tae

## Slide 32: Fusion is everywhere, and growing fast!
Source: https://remdelaportemathurin.github.io/fusion-world/
Notes: Fusion is everywhere!
I hopefully have convinced you that traditional fusion schemes, while vital, are not the only contribution to the field that the ion source community has to offer.

## Slide 33: Thank you!
Pybsimu

## Slide 34: Beamline
Differential Pumping
Deceleration and Steering
4 Stage differential pumping on total of 500 L/s
250 L/s turbopumps
>2 OOM pressure drop
Sikler geometry used to decelerate, focus, and steer into the orbitron
Notes: These may not be needed- could probably be removed

## Slide 35: TAE
  Field-reversed configuration (FRC) concept
  Neutral beams are ionized by a seed plasma
  Beam produces azimuthal current
  Closed field geometry confines plasma
Notes: https://tae.com/enhanced-plasma-performance-in-c-2w-advanced-beam-driven-field-reversed-configuration-experiments
Draw out cartoon explaining this concept (like Wikipedia image)
What developments would these companies value? Higher pulse lengths? Can put this on last TAE slide

## Slide 36
https://tae.com/neutral-beam-injection-in-the-c-2-facility/?utm_source=chatgpt.com
2012 status of C2

## Slide 37: SHINE Technologies
Source: www.shinefusion.com
Notes: Mention Janesville WI
Highlight that 1-3 are all neutrons
‘SHINE implements a staged approach where, while the ultimate goal is energy, there are staged applications for neutrons along the way
1: Neutron imaging (identifying defects, many aerospace and defense applications)
2: Medical isotopes (Weekly Lu-177 for cancer treatment)
3: Nuclear waste recycling: Waste still has nuclear potential
4: Energy (duh)

## Slide 38: Magnetic mirror concept
ECRH
ECRH
Radial field
NBI for heating and fueling
17 T peak
Notes: ECRH generates a plasma, adds energy to the electrons to reduce their drag effect on the ions
10 end rings

## Slide 39: TAE: Field Reversed Configuration
Seed plasma guns
1. Magnetic mirror baseline geometry
2. Axial plasma guns produce seed plasma
3. Neutral beam injects high energy ions
Notes: Cut this down- can talk about mirrors at first, then specialize with TAE and Realta?
Foothill Ranch, CA

## Slide 40: TAE: Field Reversed Configuration
Seed plasma guns
1. Magnetic mirror baseline geometry
2. Axial plasma guns produce seed plasma
3. Neutral beam injects high energy ions
4. Field reversal
What are the NBI Systems?

## Slide 41: Tunable beam
A. V. Brul et al., “High-Power Neutral Beam Injector with Tunable Beam Energy for Plasma Heating and Stabilization,” Plasma Phys. Rep., vol. 47, no. 6, pp. 518–525, June 2021, doi: 10.1134/S1063780X21060040.
Ti getter surfaces

## Slide 42: Realta NBI system
25 keV, 40 A
Developed at Budker INP  TAE  WHAM
Heritage system from older TAE architecture
Plans for 1 MeV neutral beams1
RF plasma source
Triode optics
Expander chamber
2x cryogenic pumps
(7e4 L/s each)
80 cm Neutralizer
D. Endrizzi et al., “Physics basis for the Wisconsin HTS Axisymmetric Mirror (WHAM),” J. Plasma Phys., vol. 89, no. 5, p. 975890501, Oct. 2023, doi: 10.1017/S0022377823000806.
1S. Frank et al., “Confinement performance predictions for a high field axisymmetric tandem mirror,” J. Plasma Phys.
Notes: FIND THIS SOURCE- What is the pulse duration
Realta achieved their first plasma in 2024 and are already in the planning phase for their higher power systems.
Verify that it is actually multiple RF sources feeding the larger chamber
1 MeV beam for Hammir = power plant version
https://arxiv.org/abs/2411.06644 - Hammir might use negative ion sources

## Slide 43: Fusion Excitement
“Global Investment in the Private Fusion Sector.” Fusion for Energy. (2025, June 10).
€1.5 B
€9.9 B
2.05 MJ input
Fusion plasma
3.15 MJ output
H. Abu-Shawareb et al., “Achievement of Target Gain Larger than Unity in an Inertial Fusion Experiment,” Phys. Rev. Lett., vol. 132, no. 6, p. 065102, Feb. 2024
2022: Scientific Breakeven
Growing investment in the private sphere
Notes: “Dramatic” increase
Mix between private funds (~6.7 B) and public funding (~1.8 B) (rest is hybrid state-private funding)