## Slide 1
Overview and performance of the MAST Upgrade Neutral Beam Injectors
M. Nicassio
21st International Conference on Ion Sources, Oxford, 08-12 September 2025

## Slide 2: Contents
Overview of the Mega Amp Spherical Tokamak Upgrade
(MAST Upgrade) Neutral Beam Injectors (NBI)
MAST Upgrade NBI ion source and accelerator
MAST Upgrade NBI operational experience
  NBI ion source maintenance, conditioning
  and characterisation
  Performance up to 1 s and 3 MW average power
Future improvements and upgrades
Summary and outlook

## Slide 3: MAST Upgrade Neutral Beam Injectors
MAST Upgrade
  largest operational spherical tokamak
  main goals: explore novel plasma exhaust concepts, de-risk spherical tokamaks as future fusion power plants
NBI is the MAST Upgrade auxiliary plasma heating system with 5 s pulse capability
  two beamlines with one injector each known as South (SS) and Southwest (SW)
  main upgrades for long pulses
    - cooling system
    - beamline elements (residual ion dumps
    and bending magnet)
  ion source and accelerator
  - JET Positive Ion Neutral Injector (PINI) design
    - tetrode accelerator
    - max design energy and current 75 kV / 65 A
    - operating gas D2
    - beam horizontal and vertical focal lengths
    14 and 6 m respectively

## Slide 4: MAST Upgrade Neutral Beam Injectors
Neutraliser
PINI
Getter pumps
MAST-U
tokamak
Calorimeter
Duct
Residual ion dumps
Bending magnet
Turbomolecular pump
MAST Upgrade
  largest operational spherical tokamak
  main goals: explore novel plasma exhaust concepts, de-risk spherical tokamaks as future fusion power plants
NBI is the MAST Upgrade auxiliary plasma heating system with 5 s pulse capability

## Slide 5: Filament driven arc discharge ion source
Schematic of the MAST Upgrade ion
source in Supercusp configuration
Thermionic emission electrons from
heated filaments accelerated to source
walls ionise gas and create plasma
Species formed in primary and
subsequent interactions
  D+, D2+, D3+
Magnetic confinement achieved by
using permanent magnets
  chequerboard pattern
  linear cusps to enhance D+ fraction
  production (Supercusp configuration)
Cons: auxiliary supplies at high voltage,
filament lifetime causing downtime

## Slide 6
MAST Upgrade PINIs
Fourth accelerator grid as
seen from the neutraliser
PINI on the SS beamline
Tungsten filaments in the ion source
Arc load resistor and
filament transformer

## Slide 7
MAST Upgrade PINI Power Supplies
HV DC switchyard to configure
the output of 4 independent HVPSs
High Voltage areas including:
  - ion source PS
  - modulation deck housing 2
  parallel connected tetrodes,
  associated supply and control
  - part of the accelerator PS

## Slide 8: MAST Upgrade operational timeline
* = PINI maintenance, beamline, PINI number
* SW 2
* SS 3
* SS 1
Brand new PINI on SS
MU01
MU02
MU03
MU04
MU05
First beam
into MAST Upgrade
Commissioning
Engineering break with installation of additional NBI and EBW
= operational period
= engineering break

## Slide 9: PINI maintenance
Three PINIs available, 2 used on MAST since 2006, 1 spare brand new used
first in 2021
PINI maintenance and inspections:
  when performance compromised
    - loss of filaments
    - when no other issues can be identified in the beamline or power supplies
  downtime about 2 weeks
  rate of filament loss in the first operational periods was abnormal
    - all replaced eventually with a new batch
  broken filaments were always randomly placed not in batches
  performed only once per PINI since the start of MAST Upgrade
  operations

## Slide 10
PINI conditioning:
  beam extracted at gradually increasing voltage, current and gas flows,
  aimed at maximising voltage, power and reliability of beams
  to remove high spots, oxide coatings, micro-particles from grids and
  implant the operating gas into the accelerator grids
  necessary in the following cases
    - use of brand new PINI
    - after a vacuum breach
    - after replacing parts of the source/accelerator
    - changing operating gas
  conditioning time varies
    - for the brand new PINI ~10k pulses up to 70 kV
Other issues and improvements:
  arcing outside of the PINI, required rerouting
  cables
  high failure rate of arc load resistors resolved
  replacing failed resistors and thermal interface
  paste
PINI operational experience - highlights
Examples of SS pulses before and after
PINI filament and arc load resistor work

## Slide 11
Example of electrical waveforms SW pulse n. 52470
PINI operational experience - highlights
A set of interdependent models
determines the arc and filament
power supply setpoints to achieve
a set beam current at fixed beam
voltage
The arc current feedback to the
filament controller adjusts the filament
voltage to achieve the requested arc
current
The arc voltage is increased at beam
turn on to facilitate beam extraction,
particularly at beam voltages > 60 kV

## Slide 12
PINI operational experience - highlights
Perveance scan on SW PINI at 65 kV
PINI characterisation: perveance
  the beam current is set through perveance,
  which determines the beam width
  at optimum perveance the beam is the
  narrowest therefore scraping losses
  minimised and less likelihood of breakdowns
  determined via scans at fixed beam
  voltage, measuring width of horizontal and
  vertical 2D beam profiles at the calorimeter
  via thermocouples
  MAST-U PINIs feature a shallow
  perveance curve  potential to run well above
  optimum perveance to increase power without
  significantly increasing scraping losses
Perveance = Ibeam/Vbeam3/2

## Slide 13
PINI operational experience - highlights
New functionality of beam blips during a pulse:
  off time down to 11 ms
  up to 40 blips per pulse
  fixed duty cycle
Benefits:
  higher resolution measurements for diagnostics measuring emissions from fast ions
  no significant plasma perturbation with short blips
  increased fidelity and duration of measurement
SS pulse n. 50968

## Slide 14
Campaign 4, about 1500 NBI pulses into plasma
  gradually increasing power available
  as PINIs are conditioned
  SW 5 months downtime due to
  HVPS 11 kV fuses failure
  highest power from both beamlines
  as a result of the optimisation of timing
  and HV breakdown handling
Performance - highlights

## Slide 15
Performance - highlights
Campaign 2 vs campaign 4: average injected power per pulse

## Slide 16
Performance - highlights
Campaign 2 vs campaign 4: average injected energy per pulse
  longer pulses run in the last operational period

## Slide 17: Future improvements
Main areas being improved
  timing and HV breakdown handling to reduce spurious reapplications
  arc power supply ripple and turn on with changes to the arc power supply topology
  hardware that limits pulse length capability
  higher bandwidth and resolution data acquisition system for PS analogue and digital signals to improve fault identification and diagnosis capability
  ageing components, e.g. HVPS replacement with JET supplies

## Slide 18: MAST-U NBI enhancement
Addition of two injectors (Double Beam Box)
  installation commencing in 2026
  5 MW of injected power
  on and off axis injection
  up to 5 s pulses
  ion source PS topology based
  on newer technologies
  cryopumps
PINIs
DBB
Upper beamline
Lower beamline

## Slide 19: Summary and outlook
MAST Upgrade NBI uses filament driven arc discharge ion sources
  positive ions from D2
  design similar to JET NBI ion sources
  operated on MAST since 2006, on MAST Upgrade since 2020
  experienced and solved during the first operational period
    - conditioning of a brand new PINI
    - high rate of PINI filament loss
    - high rate of arc load resistor loss
    - arcing outside of the PINI
  continued and extensive effort on power supplies
  functionality of beam blips implemented
  reliably delivering > 3 MW for up to 1 s
NBI are complex systems, crucial for scientific output
Experience gained and progress also influenced by staff turnover, knowledge sharing
Outlook
  several projects underway to continue increasing reliability, average injected power and pulse length
  new injector with 2 beamlines doubling power beyond 2026
See D. King talk
on JET NBI
08/09/25

## Slide 20: Backup slides

## Slide 21: NBI for magnetic confinement fusion devices
Heat the plasma, drive current and plasma rotation, measure plasma parameters
  neutral to penetrate the tokamak magnetic field, ionised by ion or electron impact
  ionisation or charge exchange, transfer energy to plasma by Coulomb collisions
  generated from positive or negative ions
  Pros: well established technology for positive ion NBI, powerful heating method, flexible
  injection geometry, efficient coupling to plasma up to high densities
  Cons: low wall-plug efficiency (neutralisation), expensive, big nuclear island
Types of ion sources
  Filament driven arc discharge
    - mainly for positive ion beams and energy ≤ 100 keV,
    e.g. JET and MAST-U NBI
  Radio Frequency driven discharge
    - mainly for negative ion beams and energy > 100 keV,
    e.g. ITER NBI
  choice of positive or negative ions dictated by
  energy needed to penetrate the plasma core
Kazakov_HC-1.pdf

## Slide 22: MAST-U NBI trajectories
Toroidal plane Poloidal plane

## Slide 23
Ion source
Multi-aperture (262) and
multi-grid accelerator (4)
with variable offset
Ceramic insulator
MAST-U PINIs
Filament transformer and arc load resistors
(JET design)
Backplate with 24
filaments feedthroughs
Water and electrical
connections

## Slide 24: MAST-U PINI simulated profiles (ideal)
75 kV, 56 A
Neutraliser exit
Calorimeter

## Slide 25
Ion source PS
Accelerator PS
MAST Upgrade PINI Power Supplies
Arc DC supply:
  voltage up to 200V, ripple <10%
  current up to 1600 A for 20 s, ripple 4-5%
Filament 50 Hz 3-phase AC supply:
  voltage up to 415VRMS
  current up to 100ARMS