## Slide 1: ICIS 2025
Beam current performance in the ITER negative ion source prototype SPIDER
Alastair Shepherd, E Sartori, V Candeloro, R Casagrande, G Emma, I Mario, A Pimazzoni, B Pouradier Duteil, G Serianni and the NBTF team
alastair.shepherd@ukaea.uk, alastair.shepherd@igi.cnr.it

## Slide 2: OUTLINE
ITER NBTF and SPIDER
SPIDER campaign overview 2024/25
Extracted current estimation
Beam current performance
Conclusions and future perspectives

## Slide 3: OUTLINE
ITER NBTF and SPIDER
SPIDER campaign overview 2024/25
Extracted current estimation
Beam current performance
Conclusions and future perspectives

## Slide 4: ITER Neutral Beam Test Facility
ITER Neutral Beam Injection (NBI)
2(+1) Heating Neutral Beam (HNB) [1]
33-50 MW
1 Diagnostic Neutral Beam (DNB) [2]
Neutral Beam Test Facility (NBTF) [3]
Hosted by Consorzio RFX (Padova, Italy)
MITICA: full scale HNB prototype
SPIDER: full scale ion source prototype

## Slide 5: SPIDER
Ion source and accelerator
CFC calorimeter STRIKE
Beam dump

## Slide 6: SPIDER requirements
Parameter | Value
Source Area | 2.0 x 0.87 m2
Extraction Area | 0.197 m2
Total Voltage | 108 kV
Extraction Voltage | 12 kV
Isotopes | H, D
Acc. Ion Current | 60 A (H), 40 A (D)
RF Power | 4 x 200 kW
Pulse Length - Plasma - Extraction | 3600 s 1000 s (H), 3600 s (D)

## Slide 7: OUTLINE
ITER NBTF and SPIDER
SPIDER campaign overview 2024/25
Extracted current estimation
Beam current performance
Conclusions and future perspectives

## Slide 8: SPIDER operational timeline
  0.3 Pa,
  68 kW/driver
  215 A/m2 at perveance match
  0.43 Pa,
  63 kW/driver
  190 A/m2 at perveance match
Divergence studies:
Core divergence; effect of pressure and bias
Decoupling FF:
ferromagnetic screen around drivers
Plasma volume: operation w/ segm. 1 and 2
SO-2:
validate the design with high beam power
develop procedures in multi-beamlet configuration
obtain large negative ion current and power
measure divergence and uniformity

## Slide 9: SPIDER contributions
Poster
Overview of Cs evaporation control and monitoring,
Basile Pouradier-Dutiel, 08/09, 16:30
Oral
Beamlet optics analysis by visible cameras,
Giulia Emma, 11/09, 11:20
Related IPP contributions
Oral
Pressure dependence on beam divergence, Christian Wimmer, 09/09, 15:20
Oral
Overlap of plasma and beam properties, Dirk Wünderlich, 09/09, 15:40

## Slide 10: OUTLINE
ITER NBTF and SPIDER
SPIDER campaign overview 2024/25
Extracted current estimation
Beam current performance
Conclusions and future perspectives

## Slide 11: SPIDER HVPS
HV current measurements:
: net current drained to ground by the accelerator
: current downstream of the EG
: current collected on the EG (not always available)

## Slide 12: Accelerator processes
Within the accelerator charges can be generated/converted by:
Dependent on:
stripping, ionisation, interception, beam plasma
pressure, beam energy, optics, geometry

## Slide 13: Beam generated plasma
Beam generated plasma downstream of the GG
Large background signal seen by cameras when acceleration is applied
With the open vacuum structure can the beam plasma influence the electrical measurements?

## Slide 14: Increasing drain current
The additional charges are reaching the source potential
Large increase in the net drain current once acceleration applied
Assume this increase is due to beam driven volume processes and is measured by both AGPS and ISEG
Negative ion current at the EG

## Slide 15: Extracted current estimation
From the corrected current an estimate of the extracted and accelerated current
Applying stripping losses from AVOCADO modelling of the beamline pressure [7]

## Slide 16: AG current correction
Evidence that it is a volume process, Ratio :
Changes with STRIKE position
→ dependent on the conditions downstream of the GG
Increases with beam energy and pressure
[kV]

## Slide 17: AG current correction
Path for the charges predominantly outside the accelerator:
Blocking return path outside the accelerator reduces :
  S25 with panel below GG
  S26 with mesh around GG
Factor greater than previous estimates of the volume processes/losses [6]

## Slide 18: Validation against EG current
Co-extracted electrons
Ie calculated from ISEG current and Iex
Comparing Ie :
S24: mean 1.11 SD 0.13
S26a: mean 1.02 SD 0.08
S26b: mean 1.03 SD 0.1
Je [ A/m2]
JEG [A/m2]

## Slide 19: Validation against calorimetry
EG calorimetry
BD calorimetry
EG calorimetry performed for 60 s EG only pulses
Gives confidence in electrical measurements
Beam dump calorimetry:
Compared to at the GG
About 10% lower for the top segment in long pulses

## Slide 20: OUTLINE
ITER NBTF and SPIDER
SPIDER campaign overview 2024/25
Extracted current estimation
Beam current performance
Conclusions and future perspectives

## Slide 21: Operating conditions
Operation with single segment (present limitations of pumping system)
  Higher Cs evaporation rates (20 mg/h at high RF) [8]
  → plasma free surfaces act as a sink
Combinations of FF direction (std. and rev. ) and biases were tested
  Plasma drifts influence plasma and beam uniformity
At the bottom of the source e/H < 1 only possible in std.
  Cs distribution influenced by plasma uniformity

## Slide 22: Scaling with RF
Extracted current scaling with RF power at ITER relevant parameters:
  0.3 Pa, perveance match, 215 A/m2 at 68 kW/driver
  Filter field in the range ⁓2.5 mT
  High bias voltages and currents (⁓50 V, ⁓250 A)
Solid State generators needed
Filter
Bias

## Slide 23: Decoupling driver and expansion region
  Fe shield around driver:
  Decreases field integral in the driver
  RF driver is partially decoupled from the expansion region
  Left/right asymmetry is greatly reduced
driver

## Slide 24: Two generators
  Illuminating top segment with two drivers:
  Increases the average current density by 20%
  Improvement in uniformity across the segment → compensation for upwards drift and offset drivers

## Slide 25: OUTLINE
ITER NBTF and SPIDER
SPIDER campaign overview 2024/25
Extracted current estimation
Beam current performance
Conclusions and future perspectives

## Slide 26: Conclusions and future perspectives
High power beam acceleration (>10 A) achieved for the first time on ¼ SPIDER
→ Challenges in operation of single edge segments
  Unexpected large factor (up to 2) increasing the acceleration drain current (AGPS)
    → downstream of the GG, shields and mesh at GG found to reduce the issue
    → Solution to be developed for ITER HNB
  Decoupling the driver and expansion region showed reasonable perspectives
  → Relevant for ITER HNB
    Beam uniformity depends on drifts and number of generators
    → Positive implications for future full source operation
    For divergence results see presentation by Giulia Emma
    SPIDER operation in 2026:
    Solid state RF generators and enhanced pumping system (non-evaporable getters)
    Full source operation aiming at ≥270 A/m2 and >80 kW/driver

## Slide 27
Thank you for listening
Any questions?

## Slide 28: References
[1] R. S. Hemsworth et al., New J. Phys., vol. 19, 025005 (2017), doi: 10.1088/1367-2630/19/2/025005
[2] A. Chakraborty et al., IEEE TPS, vol. 38 (3), pp. 248-253 (2010), doi: 10.1109/TPS.2009.2035809
[3] V. Toigo et al., New J. Phys., vol. 19, 085004 (2017), doi: 10.1088/1367-2630/aa78e8
[4] M. Pavei et al., Fusion Eng. Des., vol. 161, 112036 (2020), doi: 10.1016/j.fusengdes.2020.112036
[5] U. Fantz et al, Nucl. Fusion, vol. 64, 086063 (2024), doi: 10.1088/1741-4326/ad5dcd
[6] A. Shepherd et al., JINST, vol. 18, C07019 (2023), doi: 10.1088/1748-0221/18/07/C07019
[7] E. Sartori and P. Veltri, Vacuum, vol. 90, pp. 80-88 (2013), doi: 10.1016/j.vacuum.2012.09.022
[8] E. Sartori et al., Nuclear Fusion, vol. 62 (8), 086022 (2022), doi: 10.1088/1741-4326/ac715e

## Slide 29: AGPS current
  AGPS current reached over 355 A/m2
  Overestimation of accelerated current as exceeds CL
  Extrapolating to 100 kW/driver and 1280 beamlets ISEG and AGPS currents exceed PS limits
  Issue needs to be removed, not just corrected for

## Slide 30: Current scaling

## Slide 31: Effect of drifts on beam uniformity
#14046 – blip2 (Top)
PRF,set= 60 kW/dr- psource=0.45 Pa
Reversed FF - Ifilter= 1400 A
IBI= 108 A – IBP = 111 A
VBI= 37.4 V – VBP = 33.4 V  4.0 V
Uex= 5.75 kV
BFF
std
BFF
rev
#14216 – blip1 (Top)
PRF,set= 50 kW/dr- psource=0.45 Pa
Standard FF - Ifilter= 1400 A
IBI= 89 A – IBP = 102 A
VBI= 37.4 V – VBP = 32.0 V  5.4 V
Uex= 5.5 kV
Example of vertical profiles at top segment
DRIFT UP
DRIFT DOWN

## Slide 32: Two generators
  Illuminating top segment with two drivers:
  Similar profiles seen from ion saturation currents (Langmuir probes) and Hβ (OES)
  2nd generator enhances the plasma density in the top segment
15461
15436

## Slide 33: ITER filter field
  Long range FF in the accelerator to deflect stripped electrons