## Slide 1
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Numerical design and experimental characterization of an innovative, 3D-printed, ‘plasma-shaped’ cavity for ECR Ion Sources
D. Mascali1, G. S. Mauro1, D. Bianconi1, G. Torrisi1, O. Leonardi1, A. Galatà2, C. S. Gallo2,
A. Pidatella1, B. Mishra1, E. Naselli1, F. Russo1, E. Chyhyrynets2, C. Pira2,
A. Gallo3, D. Cester3, L. Salvò3, P. Rebesan3, A. Pepato3, R. Dima3
1Istituto Nazionale di Fisica Nucleare – Laboratori Nazionali del Sud – Catania (Italy)
2Istituto Nazionale di Fisica Nucleare – Laboratori Nazionali di Legnaro – Legnaro (Italy)
3Istituto Nazionale di Fisica Nucleare – Padova Division – Padova (Italy)

## Slide 2
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
1 / 28

## Slide 3
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
2 / 28

## Slide 4
EM modes field comp. in cylindrical cavity expressed as Bessel functions. Predominance of modes with E-field null in the origin
Characteristic ‘hollow plasma’ detrimental to source performances:
beam quality
Introduction and motivation
Improvement of ECRIS perfomance based on scaling laws:
, , ~ Bmax/Bmin
Operation at higher magnetic fields and MW frequency is the most straightforward path to achieve higher source performance.
Brute force approach cannot always be applied due to actual technological limits and rising costs (SC magnetic system complexity and cost).
D. Mascali et al., Rev. Sci. Instrum. 83, 02A336 (2012)
L. Celona et al., Rev. Sci. Instrum. 79, 023305 (2008)
Hollow E field
Hollow electron density
Hollow ion beam
RF power deposited off-axis causes plasma ‘hollowness’
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Improve source performances through plasma chamber re-design and microwave launch system optimization
3 / 28

## Slide 5
Introduction and motivation
Some reference about this topic
SERSE: demonstration of gyrotron mw transmission line + coupling system and description of the magnetic field requirements in order to obtain larger intensities and charges with ≥ 28 GHz frequency operation (D. Hitz, A. Girard, G. Melin, S. Gammino, G. Ciavola, and L. Celona, Review of Scientific Instruments 73, 509 (2002)).
SECRAL: production of beams of highly charged ions, in 18 + 24 GHz TFH operation, through the use of an optimized waveguide (∅ 20 mm) operating in the TE01 mode (gyrotron oscillator), with total power of 7.5 W (Zhao, H. W. et. al., “Intense highly charged ion beam production and operation with a superconducting electron cyclotron resonance ion source”, Physical Review Accelerators and Beams, vol. 20, no. 9. 2017. doi: 10.1103/PhysRevAccelBeams.20.094801).
TE01 wave mode is used since losses along the waveguide are very low, due to almost zero electric fields at the inner surface and axis of the waveguide (reduced probability of electric breakdown due to the employed high power).
VENUS: the microwave coupling scheme with the ∅ 20 mm waveguide has been adopted and validated with the 28 GHz VENUS ion source at LBNL (D. Z. Xie, W. Lu, J. Y. Benitez, C. M. Lyneis, and D. S. Todd, in Proceedings of the 22th International Workshop on ECR Ion Sources, Busan, S. Korea, 2016).
SECRAL II: implementation of a new mw coupling scheme based on the ‘Vlasov launcher’, a cylindrical waveguide with a shaped end able to radiate mw directly to the first ECR surface from cylindrically symmetric modes in circular waveguides (TE01) (J. W. Guo et. Al., Rev. Sci. Instrum. 91, 013322 (2020)).
HIISI: implementation of a new plasma chamber geometry that possesses reduced thickness at the hexapole magnetic poles, in order to enhance the radial magnetic field in the plasma loss area (H. Koivisto et. Al., Rev. Sci. Instrum. 91, 023303 (2020)).
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
4 / 28

## Slide 6
Innovative Resonator Ion Source – IRIS
(patent n° IT202000001756A1)
Introduction and motivation
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Plasma chamber
waveguide
Diffractive apertures (slots)
Inspired by “Stellarators” Thermonuclear Reactors
A complex asymmetric magnetic field ensures every plasma particle feels the same force, so the particle confinement is optimized and the plasma can be maintained.
Shape-matching
6 / 28
What we propose …

## Slide 7
Introduction and motivation
‘plasma-shaped’ cavity first concept:
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Cavity geometry: take into account the electrons trajectories as they move under the influence of the magnetic field.
RESULT: plasma cavity with minimized volume → determined by the maximum space occupied by electrons inside ECR plasma.
In order to employ the new cavity with the INFN-LNS CAESAR ion source setup, further mechanical and e.m. tuning operations have been performed.
D. Mascali et al 2022 J. Phys.: Conf. Ser. 2244 012003
3D occupancy map: plot of the surface enclosing all the points where an electron has passed through at least one time
5 / 28

## Slide 8
Introduction and motivation
Innovative Resonator Ion Source – IRIS
(patent n° IT202000001756A1)
Two main modifications to increase source performances:
Shape of the last e- iso-density surface set by B field
Shape obtained from self-consistent PIC simulations
Shape optimized to occupy only plasma volume
Symmetry breaking to excite on-axis EM modes
Cavity re-design
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Plasma chamber
waveguide
Diffractive apertures (slots)
Structure vacuum volumes
7 / 28

## Slide 9
Introduction and motivation
Axial rectangular waveguide replaced by a smoothly matched slotted waveguide
Better wave to plasma power coupling
Homogeneous and symmetric power distribution into plasma
Injection closer to the power deposition layer
Better overall structure compactness (more space in input f.)
Novel RF injection system
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Structure vacuum volumes
Innovative Resonator Ion Source – IRIS
(patent n° IT202000001756A1)
Two main modifications to increase source performances:
Plasma chamber
waveguide
Diffractive apertures (slots)
8 / 28

## Slide 10
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
9 / 28

## Slide 11
IRIS electromagnetic design
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
The MW injection system is based on a slotted waveguide (WR62).
It has been firstly studied as a stand-alone antenna to study the performances vs. the main parameters.
The antenna works in the band [14.2; 15.25] GHz with central frequency 14.7 GHz.
Number of slots limited by the impedance bandwidth of the slotted waveguide antenna.
Antenna efficiency is directly proportional to the number of slots and increases with these.
OBJECTIVE: maximize |S11| impedance bandwidth and obtain uniform radiation pattern.
G. S. Mauro et al., Telecom 2021, 2(1), 42-51;
10 / 28

## Slide 12
IRIS electromagnetic design
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Final ‘twisted’ version of the slotted antenna.
A prototype has been realized through AM technique.
Results obtained after measurements are comparable with the ones obtained with the simulation.
11 / 28
Aluminum
Air

## Slide 13
IRIS electromagnetic design
IRIS has been designed and optimized by employing commercial electromagnetic simulators (Ansys HFSS, CST Studio Suite).
CAESAR ion source (INFN-LNS) has been taken as starting point (dimensions and performances) and as comparison case.
Complex vacuum geometry: no analytical modes.
Compared to a standard cylindrical cavity with axial MW injection system, IRIS cavity presents:
More excited electromagnetic modes
Better wave-to-cavity coupling
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
12 / 28
Notes: Partiamo da CAESAR

## Slide 14
IRIS electromagnetic design
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
13 / 28

## Slide 15
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
14 / 28

## Slide 16
Additive Manufacturing prototype realization
IRIS geometry too complex to build with traditional tools: Additive Manufacuring
Laser Powder Bed Fusion ( L-PBF )
3D model optimized to be printed at 45° to ensure slices with a connected area and to avoid defects while cooling
3D printer: EOS M280
Material: 316L stainless steel
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Printing
surface
15 / 28
Notes: Em innovation – realization innovation

## Slide 17
Additive Manufacturing prototype realization
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Final prototype design
Input flange
Output flange
Central body
Slotted wg plug
Axial wg plug
16 / 28

## Slide 18
Additive Manufacturing prototype realization
As built with printing supports
After first post-processing to remove supports, flange polishing and engravings for closure
Printing supports
Engraving
Polished flange
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
IRIS has been designed to be mounted on a ECRIS without the need to modify I/O flanges:
the swap between IRIS and a cylindrical chamber will be automatic.
17 / 28

## Slide 19
Additive Manufacturing prototype realization
Additional post-processing steps, performed at INFN-LNL, have been necessary to control surface finishing and avoid:
RF power loss
local field hotspots (could lead to RF breakdown)
gas trapping
Technique: Plasma Electrolytic Polishing (PEP)
Risk to remove too much material and lose the desired modes (frequency shift of mode de-coupling).
EM simulation performed to remove 50, 100, 150 µm from cavity inner walls.
Etching <50 µm allows to measure the modes
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
18 / 28

## Slide 20
Additive Manufacturing prototype realization
Radiating slots
Final prototype
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
19 / 28

## Slide 21
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
20 / 28

## Slide 22
Experimental validation
The prototype has been experimentally characterized in a dedicate test-bench.
Comparison of simulated and measured S11 and axial E-field: excellent agreement between the two.
Bead-pull technique to obtain axial E-field (Slater theorem): perturbation of energy balance inside the cavity causes Δf0/f0 E2
stepper motor
IRIS
rbead = 0.8 mm
21 / 28

## Slide 23
Experimental validation
Good agreement vs. simulation, considering realization issues
Good field profile agreement
ECR surface (dashed) at high field region
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
22 / 28

## Slide 24
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
23 / 28

## Slide 25
Preliminary PIC simulations
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
EM field in empty cavity
Density map
Step 0
Step 1
Step N
Particle tracking
EM field in plasma filled cavity
Density map
Particle tracking
3D dielectric tensor
24 / 28
A. Galatà et al., Rev. Sci. Instrum. 91, 013506 (2020)
Notes: Milione di elettroni inizializzati all’interno della superficie ECR allo step 0 (non collisionale).
In seguito, il campo EM in vuoto esportato da comsol viene usato per muovere le particelle allo step 0.
Lo step 0 è compreso di due sottostep: uno collisionale ed uno non-collisionale. Quello non collesionale viene usato per calcolare la prima densità dalla quale ricavare dei parametri per implementre le collisioni, tipo la frequenza collisionale (che ha bisogno di una mappa di densità).
Alla fine dello step 0 noi otteniamo una mappa di densità e di energia.
Dopo avere la densità, calcoliamo il tensore del plasma e lo importiamo in comsol per rifare una simulaizone RF.
Quindi si va avanti fino alla convergenza (ad esempio del campo elettrico).

## Slide 26
Preliminary PIC simulations
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Energy density distribution
Particle density distribution
25 / 28
IRIS
CAESAR
IRIS
CAESAR
f0 = 14.5 GHz
Pin = 400 W
Notes: Caesar: 14.5 GHz, 400 W, Bmax_ax=1.1T, Bmax_rad=1.1, this numerically validates IRIS

## Slide 27
Outline
Introduction and motivation
IRIS electromagnetic design
Additive Manufacturing prototype realization
Experimental validation
Preliminary PIC simulations
Conclusion and perspectives
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
26 / 28

## Slide 28
Conclusion and perspectives
The design of a new ‘plasma-shaped’ cavity, able to increase ECRISs performances through a radical re-design approach, has been presented.
Structure designed with commercial simulators and build by the AM technique.
Prototype has been experimentally validated: experimental results are in excellent agreement with the numerical results.
Next steps:
‘hot’ prototype (with cooling channels) design and characterization.
Advance self-consistent plasma simulations.
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
27 / 28
Notes: Aggiungere immagini

## Slide 29
G. S. Mauro – 21st International Conference on Ion Sources – 8-12 September 2025, Oxford
Numerical design and experimental characterization of an innovative, 3D-printed, ‘plasma-shaped’ cavity for ECR Ion Sources
D. Mascali1, G. S. Mauro1, D. Bianconi1, G. Torrisi1, O. Leonardi1, A. Galatà2, C. S. Gallo2,
A. Pidatella1, B. Mishra1, E. Naselli1, F. Russo1, E. Chyhyrynets2, C. Pira2,
D. Cester3, L. Salvò3, P. Rebesan3, A. Pepato3, R. Dima3
1Istituto Nazionale di Fisica Nucleare – Laboratori Nazionali del Sud – Catania (Italy)
2Istituto Nazionale di Fisica Nucleare – Laboratori Nazionali di Legnaro – Legnaro (Italy)
3Istituto Nazionale di Fisica Nucleare – Padova Division – Padova (Italy)
Thank you!
28 / 28

## Slide 30
      [G. S. Mauro et al., Telecom 2021, 2(1), 42-51;]
Cylindrical cavity modes
D. Bianconi – 51st EPS Conference on Plasma Physics – Vilnius, 7-11 July 2025

## Slide 31
      [G. S. Mauro et al., Telecom 2021, 2(1), 42-51;]
Slater perturbation theorem
D. Bianconi – 51st EPS Conference on Plasma Physics – Vilnius, 7-11 July 2025
The Slater perturbation theorem describes the shift of the resonant frequency, when a small volume ΔV is removed from the cavity of volume V.

## Slide 32
The performances of both structures have been observed in terms of S-parameters in the band of [14; 14.5] GHz.
Number of modes and mode adaptation have been chosen as the main quality parameters.
Bad mode coupling to the cavity.
Better coupling plus mode with intense electric field at the cavity center.
How can we improve axial symmetry?
Axial waveguide injection: cylindrical vs. ‘plasma-shaped’ cavity
Notes: For the IRIS case, the observed mode with an axial electric field predominance is located around 14.303 GHz.

## Slide 33
More modes coupled inside the cavity and better wave-to-cavity match
BUT predominance of modes with off-axis electric field maximum.
More modes coupled inside the cavity and better wave-to-cavity match PLUS possibility to obtain modes with predominant axial field maximum.
Side-coupled waveguide injection: cylindrical vs. ‘plasma-shaped’ cavity
Notes: IRIS good mode at 14.466 GHz.