## Slide 1: PIBHI 2025: open mind discussions on status and perspectives of ECR ion sources
L. Celona, A. Andreev, J. Benitez, P. Ferracin, B. Gall, S. Gammino, R. Hollinger, S. Kondrashev, G. Machicoane, T. Nagatomo, V. Skalyga, L. Sun, O. Tarvainen, T. Thuillier, O. Tuske, D. Todd, R. Vondrasek, X. Wang, H. Zhao
International Conference on Ion Sources
St. Catherine’s College, Oxford, 11th September 2025
Notes: Give the highlights of the workshop called PIBHI we had in April close to Catania

## Slide 2: Workshop agenda (1/2)
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
R01- Chair: T. Thuillier (LPSC) (45’+15’)
Review opening talk: Open challenges in the ion source field
O. Tarvainen (STFC-UKRI)- What contributes to the emittance of an ion beam?
S. Kondrashev (BNL)- Application of pepper pot emittance probe for ECRIS beam studies
L. Sun (IMP-CAS)- Emittances with ECRISs: one major challenge to realize high intensity
heavy ion beam acceleration with SRF linac
R02- Chair: O. Tarvainen (STFC-UKRI) (75’+45’)
Beam emittance: role of magnetic fields and other contributions
V. Skalyga (IAP-RAS)– Fundamental processes and plasma studies
O. Tarvainen (STFC-UKRI)- Ion confinement in minimum-B ECRIS plasmas
V. Mironov (JINR)- Recent results from NAM-ECRIS simulations of TFH and afterglow
R03- Chair: V. Skalyga (IAP-RAS) Remote (50’+70’)
Fundamental processes and plasma studies
H. Zhao (IMP-CAS)- 28-45 GHz ECRIS results and development at IMP
D. Todd (LBNL)- 28 GHz ECRIS results and development at LBNL
T. Nagatomo (RIKEN)- 28 GHz ECRIS results and development at RIKEN
R04- Chair: H. Zhao (IMP-CAS) (60’+60’)
High frequency ECRIS: results and developments
R. Hollinger (GSI)- Extraction and transport of intense beams at GSI
E. Flannigan (STFC-UKRI)- Space charge compensation of pulsed hydrogen ion beams
D. Todd (LBNL)- Extraction and transport of intense beams at LBNL
O. Tuske (CEA-IRFU)- Extraction and transport of intense light ion beams
R05- Chair: R. Hollinger (GSI) (60’+60’)
Extracton and transport of intense beams
Notes: The main scope of the workshop was to stimulate the discussions among the attendees on a several topics of interest by the community, in dedicated round tables which usually are not part of the programme of classical ion source conferences. An opening review talk and 8 round tables with the policy to have almost 50% of time given to the presentations and the remaining 50% for opern discussion. I need to start apologizing with some contributors because it will be not possible to condensate in 15 minutes more than 8 hours of discussions and at the same time I would like to thank all the workshop Chairs which have been the engine of each single RT helping me in finding contributions triggering discussions among us.

## Slide 3: Workshop agenda (2/2)
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
R06- Chair: J. Benitez (LBNL) (60’+60’)
Magnetic systems for future ECRIS
R. Vondrasek (ANL)– Metal ion beam production techniques
B. Gall (CNRS) Remote - MIVOC preparation and beams, Inductive oven development,
Isotopic metal preparation for HT oven (Ti, Cr)
L. Sun (IMP-CAS)- High temperature oven development issues at IMP
Aleksandr Andreev (GSI) - Metallic ion beam production techniques at GSI
R07- Chair: R. Vondrasek (ANL) (60’+60’)
Metallic ion beam production
R08- Chair: T. Nagatomo (RIKEN) (60’+60’)
Availability, reproducibility and stability issues
R09- Chair: L. Sun (IMP-CAS) (60’+60’)
Perspectives of HCI production in HF-ECRIS and microwave coupling role
J. Benitez (LBNL)- Introduction & 45 GHz MARS - Update
L. Sun (IMP-CAS)– FECR - Update
P. Ferracin (LBNL) Remote - Beyond 45 GHz (VENUS with Nb3Sn sextupole for FRIB, ECR
designs such as Uni-layer concept, option HTS for future ECR)
T. Nagatomo (RIKEN)- HCI Beam Production and Challenges at RIKEN
L. Sun (IMP-CAS)- Production of intense HCI metallic ion beams for routine operation
D. Todd (LBNL)- VENUS operation and HCI beam production for SHE in LBNL
L. Sun (IMP-CAS)- Perspectives in high charge-state ECR ion source development and scope
G. Machicoane (FRIB) Remote- Current operational experience with ECR ion sources at
FRIB and path forward for high power operation
X. Wang (IMP-CAS) - Microwave launching studies with the 3rd generation ECR ion sources

## Slide 4: ECRIS plasma
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of T. Thuillier (LPSC)
Notes: Behind this achievement and the future ones there is the production of a plasma…
Increase of current …. increase of frequency

## Slide 5: ECRIS plasma
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of V. Skalyga (IAP-RAS)
Notes: BRUTE FORCE!

## Slide 6: SC materials status&perspects
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of P. Ferracin (LBNL)
Notes: Nb-Ti cable limitis reached.
Nb3Sn brittle, risky, expensive Labtech mainly. 1 quench and magnet to garbage…
HTS very expensive
High energy stored in the magnet coils> 1 MJ, active quench protection system required

## Slide 7: MARS
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of J. Benitez (LBNL)
3rd generation VENUS uses NbTi in conventional structure
4th generation Nb3Sn in conventional structure difficult to clamp
4th generation MARS-D allows continued use of NbTi by means of an optimized geometry providing 50% greater fields

## Slide 8: FECR
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of H. Zhao and L. Sun (IMP-CAS)

## Slide 9: FECR commissioning
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of H. Zhao and L. Sun (IMP-CAS)

## Slide 10: FECR commissioning
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of H. Zhao and L. Sun (IMP-CAS)
Notes: So, it’s all ok? No, it isn’t.
And Thomas resumed in the following slide some open questions looking also to the results of new gen. ECRIS

## Slide 11: ECRIS plasma
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of T. Thuillier (LPSC)

## Slide 12: Geller’s scaling law
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of L. Sun (IMP-CAS)
What is going on?
Notes: Based on the Scaling law, the beam current is proportional to the square of the frequency. Many experiments have confirmed this law over the last thirty years. However, with the third-generation ECR ion source appeared controversial results. For example, here are the results from SECRAL at 18 GHz and 24 GHz. Lower beam current than expected at 24 GHz. WHY?
At the beginning of ECRIS history the design of microwave injection has been not considered relevant to enhance performance of the ion sources. It has has been mainly driven from other consideration. Plasma was simply considered like a sponge.
Since ‘94 (Xie, Lyneis) the role of frequency has been evident in ECRIS, but the fine structure has been accepted from the community after ECRIS06 (i.e.: Lyneis et al., Proc. ECRIS 2012).

## Slide 13: Microwave heating in ECRIS
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Notes: In this scenario cavity effects are dominating and we are dealing with conditions that imply full-wave solution a cavity-dominated regime (Gen. I-II).
By increasing the frequency optical approximation is more and more valid, cavity role decreases and we enter in launching-dominated regime (as may be the case for Gen. III and above), the approach may make use of ray-tracing modelling. In this way, the design of the RF component becomes HIGHLY PREDICTIVE, since there is no need to rely on the self-consistency of the wave-plasma-wave interaction. In this latter case the plasma can be more easily described as a "target" and the first-pass absorption efficiency maximized.

## Slide 14: ECR heating on modal dominated cavities
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025

## Slide 15: HF ECRIS: microwave heating
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
COULD YOU IMAGINE THE DISTRIBUTION AT 45 GHz???
Microwave absorption oriented design is needed for future ECRIS. It may give a highly controlled electromagnetic radiation from a flexible RF launcher system with the possibility of reduction, increase, redistribution, power level, polarization, power deposition location of the radiated signal.
This could be of primary importance for maximizing the power efficiency, improving plasma parameters.
Simulations can be a useful tool to verify the effectiveness of the proposed scheme
Notes: As frequency increases we can say that the energy absorption mechanism from the plasma electrons remains the same.
The mode distribution will reach a «continuum».

## Slide 16: IMP movable Vlasov launcher
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of X. Wang (IMP-CAS)

## Slide 17: IMP movable Vlasov launcher
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of X. Wang (IMP-CAS)

## Slide 18: HF ECRIS: microwave heating some conclusions and other questions
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Change of paradigma needed in the design of microwave heating
for future generation ECRIS
<<L
Modal dominated cavity.
Wave Lauching is not possible
L
Launching dominated coupling. Optical approximation is valid.
Contribution of each mechanism?
Where is the switch over?
Clue: 18 GHz FTE on AISHa is still present, but… the other mechanism? Phased waveguide array!
What will happen at 21 GHz?

## Slide 19: WARNING!!!
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of V. Skalyga (IAP-RAS)
Notes: The characteristics of beams generated by a high charge state ion source critically depend on plasma parameters.
An adequate understanding of the electron and ion distribution functionsCan provide crucial information for performance optimization.
This discussion should also focus on plasma diagnostics,
Determining which diagnostic tools are most appropriate
In specific experimental contexts and identifying
Which ones might warrant further progress.

## Slide 20: ECRIS beam emittance
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of O. Tarvainen (STFC-UKRI)
kTi higher than expected. Magnetic emittance dominates at high frequencies and charge states
Non-uniform distribution of ions across the extraction aperture→ smaller than predicted emittance for high Q/M
Plasma meniscus, space charge and extraction system design affect the longitudinal energy spread
Notes: 2.45 contribution almost 1:1. Plasma meniscus and space charge in the extraction affect the longitudinal energy spread.
Monoenergetic, uniform beam at extraction has longitudinal energy spread at zero B-field. In “real extraction systems” the effect is pronounced i.e. longitudinal energy spread is larger

## Slide 21: Frequency dependence
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of O. Tarvainen (STFC-UKRI)

## Slide 22: ECRIS plasma instabilities
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of O. Tarvainen (STFC-UKRI)

## Slide 23: Final scenario
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of O. Tarvainen (STFC-UKRI)
Beam extraction effects contribute significantly.
How to make sure a factors affecting the transverse (normalised) emittance are not masked by divergence-limited extraction and collimation further down the beamline?
Does the measurement technique affect the transverse emittance values?
Is there a preferred technique?

## Slide 24: Space Charge- Child Langmuir law
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of O. Tarvainen (STFC-UKRI)
The true cause for the observed power law is “meniscus focusing” and collimation on the extraction electrode
Overfocusing
Too low focusing
Matched case always sought in simulations
Second illusion?

## Slide 25: Multi M/Q extraction
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of D. Todd (LBNL)

## Slide 26: VENUS beamline simulation
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Simulation of extraction section:
Simulation of transport section
2D slice mode (x,y) simulation:
Read particle distribution from extraction simulation
Solve Laplace for x-y potential
Move particles using solved field and any applied fields
Repeat from 2 to end of beam line
IGUN-like particle-in-cell simulation:
Ion macroparticles are tracked, depositing charge density on a 2D or 3D mesh
Solve Laplace on mesh
Apply Boltzmann-distributed electrons using potential from step 2
Repeat until relaxed
“Cheat”
Simulate extraction using 2D (3D expensive)
Track triangular initial distribution through relaxed extraction solution
Complete transport section
Courtesy of D. Todd (LBNL)

## Slide 27: VENUS simulation of O beam extraction and transport
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Simulation
Simulation
Experiment
Experiment
8 cm
Experimentally Measured Spectrum
Courtesy of D. Todd and J. Benitez (LBNL)

## Slide 28: C4+ Hollow beams
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of D. Todd (LBNL)
«Error» is generated inside the source as previously seen in other measurement with 2nd gen. ECRIS
Space charge effects

## Slide 29: Kobra 3D simulation of beam extraction and transport
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of R. Hollinger (GSI)

## Slide 30: Impact on HCI acceleration
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of L. Sun (IMP-CAS)
Notes: Long term high current HCI acceleration is challenging!

## Slide 31: Long term stability operation
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of H. Zhao (IMP-CAS)

## Slide 32: Long term stability operation
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of L. Sun (IMP-CAS)

## Slide 33: U performances@RIKEN
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of T. Nagatomo (RIKEN)
U35+ consumption @110μA →2.4mg/h
High consumption causes unstable beam intensity
U35+ consumption @ 250μA →10.5 mg/h
Anti-deposition shield
Emittance growth expected due to the higher drain currents
3 kW
3 kW
3 kW

## Slide 34: V13+ performances@RIKEN
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Emittance Growth as a function of drain current
Courtesy of T. Nagatomo (RIKEN)
RF=1.25 kW, 9x10-5 Pa
3.6 mg/h
RF power =3.5 kW, 15x10-5 Pa
consumption rate 26 mg/h

## Slide 35: Beam stability issues
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
・Beam reduction was caused by sudden evaporation of flake-shaped metal deposits inside the chamber wall when the plasma touch them.
・AD shield has the potential to suppress such changes avoiding deposition
High-power GMJT (RJT-100) was developed by SHI Cryo. Group and installed in RG28-S with cooling power of > 8 W @ 4 K
Courtesy of T. Nagatomo (RIKEN)

## Slide 36: Metallic ion beam production
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of R. Vondrasek (ANL)

## Slide 37: Metal ion beams
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of L. Sun and H. Zhao (IMP-CAS)
28 GHz ECRIS may have not yet reached its peak performance?
What new ideas and technologies may further enhance performance of 28 GHz ECRIS?

## Slide 38: SHE synthesis
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025

## Slide 39: OES for metal ion beams
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of A. Andreev (GSI)

## Slide 40: Machine Learning
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of J. Benitez and D. Todd (LBNL)

## Slide 41: AI for ECRIS?
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of L. Sun (IMP-CAS)
Notes: Personally, I feel much better with human deficience. This would be the dead of human creativity. High efficiency kills creativity because creativity requires space for exploration, ambiguity, and even failure. ECR story began with a beautiful failure and our success is still based on a lot of beatiful failures!

## Slide 42
Thanks for your attention!!!

## Slide 43: SPARE SLIDES
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
43

## Slide 44: VENUS attempt: static launcher
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Notes: Free plasma electrons are the real target. «it is not just as cooking a hot dog» (C. Lyneis cit.)

## Slide 45: FTE - Hollow beams
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
f=14.5GHz±40 MHz
Viewer in BaF located 20 cm far from extraction electrode without any optical element in between.
Acquistion time=250 sec
Video 15x
[L. Celona, G. Ciavola, S. Gammino, F. Maimone, et al., Review of Scientific Instrument 79, 023305 (2008)]
INTERPLAY between plasma structure and beam parameters (current, shape, brightness, emittance)

## Slide 46: Ion confinement
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of O. Tarvainen (STFC-UKRI)
Only a small fraction of the ions can escape
The charge state distribution of the
extracted beam is different from that of the
core plasma

## Slide 47: Plasma studies: instabilities
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of V. Skalyga (IAP-RAS)

## Slide 48: SCC Diagnostics
L. Celona et al. International Conference on Ion Sources, St. Catherine’s College, Oxford, 11th September 2025
Courtesy of E. Flannigan (STFC-UKRI)