## Slide 1: The High Intensity Polarized Proton Source
September 8-12, 2025
G. Atoian`, A. Cannavo, T. Lehn, D. Raparia, J. Ritter, B. Snyder, A. Zelenski
21st International Conference on Ion Sources, Oxford, UK

## Slide 2
Almost 25 years, the polarized proton source based on OPPIS (Optically Pumped Polarized H-Ion Source) reliably delivered the high-intensity polarized proton beam for the RHIC spin physics program at BNL.
The OPPIS polarized source for RHIC was developed in collaboration BNL – KEK – TRIUMF – INR at 1998-2002.
The source has been upgraded several times and continuously improves polarization, intensity and emittance.
Prior to Run-12, the ECR-type source was used to generate the primary proton beam. The ECR-source was originally developed to operate on a DC current and placed inside a super conductive solenoid (SCS).
In 2012, the ECR-source was replaced by a high-brightness source “Fast Atomic Beam Source”. FABS placed outside of SCS and operating in a pulsed mode. The new source improved the beam current density, angular divergence and stability.
Introduction

## Slide 3
EIC Accelerator Performance
Requirements for an Electron-Ion Collider are defined in the White Paper:
“In order to address the crucial scientific questions discussed in the previous sections, the EIC must provide:
• A Highly polarized electron (∼70%) and proton (∼70%) beams;
• Ion beams from deuterons to heavy nuclei such as gold, lead, or uranium;
• Variable e+p center-of-mass energies from 29−140 GeV;
• High collision electron-nucleon luminosity 1033−1034 cm−2 s−1;
• The possibility to have more than one interaction region.”
“White Paper on the Electron-Ion Collider in Preparation for the NSAC Long Range Plan EIC”, p.5 User Group, January 2, 2023
By the request of this White Paper we are looking to improve the polarization and the intensity of the polarized proton beam.

## Slide 4
Performance of the beam injected into the booster

## Slide 5
STAR
PHENIX
AGS 24 GeV
LINAC
BOOSTER 2.5 GeV
H- polarize source OPPIS
Spin Rotators
Strong and Partial
Siberian Snakes
200 MeV polarimeter
RHIC pC “CNI” polarimeters
RHIC
Absolute H-jet
polarimeter
AGS pC “CNI” polarimeter
The world’s only polarized proton collider: 60% proton polarization , L max=1.61032 s-1cm-2; 50<√s <510 GeV
Polarization facilities at RHIC
Siberian Snakes
Siberian Snakes

## Slide 6
Optically Polarized proton source (OPPIS)
Laser room
Pumping laser
Prob laser
SCS
Plasmatron
Acceleration
4-grids
(5-7) keV
Neutralization H-cell
Ionization He-cell
Deceleration 3-grids ~3-4keV
Neutralization Ru-cell
Ionization Na-cell
Solenoid
Extractor 35kV
LEBT
Magnet
23.70
Spin rotator
Switching Magnet (50 ms)
MEBT
Sona transition
Correction coil system
RFQ
To LINAC
SCS Magnet 23.70 Spin rotator
Spin transfer: longitudinal transverse(horizontal) vertical

## Slide 7
2013 OPPIS upgrade with FABS source
H+
H0
H+
H0
H-
H2
He
Rb
Na
Na-cell coil
Plasmatron
H-injector
Ionizing He-cell
Neutralizing
H-cell
Neutralizing Rb-cell
Sona
transition
~1mA H-
Accelerating
4-grids system
Decelerating
3-grids system
~35kV extractor system
Ionizing Na-jet cell

## Slide 8
Production of circular polarized tunable wavelength (~795nm) laser beam
Polarization of the Rb-atom (Rb-cell)
Production of electron spins polarized hydrogen atoms by capturing an electron from Rb
Polarization transfer from the electron to proton by “Sona-transition” technique
Polarization transfer technique (OPPIS)
The ionization of hydrogen atoms by capturing a second electron in Na-jet for acceleration (Na-cell)
Polarized light
Polarized electron
Polarized proton
Ionization of hydrogen atom by He (He-cell).
He-cell
Rb-cell
SC-solenoid
Sona-transition with 3 corr. coils in it
Na-jet
&
Solenoid
H0
H-
H0*
H+
H0*
Laser beam

## Slide 9
Energy separation a residual un-polarized H0 component
H+(60%)
H0(7keV)
-3.8 kV
-3.9.0 kV
-2.4 kV
H0(7keV)
He-cell
Rb -cell
H0(40%)
Deceleration
by 3-grids system
H0 + He → H+ + He + e-
H0(3keV)
+0.1 kV
-4.0 kV
H+(3keV)
H0(7keV)
Ionization
in He-cell
Neutralization
in Rb-cell
Only a portion of the beam is ionized in the He-cell (~60%) and can be further polarized.
The polarized part of the beam separates from the un-polarized by the bending magnet, LEBT (quadrupoles and steering magnets) and collimators. Energy separation ratio H-(4keV)/H-(7keV)is better by 25-30 times.

## Slide 10: Ion Source Development
PERFORMANCE
STABILITY
SAFETY
DEVELOPMENT
As a first approximation, the main parameters of the quality of the formed beam is intensity, polarization and emittance.
Since 2012, when FABS was implemented, we have made many adjustments to improve the beam parameters. We achieved the best polarization volume of over 86%, intensity over 1000uA, and a beam pulse duration of over 400us compared to the average volume of polarization of ~78-80% and an intensity of ~350uA.
Now, our goal is to have OPPIS maintain the best parameters for several months by improving monitoring and simplifying control, as well as making it fast and easy to repair and completely safe. Our goal for the future is stability and safety with the best performance.
Notes: We performed a set of upgrades in the OPPIS source to meet the requirements and goals for this Run. The idea was to base the development of the source on three main pillars: performance, stability and safety.

## Slide 11
The original copper cathode (~1085*C) in this high current cold cathode only lasted a few days (~5·105 arc pulses). Using molybdenum cathode (~2600*C) significantly improved the service life to ~5·106 arc pulses (~1-2 months).
Improving the geometric shape of the cathode by inserting a small nozzle and enlarging the outer rim, as well as improving the vacuum sealing of the plasmatron, limited the plasma dispersion, and increased the service life by more than 107 arc pulses (RUN-24).
Plasmatron (cathode and pulse-valve)
Corr. shape
After used
Cupper
Moly with nozzle
Molybdenum
~1 day
Before use
~1.5-2 months
~1.5-2 months
~1 month
The pulse valve has been upgraded several times to provide precise control and long-term stable hydrogen supply to the plasmatron to form a stable plasma.
The same type of valve is used in the helium neutralization cell.
One of the most important elements of plasma formation for a stable operation of the source is the pulse valve for injection of the hydrogen-containing gas and the cathode (arc current ~500A).
Pulse valve
Cathode

## Slide 12
Proton energy ~ 5-10 keV
Intensity ~ 2.5-5.0 A
N grids = 4
Diameter of grids ~ 50 mm
N holes = 1820
Diameter of holes = 0.8 mm
Step of holes = 1.1 mm
Transparency ~ 53 %
Radii of the spherical grids:
R1~ grid1 ~ 180 cm
R2~ grid2 ~ 150 cm
R3~ grid3 ~ 120 cm
R4~ grid4 ~ 120 cm
FABS 4-grid (spherical) Ion Optical System with “geometrical focusing”
Gap of grids:
12 ~ 0.4-0.5 mm
23 ~ 1.0-1.4 mm
34 ~ 0.4-0.5 mm
Grids system made by 0.4 mm thick molybdenum plates.
IOS# | I0,A | F, m | a, mrad | H0, mA | H-, mA
1 | 3.5 | 170 | 12 | 270 | 9
2 | 3.2 | 300 | 7 | 730 | 22
3 | 3 | 280 | 8 | 650 | 20
New slit-type IOS grid for higher brightness beam formation

## Slide 13
He-ionizer cell and 3-grid deceleration system
“Electro-magnetic” pulse valve
I
B
Lorentz (Laplace) force moves the flexible conducting plate in the high (~ 2-5 T) magnetic field. For I=10 A, L=5 cm, F=2.5 N. Current pulse duration ~100-300 us
He-pulsed
valve
3-grid beam
Deceleration system
He-cell
Two functions of the new He-cell with pulsed valve:
Ionization of the injected neutral beam in the He-cell
Deceleration of the ionized part of the beam by 3-grids system to separate from the not ionized part

## Slide 14
Rb-cell and laser spot
SS Cell (Run24)
Rb inlet
SS vessel
Heating/cooling groove
Slits
Inner Cu cylinder
5 cm
Cupper Rb-cell

## Slide 15
Nozzle
500deg.C
Collector
~150 deg.C
Boiler
~500 deg.C
NL ~2·1015 at/cm2
L ~ 2-3 cm
Return
line
Sodium-jet ionizer cell
Transversal vapor flow in the Na-jet cell. Reduces sodium vapor losses for 3-4 orders of magnitude, which allow the cell aperture
increase up to 3.0 cm .

## Slide 16
Superconducting Solenoid
The Solenoid is fully re-condensing with no measurable helium losses. 152 mm in diam. warm aperture, total length-115 cm. Flattop magnetic field (+/- 0.5%) is ~65cm.
Chart: Polarization vs. Rb(T)
| 90 | 85 | 80 | 75 | 70 | 65 | 60
20kG | 75.4 | 76.8 | 79.8 | 80.8 | 80.3
25kG | 76.9 | 79.1 | 81.6 | 81.6 | 80.5 | 80.3 | 73.8
27.5kG | 76.9 | 79 | 80.6 | 81.6 | 81
Chart: Beam current vs. Rb(T)
| 90 | 85 | 80 | 75 | 70 | 65 | 60
20kG | 394 | 326 | 260 | 197 | 142
25kG | 384 | 328 | 265 | 188 | 135 | 87 | 63
27.5kG | 430 | 360 | 280 | 215 | 150
Chart: Laser Frequency vs. Magn. Field of SCS
| 10 | 15 | 20 | 25 | 30
“Up” | 127.5 | 135 | 147.7 | 155 | 165
“Down” | 90 | 81.5 | 71 | 61 | 49.9
Spin Up: 377 THz +
Spin Dn: 377 THz +

## Slide 17
Total: 0.85 - 0.90
P = EH0 ∙ PRb∙ S ∙ BRG∙ ELS∙ EES ∙ ESona∙ Eion ~ 85-90%
Depolarization factors
Depol. factor |  | Process | Estimate
1 | EH0 | Dilution due H0 part of the beam (LEBT) | 0.99 - 0.99
2 | PRb | Rb-optical pumping (Laser system) | 0.99 - 0.99
3 | S | Rb polarization spatial distribution (Collimators) | 0.97 - 0.98
4 | BRG | Proton neutralization in residual gas (Vacuum) | 0.98 - 0.99
5 | ELS | Depolarization due to spin-orbital interaction | 0.98 - 0.98
6 | EES | Dilution due to incomplete energy separation not polarized component of the beam (LEBT) | 0.98 - 0.99
7 | ESona | Sona-transition efficiency (Adjustment) | 0.96 - 0.98
8 | Eion | Incomplete hyperfine interaction breaking in the ionizer magnetic field | 0.98 - 0.99

## Slide 18
The shape of the magnetic field in the "Sona Transition" area depends on the following factors and can be adjusted by:
The optimization of the solenoid position;
2 correction coils (LCC and SCC) with the field in the opposite direction to the SCS;
3 correction coils (ICC1-3) for fine field tuning inside the “Sona Transition”;
“Sona-shield” (soft steel cylinder- of 100 mm diameter and 120 mm length).
Na-cell coil (Na-C) - solenoid around sodium ionizer.
SCS
LCC SCC
ICC1-3
ICC1 ICC2 ICC3
Sona-shield
dBz/dZ< 0.2G/cm
Na-C
He-cell
Rb-cell
Sona-transition efficiency

## Slide 19
H- beam current and polarization at 200 MeV
Rb-vapor thickness
H- ion beam current (mA)
Polarization in 200 MeV polarimeter
H- beam current and polarization vs. Rb vapor thickness

## Slide 20
Simulation tools

## Slide 21
Polarized H- current-1.05 mA, after RFQ 750 keV
100 us/div
200 uA/div
200 MeV polarized proton after Linac
~620 µA×400µs ~1.5∙1012 p/pulse after LINAC

## Slide 22
Polarization dilution due H+ in the new source
Ionize
H0
7keV
40%
Rb-cell
60%
He-cell
H2-cell
Neutralize
In FABS-source
Inside of the SCS
Ionizer & Extractor
H-39keV
0.72%
Accelerate
32keV
3%
H-
7keV
Na-jet
8%
Decelerate, ΔE=4.0keV
He-cell
70%
2%
Na-jet
~90% of plasma
Ionize
Extr.
Extr.
Ionize
H0
7keV
H+
7keV
H+
7keV
H+
3keV
Neutralized
H0
3keV
H-
3keV
H-
35keV
0.72/3 =0.24 - polarization dilution and 4.0keV energy separation (~25-30 times) allows dilution reduction to 0.24/25~ 0.01

## Slide 23
For maximum polarization there must be an accurate selection of settings for all correction coils. Any change in the magnetic field of coils, SCS or ionizer as well as their position requires a new setting.
Polarization vs. LCC current
Polarization vs. target position
Depolarization factors by the shape of magnetic field

## Slide 24
~16.2o
~50mb/sr
~5mb/sr
~82%
~12
~99.35%
Target
proton 200MeV
Scattered proton
Recoil Atom
3.7 3.8 3.9 4.0 4.1 4.2 4.4 4.3
elastic
inelastic
L, cm
N, particles stopped in the slice of Cu-absorber
GEANT calculation of pC polarimeter for 200MeV proton beam
Measurements of the cross section and analyzing power for proton scattering from 12C at 200 MeV. The blue curves correspond to the ground state protons of carbon. The green curve corresponds the protons from the first excited state (-4.44MeV). The black curve represents the sum of the two data sets.
Cross section and analyzing power for elastic pC scattering at 200 MeV
Precision, Absolute Proton Beam Polarimeter at 200MeV

## Slide 25
Precision, Absolute Proton Beam Polarimeter at 200MeV

## Slide 26
Precision, Absolute Proton Beam Polarimeter at 200MeV

## Slide 27
12 deg and 16 deg polarimeter
Vertical polarimeter
16 deg polarimeter
The 200MeV polarimeter
Vertical and Horizontal polarization and Energy of a beam time chart
The 200MeV polarimeter simultaneous measured vertical and horizontal polarization and an energy of a beam.

## Slide 28
Summary
We believe that after:
optimization of the geometry and position of the source elements: He-cell, Rb-cell, collimators, vacuum system … based on the results of the modulation of the distribution of helium gas and Rb evaporation cloud;
improvement of laser alignment control and monitoring;
stabilization of the source parameters by implementing software with feedback control;
…
we will obtain a polarized proton source for the EIC with the required parameters.