## Slide 1: Optimization for RF-driven H- source and Low Energy Beam Transport for CSNS-II
Weidong Chen
Institute of High Energy Physics, CAS.
Spallation Neutron Source Science Center.
Sep. 12th, ICIS2025
Oxford, UK

## Slide 2: Outline
Introduction to CSNS Front-End
H- Ion source development.
Beam test on New LEBT
Summary

## Slide 3: Introduction to CSNS accelerator
Parameters | CSNS 2018 | CSNS-II 2029
I.S. Current (mA) | 30~40 | 50~55
Repetition Rate (Hz) | 25 | 50
Pulse-width (us) | 415 | 500-700
Chopping Factor | 42% | 50-65%
Linac Components | R.T. | R.T.+SC
Linac-energy (MeV) | 80 | 300
RCS-energy (GeV) | 1.6 | 1.6
Beam Power (kW) | 100 | 500
Beam-power=Current × Energy × Pulse-width × Repetition × Chopping factor
500 kW
25 Hz
1.6 GeV
50~75%
500~700 us
40~55 mA
H- Ion
Source
RFQ
DTL
Rapid Cycling Synchrotron
Target
LINAC
Spectrometer
Spoke+elliptical
CSNS-II
Front-End
System
Important front-end parameters：

## Slide 4: Introduction to the front end system
The front end of the CSNS accelerator in service
The LEBT has 3 solenoids, initially designed for the penning ion source.
The penning source has been replaced by RF-driven H- ion source in Sep. of 2021.
The ion source produces 37~42 mA, and throttled to 10~13 mA by a collimator before RFQ.
A new LEBT is constructed and tested in the lab.
Double-slit
scanner
Focusing solenoid
H- ion source
RFQ accelerator

## Slide 5: Operation status

## Slide 6: Issues of penning ion sources
Penning source cloned from ISIS, Oxford
Peak Current: 50 mA，typical 30~40 mA
Typical lifetime: 1 Month
Main problems: Extinguish， fluctuation、discharge
Principle of the penning ion source
Down-time of the penning ion source
2019-2020 I.S.-113.4 hours, RFQ-76.9 hours
Emittance@50mA, 0.8∙π∙mm∙mrad
2020-2021 I.S.-64.9 hours, RFQ-98.2 hours
Issues of penning ion source up to Sep. 2021
Survey for new design of IS started in 2015, visited PKU (Prof. S. Peng) and SNS (M. Stockli, R. Welton and B. Han) .

## Slide 7: Inspiration of RF-driven ion source with ext-antenna
H2
Inner ant. in SNS/J-PARC
External ant. in HERA
External ant. in
CSNS/SNS/CERN
Antenna failure problems in the initial stage of the commissioning. Solved by improvements of antenna.
Stable operation with high current up to now.
Jens Peters from HERA suggested an external-antenna structure.
Development in CSNS,
2016.01-- R&D Fund from CAS received.
2018.12 -- First H- beam produced in lab.
2021.09 -- Put into operation on CSNS.
2025.06 -- 1200 operation days for single source accumulated.

## Slide 8: The new RF-driven H- source
Silicon-Nitride plasma chamber is used.
Indirect cooling scheme.
Elementary cesium.
Compensation B-Field is used.
Glow dis charge igniter.

## Slide 9: The new RF-driven H- source
The glow discharge igniter
Since the pressure in the igniter is 200~400 Pa, the seed electrons are blew to the plasma chamber and guided by the weak axial magnetic field produced by the magnetic coil.
Cathode
Anode
Ceramic insulator
electrons
B-field produced by the
axial compensation coil.
Simple structure
Pulsed 560 V DC voltage
Average power less than 0.5 W
Timing sequence
<400Pa
Plasma chamber~3 Pa

## Slide 10: Operation parameters
 | CSNS service | Test bench study
Peak RF-power | 31 kW | 25~40kW
H2 flow rate | 21 SCCM | 18~24 SCCM
Repetition rate | 25 Hz | 25/50 Hz
Plasma pulse width | 680 μs | 500~800μs
Beam pulse width | 498 μs | 100~750 μs
H- peak current | 37 mA | 50~60mA
Cs reservoir temp | 80~90 ℃ | 77~120℃
Service cycle | >330days | 
Beam energy | 50 keV | 55 keV
Norm. 95% beam RMS emitt. | Not measured | ~0.21 π.mm.mrad (New LEBT)
Typical operation parameter for user service and experimental study
The RF-driven ion source installed in the accelerator tunnel

## Slide 11: Operation status from 2021.9 to 2025.6
Operation in last 4 run cycles, always be ready for neutron production or machine study.
2021.9-2022.7,
310 days accumulated
2022.8-2023.7,
323 days accumulated
2023-2024,
~330 days accumulated
2024-2025,
~300 days accumulated
Target power
1 sample/min
I.S. RF power
1 sample/s
CN New year
Summer
Maintenance
Summer
Maintenance
Summer
Maintenance
CN New year
CN New year
CN New year
Summer maintenance: disassemble  clean/fill cesium reassemble.
Chinese new year: power off, kept in vacuum.

## Slide 12: Operation status from 2021.09 to 2024.08
Beam power
1 sample/min
LEBT CT01
25 samples/s
The ion source runs unattended. The routine maintenance includes H2 gas bottle replacement, 50 kV insulation cleaning, gas/water line inspection, and plasma emission spectra check.
Ion source beam current and target beam power from May 16th to July 15th 2023.
When parameters reaches equilibrium in 30 minutes, the beam current output fluctuation is less than 1%.

## Slide 13: The new LEBT
Suppression of emittance growth
Shorter LEBT, higher beam transmission.
Beam enters the solenoid as early as possible.
Shorter Solenoids, lower fringe effect of B-field.
Parameters | CSNS LEBT | CSNS-II LEBT
Length | 1668mm | 738mm
Inner diameter | 138mm | 64mm
RFQ inlet current | ~40mA | 60mA
RMS Emitt. @RFQ inlet | 0.307@37mA | 0.24@52mA
Num. of solenoids | 3 | 2
Length of solenoids | 240mm | 127mm
Mean vacuum | 3E-3Pa | 2E-3Pa
Stripped proton removal | No deflection | 1.8 degree（3.6 to H-）
Chopper length | 50mm | 27mm
Chopper voltage | 3.8~5kV | 6~8kV
LEBT parameters comparison

## Slide 14: Emittance optimization for CSNS-II on new LEBT
Emittance optimization new LEBT
85mm
95mm
I.S.
RFQ
Many sets of parameters of LEBT is studied with the help of CST Particle-studio.
Parameter of solenoids
Acceleration gap
Meniscus simulation.
Space charge compensation via CST and IBSimu.

## Slide 15: Emittance optimization on new LEBT
Emittance measurement on new LEBT for 60mA beam
95% beam emittance x=0.221 π.mm.mrad
95% beam emittance y=0.211 π.mm.mrad
RF frequency-2.048MHz，RF power-44kW，Solenoid-316A，gas-24sccm

## Slide 16: Effect of chopper field to emittance growth
+3e+p
+2e+H
Build up/destroy of space charge compensation (SCC)
+
—
Destroy of SCC in external E-field

## Slide 17: Effect of chopper field to emittance growth

## Slide 18: Effect of chopper field to emittance growth
E.M. measurement after RFQ.
Simulated by Tracewin, beam envelope is focused from 21.5 mm to 6.8mm within 100 mm drift length.
Emittance growth v.s. current
Shorter chopper length is favorable to the emittance control.
30mm chopper length for CSNS-II.
Beam energy increased to 55keV.
Fast power supply limits the further shortening.
Influence range of chopper’s E-Field
Current (mA)
Emittance growth (%)
50mm
100mm

## Slide 19: Effect of chopper field to emittance growth
Direct measurement of phase-space change on new LEBT
The primary and chopped beam are separated in phase space with the increase of the chopper voltage.
Emittance growth caused by SCC destroy starts to saturate when chopper voltage is larger than 1kV.
0V
100V
250V
500V
750V
1000V
2000V
3000V
For a beam current of 33 mA, RMS emittances of 95% beam are measured.
Before chopped: 0.175 pi.mm.mrad, after chopped:0.206 pi.mm.mrad

## Slide 20: Stripped protons removal on new LEBT
Stripped protons
produced
Stripped protons lost
Vac. 2E-3Pa
Vac. 1E-6Pa
Risk of stripped protons to SCC with doubted frequency
Low beam energy, high residual gas density in LEBT corresponds to high stripping rate.
Protons are accelerated by RFQ, DTL, and Spoke-SCC together with H- beam with phase shift of π.
Stripped proton loss in 648MHz Elliptical cavities contributes to the heat load and radioactivity.

## Slide 21: Stripped protons removal on new LEBT
1.8degree
Bending magnet
Stripped protons production
+2e+p
The associated proton beam can be accelerated by RF cavities with 180 degrees phase shift. It may heat up and quench the super-conducting cavity. So it should be suppressed before it enters the super-conducting cavities.
Residual gas distribution.
p
RFQ acceptance

## Slide 22: Stripped protons removal on new LEBT
Small Angle
Bending Magnet
Faraday Cup
At a gas flow rate of 20 SCCM, the protons produced before the bending magnet is less than 0.5% of the H- beam. These protons can not enter the RFQ after bent by the magnet.
Proton signal
enlarged by 400
Stripped protons measurement

## Slide 23: Stripped protons removal on new LEBT
5X RFQ accept.
eclipse
5X RFQ accept. eclipse
Without the bending magnet, 37% of proton beam is captured by RFQ, p/H- in RFQ~0.15%
Simulated with IBSimu Code, tend to overestimate the captured protons.
With the bending magnet, 3% of proton beam is captured by RFQ, p/H- in RFQ~0.01%

## Slide 24: Proton-loss power in the SCL
The total power lost of protons in the linac after RFQ is approximately 0.67 W.
About 20% of the protons are lost in room temperature linacs.
In the SCL section, proton beam loss primarily occurs after the first cryomodule for spoke cavities and also near the end of the elliptical (648 MHz) cavities.
The maximum proton loss at a single mesh grid is approximately 0.25 W, located in the room temperature matching section between the first and second cryomodules.

## Slide 25: A backup scheme
Crossed beam transport rather than a parallel beam transport.
An Iris aperture 16~38 mm will be installed in chamber 2 close to the beam waist.
Additional 1000 l/s TMP in chamber 2.
In this scheme, the IBSimu simulation shows that the number of protons captured by the RFQ can be further reduced by an order of magnitude.
Drawback: Longer time to build up space charge compensation, more beam should be chopped.

## Slide 26: A backup scheme
Aperture diameter adjustable from 16~38mm, covering crossed and parallel beam transport.
Blades are made from molybdenum, working up to 800 degree.
Also as a beam scrapper for 25 W average power dump per blade (15mA×55kV, 3% d.f.)
Beam intensity regulation in LEBT without changing focusing optics.

## Slide 27: Summary
The RF-driven H- ion source with external antenna demonstrate a life-time of above 1000 days.
Emittance of the H- beam is optimized on new LEBT
1.8 degree bending in LEBT successfully suppresses the stripped protons produced in LEBT.

## Slide 28
Thanks for your attention!
SPS in plan