## Slide 1: LhARA FFA magnet design
Ta-Jen Kuo
Supervisor: Jaroslaw Pasternak, Jean-Baptiste Lagrange
Imperial College London, STFC
26/02/25

## Slide 2: Aim
LhARA FFA
Radiobiological purposes
Working point in tune stays the same
while scaling B field to accelerate
different energy ranges (constant K)
Variable extraction energy from FFA
(15-127.4 MeV)
Notes: for the studies of beam optics at different tune points

## Slide 3
Make the Integrated field follow the Scaling Law
where is the integrated field at 𝑟0,
𝑘 the integrated field index defined as:
Magnetic field required

## Slide 4
Current optimisation Procedure
Create 3D opera model with ‘Metaopera 1’, a python script that created Opera
3D models through command line
2. Vary current in each trim coil individually to obtain a Jacobian in change in
current vs integrated field at different radii
3. Solve the Opera model and analysis with my own python script.
4. Using the Jacobian and a Scipy optimisation routine, obtain new estimate of
currents to reach closer to scaling law
5. Repeat until termination condition reached
1 Developed by Thomas Planche, Hui Wen Koay, Ta-Jen Kuo and Jean-Baptiste Lagrange
The process of modelling and optimizing is similar for both projects
with slight variation due to the doublet structure of FETS-FFA

## Slide 5: Magnet parameters
LhARA FFA
H shape magnet
10 fold symmetry
F singlet spiral
spiral angle:53.9 deg
k-value range 5.23
Maximum injection proton energy 15 MeV
Maximum extraction proton energy 127 MeV
Opening angle 12.24 deg
Full gap size 96mm
Coils in red wrapped around the pole
Field clamps connected to pole magnetically

## Slide 6
Trim coils wrapped in two height layers to reduce thickness and opening angle
All return towards the outside of the pole and add towards the main coil,
most energy efficient in terms of current
On the pole face, the trim coils are wrapped in two overlapping layers (with the same set of
currents), this reduces the field error comparing to without overlapping
The dimensions of the magnet are labelled in millimetres and the
conductors are labelled from 0-18.
Cross section view of magnet

## Slide 7
Modelling the trim coils

## Slide 8
In the 3D Opera model, sweeping through theta obtain Bz on midplane at a particular radius
Repeat of different radius to obtain integrated B field at different radii
Integrated B field

## Slide 9
Central scenario: BL0 : 1.44 Tm , r0 :3.477m, k : 5.23 (15 – 127 MeV)
Oscillation in residuals due to the discretization of trim coils
Field residual after optimization

## Slide 10
Part of the pole reaching 2.66T
Flat top of field distorted at higher radii due to
Saturation and will have an impact to the tune
Saturation level and field profile

## Slide 11
Plotting the ring tune against resonance up the
4th order

## Slide 12
Clamp height varies
Between 52mm to 56.5 mm off the midplane
The vertical tune can be further controlled by
adjusting the vertical aperture of the clamps

## Slide 13
Tune after changing aperture of clamps

## Slide 14
Performance at lower energy range
For the LhARA machine, we would like to accelerate beams at different energy while
being at the same tune point.
This can be done by scaling the BL0 value in the integrated field
Setting BL0 to of the original value, 7- 57 MeV energy range

## Slide 15
Tune from optimizing integrated B field at two thirds B

## Slide 16
Tune at different energy ranges

## Slide 17
Field in the straight section
Showing the B field on
the midplane within the GFR
Highest field in straight section
is 60 Gauss
Centre of the machine towards
The origin

## Slide 18
Could affect the performance of the RF cavity
Has an impact of tune that is not well understood
Why does the amount of overshoot matter

## Slide 19
Vary aperture of clamp
Good effect on the overshoot, but fringe field extend could be scaling in
The wrong way?

## Slide 20
Tune from tracking
Currents would need to be reoptimized to obtain constant k index, but vertical
Tune spread increases significantly

## Slide 21
Cut a hole between pole and entry clamp to make it less efficient

## Slide 22
Vertical tune spread has also increased but can be flattened by shaping the aperture
Of the clamps accordingly
Another option to try: decreasing the thickness of the entry clamp
Tune from tracking

## Slide 23
Larger energy range tracking

## Slide 24
Conclusion
Latest tracking results show tune of the beam at both highest and lowest energy
are away from resonances up to forth order
Field in straight section reaches 60 gauss due to overshoot of the field caused by
the entry clamp
Methods of avoiding the overshoot is being investigated in case it affects the RF
cavity performance (Also to better understand the behaviour of the tune from a
theoretical point of view)

## Slide 25
Extra slides

## Slide 26
Vertical tune considerations
Spiral Angle
Spiral angle =
For entry and exit sides of magnet separately

## Slide 27
Spiral angle on the exit side decreases as the flat top of the B field gets affected
By saturation

## Slide 28
Flutter calculation
We can also calculate the flutter
By using the formula above and we
Have most of the variables needed
To predict vertical tune

## Slide 29
Comparing results to approximate tune equations
One problem with the equation is that it assumes
the field profile is symmetric and there is only one
spiral angle, not separately for entry and exit
Using the average of entry and exit for now

## Slide 30
May need to include other terms in equation
Is using average spiral angle the best idea?
Goal
To understand what is causing the change in vertical tune
Therefore understand better how to shape the clamps to further
Decrease vertical tune spread
Questions

## Slide 31
Disconnect entry clamp completely