## Slide 1
Measurements of Fission Fragment Masses and Proton Numbers at ILL and n_TOF, CERN
Nikolay Sosnin IOP 2025 24 April 2025
N.V. Sosnin1*, A. G. Smith1, T. Wright1, U. Köster2, Z. Eleme3, A. Sekhar1, A. D’Ottavi1, M. Wlodarczyk1, C. Lederer-Woods4, M. Diakaki5, V. Michalopoulou5, N. Patronis3,6, M. Bacak7
1 - University of Manchester, UK
2 - Institut Laue-Langevin, France
3 - University of Ioannina, Greece
4 - University of Edinburgh, UK
5 - National Technical University of Athens, Greece
6 - CERN
7 - TU Wien, Austria

## Slide 2: Structure
Nuclear Fission
Bragg Detectors and Fragment Measurements
Institut Laue Langevin
n_TOF
Conclusion
Nikolay Sosnin IOP 2025 24 April 2025

## Slide 3: Nuclear Fission
Nikolay Sosnin 77Se(n,𝛾) Measurement 25 Nov 2021
Binary fission mostly produces FF with different mass
Double-magic Z=50 N=82 (132Sn) shell closure very strong and defines the heavier fragment
Left-over matter forms a lighter fragment
Nikolay Sosnin IOP 2025 24 April 2025
K.F. Flynn et al., Phys. Rev. C 5, 1725 (1972).
I. Ahmad and W.R. Phillips, Reports on Progress in Physics 58, 1417 (1995).

## Slide 4: Fission Experiments
USEFUL OBSERVABLES
FF A,N,Z, KE → Frequently use Bragg Detectors
Prompt neutron/gamma energies, multiplicities, angular distributions
Typically, correlated measurements of fission observables needed, requiring large arrays
SPIDER (Los Alamos, USA)
STEFF (Manchester, UK)
BD
BD
BD
BD
BD
BD
BD
BD
Nikolay Sosnin IOP 2025 24 April 2025
FALSTAFF (CEA, France)

## Slide 5: Bragg Detectors and Fragment Measurements
Bragg detector is a coaxial ionization chamber
Typical gasses CF4, argon, isobutane (iC4H10)
Kinetic energy resolution 0.5 MeV
Grid ensures linear response, blocks +ve ions
FF
Bragg Detector
Anode
gas
Grid
Nikolay Sosnin IOP 2025 24 April 2025
1-meter flightpath
~100 nm formvar+Al foils
700 ps TOF resolution

## Slide 6: FiFI at Lohengrin
Nikolay Sosnin 77Se(n,𝛾) Measurement 25 Nov 2021
Fission Fragment Identification (FiFI) arm used at Lohengrin for two weeks measurement in June 2021
239Pu target
Lohengrin separates by A/q and E/q
Aim is investigating ionization signal traces for any variations correlated to fragment Z
Nikolay Sosnin Fission Studies 23 May 2022
Nikolay Sosnin IOP 2025 24 April 2025

## Slide 7: A Little Preview of Results
Nikolay Sosnin 77Se(n,𝛾) Measurement 25 Nov 2021
Lohengrin separates by A/q and E/q
For each q state of all FF produced in target, only one mass and energy will satisfy both ratios
Each peak corresponds to a single ionic charge state
Each mass contains a mix of Z
All FF have the same velocity
Bias Z yield with q gate
Nikolay Sosnin Fission Studies 23 May 2022
Beam setting: A/q = 5, E/q = 4.5
Nikolay Sosnin IOP 2025 24 April 2025
KE (arb.)
TOF (chan.)
TOF (chan.)

## Slide 8: n_TOF, CERN
0.8% geometric efficiency → Need high flux at EAR2
Higher gamma flash
2 beam collimators: ⌀6cm and ⌀2cm
FiFI TOF section shortened from 1 m to 0.5 m to improve statistics
Use ⌀6cm 235U target for testing
Use fast neutrons (0.5-10 MeV) to measure fission mass yields
Plans for 243Am and 230Th for nuclear waste in fast reactors and thorium fuel cycle
Nikolay Sosnin IOP 2025 24 April 2025
Bragg detector
Timing detectors
EAR1
EAR2
185 m beamline
20 m beamline
Neutrons
235U

## Slide 9: Test results
Nikolay Sosnin IOP 2025 24 April 2025
Thermal neutrons
KE (arb.)
TOF (ns)

## Slide 10
Nikolay Sosnin IOP 2025 24 April 2025
⌀6cm collimator isobutane
⌀2cm collimator isobutane
⌀2cm collimator CF4

## Slide 11: Conclusion
ILL analysis ongoing
Calibration is completed
Use such data to identify Z-dependent variations
Nikolay Sosnin 77Se(n,𝛾) Measurement 25 Nov 2021
Nikolay Sosnin Fission Studies 23 May 2022
n_TOF analysis ongoing
Investigated fill gases and collimation
Tests with silicon and scintillators planned
Campaigns for measuring mass yields of 243Am and 230Th in the future?
Nikolay Sosnin IOP 2025 24 April 2025
THANK YOU