## Slide 1: The challenge of VHEE planning: providing robust plans that will ease a FLASH delivery
A. Sarti
International Workshop on Very High Energy Electron Radiotherapy (VHEE’25)
STFC, Daresbury Laboratory

## Slide 2: The challenge of VHEE planning
Planning with 𝛾 (earliest) and p / 12C (more recent) has a long history… For VHE e- it’s, almost, an unexplored territory (10 y?)..
What are the VHEE characteristics that we can exploit when planning a treatment?
Vozenin, MC., Bourhis, J. & Durante, M. Nat Rev Clin Oncol 19, 791–803 (2022).

## Slide 3: Are VHEE (CONV) suited for RT?
YES! known since, at least, 2014..
But initially with a focus on E>> 100 MeV (dose reduction in entrance channel + better dose conformity)
→ Geometry and beam delivery in first attempts was inherited from IMRT
→ We kept this approach as we are looking towards FLASH: no arc, no need to reduce dose to OARs as FLASH will help us

## Slide 4: IMRT ok for complex geometries
Intracranial lesions
Pancreatic cancer

## Slide 5: To plan → we need a beam model
The exploration of ALL the possible solutions will take some time :)
We started from few (arbitrary) assumptions on a possible road towards FLASH
Compact accelerating solution (small footprint, advantage wrt p) → ‘small’ E [70 - 150 MeV]
Few irradiation fields (IMRT like)
We had in mind a ‘SAFEST’-like solution [see L. Giuliano talk] for VHEE… Most of the results can be generalised in a straightforward way!
[please be reminded that everything I show in the next slides is MC ]
Naturally VHEE from RF are coming in ‘pencil beams’ transverse size @ exit window of ~mm, with small divergence

## Slide 6: The workflow
Assumption for FLASH: 1 field <-> 1 E
Mimic IMRT
2. Choose APBS pattern
3. Define field E

## Slide 7: How to include FLASH?
Little is known yet about dependence on tissue, D and DR of the FMF (FLASH sparing)
→ D modeling as in Bohlen,Int J Radiat Oncol Biol Phys. 2022 Dec 1;114(5):1032-1044.
→ DR calculation as in Folkerts, M.M. (2020), Med. Phys., 47: 6396-6404 + Threshold (40 Gy/s)
Robustness comes from varying Dth, FMFmin, DR threshold AFTER ensuring CONV compatibility

## Slide 8: A first exercise: pancreatic cancer
Start with a “simple” exercise:
→ Implement APBS
→ Neglect, on first attempt, the DR dependence: go only for D dependence
Treatment efficacy is limited by induced duodenum toxicity → Can we increase the dose to the PTV while keeping the max dose to the duodenum under control (avoid perforation → patient death)?
Treatment of pancreatic cancer with very high dose per-fraction (e.g. 6 Gy) is likely to profit significantly from the FLASH effect!
PTV
duodenum

## Slide 9: Pancreatic cancer: results
Prescribed dose (*0.95) that can be reached in 100% of the target volume
A. De Gregorio et al., Phys Med 137, 2025, 105076 [10.1016/j.ejmp.2025.105076]
The FLASH effect could allow to significantly increase the D prescriptions!
[neglecting DR dependence, assuming FLASH in the whole OAR volume]

## Slide 10: A step forward: including DR
Neglecting the DR dependence can have a HUGE impact on the results: FLASH it’s not “only” about D but mainly about DR
→ We need to include the ‘details’ on how we want to deliver the beam to compute the DR and account for it
The perfect candidate for FLASH studies: treatment of NSCLC with very high doses per fraction, small number of PBs (small volume 4 to 10 cc), promising results from lung toxicity reduction in mice with FLASH!
Lung tumour patients treated at Campus Bio-Medico University Hospital of Rome with high D prescriptions using photons delivered with VMAT technique.

## Slide 11: Three examples.. (not exhaustive!)
‘Flat’ beam with 2D (transverse) D shaping → worse PTV coverage, but highest DR!
Spatial fractionation (minibeam) → combines advantages of SFRT & FLASH (D and DR increase in entry channel)
Active scanning with smallest number of PBs compatible with reasonable dose conformation to the PTV → slower but better PTV coverage

## Slide 12: APBS lung treatment
130 MeV are needed to reduce the dose in the entrance channel [chestwall/ribs].. No significant gain in overall plan quality going @ 200 MeV
Beam E optimisation
PBS: optimised #PB + fixed FWHM (1cm)  looking @ dose conf in CONV mode
FLAT: ‘emulated’ 2D collimation  no real entrance beam shape optimisation  conservative results
SFRT: went for highest PVDR ratio while keeping good uniformity/coverage of PTV
Same 4 fields approach for all the different options (PBS, Flat, SFRT)

## Slide 13
9
PTV
Portion of lung
tissue within 2
cm of the CTV
NSCLC results - CONV

## Slide 14: What about the ‘DR’?
When computing the DR in a multi-field approach we are facing an important challenge: account for the ‘field switching effect’.
PTV
CTV
2cm lungs -CTV
chestwall
DRVH
40 Gy/s
For now: computing a ‘per field’ DR and applying the FMF correction if (in each field) D and DR requirements (>40 Gy/s) are met!

## Slide 15: The FLASH potential
 | Lungs | Other OARs
FMFmin | 0.12 | 0.6
Dth | 6 Gy | 13 Gy
Data | Mouse lung | Zebrafish body

## Slide 16: The FLASH potential
PT 1: 4 x 12 Gy
PT 2: 3 x 15 Gy
PT 3: 3 x 15 Gy
PT 4: 8 x 7.5 Gy
Why such a small effect?
D/field outside PTV is small!
The D dependence

## Slide 17
How to increase the FLASH effect? Deliver 1 field x fraction: dose per field/fraction increases! → Switch to BED to account for new fractionation scheme..
In our example: 4 fields? → 4 fractions
What matters are the ⍺/β values:
⍺/β (PTV) : 10 Gy while ⍺/β (OAR) : 3 Gy
Can FLASH balance the huge increase in toxicity for the OARs?
The ‘one field per fraction’ approach

## Slide 18
OFPF : results
CONV exposes OARs in entry channel to

## Slide 19: Concluding remarks
VHEE (E ≥ 100 MeV) are competitive with state-of-the-art RT and PT → interesting for FLASH applications in view of fixed-E ‘SOBP’ w.r.t p
  Still room for ‘optimising tools optimisation’ → conservative results so far!
FLASH evaluation, so far, starts after reaching the CONV conformity and aiming to go beyond exploiting the FLASH sparing
The FLASH planning challenge is to balance two competing requirements: bring D and DR to maximum values while keeping BED and dose conformity at the level of CONV irradiations
  Better modelling of D, DR and tissue dependence of FMF is crucial to define the best irradiation scenario  Robustness calls for full FMFmin, Dth, tissue study for each specific plan..
  → Different fractionation approaches might help to enhance the FLASH effect..

## Slide 20: Spare slides

## Slide 21: Pancreatic cancer: results

## Slide 24: Arc? Yes we can.