## Slide 1
Sam Leadley University of Oxford & CERN
Prof. Manjit Dosanjh University of Oxford
Prof. Raj Jena University of Cambridge
Predictive Modelling of Radiotherapy LINAC Downtime using Variational Autoencoders
Notes: State I will motivate how this will be useful to VHEE RT as well…

## Slide 2: Background & STELLA
M. Dosanjh, 2025. “Towards Implementing Project STELLA on radiotherapy powered by AI”, GHC Summit. MIT, Boston, 19/09/25.
Notes: Talk about STELLA motive, etc.

## Slide 3: Motivation
Access to RT in LMICs (such as in Africa) is highly limited by available machines.
Of the few available machines, many experience significant downtime, far more than in HICs.
Machines are pushed harder to compensate for lower availability.
Ability to predict machine downtime in advance allows for repair preparation & preventative maintenance.
T.A. Ige et. al. (2021). Surveying the Challenges to Improve Linear Accelerator-based Radiation Therapy in Africa
Notes: Why my research is relevant

## Slide 4: RT Machine Log Files
Automatically recorded onto RT machines (Varian TrueBeam), no patient identifiable data.
Contains information on the exact state of the machine at any point in time.
“Severe” interlocks – known to cause machine downtime in clinical settings.
Want to predict when severe interlocks are likely to occur.
Time & date of interlock code
Interlock code
Example of processed Varian Combined Log file. All interlocks have been extracted but are yet to be filtered.
Notes: Data fed into algorithm – explain what trying to predict

## Slide 5: Variational Autoencoder, Dual-Classifier Approach
Novel dual VAE classifier splits classification into two tasks:
  severe/non-severe interlock
  most likely severe interlock (assuming interlock is severe)
Inputs are sets of 100 consecutive interlocks, plus 50 more sampled up to 1 week prior.
  Training inputs are labelled with the next interlock code.
Inputs are projected into a low-dimensional latent space:
  Severe interlocks with similar causes are spatially close in the latent space.
  Position of an input in latent space allows for probabilistic predictions of proceeding interlocks.
Dual-classifier workflow
Neural network 1 (severe/non-severe interlock)
Input sequence
Neural network 2 (interlock assuming severe)
Probability severe/non-severe interlock
All severe interlock probabilities
All probabilities (all severe interlocks & severe interlock)
Notes: No need to explain exactly how VAE works, not enough time.

## Slide 6: Binary Classifier Performance
F1 scores are very strong:
Model is better at predicting non-severe vs. severe interlocks:
  Potentially expected due to large class imbalance.
  Tried several methods e.g. class weighting to improve this with limited success.
  Improvement will likely require larger volumes of data, specifically with severe interlocks.

## Slide 7: Fault Classifier Performance
F1 Scores:
Model shows significantly better-than-even odds of predicting exactly the correct next severe interlock in series:
  Top 3 accuracy is approaching 90%.
  Most of the time all top 3 interlocks are very similar e.g. 212110, 212111, 212114 (Dose less than expected).
Significant improvement over this is difficult due to the inherently random nature of breakdowns.

## Slide 8: Comparison to other prediction methods
*Overall accuracy of stratified guessing is boosted due to almost exclusively predicting “no severe fault”
Chart: 
| VAE Double Classifier | VAE Single Classifier | Stratified Guessing* | Random Guessing
Overall accuracy | 0.8636 | 0.6027 | 0.9031 | 0.0244
Top 3 Severe Accuracy | 0.614 | 0.4936 | 0.00605 | 0.0714
Severe Accuracy | 0.4628 | 0.3502 | 0.003 | 0.0244

## Slide 9: Next Steps
This fault prediction process can be generalised away from the Varian TrueBeam.
  Algorithm is applicable to any other Varian machine, and any RT machine with a similar logging style.
  Approach is data-agnostic so can be applied to any machine with a similar fault reporting system, regardless of function.
Automatic fault-prediction is even more important in VHEE treatment systems.
  VHEE machines are more complex than regular RT machines and so are more fragile, with more scope for technical breakdown.
  Short timescales lower than human reaction time require machine-driven treatment stops.
Proof of concept for fault prediction opens the door to more powerful ML algorithms.
  Transformers can capture more information about contextual and long-term relationships with inherent temporal encoding and attention mask.
Notes: Emphasise VHEE/other applications for this conference

## Slide 10
Thank you!
Contact: samuel.Leadley@physics.ox.ac.uk
This work was supported by funding from the John Adams Institute (JAI), Oxford, and the Science & Technology Facilities Council (STFC).
  Collaborators & Supervisors:
  Torsten Liebig, Exeter-Wonford Hospital
  Jonathan Lane, Gary Grogan, Oxford-Churchill Hospital
  Andrew Robinson, Ian Dulgarn, Cambridge-Addenbrooke’s Hospital
  Manjit Dosanjh, University of Oxford
  Raj Jena & Doris (Xin) Du, University of Cambridge
  Laurence Wroe & Steinar Stapnes, CERN

## Slide 11: Variational AutoEncoder – Neural Network
ENCODING
LATENT SPACE
DECODING
μ
σ
Latent space distributions
z1
z2
Distribution samples
Interlock A
Interlock B
Interlock C
Interlock D
Interlock F
Interlock E
Input from string of previous interlocks.
Input size = vocab size.
Input vocab.
0.12
0.01
0.68
0.05
0.02
0.14
Most likely output is next fault interlock prediction. Output size = number of severe fault + 1
Output vocab.
x1
x2
x5
x3
x4
x6
Seq. encoding
e1
e2
e3
e4
Embedding layer
h1
h2
h3
h4
Hidden layer
h1
h2
h3
h4
Hidden layer
X1
X2
X5
X3
X4
X6
Output layer
Notes: Input passes through dim reducing layers to find features & patters – latent dimensions
Gaussian dists have means and variances
Distribution gives model flexibility when predicting due to uncertainty
Decoder samples from latent distribution, passes sample through layers to give interlock probs
Evaluation is based on how well the model predicts next code, and how close the latent dist. is to std. normal (smooth/well organised)

## Slide 12: Fault Classifier Latent Space

## Slide 13: Time-series Probabilities
Interlock 363002 – Laser guard fault, potential failure if often. Medium severity.
Interlock 212111 – Target under dose rate, potential HV Thyratron problem. Medium severity.