## Slide 1: Transfer Matrix Formalism of In-Air VHEE Beam Profile Measurements at PEER
J. Valerian*, M. Volpi, P. Giansiracusa1, P. Pushkarna, R. Rassool, S. L. Sheehy2
University of Melbourne, Melbourne, Australia
Y.-R. E. Tan
Australian Synchrotron – ANSTO, Melbourne, Australia
1also at Australian Synchrotron – ANSTO, Melbourne, Australia
2also at ANSTO, Sydney, Australia
*joel.valerian@student.unimelb.edu.au
The 4th International Workshop on Very High Energy Electron Radiotherapy (VHEE’25)
15 – 17 September 2025, Daresbury, UK

## Slide 2: Objective
Characterise our VHEE beams at PEER
  What do I mean by “characterise the beam”?
  How do you characterise the beam?
  Can you do that at PEER?
  Why do you need to characterise the beam?

## Slide 3: Tangent: PEER at Australian Synchrotron
Geomagnetic North Pole
Geomagnetic South Pole
Source: ansto.gov.au
Melbourne, Australia
Daresbury, UK
Pulsed Energetic Electrons for Research (PEER)
RF: 3 GHz (S-band), Buncher: 500 MHz
Gun: Thermionic triode
Energy: ~100 MeV ( 70 – 110 MeV) +/- 1%
Bunch length: ~100 ps*
Single bunch mode: 30 fC to 12 pC
Multi bunch mode: 0.48 – 4.8 nC (1 – 500 bunches)
Train length: 16 ns – 1000 ns
Repetition: 1 – 5 Hz
17.000 km

## Slide 4: Pulsed Energetic Electrons for Research (PEER)
Vacuum Beam Pipe
Ø 42.5 mm
LINAC: Linear Accelerator
HC: Horizontal Corrector
FCT: Fast Transformer
QF: Focusing Quadrupole
QD: Defocusing Quadrupole
VC: Vertical Corrector
D: Dipole
W: Vacuum Window
732.5 mm
150 mm
301.8 mm
150 mm
302.3 mm
150 mm
300 mm
198.6 mm
150 mm
127 µm
LINAC
HC
FCT
VC
QF1
QD2
QD3
D
(Off)
W
To Booster Ring
PEER End Station
2 S-Band Structures @ 100 MeV
127 µm Titanium
Transfer Line to Booster Ring
XYZ Linear Motion Stage
Quadrupole
Triplet
(QF1, QD2, and QD3)
~400 mm
~100 mm
Limited in x-axis now, possible plan to extend beamline 🤞
Faraday Cup
XYZ Linear Motion Stage

## Slide 5: What do you mean by characterise?
Courant-Snyder (CS) parameters (, , , and ) describe the distribution of position and angle of the beam:
is the covariance matrix of position and angle.
Transformation of the covariance matrix:
is the transfer matrix, specific to beamline elements (drift, dipole, quadrupoles, etc)
Why? Knowing at one point = knowing it everywhere
Measure: Quadrupole Scan -> Obtain CS parameters by observing how beam size changes as a function of quadruple current (focusing strength)
Phase (Trace) Space
LINAC
QUAD 1
QUAD2
BPM*
*Beam Profile Monitor (Scintillating Screen)

## Slide 6: Can we do that at PEER?
Vacuum Beam Pipe
Ø 42.5 mm
LINAC: Linear Accelerator
HC: Horizontal Corrector
FCT: Fast Current Transformer
QF: Focusing Quadrupole
QD: Defocusing Quadrupole
VC: Vertical Corrector
D: Dipole
W: Vacuum Window
S: Scatterer
BPM: Beam Profile Monitor
732.5 mm
150 mm
301.8 mm
150 mm
302.3 mm
150 mm
300 mm
198.6 mm
150 mm
127 µm
LINAC
HC
FCT
VC
QF1
QD2
QD3
D
(Off)
W
To Booster Ring
PEER End Station
2 S-Band Structures @ 100 MeV
127 µm Titanium
No in-vacuum BPM along beamline except an OTR screen after dipole in transfer line
or do we?
How do we characterise our beam??? In-air BPM?
Screen here?
BPM
Not valid because of scattering → we don’t know transfer matrix of the window and air…

## Slide 7: Can we include scattering?
Yes (Negra, 1971 and others):
: scattering angle
: momentum change
PDG and NIST database
Assumption:
Multiple Coulomb scattering only (small scattering)
Linear energy loss
Uncoupled beam
Include scattering

## Slide 8: Let’s do our (modified) quad scan!
Width x Height
45.00 mm x 31.82 mm
(4.5 µm/px x 3.2 µm/px )
Screen Calibration:
Screen marked by a 45 mm square box using laser cutter
Experiment parameters:
Fix charge to around 1 nC
Turn off correctors
Set QD2 to 9 A and turn off QD3
Scan QF1 from 0 A to 14 A
Vacuum Beam Pipe
Ø 42.5 mm
LINAC: Linear Accelerator
HC: Horizontal Corrector
FCT: Fast Current Transformer
QF: Focusing Quadrupole
QD: Defocusing Quadrupole
VC: Vertical Corrector
D: Dipole
W: Vacuum Window
S: Scatterer
BPM: Beam Profile Monitor
732.5 mm
150 mm
301.8 mm
150 mm
302.3 mm
150 mm
300 mm
198.6 mm
150 mm
127 µm
162.5 mm
LINAC
HC
(Off)
FCT
VC
(OFF)
BPM
QF1
(Scan)
QD2
(9 A)
QD3
(OFF)
D
(Off)
W
To Booster Ring
PEER End Station
2 S-Band Structures @ 100 MeV
127 µm Titanium
Screen
Window
100 MeV Electrons
Transfer Line
Camera
XYZ Linear Motion Stage
Setup:

## Slide 9: Result
Beam size over distance
Parameters | X-Axis | Y-Axis
(m) | 4.176 ± 0.219 | 1.996 ± 0.150
 | -1.815 ± 0.094 | -1.349 ± 0.105
(mm.mrad) | 0.198 ± 0.009 | 0.293 ± 0.014
Parameters | X-Axis | Y-Axis
 | 4.176 ± 0.219 | 1.996 ± 0.150
 | -1.815 ± 0.094 | -1.349 ± 0.105
 | 0.198 ± 0.009 | 0.293 ± 0.014
Search for CS parameters that best fit data
Expected emittance: 0.17 – 0.62 mm.mrad
Quad Scan Measurement
All good, …right?
NO
We claim transfer matrix can find the beam at any point, can we predict beam size then?

## Slide 10: Not quite right!
The real emittance should have been bigger than our prediction because our model overestimate the scattering
More work needs to be done, but seems like we’re on the right track…
BPM
PMMA
Window
100 MeV Electron Beams
2. Introduce additional scatterer:
1. Simulate titanium window AND air in TOPAS:
Optimisation can match the measurement but reach the wrong actual CS parameter by a bit
Repeat quad scan, overestimate again!

## Slide 11: Why do we need to know the CS parameters?
Beam manipulation (focusing/defocusing beams)
Beamline development (e.g. CLEAR 2nd beamline)
Accurate Monte Carlo simulation (beyond point-like source + simulating secondaries)
Dosimetry study
  Can Cherenkov radiation from water be used for VHEE beams dosimetry?
Cherenkov radiation from VHEE beams traversing a water jar with various magnet and charge setting
Takeaway
Modelling scattering in the transfer matrix formalism allows us to:
Find the initial CS parameters with in-air BPM
Predict beam diameter in air (or water?) only by knowing the upstream quadrupole setting
“Bypass” compute-heavy Monte Carlo in optimisation loop
Optimising focusing parameters of VHEE beams for radiotherapy using MC simulation. J. Valerian. Proc. IPAC’25, Taiwan

## Slide 12: Thank you! Joel Valerian joel.valerian@student.unimelb.edu.au
Installation of one of the two X-band TD24 accelerator structures at the University of Melbourne, c. 2024.

## Slide 13: How valid is this?
Simulate different material of interest and score the final phase space in TOPAS*:
*Monte Carlo Particle Transport Simulation based on Geant4
Within 4% of diameter difference, the scattering model agrees (roughly) up to certain radiation length ():
>200% for titanium (7.12 cm)
20% for PMMA (6.81 cm)
0.25% for air (75.98 cm)
Simulation parameters:
1 million 100 MeV electrons
Physics list:
g4em-standard_opt4
g4h-phy_QGSP_BIC_HP

## Slide 14: What do you mean by characterise?
Phase (Trace) Space
Courant-Snyder (CS) parameters (, , and ) describe the distribution of position and angle of the beam:
is the covariance matrix of position and angle.
Knowing CS parameters at one point = knowing it everywhere
Quadrupole Scan -> Obtain CS parameters by observing how beam size changes as a function of quadruple current (focusing strength):
Not valid if there is scattering, e.g. in-air BPM
Transportation of the covariance matrix:

## Slide 15: Evaluation
Possible source of discrepancies:
Accumulation of hard scattering over multiple different scatterers
Moving centroids: quadrupole misalignment?
Rotated beam: transverse coupling due to upstream solenoids?

## Slide 16: Quadrupole Current to Gradient and Focusing Strength
Where is the quadrupole gradient in T/m, is vacuum magnetic permeability (), is number of turns per coil, is the coil current in A, and is the aperture radius in m.
Where is the quadrupole focusing strength in m-2, c is speed of light in m/s, and E is the particle energy in eV.

## Slide 17: References for Scattering in Transfer Matrix Formalism
Several references:
  Electron beam emittance growth in thin foils: A betatron function analysis. M. Reid 1991. Journal of Applied Physics.
  Thick Scatterers seen through the Twiss Functions. A. Maier 1998. CERN Note.
  Description of Beam-Matter Interaction in the Covariance Matrix Formalism. A.-S. Muller 2001. CERN Note.
  Multiple Coulomb Scattering of Beam Particles in the Phase Space Ellipse formalism. M. D. Negra 1971. SLAC Technical Note.
  Introduction to Transfer Lines and Circular Machines. P.J. Bryant 1984. CERN Lectures.

## Slide 18: Pulsed Energetic Electrons for Research (PEER)
Vacuum Beam Pipe
Ø 42.5 mm
LINAC: Linear Accelerator
HC: Horizontal Corrector
FCT: Fast Current Transformer
QF: Focusing Quadrupole
QD: Defocusing Quadrupole
VC: Vertical Corrector
D: Dipole
W: Vacuum Window
S: Scatterer
BPM: Beam Profile Monitor
732.5 mm
150 mm
301.8 mm
150 mm
302.3 mm
150 mm
300 mm
198.6 mm
150 mm
127 µm
125 mm
LINAC
HC
(Off)
FCT
VC
(OFF)
BPM
QF1
(Scan)
QD2
(9 A)
QD3
(OFF)
D
(Off)
W
S
0/3/6 mm
37.5 mm
To Booster Ring
PEER End Station
2 S-Band Structures @ 100 MeV
127 µm Titanium