## Slide 1: External Injection into Plasma to Produce VHEE Beams
RF Gun
Solenoid Magnet
Matching Section
LWFA Stage
Driving Laser
Jordan Byrne1,4, Oznur Apsimon1,4, Mike Taylor1,2, Guoxing Xia1,4, Hossein Saberi1,4, Jiaqi Zhang1,4, Tom Pacey3,4, Hywel Owen3,4, Stewart Boogert1,4
1The University of Manchester, UK, 2The Christie NHS Foundation Trust, Manchester, UK, 3Accelerator Science and Technology Centre STFC/UKRI,
4The Cockcroft Institute of Accelerator Science and Technology, Warrington, UK

## Slide 2
External Injection into Plasma to Produce VHEE Beams
Speaker: Jordan Byrne
Acceleration gradients orders of magnitude larger than conventional RF technology.
Why use plasma?
Okay, but why use external injection?
🤔
🤔
Still room for improvement in beam quality and stability.
Removes the reliance on self-injection and promises better beam quality and stability.
Increased beamline and timing complexity.
Constantin Aniculaesei, et al.Matter Radiat. Extremes 1 January 2024; 9 (1): 014001
Gonsalves, Anthony, et.al. "Multi-GeV Plasma Acceleration Results at BELLA." 6th International Particle Accelerator Conference. 2015.
https://www.lancaster.ac.uk/physics/research/h3beams/
ESCULAP. Baynard, Elsa, et. al, Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment 909. (2018): 46–48.
https://sparclab.lnf.infn.it/

## Slide 3: Laser Plasma Wakefield Acceleration
External Injection into Plasma to Produce VHEE Beams
Speaker: Jordan Byrne
Linear wakefield formation:
(Zfocal and ramp length obtained through Bayesian optimisation)
Laser Parameter | Value
λ [nm] | 800
a0 | 0.8
τ (1/e2) [fs] | 25
w [μm] | 50
Zfocal [mm] | 3
+

Plasma density: 1x1023 m-3
a0 is comparatively low
Modest gradient: 1.7 GV/m
Plasma bucket (accelerating and focusing region): ~ 30 μm (100 fs)

## Slide 4: RF Gun
External Injection into Plasma to Produce VHEE Beams
Speaker: Jordan Byrne
Charge [pC] | 1 | 10 | 100
Laser pulse length [fs] | 30 | 50 | 50
Laser spotsize [μm] | 200 | 400 | 400
Energy [MeV] | 6.60 | 6.60 | 6.60
Normalized emittance [mm mrad] | 0.226 | 0.679 | 2.19
Beam size [mm] | 0.269 | 0.530 | 1.01
Bunch length [μm] | 13.0 | 26.0 | 104
Low charge
Implications on achievable dose rate.
Low energy
Bunch will slip back with respect to the wakefield.
Large beam size
Must use a transverse matching lattice in order to match the beam into the plasma.
Large bunch length
Bunch should occupy a fraction of the plasma bucket and hence requires bunch compression.
PHIN 2.5 Cell, 3GHz gun simulated at 100 MV/m

## Slide 5
External Injection into Plasma to Produce VHEE Beams
Speaker: Jordan Byrne
Main research questions:
Can an external injection design produce VHEE quality beams?
Can the design offer a compact alternative to conventional RF linacs?
Next steps:
Obtain an idealistic low charge bunch distribution for external injection.
Perform a more detailed RF gun investigation to assess the cathode laser parameters.
Explore bunch compression options: magnetic compression? velocity bunching? Multi-cell phase modified RF gun?
Thank you for listening!
Connect with me!
Jordan.byrne@postgrad.manchester.ac.uk
Any questions?
Thomas Geoffrey Lucas, et al , "Femtosecond-Scale MeV-UED Beamline Using a Stand-Alone Multi-Cell RF Photogun." (2025).