## Slide 1
Developments for the PoPLaR Experiment at SCAPA
Bunker B
B. C. Torrance1, R. Wilson1, E. J. Dolier1, C. J. McQueen1,2, M. Alderton1, M. P. Peat1,
J. Patel1,3, R. Nayli1, M. King1,2, R. J. Gray1,2, and P. McKenna1,2
1SUPA Department of Physics, University of Strathclyde, Glasgow G4 0NG, UK
2The Cockcroft Institute, Sci-Tech Daresbury, Warrington WA4 4AD, UK
3Central Laser Facility, STFC Rutherford Appleton Laboratory, Harwell, Oxford, OX11 0QX,UK
ben.torrance.2017@uni.strath.ac.uk
X THE PLACE OF USEFUL LEARNING
18/09/2025

## Slide 2
Talk Overview:
X THE UNIVERSITY OF STRATHCLYDE
18/01/2024
SCAPA Bunker B developments & current performance
Proof of Principle LhARA Radiobiology (PoPLaR) Experiment:
  Updated permanent magnet quadrupoles (PMQs) & Thomson parabola spectrometer (TPS) setup
  Preliminary Results: RCF & Lanex imager
Progress Towards a Calibrated High Repetition-Rate Thomson Parabola Spectrometer at SCAPA:
  High repetition rate: motivation & challenges
  ARISE: An Algorithm for Rapid Ion Spectrum Extraction
  TPS Calibration

## Slide 3
SCAPA: Scottish Centre for the Application of Plasma-based Accelerators
X THE UNIVERSITY OF STRATHCLYDE
18/01/2024
3
18/01/2024
SCAPA Laser Parameters | 
Peak Power | 350 TW
FWHM pulse duration | 25 fs
Energy per pulse (on target) | 7 J
Pulse repetition rate | 1 Hz
Temporal intensity contrast | 1010:1 @ 100 ps 108:1 @ 30 ps 104:1 @ 2 ps ASE contrast 1010:1
Central wavelength | 800 nm
Beam quality Strehl ratio | 0.85
SCAPA Laser Parameters | 
Peak Power | 
FWHM pulse duration | 
Energy per pulse (on target) | 
Pulse repetition rate | 1 Hz
Temporal intensity contrast | 1010:1 @ 100 ps 108:1 @ 30 ps 104:1 @ 2 ps ASE contrast 1010:1
Central wavelength | 800 nm
Beam quality Strehl ratio | 
High power laser facility based in the University of Strathclyde.
Capable of delivering 350TW at high repetition rates (1Hz) [1].
Three experimental areas (A,B,C) with Bunker B dedicated to ion acceleration & HRR operation.
[1]: S. M. Wiggins et al., SPIE, Apr. 2019

## Slide 4
18/01/2024
SCAPA Developments & Current Performance
4
Numerous developments have been made to Bunker B in the lead up to the Proof of Principle LhARA Radiobiology (PoPLaR) Experiment:
  Improved focal spot stability -> a std dev from the mean of around 1.46 µm (7.31 µrad) in x, and 2.26 µm (11.30 µrad) in y, equating to 1-2 spot diameters of jitter.
  Installed a new 50x objective lens on our focal spot camera -> better for spot optimisation.
  Prepulse removal -> significantly improved temporal contrast, laser energy stability, and focal spot jitter.
X THE UNIVERSITY OF STRATHCLYDE
Notes: Moving to the current performance of SCAPA:
On left we have the centroid position of our focal spot over 1000 shots relative to the nominal average position.
We see a spread of…
On the right, we have an example of one of our focal spots. This gave us a mean FWHM of 1.69 µm
Giving us an encircled energy of 23 %
We hope to improve on this through a rebuild of our objective lens setup moving from a 20x to a 50x mag lens, changing of the pellicle, and redesigning our HASO imaging line.

## Slide 5
Proof of Principle LhARA Radiobiology (PoPLaR) Experiment
X THE UNIVERSITY OF STRATHCLYDE
5
Permanent Magnet Quadrupole (PMQ) System
Cell Irradiation End Station
The design and addition of a capture beamline to Bunker B to guide and focus our laser-driven proton source to a cell irradiation end station.
Thomson Parabola Spectrometer
Multi-position cell holder
Retractable beam profiler
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 6
Updated PMQ and Thomson Parabola Spectrometer
X THE UNIVERSITY OF STRATHCLYDE
6
Figure (1): Photograph of updated Thomson parabola ion spectrometer diagnostic setup
Figure (2): Photograph of PMQs aligned to the proton beam propagation axis (green dashed). NOTE: target slightly out of position in this photo.
Figure 1 shows the Thomson parabola ion spectrometer (TPS) housed in a larger, more stable chamber compatible with the cell irradiation setup and Lanex imaging system.
A forward going laser diode was aligned through the target along the proton beam propagation axis and the TPS.
This diode was used to align the PMQs to this axis as shown in figure 2.
TPS Chamber
6-way
Cross
Cell Wheel
PMQ1
PMQ2
Target
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 7
Focused Proton Beam RCF
X THE UNIVERSITY OF STRATHCLYDE
7
Figure 4: RCF stack positioned at cell irradiation position.
Figure 5: Corresponding normalised RCF spectrum.
We successfully measured the focused proton beam outside the chamber at the cell irradiation position using an RCF stack, up to a maximum proton energy of = 11.6 MeV, as shown in figure 4.
Figure 5 shows the corresponding RCF spectrum. Calibration still required to extract real proton numbers.
PMQs
Figure 3: RCF stack showing input proton beam before PMQs.
Input proton beam to PMQs
Output proton beam from PMQs
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 8
Focused Proton Beam Lanex Imager
X THE UNIVERSITY OF STRATHCLYDE
8
Figure 6: Focused proton beam imaged using a Lanex scintillator filtered to detect ~ 8 MeV protons.
Figure 7: Normalised total light intensity on the Lanex scintillator as a function of shot number. Lines and shaded regions represent the median and ±1 std. dev. respectively.
We then placed an =700 µm mylar filter in front of a Lanex scintillator at the cell irradiation position, and imaged protons with a cut-off energy of ~ 8 MeV.
Figure 6 shows an example of the proton signal on our Lanex imager.
Figure 7 Is a plot of signal intensity which was variable, likely due to varying .
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 9
Control of Focused Proton Beam
X THE UNIVERSITY OF STRATHCLYDE
9
Figure 8: Control of proton beam focus through PMQ drive movement for ~8 MeV on Lanex scintillator
.
Figure 9: Images from a Lanex scintillator filtered to detect protons with a cut-off energy of (a) ~ 10 MeV and (b,c) ~ 11 MeV
Figure 8 shows the proton beam shape and position at the cell irradiation point being manipulated through PMQ drive control.
Both PMQs were then set to the current ‘optimal’ condition, and filtering on the Lanex scintillator was varied.
Figure 9(a) shows that protons with the desired energy of ~10 MeV have gone through focus. Figure 9(b,c) demonstrate that ~11 MeV is right at the limit of the proton energies currently being produced.
(a)
(b)
(c)
~ 10 MeV
~ 11 MeV
~ 11 MeV
~ 8 MeV
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 10
Update on Proposed Experiment Stages & Gateways
X THE UNIVERSITY OF STRATHCLYDE
10
I. Design & Procurement
II. Assembly & Alignment
III. Source Characterisation:
16th – 28th June
IV. Radiobiology:
20th Oct – 7th Nov
Start of BP1 funding
Order of PMQ XYZ stage (5-7 week delivery)
Order of cell station vacuum parts (4 weeks delivery)
Manufacture of thin window [DONE]
Manufacture of Oxford cell station
(in progress)
Construction of the cell station (in progress)
Construction of updated TP beamline [DONE]
Definition of an offline alignment line [DONE]
Construction and offline alignment of PMQ setup [DONE]
Install of PMQ system in vacuum chamber [DONE]
Change of parabola
1/2 weeks of SCAPA beamtime
Laser Beamline alignment (0.5 days)
Source optimisation w/o PMQ (0.5 days)
PMQ transmission, activation and debris test (0.5 days)
Lanex/beam profiler measurement at end of beamline (1 day)
PMQ position optimisation (0.5 days)
RCF measurements through beamline (0.5 days)
Full cell assembly RCF measurement (0.5 days)
3 weeks of SCAPA beamtime
Laser Beamline alignment (0.5 days)
Final setup of Cell mount/rotation
Alterations to PMQ/target setup and PMQ linear stage issue.
Test change to setup based on previous experiment.
Source optimisation with PMQs (1 day)
Dosimetry and source stability measurements (2 days)
Cell irradiation (6.5 days) + regular dosimetry
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 11
Required alterations identified after first PMQ beamtime
X THE UNIVERSITY OF STRATHCLYDE
11
Based on quality of proton focus, we need to get the PMQs closer to target (currently limited to approx. 100 mm from target).
This is limited by i) our target vertical stage clashing with PMQ stages and ii) the PMQ1 mounting frame clashing with target mount.
Solutions have been identified for each but require significant effort.
Identified an issue with the repeatability of the large linear stage that drives the PMQs IN/OUT.
A potential solution has been found, and two methods for confirming the drive is at the correct position, using reference wire imaging and confocal position sensor will be implemented.
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B

## Slide 12
Key Next Steps
X THE UNIVERSITY OF STRATHCLYDE
12
Beamtime Aims: Improvement of PMQ focus, finally proton focus characterisation and first cell irradiation investigations.
Roadmap to next beamtime (3 weeks in October )
i) Implement the required alterations to PMQ/target mounts to reduce distance between each.
ii) Implement required alteration to PMQ large linear stage, add position referencing systems and test repeatability.
iii) Final install and alignment of the cell rotation mount.
Aiming to complete before the start of October
iv) Pre-calculation of the expected proton dose and discussion on irradiation shot plan with those involved.
Notes: This is a CAD model of said experiment.
We plan to install a capture beamline to guide the proton source to a cell irradiation station
This will involve a permanent magnet quadrapole system as seen on left, and a cell irradiation end station which will sit at target normal in the TP line.
Very exciting application experiment for Bunker B