## Slide 1: Radioactive ion beams for real-time PET-guided adaptive particle therapy
Daria Boscolo on behalf of the BARB collaboration. GSI Helmholtzzentrum für Schwerionenforschung
IOP Nuclear Physics Conference
Brighton 13-15 April.

## Slide 2
Bragg peak in therapy
Durante et al., Phys. Rep. 2019
Durante, Br. J. Cancer 2019
Wilkinson B, Int J Mol Sci. 2023

## Slide 3
The growth of particle therapy
Locations of the 135 particle therapy facilities in clinical operation. Last update: September 2025, source PTCOG website
Proton therapy centers
C-ions therapy centers

## Slide 4
Bragg peak and range uncertainty in radiotherapy
ION THERAPY IS A CORNERSTONE FOR TUMOR TREATMENT
defined range and Bragg peak —> spare normal tissues
RANGE UNCERTAINTY
Uncertainties in conversion of CT numbers to stopping power
Quality of the CT
Daily errors: patient setup and alignment, tumor shrinkage, anatomical changes…
Knopf & Lomax, Phys Med Biol 2013
☹️
Margins have to be added to ensure tumor coverage
Advantage of Bragg peak is jeopardized
More damage to normal tissue

## Slide 5
Range Uncertainties in CPT
A.C.Kraan, et al., Phys Med (2024)
Planning CT
2nd control CT
Durante & Flanz, Semin. Oncol. 2019
With margin ~1 cm (in total)
No margin (proton penumbra ~2 mm)
Proton treatment plan
ANATOMICAL CHANGES
  Severe dose deviations
  Range monitoring is necessary
RANGE UNCERTAINTIES
  Small range deviations can result in not optimal tumor coverage
  Safety Margin (at the cost of lower conformality)

## Slide 6
In-beam PET monitoring
No additional dose
Non invasive
No repositioning
Relatively easy to integrate in the beamline
Can work online and offline
Low Signal to noise ratio: Long measurement time / Signal Washout
Contribution from different radioisotopes Multiple field? Signal contamination
Activity map does not exactly match dose map. Additional comparison with simulation is required
PRO
CONS
Image Courtesy of M.Moglioni
Notes: shift between the peaks would require additional MC simulations for data analysis

## Slide 7
Radioactive Ion Beams (RIB) for simultaneous treatment and range verification
Improved count rate (one order of magnitude larger than for stable ions)
Improved correlation between activity and dose
Reduced washout blur thanks to short lived isotopes
Compared to conventional PET imaging in heavy ion therapy, RIBs, e.g. 11C, show:
Image Courtesy of M.Moglioni
Adapted from Sokol et. al. Scientific Reports 2022
Proton Activity
12C Activity
11C Activity

## Slide 8
RIB in radiotherapy
@Lawrence Berkeley Laboratory
@GSI
@NIRS -HIMAC
Hampered by the low intensities achievable. RIB therapy is now revived thanks to the construction of therapy compatible high-intensity accelerators, e.g. FAIR Phase 0 at GSI (Darmstadt, Germany)

## Slide 9
First mice irradiation with RIB
https://www.gsi.de/work/forschung/biophysik/erc_barb
Notes: Probably to be updated

## Slide 10
Stable Beam Pattern
RIB production pattern
RIBs at GSI-FAIR
11C RIB to FRS final focal plane or to Cave M
12C stable beam from the SIS18
RIB produced at fragment separator FRS In flight separation: Using a beryllium target Bρ-ΔE-Bρ separation.
FAIR Phase 0: upgrade of the SIS-18 accelerator at GSI
Isotope | 11C | 10C | 15O | 14O
Half-life, min | 20.4 | 19.3 s | 2.04 min | 1.17 min

## Slide 11
RIBs candidates
 | 11C | 10C | 15O | 14O
Half-life: | 20.4 min | 19.3 s | 2.04 min ✅ | 1.17 min
Intensity in the SIS18: | ~1010 pps | ~1010 pps | ~1010 pps | ~1010 pps
Intensity @FRS final focal plate | ~107 pps | ~106 pps | ~107 pps | ~106 pps
Purity | > 99% | > 94% | >99% | >95%
Transported to Cave M | ✅ |  | ✅ | 
Additional Prompt–Ɣ |  | ✅ |  | ✅
Stable ion in use for therapy. | ✅ | ✅ |  | 
Boscolo, Lovatti, Sokol et al. Nat. Phys. 2025
11C for preclinical studies
209 MeV/u
Beam
Beam
Beamspot
2D dose distribution

## Slide 12
First mice irradiation with RIB
https://www.gsi.de/work/forschung/biophysik/erc_barb
Notes: Probably to be updated

## Slide 13
SIRMIO PET detector
Pixel size 0.9 mm x 0.9 mm x 6.3 mm
Na-22
1 mm
0.4 mm
PET detector
In collaboration with NIRS-QST (T. Yamaya and H.G.Kang).
56 three-layer depth-of-interaction detectors.
Each DOI PET:LYSO scintillator block with a pixel size of 0.9 mm readout by an 8 × 8 silicon photomultiplier (SiPM) array
G. Lovatti et al., Phys. Med. Biol. 2023
G. Lovatti et al., Phys. Med. Biol. 2025
Beam
Data acquisition and reconstruction software: Tailored to stream out and reconstruct the list mode data with user-defined time intervals, set in this experiment to cycles of 60 s
Notes: A spherical high-resolution PET scanner developed at LMU within the SIRMIO project was used for in-beam imaging.
The scanner consists of 56 depth-of-interaction detectors arranged in a sphere with 72 mm inner diameter, achieving sub-millimetre resolution.
The acquisition and reconstruction software were optimized for online imaging, producing reconstructed images every 60 seconds during irradiation.
This enabled real-time visualization of the beam stopping position and PET signal build-up during treatment.

## Slide 14
First mice irradiation with RIB
https://www.gsi.de/work/forschung/biophysik/erc_barb
Notes: Probably to be updated

## Slide 15
Animal model
Animal model | 11–12-week-old female C3H mice
Tumor Model: | LM8 cells injected in the nek area
OAR: | Spinal cord
Irradiation | 2 weeks after tumor cell injection
Doses: | 20 Gy
Boscolo, Lovatti, Sokol et al. Nat. Phys. 2025
Notes: the animal model were female C#H mice and we used a osteosarcoma tumor model implanted in the neck area. this area was chosen because there is a little space, the tumor can be placed just before a organ at rick (in this case the spine) and it is still superficial enough to be seen and somehow positioned in the irradiation field.
since the kin is still relatively soft and the tumor had all slightly different position and size we used as a CTV the pink area which was defined by the sum off all the possible location where we observed tumors in all the preparatory studies.

## Slide 16
Boscolo, Lovatti, Sokol et al. Nat. Phys. 2025
Experimental Setup
Notes: The mice where then anestetized and placed inside this dedicated mice holder which can be inserted directly in a sSAARP for CT imaging right before the treatment and then on the PET. The mice was irradiated vertically and the beam was shaped to be as conformal as possible in the ctv with a fullpassive beamline cosisting in a series of collimators and energy degraders,

## Slide 17
Boscolo, Lovatti, Sokol et al. Nat. Phys. 2025
Proof of concept: Image-guided treatment with RIB
Goal: Demonstrate that measured activity map correlate with toxicity in the OAR
Approach: 20 Gy SOBP irradiation to the CTV while trying to spare the spinal cord
Toxicity evaluation
No severe morbidity (confirmed by PET measurements)
Significant correlation between activity in the spine and decreased mouse forelimb strength
Irradiation and PET imaging
Notes: With this set up we then performed a first proof of concept experiment with the aim to demonstrate that the PET images reconstructed where able to predict the outcome of the treatment in terms of toxicity
the strategy was to irradiate the CTV as good as we could, acquire PET images during the irradiation and then correlate the activity measured in the OARs with the actual outcome of the mice long term toxicity.
As to be expected we did not see acute toxicity because we never aimed at giving a high dose to the spine, but we saw a significative correlation between the signal measured in the spine volume with a loss of strength in the mice upper limb.

## Slide 18
Real-time adaptive RIB treatment
Approach: 5 Gy probe pencil beams used to verify the ranges and then deliver 20 Gy SOBP
Goal: To show that dynamic repositioning of a ß+ -emitting 11C-beam along the mouse body results in spatially resolved imaging signals that correlate with distinct treatment outcomes.
M. Moglioni et al., in revision Comms. Med
Short
Right
Long
Notes: This was a very nice result already but here the next question come up naturally: Can we then go for real adaptive?
Is there a way that I can demontrate that I would actually be able to see the range and correct directly during the treatment?
then we come up with a possible whay to dempontrate it: we thought of doing a possible scenario where we give a first imaging probe beam to look at the range and then correct or proceed to the full treatment with a SOBP and full dose.
And we test it by shooting at three different ranges one a bit too short one too long and one of course right.
In our case however it would not have made sense to actually correct after the probe beam because we needed to dempnstrate that the probe beam position was actually trustable and we did the full irradiation at the correspective position. with the expected outcome that is the probe beams were where we wanted in the S range we would not see toxicity but also no tumo control, in the righ all ok and in the long tumor control but toxicity
here a video of the three irradiations

## Slide 19
S
R
L
Control
L
L
L
R
R
R
Histology
Weight loss
Grip test

## Slide 20
Conclusion
Using radioactive ions for particle therapy could lead to real-time imaging of radiation doses to improve the precision of treatment.
RIB can be produced at GSI with sufficient intensities for systematic preclinical studies
5-11 fold improvements in the PET SNR compared to 12C but also higher than proton
Allow to reduce acquisition time/ reduce the washout
Range discrepancies can be detected few seconds after the treatment starts
Allow to reduce the margins and can detect eventual morphological changes
RIB can be used as radio-tracers for washout and radiobiological studies

## Slide 21
GSI Biophysics Department
Marco Durante
Olga Sokol
Martina Moglioni
Andreas Bückner
Christian Graeff
Tamara Vitacchio
Walter Tinganelli
Christoph Schuy
LMU Group
Katia Parodi
Giulio Lovatti
Francesco Evangelista
Munetaka Nitta
Jonathan Bortfeldt
Peter Thirolf
Thank you for the attention!
GSI FRS/SFRS Departments
Christoph Scheidenberger
Emma Haettner
Sivaji Purushothaman
Daria Kostyleva

## Slide 22
Can we do more?
Can we use RIBs as “radiotracers” for monitoring of vascular damage caused by high doses of radiation?
Crated with Midjourney

## Slide 23
Activity Washout
  Hypotesis: High doses induce vascular damage. Possibly mediated by an ischaemic–reperfusion mechanism. (Bodo, S. et al J. Clin. Invest., 2019).
Approach: Activity in tumor region continuously measured for 30 min after the irradiation with high 20 Gy and low 5 Gy doses.
Boscolo, Lovatti, Sokol et al. Nat. Phys. 2025
Ws . e( -ks . t ) + (1 – Ws) . e( -kf . t )
‘slow’ decay component
‘fast’ decay component
A(t) = Aphys × Abio(t)

## Slide 24
Activity Washout
  Hypotesis: High doses induce vascular damage. Possibly mediated by an ischaemic–reperfusion mechanism. (Bodo, S. et al J. Clin. Invest., 2019).
Approach: Activity in tumor region continuously measured for 30 min after the irradiation with high 20 Gy and low 5 Gy doses.
Boscolo, Lovatti, Sokol et al. Nat. Phys. 2025
Ws . e( -ks . t ) + (1 – Ws) . e( -kf . t )
‘slow’ decay component
‘fast’ decay component
A(t) = Aphys × Abio(t)
Fast Component
Slow Component
Slow Component
Data fit assuming 96% 11C, 3% 10C and 0.5% 15O
Result: @ 20 Gy the fast component essentially disappears. Suggests a quick vascular injury that delays the washout process in the first 30 min after the irradiation.

## Slide 25
Real time range verification for the three groups
Consecutive irradiation of the three probe beams in an ex vivo model and real time visualization.
PET signal acquisition during irradiation. Overlay of SARRP scan and PET signal
Courtesy of G. Lovatti and M.Moglioni
S
R
L

## Slide 26
Not every beam works for therapy !!!
We need to ensure that
Beam contamination is negligible
Energy has to be well defined
Beam has to be symmetric and small
Beam contamination
Boscolo et al. NIM A, 2022
Spot size and energy spread
10C monochromatic mode
10C
10C achromatic mode
±Suitable
Not suitable