## Slide 1
Benchmarking the High-Spin Capabilities of the 1π AGATA Spectrometer at LNL
The Dawn of The High-Spin Renaissance
Dr. Conor Sullivan – 14th April 2026

## Slide 2: Introduction – Gammasphere
https://www.phy.anl.gov/gammasphere/pub/logos_98.html
Gammasphere represents the best of the previous generation in -ray spectroscopy
It is a large, BGO-suppressed HPGe array (up to 110 detectors)
Residencies in Berkeley and Argonne National Labs, USA.
https://www.phy.anl.gov/gammasphere/doc/efficiency/
Notes: So I’m going to start off with a brief introduction not on AGATA, but instead on Gammasphere, which represents the best of the previous generation of spectrometers for high-spin gamma-ray spectroscopy. The array has had residencies at both Argonne and Berkley National Labs in the US, and consists of up to 110 Compton suppressed, highly pure germanium detectors. We can see in the figure in the bottom left that it boasts a high detection efficiency peaking at just over 20%. On the right-hand side we see the Gammasphere itself at Argonne sometime in the late 90’s with Robert Janssens in the middle inspecting one of the cryostats and BGO suppression shields. The use of BGO suppression was crucial to the Gammasphere’s success, enabling the collection of huge data sets with an unparalleled peak-to-background ratio.

## Slide 3: Introduction – AGATA
https://www.agata.org/
AGATA (Advanced GAmma Tracking Array) is the flagship European -ray spectroscopy project
Removal of BGO shielding allows for a solid sphere of germanium surrounding target position efficiency!
Removal of BGO shielding means you can no longer reject Compton scattered events background!
Compensate using PSA (Pulse Shape Analysis) and -ray tracking
In addition to energy, PSA yields position information
  Essential for tracking
  Better Doppler correction (smaller broadening)
  Compton scattered -rays are folded back into the data! further improved data
Digital electronics promise higher counting rates than analogue systems
Notes: With this in mind, we now take a look at the AGATA spectrometer, which is the flagship European gamma-ray spectrometer and exists in its 1\pi form, or roughly a quarter of its full size, in laboratori nationali di legnaro, Italy, since 2021. AGATA is a new kind of gamma-ray spectrometer known as a gamma-ray tracking array. The advantage of a tracking array compared to a classic single-crystal device such as Gammasphere is that we have done away with the BGO shielding, which allows for a solid sphere of germanium to surround the target position, maximising solid angle coverage and therefore efficiency. The disadvantage of a tracking array compared to a classic device like Gammasphere is that we’ve done away with the BGO shielding, meaning Compton scattered events are no longer rejected, and – without proper treatment – will introduce a large background which defeats the point of the array. The way tracking arrays circumvent this problem is by using advanced pulse shape analysis algorithms to yield the interaction positions of gamma rays within the array, as well as the energies of these events. This information is then fed into tracking algorithms ,which reconstruct the gamma-ray event. In principle, this means Compton scattered events are folded back into the data further improving data quality, but in reality, the tracking efficiency is not perfect, and – especially with high multiplicity events and an incomplete array - can introduce more background than an equivalent Compton suppressed array.

## Slide 4: Experimental Methodology – Why 158Er?
In response to problems encountered during previous high-spin experiments, a new test was needed
158Er is ideal!
  Long, intense rotational bands
  Relatively easy to produce with many beam + target combinations available
  Produced with large production cross-section
  Studied many times before using EUROGAM, GAMMASPHERE, GRETINA and AGATA (at GANIL) spectrometers
Day 1: AGATA Standalone – 32S beam @ 156 MeV, 130Te target.
  Various beam currents to allow for characterisation of spectra as a function of event rate.
Days 2 & 3: AGATA + SAURON – 32S beam @ 156 MeV, 130Te target.
  Hardware trigger set requiring charged-particle coincidence with SAURON. Dramatic reduction in TP rates (~400 Hz @ 4.5 pnA)
A. Korichi, et al. Presentation at AGATA Week 2017, Sept. 2017. Milano, Italy.
Notes: Now, in response to problems encountered in previous high-gamma-multiplicity, high spin experiments performed at AGATA, it was clear there was need for a proper test experiment designed to benchmark the system under these extreme experimental conditions. There are many nuclei that fulfil the requirements for such an experiment. We want something with long and strongly populated rotational cascades. In this proposal we focused on 158Er. This nucleus is a darling of the high-spin community, seen as a textbook example of a rotational nucleus, characterised by long and intense rotational bands, observable up to ultra-high spin. We can make thorough comparisons between datasets obtained in the past using the GRETINA, Gammasphere and AGATA arrays. We see an example of the spectra here obtained using these multiple generations of spectrometers. Making these comparisons is crucial to understanding how to further develop the spectrometer. We can do this by measuring essential experimental quantities such as the peak-to-background ratio, and peak resolution as a function of energy. We also must optimize tracking parameters which is a unique part of the analysis compared to the older generation of arrays, and study how these change as a function of the event rate, and therefore as a function of the beam intensity.

## Slide 5: 158Er Yrast Band To High Spin with AGATA
Spectrum produced using sum of double gates on triple- coincidence matrix (cube)
158Er yrast band observed up to spin 46+, the band terminating state!!
Notes: Now enough with the introductory material, and let’s look at some results! This beautiful gamma ray spectrum is obtained from a gamma-triples coincidence matrix, or cube, which already represents a strenuous test on AGATA, requiring a minimum of three coincident and tracked gamma rays to increment this spectrum. It’s produced using a sum of doubles gates on the transitions in the yrast band of 158Er and we can see in the inset we have managed to extend our observations into some of the weakest transitions in 158Er, measuring all the way up to the band terminating states at 46 hbar. Ultimately for me this spectrum is the showpiece of my talk, and shows that high-spin experiments with AGATA are possible. However This spectrum just represents one band, and we should look at broader performance characteristics to make this conclusion with greater certainty.

## Slide 6: How do we compare to Gammasphere?
158Er
GS2K059, 102 HPGe
Simpson, et al. https://doi.org/10.1103/PhysRevC.107.054305
Notes: Now, this sprawling level scheme represents everything known about 158Er measured in thin-target experiments, and is obtained from a paper by John Simpson, Mark Riley and Eddie Paul. The paper is linked here and it’s a fantastic read if you haven’t read it already, really showcasing the best of what Gammasphere can achieve and highlighting the broad diversity of nuclear phenomena at high spin. In this experiment the Gammasphere was absolutely flying, near peak capacity with 102 HPGe and the finest analogue electronics, which Eddie would be very upset if I didn’t point out.

## Slide 7: How do we compare to Gammasphere?
158Er
GS2K059, 102 HPGe
Simpson, et al. https://doi.org/10.1103/PhysRevC.107.054305
AGATA, 10 ATC (0.666 !!)
Notes: And here I’ve overlaid how much of this scheme we observed in our AGATA data, which as you can see is most of it. We struggled to see some of the non-yrast states and weak linking transitions, but when we consider that this data was obtained with less than a quarter of AGATA 0.666\pi, running at a relatively low beam intensity and with just under 2 days of beam time, this is a great success!

## Slide 8: Neutron-Damage Correction
Essential part of AGATA analysis: neutron-damage correction
Neutron damage in the form of Ge lattice defects causes low-energy tailing in -ray peaks.
Position resolution from PSA unaffected by damage:
  Produce map of correction coefficients as function of position! (see e.g Bruyneel, et al. https://link.springer.com/article/10.1140/epja/i2013-13061-4 )
Comparison with Gammasphere (green line)!
AGATA energy resolution superior at high energy
  We expect this since AGATA position sensitivity results in lower Doppler broadening effects
BUT, not necessarily “apples and apples comparison”:
  Beam and target not the same between experiments. GS had faster recoil therefore larger Doppler broadening and expect worse resolution.
Notes: Now, one optimisation is the neutron-damage correction which is unique to the AGATA analysis workflow. Neutron damage causes a substantial degradation in photopeak resolution, but thanks to the position sensitivity enabled by the pulse shape analysis, we can correct for this and restore the resolution of the array. I show the before and after full-width-half maximum measurements where we can see substantial improvements, especially at high gamma ray energies. We can also compare the resolution to the 158Er Gammasphere experiment, and we can see the resolution performance is comparable between Gammasphere and AGATA, with AGATA boasting finer resolution at high energies. This might be expected, since the position sensitivity offered by AGATA results in a substantial decrease in Doppler broadening effects, but we also must consider that the reactions used in each of these experiments were not identical, with the Gammasphere experiment having a faster recoil energy and therefore greater Doppler broadening effects.

## Slide 9: High-Fold Sorting
-ray multiplicity == amount of -rays emitted in a single cascade
-ray fold == amount of -rays detected in a single event
Define a “gatelist” for band of interest. For 158Er: [192, 335, 443, 523, 579, 608, 510, 473, 566, 659, 740, 806, 846, 858, 876, 906, 959, 1019, 1059]-keV
“Spikeless” high-fold sorting method C.W Beausang, et al. https://doi.org/10.1016/0168-9002(95)00438-6
  At least M -rays from gatelist must be present in the event to increment the Fold M histogram.
Notes: So we’ve established that the spectrometer is capable of resolving weak transitions at high-spin, but how is the performance for high gamma multiplicity? For this discussion we must distinguish between the concepts of multiplicity which is the number of gamma rays emitted in a single cascade, vs fold which is the number of gamma rays detected in a single event. On this slide we have a utilised the spikeless sorting algorithm of Con Beausang and collaborators, where to increment a histogram labelled Fold N, we require an event to have at least N tracked and coincident gamma rays from a list representing our band of interest which here we’ve selected to be the 158Er yrast band. We see that as we require more and more gamma rays, the number of counting statistics decreases, but the selectivity increases massively.

## Slide 10: High-Fold Sorting
We see clear peaks up to Fold 6!
To increment this spectrum requires at least 6 coincident, tracked rays satisfying our gatelist.
Notes: To exemplify this we zoom in on the fold 6 histogram where we are indeed struggling for counting statistics, but the peaks that are present show the yrast band of 158Er cleanly up to high spin, which is a fantastic technical achievement for the array when we consider we require at least 6 tracked and coincident gamma rays from our gate list to increment this histogram, and this is without any background subtraction at all!

## Slide 11: High-Fold Sorting
Peak-to-background ratio increases exponentially with fold.
See also e.g Brinkmann, et al. https://doi.org/10.1063/1.41218
Moreover, high-fold events can be unfolded into combinations of lower fold events for a dramatic increase in spectra quality and counting statistics
  e.g. A fold-7 event unfolds into 35 fold-3 events. A fold-9 event into 84!!
Comparable performance between AGATA and Gammasphere but again must be careful when comparing and especially extrapolating such simple models… Let’s look at a more general case!
Notes: Now, we’re not just showing off by trying to get these high-fold events, and we can argue that they’re actually essential for studying the weakest decays at high spin. The first use of the high-fold events as we can see from this plot is that the peak-to-background ratio increases roughly exponentially as we increase the fold requirement. We see this with our AGATA data as well as 158Er dataset with gammasphere, and another Gammasphere dataset studying 132Ce. This then feeds into the second use of the high-fold event comes from combinatorics, where we can unfold the very clean high fold events into exponentially more combinations of low fold events, dramatically increasing the number of counting statistics and the peak-to-background of these low-fold events. And it’s really this ability to register these very high fold events that is what made gammasphere such a powerhouse for these high-spin studies.

## Slide 12: High-Fold Sorting
The graph displays the AGATA -ray fold at various stages of the data processing chain
nbHits represents the number of segments fired in a single event
nbCores represents the number of cores fired in a single event
nbTrack is the number of tracked rays in a single event
A gate is placed on energy (0 – 5 MeV) and timing (0 – 100 ns) for further processing
What can this tell us about the future performance of the array?
Notes: So with this in mind, we can look more in general at the high-multiplicity performance of the AGATA array by plotting these diagrams of gamma-ray fold per event.

## Slide 13: High-Fold Sorting
The tracked fold distribution is well-described by a convoluted Gaussian-binomial model: where M is the “true” number of rays emitted, is the average event multiplicity, is the average spread of that multiplicity, n is the number of detected rays (i.e fold), is the average efficiency of the array and A, are scaling and normalisation factors
The fit yields for
Now let’s extrapolate this model for a future, larger AGATA array…
Notes: If we concentrate on the tracked fold we find it is well described by a convoluted Gaussian-binomial model, which is parameterised by numbers representing real physical values such as the average event multiplicity, and the detector efficiency.

## Slide 14: High-Fold Sorting
AGATA will have 30 ATCs. So to get a rough estimate of the efficiency we simply scale by 3!!
  %
Real AGATA should have even higher efficiency than this since proportionally fewer rays escape out of the sides…
Extrapolated model is promising, but is it realistic?
Notes: Now, AGATA is in the process of being upgraded to a larger, 2pi configuration, and we can extrapolate our simple model to predict what the performance of the detector might be, simply by increasing the average efficiency of the detector to what we might expect it to be in the 2pi configuration. We will have three times as many detectors as in our experiment, so I have simply multiplied the efficiency by three. The predicted gamma ray fold looks very promising, but is it realistic?

## Slide 15: High-Fold Sorting
Compare once again to the fantastic GS 158Er data…
Normalise their observed fold distribution to our total number of events
  Caveats: they set a minimum fold threshold of 7 (show offs!); events with fold < 7 are from invalid events in some detectors for that event (pile up, energy, timing etc)
  Hard cut off at fold 20, so the line is extrapolated beyond this
The extrapolated AGATA distribution is consistent with the Gammasphere one!
Notes: To check, we once again turn to the fantastic 158Er gammasphere data. Here we see the fold distribution obtained from that experiment, which has been normalised to match our total number of counts. We can see that it is consistent with our predicted distribution for 2pi agata with a couple of caveats, the main one being that they were showing off and set a minimum fold requirement of 7, rendering the bars below fold 7 incompatible with our model. But when we consider that half of the full AGATA array might have comparable performance to the previous state of the art, I’m filled with hope for the future of high spin physics.

## Slide 16: Conclusion and Future Outlook
Outlook for this experiment
  Influence of SAURON. Similar effect to setting TP threshold?
  Tracking:
    Machine Learning Tracking
    How does high multiplicity affect the tracking efficiency? Simulations needed.
  Neutron damage correction
    Effect of “ForceSegmentsToCore” for high rates?
    Joa’s basis vs Regular Basis
  Comparison with GRETA/GRETINA, EUROBALL/GAM
Outlook for the future
  High-spin spectroscopy with tracking arrays not only possible, but potentially better than ever!!
+ D. Stramaccioni and S. Carollo the best liaisons you could ask for, M. Loriggiola for his excellent target production & TANDEM Beam Operators!
Thanks for listening! Any questions?

## Slide 17: Impact of Rates
Trigger Processor can handle a maximum of ~4-5 kHz incoming trigger requests per crystal.
For trigger request rates beyond this, the trigger processor starts to reject (throw away) valid events
  Disaster for a tracking array – how do you track a ray with missing hits in the track?
How does this affect the spectra?
Notes: So we’ve seen a lot of successes in this experiment, and I thought I’d finish by touching on some of the limitations. We saw that one of the biggest issues with the hardware was the Trigger Processor’s inability to accept very high frequencies of trigger requests. This is exemplified here in this chart where we see the difference between accepted and requested trigger requests and beyond 1.0 pnA in our case, the trigger processor starts to throw away otherwise valid events. Now this is a disaster for a tracking array, since we cannot adequately track gamma rays with missing hits!

## Slide 18: Impact of Rates
-ray spectra measured using AGATA standalone at various beam currents
The spectra have been normalised so the background between 100-180 keV and 200-280 keV is equal
Clear decrease in peak-to-background ratio with increasing beam current!!
Notes: Indeed, this is reflected in the gamma ray spectra, where we can see the peak to background decreasing steadily with increasing beam current. The tracking algorithm simply cannot track a gamma ray with missing hit information. So, is this it? Is the limit for standalone AGATA experiments stuck at a relatively small 1 pnA?

## Slide 19: Impact of Rates
Peak-to-background under high beam intensity can be recovered by setting a minimum “fold” threshold at the trigger processor
Still not quite as good as for low rates. A problem for further investigation.
Notes: Of course I could not finish on such a negative. We see here from this plot of peak to background vs beam current that, if we set a threshold requiring a minimum amount of hits in the AGATA segments, per event, we can bring the rates back into acceptable territory and recover the peak to background to almost as good as it was at the very low beam current.