## Slide 1: Position Resolution of Adaptive Grid Search Method for Multi-site Interactions in 'SIGMA’ Detector.
Presenter: Nawaf Altasan

## Slide 2: What is SIGMA?
SIGMA is a p-type Segmented inverted coaxial high-purity germanium detector.
Consists of 18 segments and point contact (PC).
  8 azimuthal segments
  8 longitudinal segments
  2 radial segments.
Long drift, excellent position resolution

## Slide 3: What is the Purpose of SIGMA?
SIGMA is a position sensitive detector that can be applied in:
Nuclear decommissioning
[1]
[1] Parajuli, R.K., Sakai, M., Parajuli, R. and Tashiro, M., 2022. Development and applications of Compton camera—A review. Sensors, 22(19), p.7374.
[2] Griffiths, O., 2025. Proof of Concept Gamma-Ray Imaging using the Segmented Inverted Coaxial Germanium (SIGMA) Detector for Industrial Applications (Doctoral dissertation, University of Liverpool).
[2]

## Slide 4: What is the Purpose of SIGMA?
Jyvaskyla decay correlation measurements
Veto-out event
Veto-in event
Large Distance

## Slide 5: Localising the Position of Interaction
Signals from each segment combined into a Superpulse
Pulse Shape Analysis (PSA), localises (x,y,z) position of Ɣ-ray interaction
Segment

## Slide 6: Pulse Shape Analysis (PSA)
PSA relies on a validated AGATA Detector Library (ADL) database.
This database is created on 1 mm grid covering the entire detector volume with 204,000 points.
Finding best match is based on Figure of Merit (FoM) calculation.

## Slide 7: Multi and Single fold Interactions
Fold refers to the number of segments that collected charge in one interaction
In single-fold, only one segment collected charge.
In multi-fold, multiple segments collected charge.
In the multi-fold case, the signals are convolved linearly as:
Multi-fold
Single-fold

## Slide 8: Adaptive Grid Search (AGS)
In PSA, single-fold case is computationally trivial, whereas the multi-fold case is computationally expensive.
AGS method reduces the computational cost by dividing the search areas into coarse and fine areas.
First, a coarse search is done on small number of grid points
Then, a fine search on 1 mm grid around the best coarse area.

## Slide 9: Position Resolution
Position Resolution (PR) is defined as the mean Euclidean deviation distance between the true and PSA found positions.
Knowing the true position is only possible through GEANT4 (G4) simulation.
By validating the G4 simulated output and experimental data, an estimation of PR can be calculated.

## Slide 10: Generating Simulated Traces
Raw G4 positions
ADL database
Raw G4 energy
Normalisation by total energy
Adding noise

## Slide 11: Compton Imaging
Compton Imaging (CI) is used to reconstruct gamma-ray sources using Compton kinematics.
It requires at least two interactions
In SIGMA it is scatter and absorption.
CI is one method to estimate PR of multi-fold PSA.
[1] Parajuli, R.K., Sakai, M., Parajuli, R. and Tashiro, M., 2022. Development and applications of Compton camera—A review. Sensors, 22(19), p.7374.
Figure from [1]
10 Cones
10,000 Cones

## Slide 12: Validation Setup
In the validation setup, two sources are used for Compton imaging with two different positions.
Measurement 1:
  137Cs at 10 cm standoff and +7 cm in y-direction.
Measurement 2:
  60Co at 10 cm standoff and -7 cm in y-direction.

## Slide 13
137Cs Exp
60Co Sim
60Co Exp
Simulation
Experimental
Measurement 1
137Cs at 10 cm standoff and +7 cm in y-direction.
Hotspot corresponds to most probable source location.
Measurement 2
60Co at 10 cm standoff and -7 cm in y-direction.
Validation Results

## Slide 14: Maximum Overlaps Slices
60Co
137Cs
Intensity slice through y taken at maximum x intensity
Good agreement is observed between G4 generated signals and experimental data.
AGS PSA has been validated against experimental setup.
The offset between reconstructed and true positions arises from multiple sources of uncertainty.

## Slide 15: Position Resolution Estimation
Based on the validated datasets, a minimum position resolution achievable with PSA can be estimated.
Due to the large volume of segment 18, the position resolution is degraded when it is included.
 | Position Resolution (mm) |  | Efficiency drop by removing S18 (%)
Dataset | No Segment 18 | With Segment 18 | 
137Cs | 5.57 ± 0.02 | 6.24 ± 0.02 | 50.42
60Co | 6.42 ± 0.02 | 7.25 ± 0.02 | 52.45

## Slide 16: Position Resolution Distribution
Most of the found positions lie closer to true position.
The distances then falls nearly exponentially.

## Slide 17: Future Plans
SIGMA has been integrated in an experiment in Jyväskylä focal plane.
Applying PSA would help identify gamma rays from nuclei of interest from uncorrelated background events.
By vetoing out background radiation a better P/T ratio could be achieved.

## Slide 18: Thank you for listening Any Questions?
Thanks to SIGMA group:
Prof. Laura Harkness
Dr. Ellis Rintoul
Dr. Daniel Judson
Dr. Owain Griffith
Dr. Sneha Das
Dr. Fraser Holloway
Emily Richardson