## Slide 1
Particle identification with Bragg spectroscopy at ISS
Michał Włodarczyk and the ISS collaboration

## Slide 2
1. Motivation
Solenoidal spectroscopy
Measure the differential cross sections of protons in transfer reactions in solenoidal magnetic field
Spin-parity assignments of excited states of exotic nuclei
Proton's trajectory
Deuterated
target
Silicon detector array
Magnetic field
Heavy
ion beam
Recoiling nucleus

## Slide 3
1. Motivation
Beam production with the ISOL method
High intensity radioactive beams
Small energy and momentum spread
May introduce contamination for short-lived species (~200 ms)
  Beam decays in-flight
Primary
beam
Thick target
Diffusion
Ionisation
Beam
dump
Lasers
Ion beam
Mass
separation
Charge
breeding
Acceleration
Radioactive
beam

## Slide 4
1. Motivation
Need to identify beam components on an event-by-event basis.
For low mass beams (A < 30), silicon-based detectors are used
For heavier beams, their performance deteriorates, so a different approach is required
Proton's trajectory
Deuterated
target
ΔE-E
telescope
Silicon detector array
Magnetic field
Heavy
ion beam
Recoil nucleus’
trajectory

## Slide 5
5
1. Motivation
Need to identify beam components on an event-by-event basis.
For beams with higher mass (A > 30), a different approach was needed
A gas-filled detector was chosen due to its resolving power, radiation tolerance, and low cost
Proton's trajectory
Recoil nucleus’
trajectory
Deuterated
target
Ionisation chamber
Heavy
Ion beam
Magnetic field
Silicon detector array

## Slide 6
6
2. Background
Gaseous detectors
Chamber filled with a gas
Ionising radiation creates electron-ion pairs
Notes: How proportional counters work

## Slide 7
7
Gaseous detectors
Chamber filled with gas
Ionising radiation creates electron-ion pairs
Potential difference accelerates charge carriers
Voltage drop across a resistor in an RC circuit measured
Signal proportional to the energy deposited in the gas
V
C
R
VR
VR
Time
2. Background
Notes: High voltage -> avalanches

## Slide 8
8
The Bragg curve
Characterises the energy loss rate of ionising radiation
Shape, described by the Bethe-Bloch formula, dependent on the properties of the beam (loss rate Z2)
Comparison with simulations to find the composition of the beam
Energy loss
Depth
2. Background

## Slide 9
9
3. Design
Two independent chambers
Flange attached on the downstream side of the MRI magnet
Two 0.9 μm thick mylar windows supported from the upstream side
`
60 cm
Notes: sneezing

## Slide 10
10
3. Design
Segmented Bragg chamber
13 segments to trace the Bragg curve
Segmentation improves the rate capability
Tilted grid geometry found unsuitable
Filled with CF4 at a tuneable pressure (~100 mbar)
Notes: Graph showing energy losses

## Slide 11
11
3. Design
Multi-Wire Proportional Counter (MWPC)
Chamber filled with C3F8 at 5 mbar
Anodes made of thin, evenly-spaced wires connected by delay lines
Beam tuning and pile-up rejection
High voltage applied (~ 700V)
1mm
14 cm
Notes: How the ionisation works

## Slide 12
12
4. Results
Detector used in two experiments at ISS
The energy resolution of the Bragg chamber around 5%
The detection limit to be determined (around )
Maximum detection rate of about 150kHz
129Xe
94Rb
94Kr
Energy loss (MeV)
Segment
0
2
4
6
9
8
7
5
3
1
20
40
60
80
100
120
Unreacted 94Kr beam
10
20
30
40
50
60
70
80
Counts
20
40
60
80
100
Energy loss (MeV)
100
200
300
400
500
94Rb
94Kr
Counts per 100 keV
Projection from segment 9

## Slide 13
13
4. Results
Detector used in two experiments at ISS
The spatial resolution of the MWPC of 1mm
The maximum counting rate of about 300 kHz
-6
-4
-2
0
2
4
6
8
10
12
X position (mm)
-10
-8
-6
-4
-2
-0
5
10
15
20
25
30
35
Y position (mm)
Hitmap measured by MWPC
Counts
0
-2
-4
-6
-8
-10
100
200
300
400
500
600
700
Counts per 50 um
Y position (mm)
Projection on the Y axis

## Slide 14
14
5. Summary
The detector achieved satisfactory performance
Energy and positional resolution in agreement with expectations
Maximum event rate of about 150 kHz
  Sufficient to allow for event-be-event analysis
    Wasn’t possible during the beamtime
The detection limit to be determined

## Slide 15
15
Thank you to the collaborators
S. Bennett1, D. K. Sharp1, S. J. Freeman1, F. Browne1, P. T. MacGregor2, A. Dolan2,
L. P. Gaffney3, A. Heinz4, O. Orlandi5, M. Rocchini6, F. Rowntree3, P. Spagnoletti3
1University of Manchester, UK,
2CERN, Switzerland,
3The University of Liverpool, UK,
4Chalmers University of Technology, Sweden,
5The University of Florence, Italy,
6INFN - Division of Florence, Italy.
This project has received funding from the European Union’s Horizon Europe Research and Innovation programme under Grant Agreement No 101057511.