## Slide 1
10 Years and 100PB of Ceph
Rob Appleyard
UK Academic Ceph Workshop
Manchester University, 3rd December 2025

## Slide 2
Early 2010s:
We have CASTOR! CASTOR everywhere!
  Needed to migrate away
2015-6: Let’s replace it with Ceph
…which produced Echo
Then, what else can we use Ceph for?
  Various services for local facilities
Now:
  Mature Ceph services running at scale
  Experienced team
History of Ceph at RAL
Image © STFC John Dawson

## Slide 3
User-facing experimental facilities at RAL – ISIS, Diamond, CLF
  Users turn up for a tightly-constrained period of experimental time and wish to guide their work with live data analysis.
  Analysis tasks are user-defined
Users who want to make large datasets securely available to external institutes.
Organisational private cloud hosts a large, diverse collection of VMs
  Needs high-performance data storage for VM images and working data.
WLCG Tier 1 requires very high capacity, high-throughput and low cost data access to local batch, large amounts of inter-site I/O, and an interface to the tape system.
Experimental Use cases
Notes: Tape system is CERN’s CTA system – we are talking to the EOS buffer layer

## Slide 4
An architecture diagram of how Echo is accessed, from Tom Byrne’s presentation at Cephalocon 2023
Echo for the WLCG
First production Ceph cluster at RAL
100PiB usable (137PiB raw), 320 hosts, 8050 active OSDs, 8+3EC.
Low-level (RADOS object store) access provided by an XrootD Ceph plugin developed in-house
  All files are stored as 64MB stripes
Dedicated cluster of external XrootD gateway hosts, plus an XrootD gateway process on every worker node.
CERN/Other sites
Worker Node
XRootD server
XrdCeph
libradosstriper
GW container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD client
User job
Job container
XRootD disk cache
x31
x400
Gateway
XRootD server
XrdCeph
libradosstriper
XRootD memory cache
Ceph Cluster
Experiment data pool
Experiment data pool
Newest storage node spec (last year):
  24*18TiB HDD
  2*16C/32T Xeon Silver 4514Y@2.0-3.4GHz
  256GB RAM
  25Gb Networking
Typical gateway host spec:
  2*16C/32T Xeon Silver 4214R@3.5GHz
  192GiB RAM
  25Gb Networking
Notes: We’ve engineered for bulk throughput rather than responsiveness. Don’t care if there’s a bit of latency in there.
This year we expect to be buying 22TB HDDs

## Slide 5
Sirius
  “Our private cloud needs block device storage”
  All flash, 3*replication
Deneb
  “Local users want a large shared filesystem”
  8-12TB HDDs, 8+3 EC
Arided
  “People want to self-provision shares on a high-performance filesystem”
  All flash, 3*replication
Non-WLCG Services

## Slide 6
Early Problems: the 2015 disk generation
Early Echo hardware generation had a really bad batch of HDDs
  Constant bad sectors, crashes, etc.
  Major time sink
Implemented “recyclotron”
  Dedicated SN which repeatedly overwrote disks until they either failed or remapped all sectors
  Give the disk firmware chance to fix itself
  Or fail cleanly, in which case get a warranty return
Vendor agreed that warranty replacement disks would be from a different supplier

## Slide 7
2016: Sirius was the original underpinning storage for our private cloud
  RBD Ceph cluster providing block storage for the system volumes
We bought HDD storage nodes.
  Not nearly enough IOPS
  
Whole new procurement needed for NVMe storage
Re-used SNs for the first iteration of Deneb
Early Problems: Sirius storage media
By NASA, ESA, H. Bond (STScI), and M. Barstow (University of Leicester) - http://www.spacetelescope.org/images/heic0516a/, Public Domain, https://commons.wikimedia.org/w/index.php?curid=477445

## Slide 8
Early Mishaps: Echo EC Backfill
2017, Echo (Ceph Luminous)
  In some cases, when a disk failed Ceph would identify the wrong disk.
    Admins saw crashing disks, removed crashing disks
    Removed 5 disks before realising error
  8+3 EC means we can tolerate only 3 losses…
  23k ATLAS files lost
  

## Slide 9
Xrootd Vector Read Overload (I)
Local batch has an XrootD gateway on every worker node
  Massive parallel throughput available with no reference to MD server
Parallel ongoing story – quest to optimise data transfers from storage to worker.
  Immutable files
Trade-off between throughput intensive read patterns (copy-to-scratch) and IOPS intensive read patterns (‘vector read’)

## Slide 10
Xrootd Vector Read Overload (II)
We discovered the limit of the IOPS-for-throughput trade in May 2023
Change to batch farm deployed Friday morning
Cluster up-and-down for a whole overweekend
Monday – reverted XrootD change, reimplemented with some changes
Image by https://www.vectorportal.com, licensed under CC BY 4.0

## Slide 11
Echo Overflowed Ceph (I)
Did you know – if you have a Ceph cluster over 72PB and don’t change the defaults, it will refuse to let you add any more storage?
  CRUSH weights have a hardcoded limit of 65535
Hit this in June ‘23
  The fix: The Great Rescaling
  Echo now thinks in petabytes
  Modify the CRUSH map offline, inject the new one… magic!

## Slide 12
Echo Overflowed Ceph (II)
Did you know – if you try to add a storage node that’s 1000 times the size of all the others, your cluster will get very sad?
  We re-scaled Echo, but not the documentation for hardware addition
  Innocent new admin followed docs and added a ‘300PB’ SN
    
  Result – very sad cluster
    Externally inaccessible
    Very slow admin commands
    Constant mon crashes
    Slow OSD operations
  Fixed when we removed the problem host
Image from BBC

## Slide 13
Inappropriate Deneb Use Cases
2024 – new user came along – “I want to host RAL’s CVMFS Stratum-1 on Deneb’s CephFS”
  CVMFS assumes that it is talking to a fast local filesystem
  Deneb’s HDD CephFS is not a fast local filesystem
  
Result:
  OSDs couldn’t keep up, constant MDS crashes, large scale breakage for everyone
  Exiling problem user fixed problem
By Pablo Carlos Budassi, CC BY-SA 4.0 https://creativecommons.org/licenses/by-sa/4.0, via Wikimedia Commons

## Slide 14
Common Threads
Echo is a very, very large Ceph cluster
Environment/budget force aggressive development practices
  WLCG risk tolerance
Shared infrastructure means uncivilised users can have outsize impact
Admin inexperience led to poor choices of hardware/incident response
“sewing thread” by In Memoriam: Christopher Bulle, CC BY 2.0

## Slide 15
Mitigating Risks
Many risk factors are hard to mitigate
  Money
  Distinctive user requirements
But many can be
  Building institutional experience of the software
  Greater automation
    CephADM
  Compartmentalisation

## Slide 16
The Future
Near term goals (Q4 2025/Q1 2026)
  EL9
  Ceph Squid
  Decommission Sirius
Medium term
  Failure domains for Echo
    Yes I know…
  Broader deployment of CephADM
  S3 Separation
Image used under CC BY-SA 4.0
Title: Moby Dick by Palmovish
Originator: Artist Palmovish
Source

## Slide 17
Thank you
Facebook: Science and Technology Facilities Council
Twitter:@STFC_matters
YouTube: Science and Technology Facilities Council