## Slide 1: Improving beam tracking using a hybrid code strategy LhARA Collaboration meeting
30/04/2026
Marie Mannie-Corbisier (ULB)
Supervisor: William Shields (RHUL)

## Slide 2
LhARAlinearOptics
GPT
BDSIM
Injection: Nozzle with Space Charge effect
TNSA beam production
Stage 1 beamline
Space charge effect missing
Beam tracking workflow: Previous
Focus point
Small size after the nozzle
Space charge effect significant where the beam density is high
GPT
Dispersion missing
+ tricky way to handle magnets

## Slide 3
RF-Track: particle tracking code
Collective effects: space charge, wakefield,…
Beam of different particle species
User friendly (python code)
Dispersion
...
developed at CERN for the design and optimisation of particle accelerators

## Slide 4
FFA injection line design with dispersion
No dispersion at the start
Dispersion at the exit
Losses (BDSIM: , RF-Track: , GPT: )
Space-charge effect (RF-Track: ,GPT: ,BDSIM: )
Dispersion ( BDSIM: ,RF-Track: , GPT: )
Various physical effects to simulate
Dx=0
Dx=
0.4m
Without SC

## Slide 5
LhARAlinearOptics
RFTrack
BDSIM
TNSA beam production
Full Stage 1 beamline with Space Charge effect
Beam tracking workflow: Next
B
B
B
B
Software used:
R
R
R
R
Discretised element
INTERFACE

## Slide 6
Preliminary simulation results: validation
GPT VS RF-Track space charge effect: work in progress.
Comparison without space charge effect

## Slide 7
Conclusion
BDSIM is well suited for particle–matter interactions, but not sufficient alone for accurate collective beam tracking.
GPT presents limitations, especially in dispersive regions and magnetic elements for long beams.
A hybrid strategy combining BDSIM and RF-Track appears to be the most appropriate solution.
Next steps:
Extend tracking in RF-Track by using time integration instead of space.
Validate space-charge simulations in RF-Track against GPT.

## Slide 8
Thank you for your attention!