## Slide 1
RF requirements for HALHF
Background
HALHF is a linear collider, where a plasma linac is used as the main linac for the electron arm, and cold copper-technology structures are proposed for the positron arm.
The remaining subsystems are to a large degree based on technologies already developed or being developed for RF-based linear colliders.
While the current HALHF baseline is sufficiently detailed to progress with research on the plasma linac
The remaining subsystems would need to be further developed in order to reach CDR maturity, ideally in collaboration with existing efforts, as detailed below.

## Slide 2
Identify the critical RF challenges to be addressed
Confirm the RF design specifications
Identify timescales for the required RF-specific R&D
Determine the level of staffing resources needed to complete the proposed R&D
Identify the additional infrastructure required to achieve a TRL 6–level demonstration
Define a roadmap plan for the identified objectives
Feedbacks received for HALHF

## Slide 3
Identify the critical RF challenges to be addressed.
Drive beam: high current (2A) 3.9 GeV L-band linac, recombination by a factor 48 in a delay loop and two combiner rings with 0.5 GHz RF deflectors (Energy factor two larger than CLIC Design).
Deflection systems for drive beam injection in plasma modules: fast kickers (harmonic rf kickers, to deflect each bunch of the 48 drive bunch train 0.167 ns separation), stability, synchronization.
Main electron LINAC: high degree-polarized, 3 GeV, low-emittance.
Positron linac: in case of cool copper technology structures (C3 linear collider proposal), demonstration of the reliability of the 42 GeV linac operation.

## Slide 4
Confirm the RF design specifications (CoM 250 GeV Higgs factory)
Drive beam LINAC: 1 GHz, 4 MV/m av. cavity gradient, 3.9 GeV, 4 ns bunch separation, 8 nC per bunch, 2 A average current in the RF pulse, 1.3 km, ~31 ms RF pulse/bunch train length, 409-21 MW klystrons, 100 Hz.
Deflection systems for drive beam injection in plasma modules: required drive-beam injection relative to the accelerated beam stability/sinchronization at the level of 10 fs
Main electron LINAC: 100 Hz, 3GeV, 160 bunches 1.6nC, 16 ns bunch separation, 2.5 ms bunch train length.
Positron LINAC 42 GeV, 100 Hz, 160 bunches, 4.8 nC, 16 ns bunch separation, 2.5 ms bunch train length:
  cool copper option: 3 GHz, 40 MV/m av. cavity gradient, 321 67MW klystrons, 1.1 km.
  room temperature: 3 GHz, 25 MV/m av. cavity gradient, 2.1 km

## Slide 5
3. Identify timescales for the required RF-specific R&D, FTE and cost.
Drive beam complex: synergy with linear colliders projects, preliminary discussion already have taken place. While there is currently no visible source of funding available, preliminary numbers for reaching a CDR for this subsystem are given in the HALHF documentation; CDR in 5 years, 20 FTE, 7 MCHF.
High-frequency RF deflection systems for drive beam injection in plasma modules, where the bunch spacing will be on the order 167 ps. The first designs are currently being made.
Main electron LINAC: the linac is similar to that of linear colliders projects, and will profit directly from linear collider R&D
Positron LINAC: the baseline is to use cool copper, currently being developed mainly by the C3 collaboration at SLAC. Preliminary discussions with SLAC have taken place. While there is currently no visible source of funding available, preliminary numbers for reaching a CDR for this subsystem are found in the HALHF documentation; CDR in 5 years, 10 FTE, 10 MCHF.

## Slide 6
6. Define a roadmap plan for the identified objectives.
Defining additional infrastructure and defining a roadmap for the RF parts of HALHF will benefit from strong synergy with the linear collider projects and the C3 collaboration, and would need to be developed in concert with them.