## Slide 1: ESDG current ATLAS contributions

## Slide 2: outline
ATLAS TDAQ overview
ATLAS TDAQ Phase-II upgrade
ESDG contributions
  L0Calo
    Management
    F/W
  L0Global
    Management
    H/W
    F/W

## Slide 3: ATLAS TDAQ overview
ATLAS trigger and data acquisition (TDAQ) system
  Data stored in synchronous scrolling memories on detectors temporarily before its trigger decision arrives
  Trigger latency (trigger algorithm + cable propagation delay) < Scrolling memory length
Data acquisition (DAQ)
Trigger
40MHz peak collision rates
~10,000,000 detector channels
Real time data generation ~ PB/s

## Slide 4: LHC Schedule

## Slide 5: ATLAS TDAQ Phase-II Upgrade

## Slide 6: ATLAS L0Calo
ESDG contributions:
  Management
    Ian Brawn is the L0Calo coordinator
  F/W
    Geoffrey Betts is updating the eFEX f/w for Phase-II upgrade
      Main drive
        Trigger latency increased x4
        Trigger rate increased x10

## Slide 7: eFEX f/w Phase-II upgrade details
A lot of firmware changes needed
  Significant increase in readout buffering
    Longer latency → Keep data for longer before filtering
  Process 10x events
  Process more data per event
  General optimisation
Comprehensive rewrite
Timing closure is a big challenge
Notes: Emphasise readout path

## Slide 8: ATLAS Global Trigger

## Slide 9: ATLAS Global Trigger
ESDG contributions
  Management
    I’m co-coordinator for the Global hardware project with BNL (US)
  H/W
    I’m the co-designer for Global Common Module
  F/W
    Mohamed Siyad is involved in the gCTPi f/w design

## Slide 10: GCM hardware Technology Choices
Platform
  ATCA front board
    1 MUX node + 1 GEP node per board
FPGA
  Versal Premium adaptive SoC VP1802 for MUX node
  Versal Premium adaptive SoC VP1802 for GEP/gCTPi node
  VSVA5601 package
    75x75, 0.92mm pitch
    Minimizing crosstalk
Optics
  20 Firefly 28G parallel optical engines
    12 ch/optical engine
PCB
  26 layers
  Via-in-pad
  Backdrill

## Slide 11: GCM hardware work examples

## Slide 12: gCTPi f/w example
GTPY link design
  Fixed latency
  Minimal latency

## Slide 13: Summary
ATLAS is a very big experiment involving huge internation collaborations.
ESDG is making crucial contributions to the ATLAS TDAQ Phase-II Upgrade.