## Slide 1: RF Linear accelerators L1: Introduction: Coupled cavity linacs
Prof Graeme Burt
Lancaster University

## Slide 2: Multi-cell structures
It is simpler to drive multiple cavities (cells) with a single RF source. This requires the separation between cells to be adjusted to achieve the correct phasing of cavities to achieve maximum acceleration.
Once b~1 all cavities are a half wavelength apart,

## Slide 3: Synchronous particle
Imagine we have a series of gaps. The phase change between two gaps when the beam arrives is given by
Where ja is the phase advance, (the phase difference between adjacent coupled cavities)
Hence the distance between cells should be
In a linac we choose a synchronous phase fs and design the lengths so that the synchronous particle sees the desired phase (not always constant)

## Slide 4: Low beta electron synchronism
For electron guns and industrial/medical linacs the electrons are injected at a beta less than one and are accelerated to beta=1 in the first cell.
However at X-band (9-13 GHz) the gaps are small hence the first few cells are non-relativistic, hence

## Slide 5: Cell-to-cell coupling
k
k
I1
I1
I2
I2
Vc= IZ = (I1-I2) Z = 0
Vc= IZ = (I1+I2) Z = 2I1Z
Kirchoff’s voltage law:
If we move two resonators close to each other they become capacitively coupled. The potential drop across this capacitor is dependant on the phase difference between the resonators.
This results in a different resonant frequency.

## Slide 6: T-network
A periodic array of impedances of the form below, is called a T-network
Kirchoffs law gives
and has the solution
Zn
Zn-1
Zn+1
Yn
Yn-1
Yn+1

## Slide 7: Electric coupling
We can couple via an inductance (Y=1/wL2) or a capacitance (Y=wC2) depending on where we place our coupling slots. Lets start with capacitive
If we set
And insert into the T-network equation we obtain
Which gives

## Slide 8: Electric coupling
If we set
We obtain for k<<1
Hence when k<<1, k can be found by

## Slide 9: Phase advance
Phase advance is the phase difference between adjacent cells.
In standing wave cavities this means that all cells have different amplitudes (except in 0 or pi phase advances).
In the pi/2 mode every 2nd cell is empty.
Amplitude is given by
A=sin(nja)cos(wt)
where n is the cell number
2pi/3 mode deflecting cavity
pi/3 mode deflecting cavity

## Slide 10: Magnetic coupling
If we follow the same procedure for an inductive coupling we obtain
where
Hence when k<<1,
k can again be found by

## Slide 11: Coupling Cells
If we wish capacitive coupling we couple through the beam tubes. This needs a large aperture which often results in higher peak fields and a lower shunt impedance.
If we want magnetic coupling we need to cut coupling slots in the cavity walls near the peak magnetic field on the equator. This allows strong coupling without affecting the fields.

## Slide 12: Slot coupling
Coupling=(fpi-f0)*2/(fpi+f0)
Each point is at 3 GHz
The electric field comes from coupling to the TE11 mode in the slot.
Sensitivity to manufacturing errors is proportional to the coupling

## Slide 13: Three cell cavity example
We can set up Kirchoff’s law as a matrix and solve for the eigenvalues, x, which is a normalised current
We get three eigenmodes of the system
q=0,1 and 2 (ja = 0, p/2, p)

## Slide 14: Manufacturing tolerances
Normal Uni machine shop 100 mm
Good machine shop in a Uni 50 mm
Precision manufacturing 15 mm
Diamond tipped lathes 5 mm
This is related to frequency errors by
Hence the proportional frequency error is proportional to frequency. This is the main limit on going to higher frequency linacs.

## Slide 15: Perturbation theory
We can study the effects of frequency errors by applying perturbation theory. dw1 is the frequency error of the mid cell and dw0 is the error of the end cells
The effects are that a new eigenvector is created containing corrections from mixing from all the unperturbed eigenvectors.

## Slide 16: Fields stability
It can be seen that the amplitude in the p mode varies as
While the p/2 mode varies as
It can be seen in both cases the perturbation is inversely proportional to k so strong coupling is desired.
Also that the p/2 mode is more stable than the p mode by a factor of (normally 10-100 times smaller error)

## Slide 17: Power-flow phase shift
So far we have not included cavity losses or power coupling.
If we add a generator on one side and add resistance to the circuit we can investigate the effects. We implement these in the form Aejf
The p mode has a phase droop and the p/2 mode has an amplitude droop
Mode | Amplitude | Phase
0 | 1 | 
p/2 | 1/kQ | 
p | -1 | 
Mode | Amplitude | Phase
0 | 1 | 
p/2 | -1 +2/(kQ)2 | 0
p | 1 | 
Cell 2
Cell 3

## Slide 18: p/2 mode stability
Why is a p/2 mode so stable
Each mode in the passband contributes a small error term to the excitation of any one particular mode when there are frequency errors. Having a larger mode spacing, by increasing k, reduces this error term.
For the p/2 mode the error terms for the higher frequency modes almost exactly cancels the contributions from the lower frequency modes.
For this reason most long standing wave structures work in the p/2 mode.
Chart: Mode No.
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 0.95609 | 0.96377 | 0.9759 | 0.99143 | 1.0088 | 1.026 | 1.0407 | 1.0506 | 1.0541

## Slide 19: Field profiles
The 0 and p modes have field in every cell, hence every cell contributes to the acceleration.
However in order to meet synchronism conditions the 0 mode and the transit time factor a zero mode needs long drift tubes which makes lowers the average accelerating gradient as the beam is not accelerated in the drift tubes.
The p/2 mode has the middle cell empty hence only the two end cells will contribute to acceleration
For these reasons the p mode gives the highest accelerating gradient.
0 mode
p/2 mode
p mode

## Slide 20: Longer structures
If we have N cells in a cavity we get N eigenmodes (q=1-N). If we adjust the end capacitance to give field flatness. The frequencies and amplitudes are given by
Chart: Mode No.
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 0.95609 | 0.96377 | 0.9759 | 0.99143 | 1.0088 | 1.026 | 1.0407 | 1.0506 | 1.0541
9 cell cavity with wp/2=1 and k=0.1
n=1
n=3
n=5
n=7
n=9

## Slide 21: p mode errors
For an N cell cavity in the pi mode the power-flow phase shift between the first and last cell is
This means k can be chosen to limit the phase shift.
The amplitude stability is given by
Where Dw is the frequency shift due to manufacturing errors. In this case we can use a lower k but our machining will cost more (ie HEP machines), or have a larger k and have looser tolerances (ie medical linacs)

## Slide 22: Example: Linac4 PIMS
For an error of 11% in shunt impedance the coupling factor was chosen to be 5%.
Other effects are expected to further reduce the shunt impedance such as surface roughness and the effect of the coupler
Based on standard manufacturing errors of 25 kHz the voltage error as a function of coupling can be calculated.

## Slide 23: Effect of cell errors on amplitude
Below is an example of the effect of end cell frequency errors in a pi mode structure fed from the central cell.
This leads to early onset of breakdown in the central cell limiting gradient.
Chart: 

## Slide 24: p/2 mode structures
As we have seen p/2 modes are more tolerant to frequency errors (due to manufacturing tolerances) than p mode structures.
We can adjust the cell length to make the p/2 mode synchronous using
But the mode still has a low efficiency as every 2nd cell is unfilled
p-mode
p/2-mode
high shunt impedance
high field stability

## Slide 25
Side coupled or bi-periodic cavity
p-mode
p/2-mode
p/2-mode
Side coupled
high shunt impedance
Beam sees a p-mode high acceleration
RF sees a p/2-mode field highly stable
high field stability
both !
We can improve the shunt impedance by making the coupling and accelerating cells have different geometries for p/2 mode structures.
Side coupled structures move the coupling cells off axis
Bi-periodic cavities use very short coupling cells
L
p/2-mode
bi-periodic
both !

## Slide 26: On-axis coupled infinitely periodic BPC
wc
wc
2N coupling cells
2N+1 accelarating cells
wa
wa
wa
k=coupling constant between acc and coup cells
wa=natural freq. of acc. cell
wc=natural freq. of coup. cell
wm= frequency of mode m
Chart: Phase, deg
| 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180
fc=9.3 GHz, fa=9.5 Ghz | 9.5 | 9.5082 | 9.5292 | 9.5564 | 9.5847 | 9.6111 | 9.6335 | 9.6504 | 9.661 | 9.6646
" | 9.1531 | 9.1561 | 9.1651 | 9.1796 | 9.199 | 9.2223 | 9.2478 | 9.2726 | 9.2922 | 9.3
fc=fa=9.3 GHz | 9.3002 | 9.3404 | 9.3803 | 9.4183 | 9.4529 | 9.4832 | 9.508 | 9.5264 | 9.5377 | 9.5416
" | 9.0759 | 9.0792 | 9.0889 | 9.1049 | 9.1268 | 9.154 | 9.1858 | 9.2214 | 9.2597 | 9.2998
fc=9.3 GHz, fa=9.2 Ghz | 9.3 | 9.3079 | 9.3281 | 9.3544 | 9.382 | 9.4077 | 9.4295 | 9.446 | 9.4563 | 9.4598
" | 8.9575 | 8.9604 | 8.9692 | 8.9833 | 9.0023 | 9.0249 | 9.0496 | 9.0737 | 9.0925 | 9.1
Dispersion relation
Structure
Dispersion diagram contains a stop band at p/2 of width dw=wa-wc
If we use a bi-periodic structre the benefits of the p/2 mode are only received if the frequency of both accelerating and coupling cells are the same.
If they are different we just get a weakly coupled p mode which is worse than a normal p mode

## Slide 27: p/2 modes errors
For a cavity with 2n+1 cells with the coupler located in cell m the field amplitudes in the accelerating cells are given by
Where Dw is the frequency difference between the coupling and accelerating cells. The first term is the power-flow droop and the 2nd is the power-flow phase shift.
As the error is proportional to (m2-n2) it is often best to locate the coupler in the centre of the structure
And the field in the coupling cells are given by

## Slide 28: Example: Industrial & medical side-coupled linac
Siemens 6 MeV SILAC
Varian Clinac
SAMEER structure
Mass produced commercial cavities need to be manufactured cheaply
Ie side-coupled pi/2