## Slide 1: RF Linear accelerators L3: Travelling wave structures
Prof Graeme Burt
Lancaster University

## Slide 2: Dispersion Diagrams
If we plot out the axial wavenumber as a function of frequency we get a dispersion diagram.
The relationship between the magnitude wavevectors in each direction is given by the summation of vectors.
k2 = kz2 + kT2
k is the free space wavenumber/vector and is given by
k=w/c
If k is less than kT then kz is imaginary. This means the mode decays exponentially. This leads to a cut-off frequency below which no wave can propagate.

## Slide 3: Acceleration in a smooth walled waveguide
The phase velocity in a smooth walled waveguide is given by
Which is always greater than c. In order to not over mode the waveguide we will operate at vp>1.35c
If we insert a beam of velocity bc at the Ez maxima the phase will slip by
This limits the maximum length of acceleration to around two wavelengths for beta=1 or less for low beta. This is clearly too short and also inefficient.

## Slide 4: Floquet theorem
We can modify the TM01 modes field pattern and dispersion by inserting periodic isis along the length of the waveguide.
This creates a z dependance in the field pattern
Ez=Ep(z,r)exp[i(wt-kzz)]
Floquet theorem states that
“In a given mode of an infinite periodic structure, the fields at two different cross sections that are separated by one period differ only by a constant factor, which in general is a complex number.”

## Slide 5: Spatial harmonics
A travelling wave cavity isn’t a real travelling wave, the amplitude does vary with position.
If we look at the field in a single cell (the space between the centre of two adjacent iris’) we see that the fields are not constant in z, there is a spatial variation
Due to Floquet theorem the variation is the same in each cell except a phase shift
If we take a Fourier series of the field variation we end up with a number of spacial harmonics
On a dispersion diagram each harmonic has a smaller wavelength and kz increases by 2pn/L
Chart: axial wavenumber
| 0 | 7.7466121627447933E-3 | 2.451530134426233E-2 | 7.8102496759066706E-2 | 0.2645751311064593 | 0.4 | 0.51961524227066369 | 0.63245553203367744 | 0.74161984870956665 | 0.84852813742385802 | 0.95393920141694566
 | 0.3 | 0.3001 | 0.301 | 0.31 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0.3 | 0.3001 | 0.301 | 0.31 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0.3 | 0.3001 | 0.301 | 0.31 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0.3 | 0.3001 | 0.301 | 0.31 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0.3 | 0.3001 | 0.301 | 0.31 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0.3 | 0.3001 | 0.301 | 0.31 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1

## Slide 6: Brillioun diagrams
Chart: axial wavenumber
| -1.5 | -1.4 | -1.3 | -1.2 | -1.1000000000000001 | -1 | -0.89999999999999991 | -0.79999999999999993 | -0.70000000000000062 | -0.60000000000000064 | -0.5 | -0.40000000000000008 | -0.30000000000000032 | -0.2 | -0.1 | 1.1102230246251632E-16 | 0.10000000000000009 | 0.20000000000000009 | 0.30000000000000032 | 0.4 | 0.50000000000000011 | 0.60000000000000064 | 0.70000000000000062 | 0.8000000000000006 | 0.90000000000000013 | 1.0000000000000002 | 1.1000000000000001 | 1.2000000000000002 | 1.3000000000000003 | 1.4000000000000004 | 1.5000000000000002
 | 0.55 | 0.52708 | 0.46708 | 0.39292 | 0.33292 | 0.31 | 0.33292 | 0.39292 | 0.46708 | 0.52708 | 0.55 | 0.52708 | 0.46708 | 0.39292 | 0.33292 | 0.31 | 0.33292 | 0.39292 | 0.46708 | 0.52708 | 0.55 | 0.52708 | 0.46708 | 0.39292 | 0.33292 | 0.31 | 0.33292 | 0.39292 | 0.46708 | 0.52708 | 0.55
 | 0.63 | 0.65292 | 0.71292 | 0.78708 | 0.84708 | 0.87 | 0.84708 | 0.78708 | 0.71292 | 0.65292 | 0.63 | 0.65292 | 0.71292 | 0.78708 | 0.84708 | 0.87 | 0.84708 | 0.78708 | 0.71292 | 0.65292 | 0.63 | 0.65292 | 0.71292 | 0.78708 | 0.84708 | 0.87 | 0.84708 | 0.78708 | 0.71292 | 0.65292 | 0.63
Stopband
At each intersection there is a forward and backwards wave coupled.
This has the solution that no wave can propagate and any wave entering the structure will be reflected.
The coupling creates a “stopband” in the dispersion diagram (or avoided crossing) and we find the same solution as found with the standing wave structures .
Axial wavenumber is related to phase advance by f=kzL.
This is the same as bragg scattering in X-ray crystallography.

## Slide 7: Phase Advance
In a travelling wave structure, the phase advance is phase shift between adjacent cells and is the axial wavenumber multiplied by the iris spacing (f=kzL)
An iris loaded structure will have a group velocity of zero (standing wave structures) at phase advances of 0 and p.
At all other phases the group velocity is non-zero and will travel.
If we can avoid reflections at the input and output then the wave will move through the structure.
  Eg a p/2 travelling wave structure will have all cells filled at some point, but at any instant every 2nd cell is unfilled
  A p/2 standing wave structure always has every 2nd cell unfilled.
CLIC crab cavity prototype 2p/3

## Slide 8: Phase advance
p-mode
p/2-mode
standing
p/2-mode
travelling
0 deg
90 deg
0 deg
90 deg
Chart: position (mm)

## Slide 9: Iris loaded structure
The spacial harmonics in periodically loaded structures means there is a wave with a phase velocity equal to or less than the speed of light
Synchronism is met when the beam and waves velocities are equal and the two travel down the structure together.
The beam always see’s the same field and doesn’t see any variations between cells.
Note that the group velocity is now much less than c. (typically between 0.5-10%)
Speed of light synchronism

## Slide 10: Travelling wave structures
Power can flow through all the cavities and out the other side, very low Q.
Power is also dissipated in the cavity walls.
Due to conservation of energy the power lost in the walls must equal the difference in input and output power.
The group velocity is also the power flow velocity per unit length giving
Pw=vgU/L
Stating this as a differential equation gives (where rL is the impedance per unit length)

## Slide 11: Attenuation
We define the field attenuation per unit length as a0=w/2Qvg
This gives the power as
This leads to a power flow that decays along the structure by
Where P0 is the input power
This leads to a gradient that decreases along the structure

## Slide 12: Energy gain
The gradient decreases as
We define the total power attenuation per structure as t0=a0L=wL/2Qvg
The energy gain is given by
Or using the shunt impedance per unit length rL and the input power P0

## Slide 13: Reflections Output power
The power decays along the structure and any remaining power at the end is dissipated in a load, PL.
However there are no reflections at the input coupler in an ideal cavity.
The required input power, P0, for a travelling wave structure is hence the sum of the power dissipated in the structure, Pc, and the output power, PL
P0=Pc+PL
Hence the group velocity should be tailored to avoid wasted power.
A 1 meter structure will have a lower group velocity (more losses but higher gradient for a given input power) than a 3 meter structure.

## Slide 14: Filling time
Due to the group velocity the structure takes a set time for the wave to propagate from the start to the end of the structure given by
tf=L/vg
Due to the high power flow between cells the filling time is long compared to the time to fill each individual cell (tf>2Q/w). CLARA tf ~900 ns, 2Q/w ~ 50 ns
A travelling wave structure will fill one cell at a time while a standing wave structure has all cells fill at the same time. The filling time is short compared to the time to fill each individual cell (tf<2Q/w). CLARA gun 2Q/w ~800ns
Standing wave filling
Travelling wave filling

## Slide 15: Constant Impedance/Gradient
We can also adjust the iris radii to change the group velocity across the structure. It is assumed that the shunt impedance keeps roughly constant.
Ez2=wrLPw/Qvg
Ez2=rL(-dPw/dz)
If the power flow varies linearly along the surface we find we can have a constant gradient rather than a constant power.
Where PL is the output power.
In practice rL is not constant so this needs adjustment.

## Slide 16: Constant Gradient Attenuation
This gives the power as
This leads to an output power at the end of the structure of
where
Inserting this into the linear power flow gives

## Slide 17: Constant Gradient Energy gain
The energy gain is given by
Or using the shunt impedance per unit length rL and the input power P0
The filling time is given as

## Slide 18: CLARA TWS
The linac sections are 4.15 m long from flange to flange, and are constant 2p/3 TW structures based on the mechanical design of linac II DESY structures.
The shunt impedance was increased to reduce the peak RF drive power required to provide the accelerating gradient and the RF symmetry is maintained with a split input coupler.
It is a constant gradient structure (well almost)

## Slide 19: CLARA structure
The CLARA linac is not constant gradient or constant impedance, its constant power dissipation.
This is because the shunt impedance is not constant so constant power dissipation and constant gradient cannot be achieved at the same time.
As its high rep rate heating is an issue so the design aims to provide a constant heat load in each cell.

## Slide 20: CLARA Parameters
vg=L/tf=4.07/995 ns
vg=1.4% c (not quite right as its not constant impedance)
a=w/2vgQ =0.15
t0 = tFw/2Q=0.68
PL=P0*exp(-2t0)= 9.5 MW
Pc= 27 MW
Ptot= 37 MW

## Slide 21: TW Matched Couplers
A travelling wave structure has two (or four) couplers, and input and an output.
The power travels from the input to the output

## Slide 22: Matching travelling wave structures
The two S11 plots are for the same cavity and both have S11<0.1 at 2.9985 GHz but they have different Q’s for the couplers.
If S11=0 is the cavity matched?

## Slide 23: Is it matched?
It depends what you mean by matched?
The reflections are zero in steady state for both cavities but if we wish a travelling wave then there should be no reflections at any time not just in steady state.
If there is a mismatch between each coupler and the cavity then the reflections from each coupler could cancel, similar to stub matching, giving S11=0
But the downside is that there is a standing wave between the couplers with waves going in both directions inside the coupler
This increases the losses without increasing acceleration as well as creating “hot” cells where the field exceeds breakdown limits

## Slide 24: Matching TWS
E = field
P = cell length
R = internal reflection coefficient
y = phase advance
This is not the same as S11=0 (global matching) . Here we have no internal reflections
For a true travelling wave there is also no reflection at the start of the pulse.
In order to verify a structure is matched we must measure the fields inside the cavity.
By measuring how the field varies between a cell and its nearest two neighbours we can use Floquet theorem to calculate the phase and internal reflections. For a TWS |R|=0.

## Slide 25: Matched Couplers
For a matched coupler we must consider the matching of each cell rather than the entire structure, ie considering the power flow between cells. As before a coupler is matched if Qe=Qinternal
Here
Where Qf is calculated from the power flow from cell to cell. If Q0 >> Qf
Example: CLARA S-band TWS Phase advance = 2p/3
Group velocity = 3 % c at the input
Qe = 70
This is a very low Q compared to that of a standing wave cavity which gives the fast filling time and large bandwidth.
This is not power loss but power flow so the structure can still be efficient if made sufficiently long.
Note we also need to ensure the phase advance is respected as well so its not as simple as getting the right Q factor

## Slide 26
Measuring match: Example CLIC crab cavity
119.870
If we look at the phase of reflections from a beadpull measurement we can find the amplitude and phase of each cell.

## Slide 27: Beamloading
As we have a travelling wave structure any fields induced by the beam will also travel down the structure.
This leads to a reduction in the gradient along the structure with higher fields at the input coupler
This increases the peak field for a given gradient.
Beamloading in CLIC main linac

## Slide 28: Advantages of travelling wave
Fast filling time (shorter pulses)
No reflections (circulator not required)
Better stability to manufacturing tolerances than p mode structures (so can be longer)
Small frequency changes can be used to vary beam voltage in industrial linacs.
Disadvantages of travelling wave
Power loss at output port
Beamloading leads to asymmetric loading of fields
Needs two couplers