## Slide 1: RF Linear accelerators L5: Low beta linacs (a day trip to the zoo)
Dr G Burt Lancaster University
with some slides borrowed from
M. Vrentinar Linear Accelerators CERN Accelerator School
and
F. Geirigk Cavity Types CERN-2011-007, pp. 277-298 arXiv:1111.4897

## Slide 2: Low Beta
As the beam velocity is reduced the cell period decreases as L=bl/2.
This means the number of discs loading the waveguide per metre is given by N=2/lb
Each disk is a source of losses so the shunt impedance decreases.
The disk thickness is required for mechanical stability and heat removal so this cannot be decreased. These take up a space 2d/lb where d is the disk thickness.
This means the useable accelerating length is reduced
Also at low beta space charge forces are important and we want to minimise RF defocusing so low frequency is preferred.
L
d

## Slide 3: Low Beta Linacs
The solution is to use a structure with no end walls.
Three solutions exist
  Use a structure with two separate conductors carrying out of phase voltages (Widroe)
  Use a single long cavity and shield the beam from the decelerating fields (Alvarez)
  Use alternative modes (TE or TEM modes)

## Slide 4: Alvarez drift tube linac (DTL)
A DTL uses a single long TM010 mode cavity such that the length is much longer than L=bl/2.
The when the transit time causes the field to be decelerating the beam will be shielded in drift tubes (small cylinders), hence the DTL will only operate at a single gradient.
Each DTL is supported by a stem which has a low current on it. High coupling between cells as no walls.
At higher frequencies the field starts to vary along the drift tube/stem and the DTL becomes inefficient. Size increases at low frequency so range is 200-400 MHz

## Slide 5: Alvarez DTL
B-field
E-field
The DTL has a phase advance between the gaps of 0/360 degrees.
The beam theresfore is shielded from the fields at least 50% of the time normally more.
This results in a low gradient of 3-5 MV/m.
Inefficient because of this at beta > 0.5.
Difficult to fit in drift tubes and focussing at really low beta so 0.05<beta<0.5

## Slide 6: Tuning posts
In SCL we use a resonant coupling (side cells) to provide more stable operation (more tolerant to manufacturing errors).
In DTL’s we can do something similar by having a resonant element between each gap.
This is commonly achieved by using l/4 coax lines called post couplers.
The electric field of the post and magnetic field of the cavity create a longitudinal Poynting vector and hence energy flow.
This shifts the TE11 mode frequency in confluence with the TM01 mode.

## Slide 7: DTL Focussing
As DTL’s work at low frequencies and the drift tube are fairly long (d~bl/2) we usually have enough space to fit a focusing quadropole inside the drift tube.
Often if more focussing is required some or all drift tubes are made to be 3bl/2 long. If it is only every 2nd or 3rd drift tube that contains the quadrupole it is known as a quasi-Alvarez linac.
Sometimes its easier to just split the structure in two and add a boublet in between and that’s called a separated DTL (SDTL)

## Slide 8: The Linac4 DTL
beam
352 MHz frequency
Tank diameter 500mm
3 resonators (tanks)
Length 19 m
120 Drift Tubes
Energy 3 MeV to 50 MeV
Beta 0.08 to 0.31  cell length (bl) 68mm to 264mm
 factor 3.9 increase in cell length

## Slide 9: CC-DTL
The bests elements of a drift tube and a coupled cavity linac are combined in a coupled-cavity drift tube linac (CC-DTL).
Each cell has a drift tube inside it.
It has a higher shunt impedance than an Alvarez DTL as you get three gaps per drift tube as the field goes to zero at the CC aperture, but allows smaller drifts with larger spacing between walls.
Can also have quadrupoles in the drift tubes.
Not so good at very low beta.

## Slide 10
DTL= Drift Tube Linac
CCDTL- Coupled cavity DTL
SDTL- Separated DTL
SCL- Side coupled Linac
PIMS- Pi mode structure

## Slide 11: TM, TE and TEM modes
Transverse electric (TE) modes only have transverse electric fields (Ez=0).
They are smaller than TM mode cavities.
Transverse magnetic modes (TM) only have transverse magnetic fields but always have longitudinal electric fields (good for accelerating)
E field
E field
E field
Transverse electromagnetic modes (TEM) have no longitudinal fields.
They need two isolated conductors.
Frequency is not dependant on transverse size so can work at very low frequencies.

## Slide 12: TE and TEM drift tube structures
The definitions TE and TEM (Ez=0) are only strictly true in cavities of constant cross-section. Any discontinuities cause the field to bend round the discontinuity giving rise to hybrid mode components. One method is to use drift tubes.
TE mode with drift tube.
These modes have low magnetic fields on the walls so have low losses.
TEM mode with drift tube
These modes have very low frequencies so less RF defocussing.

## Slide 13: Widroe Linac
In a widroe linac we uses two conductors supporting a TEM similar to biaxial transmission line. This was the first linac structure and is still in use today.
Each conductor has a number of electrodes which contain the beam apertures.
The electrodes from each conductor are alternated so that an electric field is created between them, and the field alternates at each gap (like a pi mode).
The distance between gaps is a L=bl/2 as in a pi mode structure.
As the transverse size is not dependant on frequency the structure can work at very low frequencies.
Still used for very low beta (heavy ion) injectors.
GSI Unilac Widroe

## Slide 14: CH and IH structures
One such set of TE cavities are the H-mode cavities (some people call TE modes H modes).
They can operate in the TE11 mode (Interdigital) or TE21 mode (crossbar)
They have very high shunt impedances at low energy
At high energy the voltage is low as the gaps get longer and the H-mode only has Ez near the drift tube ends

## Slide 15: Alvarez vs CH DTLs
Image from W. Barth

## Slide 16: Frankfurt CH-DTL
Smaller than an Alvarez DTL at 350 MHz and higher shunt impedance as it operates in a pi-mode.
This allows smaller drift tubes (high shunt impedance) but doesn’t allow magnets to be put in the drift tubes.
Cannot have large aperture.
Superconducting and normal conducting versions exist.
Will be used for the first time at FAIR.
At high beta the gaps get larger and the CH structure becomes less efficient. 3-100 MeV (up to beta=0.3c)

## Slide 17: The normal conducting zoo
For normal-conducting, the goal is designing high-efficiency structures with a large number of cells (higher power RF sources are less expensive).
Two important trends:
Use p/2 modes for stability of long chains of resonators → CCDTL (Cell-Coupled Drift Tube Linac), SCL (Side Coupled Linac), ACS (Annular Coupled Structure),....
Use alternative modes: H-mode structures (TE band) → Interdigital IH, CH
17
SCL
CCDTL
PIMS
CH
DTL
Notes: Help you to find your way inside the zoo…

## Slide 18: Radio frequency Quadropole (RFQ)
At very low energy focussing and bunching is critical
It would be really useful if we could make a structure that focussed, bunched and accelerated at the same time.
Magnetic fields are not ideal for focussing at low energy as the lorentz force is q(E+vxB), hence electric focussing is preferred.
We can create an RF electric quadrupole by using a TE21 mode.
In an RFQ we load the cavity
with rods or vanes to make
the TE21 the lower in
frequency and increase
focussing.

## Slide 19: RFQ 4 vane
However the TE21 mode has no longitudinal electric field.
In order to create an electric field the vanes are corrugated to create a longitudinal component.
The depth of corrugation increases acceleration but decreases the focussing.

## Slide 20: Accelerating fields
The accelerating field depends on the modulation depth.
The accelerating voltage is always less than potential between the vanes
While the electric focussing is very useful at low energy, the low gradient is not suitable at high energy.
RFQ’s work between beta=0.01c -0.06c

## Slide 21: Adiabatic Bunching
The amplitude and synchronous phase is slowly increased along an RFQ.
The beam is injected at fs=-90 degrees to provide bunching and it slowly drifts towards fs=0 deg.
This allows adiabatic bunching and avoids large space charge forces which limit older buncher cavities.

## Slide 22: Four Rod RFQ
If a lower frequency is preferred (for more focussing) the four vane structure can get quite large.
A four rod structure (similar to a widroe linac) can be used which support TEM waves.
These structures are harder to cool but do allow compact low frequency RFQ’s.

## Slide 23: Single TEM resonators
We can also use a half-wave resonator (HWR) consisting of a l/2 coaxial line with a TEM mode in it.
The beam enters the cavity along the direction of the electric field and has two gaps for acceleration.
Mostly beta=0.1-0.3, 150-300 MHz
To make the cavity shorter we can add an open circuit at one end to make a quarter wave resonator (QWR).
However as the cavity is asymmetrical the field contains dipole components that will kick the beam.
For normally beta 0.01-0.15, 50-150 MHz.

## Slide 24: Spoke cavities
We can make multicell half-wave resonators called spoke cavities.
Work well at intermediate beta (0.15-0.62).
They are also being investigated for beta=1 applications due to their small size.
Single spokes also exist, they are different from HWR due to their outer can shape.
Larger that a HWR so do not work below 350 MHz
Triple spoke FZJ
RIA multi-spoke

## Slide 25: Lower frequency = Lower Beta
Borrowed from M. Kelly
Spoke (low beta)
[FZJ, Orsay]
QWR (low beta)
[LNL, etc.]
Elliptical cavities [CEA, INFN-MI, CERN, …]

## Slide 26: SNS

## Slide 27: ESS
1

## Slide 28: Linac 4 (CERN)

## Slide 29: Warm to Cold transition
SRF structures are more efficient but add complexity, the energy at which the linac should switch from normal conducting to superconducting typically depends on duty cycle and hence wall plug power.