## Slide 1
Neutron spectroscopy
Svemir Rudic
ISIS Molecular Spectroscopy Group scientist

## Slide 2
OSIRIS/IRIS
LOW
energy
High
energy

## Slide 3
X-ray
Neutrons
H
D
O
Fe
Why neutrons for dynamics?
The perfect tool for self correlation of Hydrogen!
distinguish different molecular groups
All modes are active unlike IR/Raman
Selective deuteration

## Slide 4
Density functional theory can be used to calculate vibrational modes
Data can then be weighted by neutron cross sections
Combinations and overtones can be added
Gives atomic insight
abins
Identifying peaks on Tosca

## Slide 5
A. Michalchuk et al., Chem. Commun. 57, 11213 (2021)
I. Vazquez-Fernandez et al., J. Phys. Chem. C 125, 24463 (2021)
Examples of TOSCA INS studies

## Slide 6
Basic principles of quasi elastic scattering
Similar to TOSCA, but lower energy and multiple detector angles (Q)
Uncertainty in Ei defines the lowest accessible timescale/energy
Broadening beyond instrumental resolution increasing motion (diffusion, low frequency bending of polymers, local confined motion)
Fickian diffusion has a linear relation between FWHM and Q
Many other models describe hopping etc.
Peaks indicate tunnelling

## Slide 7
The scarcity of Li, has sparked interest in Na
Replacing Li with Na!
Lorentzian fitting
Jump diffusion model fitting
Diffusion coefficients are extracted as a function of T
T.J. Willis et al., Scientific Reports 8, 3210 (2018).

## Slide 8
Molecular dynamics (MD) with qens
MD can probe diffusive/long time regimes as in QENS
Ab Initio and empirical force-fields may be compared directly to QENS via MDANSE
QENS can even be used to parameterise MD models
I. Silverwood and J. Armstrong, Surface Science 674, 13 (2018).

## Slide 9
VESUVIO is a unique instrument in the world!
Can we do any better?
Unlike other instruments, it looks at materials one atom at a time..
1. Neutron Compton scattering (NCS)

## Slide 10: 4 new techniques on VESUVIO and made them integral part of the user programme
3. Neutron transmission
VESUVIO+:
4. resonant neutron
absorption Dopplerimetry
5. PGAA and multi-dimensional
PGAA
2. High-resolution
wide d-spacing range
neutron diffraction
50 k£ budget and 4 years!

## Slide 11
sample environment
High pressure cells
(Up to 7 Kbar)
Sample Changers
TOSCA (36 samples)
IRIS (3 samples)
Gas Panel
(Many gases available)
High P phase changes
Gas absorption vs pressure
Studies of entire class of
material

## Slide 12
Catalysis rig
Mass spec
Gas manifold
furnace
Flow through
Reaction cells
Catalytic reactions at the target station, which can be put straight onto TOSCA
Study reactions under different conditions

## Slide 13
Excitations Group
https://isis.sis.stfc.ac.uk/instruments/let/

## Slide 14: Why bother?
pS timescale is that of atomic or magnetic vibrations.
Information about the interatomic bonding or magnetic interactions.
What is driving a phase transition?
How does heat travel through this material?
What are the important magnetic excitations in this spintronic?

## Slide 15
Xpress Access

## Slide 16
STFC ePubs – the open archive for STFC research publications

## Slide 17: Overall summary
Neutron spectroscopy provides a view of the atomic dynamics.
These dynamics are integral to the materials performance in a wide range of areas.
This means there are a lot of applications gaining fundamental understanding of technological materials i.e. solar cells.
If you wish to apply for time, do drop me an email
  OR david.voneshen@stfc.ac.uk

## Slide 18
Thanks for listening