## Slide 1: Signal Integrity 101
High-speed digital design
Weiming Qian 04/2026

## Slide 2: What is Signal Integrity
Signal Integrity
Transmission lines
Ground Planes
Terminations
Crosstalk
Power Supply Noise
Via design
…
Hardware Designer
EMC specialist
PCB designer
Circuit theory
Chips
Probes
Bus architecture
Shielding
Grounding
Routing
Bypass Capacitors
Clock/bus skew
You don’t need it until your system breakdown?

## Slide 3: Digital world vs Real world
Digital logic timing diagram
Real world high-speed signal after a channel

## Slide 4: Eye diagram view
What is the margin?
Speed, channel length, clock jitter…

## Slide 5: Digital Signal Spectral
Bandwidth of digital signal depends on rise time (Tr), not the toggle frequency
3dB BW = 0.35/Tr
Digital Knee Frequency = 0.5/Tr
1-nS  500MHz

## Slide 6: Digital signal measurement
Oscilloscope must have enough bandwidth
  > 1/Tr
Ttotal = sqrt(Tr2 + Tscope2)

## Slide 7: Probing effect
Probe must have enough bandwidth as well

## Slide 8: When SI problems most likely arise
Channel length is comparable or bigger than the signal rising edge
  Distributed model needed
Ltr ~ Tr * C0/2 in FR4 PCB
1 ns  6 inches

## Slide 9: Transmission Line (tline)
Lossless transmission line model
  Only work at low to medium frequency
  Impedance is constant
    like a pure resistor
  Proper termination needed
L
C
L
C
L
C
L

## Slide 10: Transmission Line (tline)
Lossy transmission line model
  Much more complicated
  Impedance changes over signal frequency

## Slide 11: Transmission Line (tline)
Lossy transmission line
  Higher frequency has higher attenuation
    Slowing down signal edges
      Causing inter-symbol-interference
        Smaller eyer opening

## Slide 12: Transmission Line (tline)
Lossy transmission line
  Termination needed
  Encoding (8b/10b, 64b/66b, …)
    Limiting length of continuous ‘1’ and ‘0’
  Equalization
    Boost high-frequency components

## Slide 13: @ 10Gbps
Tr ~ 30ps
  Length ~ 4.5mm
PTH Via length ~2.5mm
  PCB thickness approaching signal Tr length
  Detailed modelling of vias and connectors needed

## Slide 14: Crosstalk control

## Slide 15: Crosstalk control
Continuous ground plane reference is essential
  Majority of return current on ground plane
    Crosstalk is proportional to (h/d)2
d

## Slide 16: Power distribution network (PDN)
PDN in high-power high-speed PCB is far more complicated than indicated in the schematic

## Slide 17: PDN design
PDN needs to carry high DC current to devices
  100A is not uncommon
    DC simulation needed to ensure enough cooper

## Slide 18: PDN design
PDN also needs to have a low enough impedance via decoupling caps
  AC simulation
  Cap placement on PCB matters

## Slide 19: Clock jitter
Low jitter reference clock
  Jitter is a discrete-time random signal
    Jitter possesses a frequency spectrum
      Measurement requires special equipment and methods
        High-end real-time scope with jitter analysis software
        Real-time spectrum analyzer

## Slide 20: Design for Test
Dedicated testpoints
  Tp for powers
  Tp for clocks
  Tp for typical signals

## Slide 21: Challenges in multi_Gbps PCB design
High-speed PCB design
  Impedance control
    PCB trace, via, connector
  High frequency attenuation
    Skin effect, dielectric loss
  Crosstalk
    Near-end crosstalk (NEXT)
    Far-end crosstalk (FEXT)
  Clock jitter
    Synchronous vs. asynchronous link
  PCB differential skew
    PCB material weave pattern
  Power distribution system
    Nominal voltage +/- 2.5% for Xilinx Virtex-7 GTH

## Slide 22: Speed regimes of high-speed link (1)
Up to 1Gbps
  Signal edge physical length on PCB > 5cm
  Signal loss over PCB tracks is relatively small
  PCB via effect on signal integrity is negligible
  Tight impedance control and good termination
  Channel simulation is optional
    ~1000 bit simulation will suffice
  Link validation by direct EYE measurement

## Slide 23: Speed regimes of high-speed link (2)
2~5Gbps
  Signal edge physical length on PCB ~ 1cm
  Frequency dependent loss on PCB causes significant ISI
  PCB via begins to distort signal integrity
  Tx pre-emphasis (Rx equalization optional)
    Linear Time Invariant (LTI)
  Open EYE achievable at Rx input pin
  Channel simulation is important
    ~1,000,000 bit simulation needed to qualify the link performance
    Time domain simulation + statistical analysis
  Validation by simulation/direct EYE measurement

## Slide 24: Speed regimes of high-speed link (3)
Over 6Gbps
  Signal edge physical length on PCB ~ mm
  Signal frequency dependent loss on PCB causes huge ISI
  PCB via has big impact on signal integrity
  Tx multi-tap equalization
  Close EYE at Rx input pin
    Open EYE hidden inside the Rx after equalization
  Rx adaptive equalization + Decision Feedback Equalization (DFE)
    Non linear, time variant
  Channel simulation is essential
    ~10,000,000 bit simulation needed to qualify the link performance
    Time domain simulation + statistical analysis
    Algorithmic Model Interface for Rx DFE and CDR
  Validation by simulation/BER measurement

## Slide 25: Strategy for multi_Gbps PCB design
Pre-layout simulation
  Derive PCB layout rules
Post-layout simulation
  Verify PCB layout quality
Time Domain Reflectometry /Transmission (TDR/TDT) test
  Verify PCB manufacture quality
Eye/BER (Bit Error Rate) test
  Correlate PCB channel simulation to hardware

## Slide 26: Hardware test example
High-speed demonstrator GTX 5Gbps measurement

## Slide 27: Simulation and Correlation
Eye Simulation

## Slide 28
Questions or Comments?
Signal Integrity 101