## Slide 1
Radon Control and Measurement at SNOLAB for Current and Next-Generation Rare-event Search Experiments
Dr Nasim Fatemighomi (she/her)
SNOLAB Research Scientist
Queen’s University adjunct Professor
2026/09/17
Rutherford Appleton Laboratory, September 2026

## Slide 2
Outline
Introduction
  Neutrinoless double beta decay and dark matter
  Sources of background
Why controlling radon is important
Techniques applied to measure radon ex-situ at SNOLAB
Radon removal techniques
Techniques to create low radon environment
Summary
Notes: Outline:

## Slide 3
Introduction

## Slide 4
https://webbtelescope.org/news/first-images/gallery
Universe looks like this
… and not like this
Notes: The Big bang should have created equal amount of matter and anti-matter in the universe so why in today’s Universe there is a more matter than anti-matter in the universe. In other words why our universe likes this? Made of galaxies, stars, planetns and life which all made of matter, rather than the matter and antimatters from big bang annihilate each each other and create and empty Universe? So what is the physics mechanism behind matter anti-matter symmetry?

## Slide 5
Can Neutrino-less Double Beta Decay (0be the answer?
Neutrinoless double beta decay (0
  Physics beyond Standard Model
  Occurs if neutrinos are Majorana particle
0can be the mechanism which annihilates anti-particles
Peak at the end-point of 2 which is smeared by the energy resolution of the detector
Extremely rare process
Need large-scale experiments with very low background

## Slide 6
Evidence of Dark Matter (CMB)
CMB data most convincing evidence of dark matter
Look at the tiny variation of temperature of the universe 400000 years after the Big Bang
Can precisely calculate what the Universe is composed of
GeV to TeV scale dark matter particles are predicted in several beyond standard model theories

## Slide 7
A detector with an order of magnitude higher background, reaches its maximum sensitivity sooner
Longer measurements do not improve the sensitivity
Next generation of xenon and argon experiments aim for 1 event or less in 10 years!
In a low background experiment, higher exposure gives better cross section sensitivity
Effect of background
An Dark Matter Experiment
https://ar5iv.labs.arxiv.org/html/1509.08767

## Slide 8
SNOLAB Underground Facility
SNOLAB hosts neutrino and dark matter experiments
Located 2 km underground in the active Vale Creighton nickel near Sudbury, Ontario, Canada
arXiv:2406.10339

## Slide 9
Notes: Merge slide 4 and 5

## Slide 10
Example of Large-Scale Detectors
A Future Dark Matter and 0 liquid xenon experiment
SNO+
XLZD (SNOLAB or Boulby?)
12 m
Current generation 0 liquid scintillator experiment
~ 3 m

## Slide 11
Background sources
Gammas () and betas () from natural radioactivity
Alphas () from natural radioactivity
  : interaction of s with detector material
  Surface alphas s
Muons
    Muon-induced neutrons
    Cosmogenic activation
13C
16O
Detector Medium
Detector Wall
Notes: For these experiments to be successful, they need to control and mitigate background , these are gamma and betas from natural radioactivity, alphas from natural radioactivity which can create neutrions by interacting with detector material. Can create surface alpha background which can have similar recoil energy as a dark matter candidate. Or muons. The focus of my talk today is radon induced background which can create gamma and betas from natural radioactivity and alphas from natural radioactivity.

## Slide 13
Long-lived isotope:
226Ra, 222Rn and short-lived progeny
Longer-lived 222Rn progeny

## Slide 14
Long-lived isotope:
226Ra, 222Rn and short-lived progeny
Longer-lived 222Rn progeny
Complex processing can cause radioactive disequilibrium
Must study each sub-chain separately

## Slide 15
Long-lived isotope:
Inductively Coupled Plasma Mass Spectrometry (ICP-MS)
Commercially available instruments
Sensitivity: 0.1
226Ra, 222Rn and short-lived progeny
High Purity Germanium Detectors (HPGe),
Sensitivity: 10-100
Radon emanation systems, Sensitivity: 20- 200
Longer-lived 222Rn progeny
Alpha spectroscopy – such as XIA UltraLo-1800 alpha counter
Sensitivity: ~ 1 mBq/kg
ICP-MS at SNOLAB
XIA UltraLo-1800 at SNOLAB
A VdA HPGe detector at SNOLAB

## Slide 16
Radon Emanation Measurement
222Rn is a progeny of 238U
It is a noble gas, ie. can travel
Emanates from material surfaces
  Recoil from 226Ra
  Diffusion from bulk
Present in SNOLAB air 120 Bq/m3
Experiments require radon reduced environment and ultra low radon emanating material

## Slide 17
Mitigation strategy
Strict material selection by performing radon emanation measurements
Regular monitoring of Rn levels
Rn removal from liquid and gas
Controlling radon ingress in the detector
Preventing surface contamination
Cleaning and removal of surfaces to remove 210Pb

## Slide 18
Radon Assay Systems at SNOLAB

## Slide 19
Radon Assay
222Rn assay refers to the measurement of emanation rate from a material surface and 222Rn concentration in gas or water samples.

## Slide 20
Radon Trapping Technique
Based on a design developed by Queen’s (M. Liu, et al. NIM A, 517)
Radon atoms collected by cooling down radon traps using liquid nitrogen (LN)
Radon released by warming up the traps (100C)
Radon transferred to a Lucas cell (LC) through volume sharing
LC is detached and put on top of a PMT for counting
Emanation Chamber
(under vacuum)
Notes: Bigger figures, remove white space, make the text more readable

## Slide 21
Vacuum Pump
Emanation
Chamber
SNOLAB Radon Emanation System
Sensitivity: ~ 50
Plan to increase the emanation chambers
Notes: Make the picture bigger, cover the whole slide, and put the information in text boxes ,

## Slide 22
Portable Lucas cells (LCs) with ZnS(Ag) coating
ZnS(Ag) scintillates with α particles → ideal for radon detection
Sixteen LC channels available
LC Counting System
2” diameter PMTs and CAEN electronics
2” diameter
4 μs window
Notes: Justify why LC compare to other type of like electorstatic chamber, cheap to produce, if you want to count 16 assays at the time you need to make 16 electrostatic chamber.. Which makes it expensive. I think this type of detector is unique to SNOLAB and while we should investigate other type of technology, high efficiency compare with electrostic chambers… I think we should push impoving this as well… talk about justin , keegan etc work … less sensitive to moisture and other impurities compare to electrostic and proportional counters. Less affected by noise during radon correction.

## Slide 23
LC Efficiency
Purchased a 30.0 1.5 Bq RNC pylon source to measure efficiency at SNOLAB
Courtesy of J. Suys
SNOLAB recent simulation
(Preliminary)
  I. Blevis, et al. NIM A, 517
  M. Liu, et al. NIM A, 329
GEANT4 simulation
Notes: Put Justin’s plot here, how to make the error in data smaller.
Tension between the two measurment

## Slide 24
LC Background
Increasing age
New LCs have background of 3 to 5 alpha counts day
LC 210Po background increases with 210Pb build up
The background is from ZnS(Ag)
Every few years we make new LCs
New LC made at SNOLAB
Coated with commercial ZnS(Ag)
Notes: Background cells build over time
Reduce the background, think about conclusion, ages

## Slide 25
Ongoing Research and Development
XLZD Goal: radon level inside liquid xenon target < 0.1 /kg
Need to reduce background of our systems by factor of 100.
Require lower background radon detectors
  R&D toward lower background ZnS (Ag)
  Developing ultra low background proportional counters
In-house ZnS(Ag)
scintillation
in-house ZnS(Ag)
Spherical Proportional Counter (a la NEWs-G)

## Slide 26
Recirculation Technique using Electrostatic Chambers
Developed for224Ra and 226Ra measurement in SNO
Used for 222Rn assay measurement for EXO-200 and nEXO.
Detect positively charged radon progeny drifting to a negatively biased detector
A recirculation pump forces a carrier gas gas through the sample and into the ESC for analysis
Continuous radon transport and detection
Two units being refurbished with a new DAQ system (expected sensitivity: 200

## Slide 27
Measurement of radon concentration in gas
N₂ is widely used as a cover gas to prevent Rn ingress in the detector
For large-volume systems, N₂ is used as a carrier gas to sweep out emanated Rn
PICO-500 Dark Matter Experiment Steel Shell
SNO+ Cover Gas System

## Slide 28
The UG Mobile System
Designed for vacuum radon emanation measurement
Was adopted to perform N2 gas assays
Cover Gas system filled with N2
vapor trap
Notes: . The commercial trap contained a helically wound titanium coil filled with a coolant called R290/R1150 (a blend of propane and ethylene) a

## Slide 29
Primary Trap Limitation for Gas Assays
Radon traps use porous materials to enhance trapping
Bronze wool highly efficient under high vacuum
Gas assay efficiency decreases with longer duration or >1 SLPM flow
Limited extracted gas volume constrains sensitivity (> 3.3 mBq/m3)
Need for traps with more porous material
S.M.A. Hussain MSc thesis (2022)

## Slide 30
Activated Charcoal Trap
Activated charcoal traps used for gas purification
  G. Heusser, et al. Appl. Radiat. Isot., 52 (2000)
Gas assays require both trapping & efficient radon release
Developed a portable activated charcoal trap to enhance radon trapping
  Nasim Fatemighomi et al: Nucl.Instrum.Meth.A 1076 (2025)
Used low background Calgon OVC 4 × 8 (coconut-based)
In-house nitric acid etching to remove ²³⁸U background
Radon emanation: 183 mBq/kg at room temperature
100μm
22 g trap

## Slide 31
Trap Efficiency Test Set-up
N₂ flow through the source introduces radon atoms to trap
Charcoal cooled with LN₂–alcohol mix to trap radon
Radon released from charcoal trap by heating
Released radon were extracted using the radon board

## Slide 32
Unlike bronze wool trap, charcoal trap is 100% efficient after one hour of assay duration
The trap is also 100% efficient for flow rate of up to 5 SLPM
N2 assay sensitivity 90Bq/m3
This sensitivity is sufficient for external systems at SNOLAB (need to reevaluate for XLZD)
Plan to develop lower background traps
The method developed to test this charcoal trap can be used to test other radon traps
Charcoal versus Bronze Traps

## Slide 33
Water Radon Assay System
Designed and built by the SNO collaboration (DOI: 10.1016/j.nima.2003.10.103)
Operated by SNOLAB and SNO+ to monitor 222Rn level of SNO+ cavity UPW and SNOLAB UPW plant
For double beta decay physics knowing level of external 214Bi is important
Water trap
Degassser
Trap A
Trap B
The SNO+ experiment
Water shielding (7000 tonnes UPW)

## Slide 34
Water trap (-60 C)
Degasser
Radon extraction board
H2O from SNO+ cavity/UPW plant (19 SLPM)
Water return to cavity

## Slide 35
V203: Between Acrylic Vessel and PMTs
Results are consistent with SNO times
SNOLAB UPW plant radon level is ( 294) Rn atoms/L

## Slide 36
Radon Removal Techniques

## Slide 37
Removal of Rn from liquid/gas
Rn
Boiled-off liquid/gas
Heater
Condenser
Liquid/gas
Cryogenic Distillation
Using Raoult’s law: the concentration (Rn) in the gas equals the vapor pressure times its mole fraction
Application: Liquid Xenon
Physical Adsorption
Making a cryogenic trap from activated charcoal
Application: Liquid Argon, boil-off N2
Making a trap with silver exchanged zeolite
Room temperature
Application: Liquid Argon, boil-off N2

## Slide 38
Silver Exchanged Zeolite for Rn Removal
S. Heinitz, et al. Nature: Sci Rep 13, 6811 (2023)
17 g adsorbent at room temperature
Demonstrates 10–100 times higher adsorption efficiency than activated charcoal at room temperature
Planned usage at SNOLAB radon removal from N₂ cover gas systems
Currently testing Ag-13X at room temperature at SNOLAB
Efficiency measurements of a radon trap is ongoing using surface board setup
Collaboration with Queen’s argon and xenon astroparticle group to develop a radon trap for argon and xenon systems
Nitrogen
Notes: Time that radon breakthrough the trap, ideal trap is lets everything through but radon

## Slide 39
Silver Zeolite for Rn Removal (Argon-Xenon (?))
S. Heinitz, et al. Nature: Sci Rep 13, 6811 (2023)
17 g adsorbent at room temperature
Rn breakthrough is longer when carrier gas is argon
No published data with Xe
  Maybe because zeolite also traps Xe?
Need to work with the company to see if we can optimize the material to not to trap Xe.
Xe experiments currently use distillation technique for radon removal.

## Slide 40
Controlling Radon Ingress in the Experiments

## Slide 41
Radon Reduced air
Can use columns of activated charcoal (or silver exchanged zeolite) to create a low radon concentration environment
SuperCDMS achieved <0.1 Bq/m3
Such systems will be needed for future large-scale projects
arXiv:1708.08535

## Slide 42
N2 Cover Gas Systems
SNOLAB provides boil-off N2 to experiments by surface LN Dewar's, UG LN plant and N2 bottles
SNOLAB UG LN plant Boil-off had radon level of mBq/m3
Can achieve lower concentration if we use a zeolite trap

## Slide 43
SNO+ unique N2 Cover Gas system
Designed and fabricated at Queen’s University
Sealed system which adjusts for pressure fluctuation (up to 9%) in the lab
Main components:
  Three flexible bags
  Failsafe (pressure relief system)
  Universal interface
Current activity 0.1 Bq/m3
Meets the requirements for double beta decay physics
For solar neutrino physics, radon levels can be further reduced using zeolite traps

## Slide 44
Summary
SNOLAB’s rare-event experiments probe fundamental questions in particle physics
Controlling ²²²Rn-induced backgrounds is critical to achieving physics goals
SNOLAB continues to strengthen its radon mitigation program by:
  Building and operating low-background radon assay systems
  R&D toward making low background radon counting systems
  Developing advanced radon removal techniques
  Creating radon reduced environments with boil-off N2
  Maintaining existing radon systems

## Slide 45
Back up

## Slide 46
Radon Calibration Source for Trap testing
A calibrating source was made using Nora Xp 5319 rubber floor tile
10cm
14 x 10 cm2 floor tiles
Calibration Can
Fit is based on²²⁶Ra-supported emanation and ²²²Rn outgassing from porous rubber tiles

## Slide 47
Procedure and the current challenge
ZnS is made using a two-stage selective precipitation
To activate with Ag: add 100 ppm of Ag and recrystalise using NaCl/kCl as flux at temperature of 950 C
In addition to ZnS(Ag), ZnO is also observed (confirmed with Raman spectroscopy)
This occurs because the annealing process is performed in an open-air furnace, leading to oxidation.
The presence of ZnO reduces the α-particle detection efficiency.
SNOLAB plans to purchase an oxygen-free tube furnace to mitigate this issue.
ZnO scintillation
Notes: Here talk about both making new LC and to make ZnS

## Slide 48
More LC related research (improving efficiency)
The design of the LC needs to be revisited
Use a transparent scintillator on the window (PEN)
Make a spherical LC, take advantage of light being reflected from ZnS surface
Requires GEANT4 simulation
Possible graduate student project
Silicon photo multiplier

## Slide 49
Trap Efficiency Test Set-up
N₂ flow through the source introduces radon atoms to trap
Charcoal cooled with LN₂–alcohol mix to trap radon
Radon released from charcoal trap by heating
Released radon were extracted using the radon board