## Slide 1: The Laser-hybrid Accelerator for Radiobiological Applications
… and the LhARA initiative

## Slide 2: Acknowledgements
DOI: 10.5286/stfctr.2026007

## Slide 3: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy:
    Indicated in half of all cancer patients
    Contributions to 40% of cures
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 4: Radiotherapy; the challenge
Cancer incidence in 2022 in (millions).
Patients needing radiotherapy in 2022 (millions).
Cancer incidence in 2025 (millions).
Patients needing radiotherapy in 2025 (millions).
The Lancet Global Health 2024 12e1945-e1953DOI: (10.1016/S2214-109X(24)00355-3)

## Slide 5: Radiotherapy; the challenge
Scale-up in provision essential:
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new techniques; and
  Cost-effective system integration
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 6: Hadron beams for radiation therapy
Wilson, then at Harvard designing 150 MeV cyclotron:
  Identified benefits and properties of proton beams for RT
  Pointed out potential of ions (carbon) and electrons
Robert R. Wilson
Radiology 47:48a7–91 (1946)

## Slide 7: Evolving state of the art
Cyclotron
Laurence; 1932
Synchrotron
Goward, Barnes; 1946
Biological studies; 1948
Clinical studies (pituitary gland);
1954
Cancer therapy
(Mass Gen Hosp)
1974

## Slide 8: Particle beam therapy today
Cyclotron based:
  Limitations:
    Energy modulation
    Instantaneous dose rate
Synchrotron based:
  Limitiations:
    Complexity
    Instantaneous dose rate
Christie Hospital, Manchester
MedAustron, Austria
 reduce footprint, cost and complexity
‘PBT for the many’!
 increase flexibility
optimise treatments
8

## Slide 9: Particle beam therapy today
 Increase automation, monitor motion
‘shoot on demand’!
 increase throughput reduce cost/treatment

## Slide 10
The LhARA initiative:
Deliver a systematic and definitive radiation biology programme
Prove the feasibility of laser-driven hybrid acceleration
  Spin into curiosity-driven science
Lay the foundations for the transformation of ion beam therapy
  automated, patient-specific proton and ion beam therapy
10

## Slide 11: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno therapies
Multidisciplinary approach essential

## Slide 13
Dual-view Oblique Plane Microscopy
https://mach3cancer.org/news/

## Slide 14: Specifications
DOI: 10.5286/stfctr.2026007
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u

## Slide 15: Source
R&D objectives:
  Tests: building to LhARA specification
    Diagnostics and target development
    High-rep rate, automation/longevity studies
    Numerical modelling 3D simulation codes
SCAPA

## Slide 16: Plasma (Gabor) lens
Electron plasma:
  Created through ionisation of CO2 by “seed” electrons
Confined in
  Penning-Malmberg trap

## Slide 17: Plasma lens; status
Plasma-trap beam line at University of Swansea

## Slide 18: Rapid, flexible acceleration for stage 2
Fixed-field alternating-gradient accelerator (FFA):
  Compact, flexible solution:
    Multiple ion species
    Variable energy extraction
    High repetition rate
      Rapid acceleration
    Large acceptance
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738
LhARA FFA
10 cells
2 MA loaded RF cavities

## Slide 19: Dose mapping in real time: ion-acoustic imaging
LION @ CALA

## Slide 20: Three pillars
Science:
radiobiology
LhARA, the project
Co-creation;
science for growth

## Slide 21: PoPLaR at SCAPA (Strathclyde) [Nov26]
First irradiations:
  Cell survival rates
  Compare to cyclotron
  Promising results!
Capture with 2 PMQs
RCF stack for dose estimation

## Slide 22: The LhARA initiative
2026/27
2028 …
2030 …
2035 …
2040 ..
Preparation
Proposals:
Establish R&D
R&D:
Stage 1
Project:
Stage 2
Project:
Stage 3
Ambition:
EU: MCSA
UKRI: TBD
IS-8+ Bucket 2
...
Business case
Radiobiology
Laser/accel.
Science,
Industrial partnership
End station
Interpretation
Staged build & operation of laser-hybrid source serving low-energy in-vitro end station
Staged build & operation of boosted beam serving high-energy in-vitro and in-vivo end stations
LhARA facility: radiobiology
Co-creation of laser-hybrid system for the clinic

## Slide 23
Opportunity, through the LhARA initiative:
Deliver a systematic and definitive radiation biology programme
Prove the feasibility of laser-driven hybrid acceleration
  Spin into curiosity-driven science
Lay the foundations for the transformation of ion beam therapy
  automated, patient-specific proton and ion beam therapy