## Slide 1: Deuterated Liquid Scintillator for Low-Energy Neutron Measurements in Nuclear Astrophysics
Rhys Bonnell
University of Edinburgh
https://www.erc-nuclear.uk​

## Slide 2
Skype meeting | 17 July 2014
The Chemical Evolution of the Universe (in a Nutshell)
Big Bang Nucleosynthesis
3-20 min after BB
how do we breakout from BBN to synthesise CNO elements and beyond?

## Slide 3: Measurements at LUNA
N
Z
~ 1400 m
(3800 m.w.e.)
LUNA 1
50 kV
(1991-2001)
LUNA400
400 kV
(2000 → present)
Bellotti IBF
(2023  present)
Cosmic ray attenuation: μ → 10-6
n → 10-3
LUNA400 Facility:
400keV accelerator
H+ and He+ beams
I = 200 – 300 uA
DE = 100 eV
Goal:
Measure a+10B reactions down to lowest feasible energies
3

## Slide 4: 10B(a,n)13N reaction measurement
Measured this year via activation technique (integrated - 𝜎)
Previous measurements via Liu et al (2020)[1] measured at 0-degrees (Differential - )
We plan to measure directly at 0 and 90 degrees with EJ-301D detector
BGO 6
BGO 1
BGO 5
BGO 2
BGO 4
BGO 3
511keV
511keV
LUNA BGO no shielding
EJ-301D
Target Holder
10B(a,n)13N
Q = 1.054 MeV
10B+a
13N+n
13C (+n)
14N
b+
Sa = 11.612 MeV
11510 keV
11680 keV
[1] Q. LIU et al. PHYSICAL REVIEW C 101, 025808 (2020)

## Slide 5: What issues do we face with direct neutron detection?
Solid targets of enriched Boron-10 (10B4​C ) on tantalum
Targets contain 11B and 13C
These generate neutrons through (α,n) reactions of varying energies
  11B(a,n)14N: Q-Value = 158 keV
  13C(a,n)16O: Q-Value = 2215 keV
  10B(a,n)13N: Q-Value = 1059 keV
Moderated 3He Counters can be, and are, used for (a,n) reaction due to high efficiency but no energy information
13C(a,n)16O – 3He counter set up at LUNA
Csedreki et al Nuclear Inst. and Methods in Physics Research, A 994 (2021) 165081
10B4​C Target

## Slide 6: What is EJ-301D?
EJ-301D
Liquid Scintillator
  p-Xylene-d10: 85-96%
  Naphthalene-d8: 5-15%
  C:D ratio => 1:1.2
p-Xylene-d10
https://eljentechnology.com/products/liquid-scintillators/liquid-scintillator-cells

## Slide 7: Pulse Shape Discrimination
Neutrons
Gammas
PSD of AmBe Source
Neutron Light Output For AmBe Source

## Slide 8: Detector Response Matrix (DRM)
The DRM maps the light output to neutron energy
Obtained experimentally (Time of Flight using AmBe source, accelerator-based fast neutron production) or via simulations (e.g. MCNP…)
DRM Courtesy of University of Notre Dame

## Slide 9: Maximum Likelihood Expectation Maximization (MLEM)
The expected light output is compared to the experimental light output and the neutron spectrum estimate is adjusted
Liu et al. PRC 101, 025808 (2020)
M. Febbraro et al. NIM A989 164824 (2021)
Kanj et al. Radiation Measurements 176 107206(2024)
Becchetti et al. NIM A820 (2016) 112 and refs therein
From Liu et al. PRC 101, 025808 (2020)
From Liu et al. PRC 101, 025808 (2020)
From Liu et al. PRC 101, 025808 (2020)
MeV

## Slide 10: AmBe Results
Data Acquired over 1 hour with AmBe Source – low stats
https://r2e.web.cern.ch/about-radiation/test-facilities/ambe
PRELIMINARY

## Slide 11: Fast Neutron Background
Taken for 20.6 hours
LUNA400 accelerator hall
Longer measurement time needed
Not efficiency corrected
PRELIMINARY

## Slide 12: What reactions are dominant?
Half of the total (a,n) neutron production is from Mg, which only makes up 6% of the rock [2]
Sources: 25Mg(a,n)28Si (Q-Value = 2.65 MeV) + many other (a,n) reactions and neutrons from 238U and 232Th
Or potential Alpha Contamination in detector
PRELIMINARY
[2] H. Wulandari et al. / Astroparticle Physics 22 (2004) 313–322
[2]
[2]

## Slide 13: 10B(a,n)13N Result
10B(a,n)13N
13C(a,n)16O ?
4He+ = 400 keV on a 10B4C target
Expected 10B(a,n)13N = 1.35 MeV
Not efficiency corrected
PRELIMINARY

## Slide 14: The future use of the EJ-301D Scintillator
October 2026 LUNA
  10B(a,n)13N Measurement at LUNA
  (0 and 90 degrees)
  Further Background measurements
Ongoing at Edinburgh - Time of Flight set up for neutron energy tagging
  Improvement to DRM via improved resolution
    Detector specific DRM
  Testing of new unfolding procedures
    Event by Event and Bayesian Neural Network
EJ-301D
EJ-301D
Planned LUNA-setup

## Slide 15
THE LUNA COLLABORATION
http://luna.lngs.infn.it
M. Wiescher, J. deBoer, V. Picciotto,
K. Manukyan, M. Sorensen
+ local staff and students
https://www.erc-nuclear.uk
Contact: R.Bonnell@sms.ed.ac.uk
Special Thank to M. Febbraro
PI: Prof. Marialuisa Aliotta
R. Bonnell, P. Black, S. Baltaci,
A. Compagnucci, L. Dalla Vedova,
T. Davinson

## Slide 16: Extra Slides

## Slide 17: EJ-301D Efficiency
Computed using Monte Carlo N-Particle (MCNP) code
Derived from the kinetic energy transferred exclusively to deuterium nuclei
Applied a low-energy cutoff (≈100 keVee) mapping to the experimental light output limits
Incorporated neutron scattering and absorption by carbon atoms to reflect true in-volume physics

## Slide 18: Light Output to neutron energy through Maximum Likelihood Expectation Maximization
For a neutron spectrum estimate of iteration the expected light output is obtained using the DRM
The expected light output is compared to the experimental light output and the neutron spectrum estimate is adjusted
To prevent over fitting to noise the residual is calculated
If either criteria is met the fitting is stopped and the resulting neutron spectra is outputted
Criteria not met
Monte Carlo sampling done to obtain neutron spectra error
Criteria met