## Slide 1: ISIS-II Neutron Targets Baseline:
Daniel Wells Calvo, Dan Wilcox, Peter Loveridge, Lina Quintieri
High Power Targets Group
STFC - ISIS II Project
ISIS-II Artist Render, provisional.

## Slide 2: Contents:
Facility Baseline
TS-II Static Target Design.
  Static target thermal gradient optimising.
Rotating Target Size Considerations:
  Pulse Timing
  Rotating Kinetic Energy.
  Compact radius targets
  Comparison.
Conclusions
Discussion

## Slide 3: ISIS-II Baseline
Courtesy of D. Wilcox
TS-II at 0.8 MW (15 Hz), static target proposed
  Ok for direct beam
  Very close to limit for decay heat
TS-I at 1.6 MW (30 Hz), rotating target required.
Rotating target is required to manage both decay heat & direct beam.
Preference for compact wheel for ease of manufacture and remote handling.
All limits and studies performed with 1.2 GeV beam
Notes: ISIS-II, the proposed successor to the UK’s pulsed neutron and muon source, has been baselined with two newly-designed spallation targets [1]: A 0.8 MW high-brightness stationary target (TS-II), and a 1.6 MW, high-resolution rotating target (TS-I).
The initial design study highlighted decay heat as the key limiting factor for the stationary target and rotational inertia or complexity for the rotating target. A combination of numerical models and theoretical calculations were employed to assure design reliability and to compare with existing international facilities.

## Slide 4: TS-II static target design:
Courtesy of D. Wilcox
2 coolant fluids under consideration:
D2O cooling (with Ta cladding) has been successfully used for current ISIS TS1:
  Max of 14 plates (cladding limits max plate count).
  Ta decay heat limits achievable power to ~200 kW.
Helium (He) cooled alternative - no cladding required:
  More plates required as heat transfer coeff. is lower
  Power limit is W material decay heat
TS-II at 0.8 MW (15 Hz), static target proposed.
Ok for direct beam
Very close to limit for decay heat
Chart: ISIS II TS-II: Max Power Against Number of plates
| 10 | 12 | 14 | 20
1 Bar | 101.2937 | 118.537 | 137.735 | 206.5421
5 Bar | 195.7735 | 238.0618 | 296.046 | 493.779
10 Bar | 247.8645 | 324.5957 | 400.4 | 693.9112
Water Cooling | 344.8125 | 462.3166 | 616.0467
Max achievable power (with stress as the only limiting factor) for different coolants and plate counts.
Higher He
Pressure (bare W)
D2O coolant (Ta-clad W)

## Slide 5: TS-II static target design:
Current ISIS (D2O cooled) | TS-1 | TS-2
Plates | 10 | 1
W Mass (kg) | 60 | 15
Peak Power (kW) | 128 | 32
Avg Power Density (kW/kg) | 2.1 | 2.1
ISIS II TS-II Targets | D2O Cooled | He Cooled
Plates | 14 | 23
W Mass (kg) | 140 | 140
Power (stress limit) (kW) | 621 | 800
Avg Power Density (kW/kg) | 4.4 | 5.7
Heat Decay limit (kW) | 250 | 800
2 coolant fluids under consideration:
D2O cooling (with Ta cladding) has been successfully used for current ISIS TS1:
  Max of 14 plates (cladding limits max plate count).
  Ta decay heat limits achievable power to ~200 kW.
Helium (He) cooled alternative - no cladding required:
  More plates required as heat transfer coeff. is lower
  Power limit is W material decay heat

## Slide 6: Static target thermal gradient optimising:
Narrower (in height) cooling channels: concentrate cooling on core, reducing thermal gradient and stress, thus fewer plates/cooling channels required.
  Power increase allowed = +36%.
  Requires complex manifold to reduce height of each channel.
Fluid (CFX) simulations of 14 plate target, top view.
Fluid (CFX) simulations of a target's top half, highlighting example of flow concentration.

## Slide 7: Static target thermal gradient optimising:
Super-Gaussian (“flat top”) beams improve achievable heat distribution with less intrusive methods (to the neutron generation).
Allowable beam power increased by 63% due to lower stresses.
Neutronic studies (L. Quintieri & G. Skoros) pointed at a low 10% loss in brightness.
Gaussian Profile
Super-Gaussian Profile
Possible Beam power (DW)

## Slide 8
Impact of the “2-out-of-3” pulse structure 45Hz pulse repetition rate, but every third pulse is missing!
4-segment wheel rotating at 675 rpm
6-segment wheel rotating at 450 rpm
YES!
NO!
Courtesy of P. Loveridge
Accelerator runs at 45Hz, TS-I receives 2/3 pulses
After every two TS-I pulses, there is a “gap” with no pulse (as the pulse is directed to TS-II).
  “Bow-tie” target option leaves space for 2 not installed segments (total of 6).
  This lowers the rpm and kinetic energy but requires accurate wheel positioning.

## Slide 9
Rotating target size considerations:
High frequency, low segment count requires high target rpm.
  Kinetic energy higher than ESS or SNS STS target wheels, but lower than neutron choppers e.g. FREIA
  Mechanical stability and pulse timing will be further studied.
FREIA Chopper (ESS)
Cross target
8-target
Bow tie-target
Studied Concepts (1.6 MW)
ESS (5 MW)
SNS (0.7 MW)
Kinetic Energy of Rotating Targets
Pursuit of a compact wheel driven by ease of manufacture, remote handling and disposal.
  Use trolley exchange system like current ISIS if possible
Notes: This target will be D2O cooled (to avoid rotating He seals), requiring cladding. Alternative cladding or low thickness options will be studied.

## Slide 10
Rotating target size considerations:
Studied the influence of common central blocks to reduce diameter and mass at high segment counts beam overlaps (see right pictures) higher heat & stresses
  Increased stresses from overlapping heat deposition remains near limit (150 MPa) with more channels.
Reduced overlap, but still challenging to manufacture
Preferred option: compact diameter but minimal overlap
8x closely overlapping segments: high heat at centre
Courtesy of D. Wilcox

## Slide 11: Rotating Target Options for 1.6MW, 30/45Hz
Courtesy of D. Wilcox
 | Compact 4-Way Cross | Compact 4-Way “Bow Tie” | 8-Segment “SNS-like” Wheel
Manufacturability | Manufactured as a single unit. ~8x mass of TS1 Project Target. | Comparable mass to 4-way cross. Cooling path may be slightly more complex. | ~2.5x mass of 4-way cross. Recommended to have individually replaceable segments.
Ease of remote handling | Lightest and most compact. | Similar mass and diameter to 4-way cross. | Heavy, large diameter. May require complex SNS-like scheme for replacing individual segments.
Direct beam dissipation | 400kW per segment, which should be readily achievable. | 400kW per segment, which should be readily achievable. | 200kW per segment. Gives extra margin to reduce number of plates or dimensions of target.
Decay heat dissipation | Expected to be close to limit, may require alternative cladding materials or other modifications. | Expected to be close to limit, may require alternative cladding materials or other modifications. | 2x better than 4-segment options. Awaiting full neutronic simulation, but not expected to be an issue.
Rotating kinetic energy | High due to rapid rotation, but partly mitigated by compact diameter. | ~2x lower than 4-way cross. Still higher than ESS or SNS. | Higher than 4-way cross, unless central blocks can be overlapped to a large extent.

## Slide 12: Conclusions:
Stationary TS-II target can reach 0.8 MW with 10 Bar He coolant or ~1/2 of this with D2O (limited by decay heat in Ta cladding).
  Decay heat power limit can be increased with high emissivity black painted reflectors and target, improving passive cooling.
  Super-Gaussian beam profile proposed for both targets, to better distribute direct beam and decay heat
To reach a power level of 1.6 MW, TS-I requires a rotating target.
  Compact wheel with few segments preferred for ease of manufacture, remote handling and disposal.
  4-8 segments should be sufficient to achieve ~1.6 MW without surpassing direct stress or decay heat limits
Be/Pb reflector between targets.
Target Wheel Housing
Shaft with concentric in/out D2O flow.
(ID & OD = 125 – 200 mm each)
316L steel pressure vessel
W target plates
  4-segment target wheel concept

## Slide 13: Future Work (Pending funding):
Consider alternative cladding methods to mitigate high decay heat from tantalum
  Cladding alternatives: HIPed Ta 1.5 mm (baseline) to 0.3 mm (min); Ta with few % W; Zircaloy with Ta or V interlayer; CVD thin Ta; Nb (waste management issues?).
  Canning (unbonded cladding): Inconel; Stainless or ODS steel; high entropy alloys.
Study mechanical and motion effects of rotating wheel targets.
Detailed heat decay studies and neutronic performance of rotating wheel.

## Slide 14: References:
//te0dfs01.te.rl.ac.uk/groups/HPTshr/Papers/Target_Design_Papers/SNS/S03020000-DES1000,%20Design%20Description,%20Target%20Assembly.pdf
\\TE0DFS01\projectsHPT\Workshops_Conferences\2024-09-RaDIATE_Granada\Tue\1610_Challenges_and_opportunities_for_the_thermal_interface_selection_and_diffusion_bonding_in_the_STS_target_segment
//te0dfs01/projectsHPT/Workshops_Conferences/2023_HPTW_Japan/Monday/Topic1/1645_Design_of_Rotating_Tungsten_Target_with_Segmented_Modules_for_Replacement/PRES-ORNL-23-11-4%20HPTW%20Current%20Status%20of%20the%20STS%20target%20Segment%20&%20Analysis.pdf
(S.Peggs et al, 2013)
  //te0dfs01.te.rl.ac.uk/groups/HPTshr/Papers/Target_Design_Papers/ESS/ESS_TDR_final_130423_blue.pdf
S. Fedorenko, 2024
  \\te0dfs01.te.rl.ac.uk\projectsHPT\ISIS\ISIS-II\ISIS_II_NeutronTarget\reports
  Recommended Vessel Geometry states it might weigh 16.8 kg.

## Slide 16: Static Target Limits
Decay heat is the limiting factor in every case
  Decay heat limit driven by need to keep tungsten below 800°C in LOCA
    Best case decay heat scenario assumes mitigation measures can be guaranteed to work. This may include high-emissivity coatings, backup cooling systems, and other novel technologies not in use at other accelerator facilities.
    Worst case decay heat scenario assumes no changes to current technology
    Both scenarios include total loss of void vessel helium (conservative), but use FLUKA rather than MCNPX (optimistic, but supported by TS1 experiment)
Power limits for static target (MW) | Super-Gaussian beam profile |  | 
 | Direct beam | Decay heat (best case) | Decay heat (worst case)
Ta-clad W, water cooled | 0.8 | 0.4 | 0.2
Bare W, He cooled | 1 | 0.8 | 0.4

## Slide 17: Mass Moment of Inertia Estimates:
ESS provided value: 5,730 kgm2.
  Equation for hollow cylinder (wheel and shaft):
  ESS wheel mass = 4,868 kg
    Wheel dimensions = 2500x1500 (outer, inner diameters).
  Entire shaft mass = 12,156 kg
    Shaft dimensions = 700x640 (outer, inner diameters).
Results using components and equation = 5,730.9 kgm2.
  Method is useful to estimate SNS and others with same process.
SNS shaft weight (provided by SNS documents) of 1,700 kg, used for SNS inertia estimate, as well as for ISIS II concepts estimates. (An over estimation for a worst-case scenario picture).

## Slide 18: Bending Stresses Methodology:
Chose simply supported scenario as most other scenarios required a fully fixed surface or 2 contiguous free surfaces.
q corresponds to the pressure: Force/Area. b is the height of the plate (106 mm) and t the thickness (11.4 mm). The ‘a’ value is the width (212 mm) of the plate.
Extract from Roark’s Book of stresses and formulas.

## Slide 19: Key Rotating Metrics:
Key Rotating Metrics | Equation | Cross Target | 4/6 Cross | 8 Target | ESS | STS SNS | ISIS TS1 | ESS Freia Chopper
Segments | - | 4 | 4 | 8 | 36 | 21 | 1 | 1
Beam Frequency (Hz) | - | 45 | 45 | 45 | 14 | 15 | 40 | 11
Rotation Speed (rpm) | - | 675 | 450 | 338 | 26 | 43 | 0 | 3360
Mass of wheel (Kg) | - | 620 | 665 | 1,402 | 4,868 | 4,728 | 119 | 20
(mm) | - | 700 | 700 | 950 | 2,500 | 1,166 | 350 | 1,300
(mm) | - | 0.00 | 0.00 | 250 | 960 | 415 | n/a | 0
Rotational Moment of Inertia (kg*m2) |  | 45 | 47 | 162 | 5,731 | 1412 | n/a | 4.2
Rotational Kinetic Energy (kJ) |  | 112 | 53 | 101 | 20 | 14 | n/a | 262
Power (MW) | - | 1.6 |  |  | 5 | 0.7 | 0.16 | 5
Equivalent Ford Fiesta Speed (km/h) | - | 54 | 37 | 51 | 23 | 19 | n/a | 82
1st Plate Considerations and forces: |  |  |  |  |  |  |  | 
Centrifugal Force/segment (kN) |  | 122 | 54 | 48 | 1 | 2 | n/a | 805
Centrifugal Force 1st Plate (kN) |  | 8 | 3.7 | 3 | 3.0e-5 | 1.4e-2 | n/a | n/a
Acceleration 1st plate (G) |  | 178 | 79 | 61 | ~1 | ~1 | n/a | 8,203
Bending Stress 1st plate (MPa) |  | 21 | 9 | 7 | 1.5e-3 | ~0.1 | n/a | n/a
Beam Spot Movement During Pulse Length |  |  |  |  |  |  |  | 
Arc Travelled/pulse () |  | 12.4 | 8.2 | 8.4 | 6,108.7 | 2.0 | n/a | n/a
Key Rotating Metrics | Equation | Cross Target | 4/6 Cross | 8 Target | ESS | STS SNS | ISIS TS1 | ESS Freia Chopper
Segments | - | 4 | 4 | 8 | 36 | 21 | 1 | 1
Beam Frequency (Hz) | - | 45 | 45 | 45 | 14 | 15 | 40 | 11
Rotation Speed (rpm) | - | 675 | 450 | 338 | 26 | 43 | 0 | 3360
Mass of wheel (Kg) | - | 620 | 665 | 1,402 | 4,868 | 4,728 | 119 | 20
 | - | 700 | 700 | 950 | 2,500 | 1,166 | 350 | 1,300
 | - | 0.00 | 0.00 | 250 | 960 | 415 | n/a | 0
Rotational Moment of Inertia (kg*m2) |  | 45 | 47 | 162 | 5,731 | 1412 | n/a | 4.2
Rotational Kinetic Energy (kJ) |  | 112 | 53 | 101 | 20 | 14 | n/a | 262
Power (MW) | - | 1.6 |  |  | 5 | 0.7 | 0.16 | 5
Equivalent Ford Fiesta Speed (km/h) | - | 54 | 37 | 51 | 23 | 19 | n/a | 82
1st Plate Considerations and forces: |  |  |  |  |  |  |  | 
Centrifugal Force/segment (kN) |  | 122 | 54 | 48 | 1 | 2 | n/a | 805
Centrifugal Force 1st Plate (kN) |  | 8 | 3.7 | 3 | 3.0e-5 | 1.4e-2 | n/a | n/a
Acceleration 1st plate (G) |  | 178 | 79 | 61 | ~1 | ~1 | n/a | 8,203
Bending Stress 1st plate (MPa) |  | 21 | 9 | 7 | 1.5e-3 | ~0.1 | n/a | n/a
Beam Spot Movement During Pulse Length |  |  |  |  |  |  |  | 
 |  | 12.4 | 8.2 | 8.4 | 6,108.7 | 2.0 | n/a | n/a
- Bending Stresses calculated using simply supported Roark Formula. See slide 18.
ESS arc travelled/pulse result of 2 ms pulse.
If ESS &/or SNS ran at 45 Hz, their KE would increase by 9x.
Notes: Size reduction is proven as a useful measure to half or divide by 4 the rotational KE.
Cross target and bowtie target are fully overlapped. 8 Segment target has 25 degree taper at back end.

## Slide 20: Key Dimensions Cross Target:
The shaft outer radius is ~100 mm.
  Distance front of target to back of reflector = 412 mm.
  Means wheel must be at least: (412+100)*2 = 1024 mm wide.
  350 mm long Target segments -> margin of: 62 mm*2 = 124 mm.
Port holes do not see any obstruction by shaft.

## Slide 21: Neutron Port Clearance:
Concerns about rotational energy = incentive to reduce diameter = question about shaft – neutron port clearance.
Distance of shaft to port ~ 75 mm. Possibility to reduce diameter dependant on thickness margin to decoupler.
Top
Top
Bottom
Bottom
Wheel Diameters = 700 mm & 912 mm respectively.
Notes: 77.8 mm to be exact

## Slide 22: 4 out of 6 Target extra images

## Slide 23: 8 Segment Target (In Progress):

## Slide 24: International Rotating Wheel Targets:
ESS rotating Wheel
SNS STS rotating Wheel
5 MW
36 Segments
He Cooled
0.7 MW
21 Segments
Water Cooled

## Slide 25: Progress Stationary Target
Clear benefit to avoid cladding by using He cooling.
  Thermal shock concerns on bare W must be addressed.
Super Gaussian allows peak power without complex geometry changes improvements.
Possibility to increase volume fraction by reducing plate count.
Temperature Limit
Decay Heat Temperature limit depending on beam power(DW)

## Slide 26: More useful data

## Slide 27: Source for SNS Data:
Copper thickness = 1 mm top and bottom.
  Radiate 2024 Conference. \\te0dfs01.te.rl.ac.uk\projectsHPT\Workshops_Conferences\2024-09-RaDIATE_Granada\Tue\1610_Challenges_and_opportunities_for_the_thermal_interface_selection_and_diffusion_bonding_in_the_STS_target_segment
Shaft weight and height of wheel (78 mm. 58 mm of W).
  SPALLATION NEUTRON SOURCE SECOND TARGET STATION CONCEPTUAL DESIGN REPORT VOLUME 1: OVERVIEW, TECHNICAL AND EXPERIMENT SYSTEMS

## Slide 28: Source for ESS Data:
ESS Technical Design Report (23/04/2013):
ESS_TDR_final_130423_blue.pdf
An evaluation of activation and radiation damage effects for the European Spallation Source Target
  Full article: An evaluation of activation and radiation damage effects for the European Spallation Source Target