## Slide 1
Radiobiology research using laser-driven ions: Experimental workflow and infrastructure requirements
Professor Jason Parsons
Department of Cancer and Genomic Sciences
School of Physics and Astronomy
j.parsons.3@bham.ac.uk

## Slide 2
Typical cell models and growth formats
Patient-derived organoids
Tumours grown in chick embryo model
2D monolayer cells
Each organoid is ~10-1000 µm in size
Tumour is ~2-3 mm in size
Each cell is ~20 µm in size
Each spheroid is ~50-500 µm in size
 | 6-well | 12-well | 24-well | 48-well | 96-well
Diameter (mm) | 35.43 | 22.73 | 16.26 | 11.56 | 6.86/ 6.35
Area (cm2) | 9.5 | 3.83 | 1.93 | 0.95 | 0.32
Thickness (mm) | 1.27 | 1.27 | 1.27 | 1.27 | 1.27
Elevation (mm) | 2.54 | 2.16 | 2.54 | 2.87 | 3.55
  Multi-well plates (127 mm x 85.5)
1000 µm
25 or 75 cm2 surface area
3D spheroids

## Slide 3
Clonogenic assays for analysis of cell sensitivity
Cells as a monolayer
Irradiate, count and seed into individual colonies
Allow colonies to grow for 7-14 days
Fix, stain and count colonies
Trypsinise cells and plate as single colonies
Irradiate colonies
Clonogenic assays is a measurement of the ability of single cells to grow and divide into colonies.
This is the gold standard technique for radiobiology.

## Slide 4
Typical clonogenic assay protocol
Equipment
Class II safety cabinet
A radiobiologist or two!
Hypoxia workstation
(different oxygen tensions)
CO2 incubator
Schedule
A week in advance – cells need to be growing well and are healthy.
Day 1 - Seed cells into the appropriate dishes/plates and leave to settle for 24-48 hours.
Day 3 – Prepare cells for irradiation (e.g. seal dishes/plates from air; assemble into holding platform).
– After irradiation, cells would be harvested, counted and plated (~1 h).
– Allow colonies to grow for 7-14 days.
Day 10-17 – Colonies are stained and can be counted (offsite).
A single experiment (one cell line, 4 radiation doses, triplicate samples) may involve ~50 irradiations.
Notes

## Slide 5
Radiobiology setup at SCAPA
Internal diameter – 18.5 mm
Outer diameter – 22.5 mm
Chart: Dose (Gy)
| 0 | 1 | 2 | 4
ED | 1 | 0.67846 | 0.67819 | 0.3889
3.5mm | 1 | 0.7449 | 0.56597 | 0.3475
4mm | 1 | 0.62006 | 0.46637 | 0.309
4.5mm | 1 | 0.61365 | 0.4409 | 0.25077
Survival curves as a function of dose

## Slide 6
  No-IR
  No-IR
  1 Gy
  2 Gy
  Day 10
  Day 3
  UMSCC74A
  UMSCC6
1000 µm
Chart: Day post-seeding
| 3 | 5 | 8 | 10 | 12 | 15
Unirradiated | 0.68455 | 2.892 | 5.5154 | 7.4454 | 7.8132 | 8.3521
1 Gy | 0.68704 | 2.1897 | 2.9857 | 4.2025 | 6.2382 | 6.4824
2 Gy | 0.63887 | 1.9166 | 2.1422 | 3.0243 | 3.8856 | 5.0537
5 Gy | 0.67744 | 1.755 | 1.8187 | 1.8002 | 1.8361 | 1.8768
Spheroid growth data
Spheroids are advantageous as they recapitulate 3D tumour structure.
However, spheroids grow in 96 well plates (generally round bottom, plastic is ~1.5 mm thick but tapered).
Spheroids are also free floating in the media (challenging for energy/LET targeting).
Notes
800 µm
Similar protocol for patient-derived organoids, although these usually fixed in a matrix to the bottom of the plate (easier for energy/LET).

## Slide 7
Typical spheroid growth assay protocol
Equipment
Class II safety cabinet
A radiobiologist or two!
CO2 incubator
Imaging microscope
Schedule
A week in advance – cells need to be growing well and are healthy.
Day 1 - Seed cells into 96 well plates and leave to settle for 48 hours for spheroids to form.
Day 3 – Prepare cells for irradiation (e.g. seal dishes/plates from air; assemble into holding platform)
– Allow spheroids to grow for 14-21 days.
Days 3-24 – Capture images of spheroids every 2-3 days (could be done offsite).
A single experiment (one cell line, 4 radiation doses, triplicate samples) may involve ~50 irradiations.
Notes

## Slide 8
Analysis of DNA damage: gH2AX foci as a surrogate DNA double strand break (DSB) marker
Control
1
4
Hours post-IR (4 Gy)
Each gH2AX foci corresponds to the site of a DSB.
Can also use other markers of DNA damage (53BP1, RAD51, OGG1) giving information on DNA repair pathway dependence.
UMSCC74A head and neck cancer cells

## Slide 9
Typical immunofluorescent staining protocol
Equipment
Class II safety cabinet
A radiobiologist or two!
CO2 incubator
Fluorescent microscope
Schedule
A week in advance – cells need to be growing well and are healthy.
Day 1 - Seed cells onto 0.1 mm glass coverslips placed within plates/dishes and leave to settle for 24-48 hours.
Day 3 – Prepare cells for irradiation (e.g. seal dishes/plates from air; assemble into holding platform).
– Allow cells to repair for 1-48 hours, fix at these different times (e.g. formalin).
Days 5 – process using antibodies (usually takes 2 days).
– Alternatively, cells can be moved offsite and processed.
Coverslips can be replaced and cells irradiated as normal, although another piece of equipment (Cytospin) is needed to mount cells on microscope slides.
A single experiment (one cell line, single radiation doses, 4 time points, triplicate samples) may involve ~50 irradiations.
Notes

## Slide 10
Comet assay used to measure the efficiency of DNA repair in individual cells
Control
240 min
UMSCC6
0 min
UMSCC74A
UMSCC47
UPCI-SCC090
Nickson et al (2017) Oncotarget
Chart: min post-IR
| Control | 0 | 60 | 120 | 240
UMSCC6 | 0.061265 | 1 | 0.60297 | 0.25389 | 0.060781
UMSCC74A | 0.042899 | 1 | 0.63909 | 0.36324 | 0.058959
UMSCC47 | 0.08603 | 1 | 0.60017 | 0.49933 | 0.39197
UPCI-SCC090 | 0.062363 | 1 | 0.96342 | 0.74221 | 0.44351
*
*
**
***
*
HPV-negative (UMSCC6, UMSCC74A)
HPV-positive (UMSCC47, UPCI-SCC090)
4 Gy x-rays

## Slide 11
Cells in culture
Microscope slide
Cells embedded in agarose
Electrophoresis
DNA stained with SYBR Gold
Analysis using fluorescent microscope and Komet software
Lysis of cells
+
-
Current
Measures DNA strand breaks and/or alkali-labile sites within single cells
The Comet Assay
DNA damage treatment
1 % agarose added to cells
Nickson and Parsons (2014) Front Genet

## Slide 12
Typical comet assay protocol
Equipment
Class II safety cabinet
A radiobiologist or two!
CO2 incubator
Schedule
A week in advance – cells need to be growing well and are healthy.
Day 1 - Seed cells into the appropriate dishes/plates and leave to settle for 24-48 hours.
Day 3 – Prepare cells for irradiation (e.g. seal dishes/plates from air; assemble into holding platform).
– Collect cells at different time points for 1-24 hours.
Days 4 – Process cells onto slides, lyse cells and electrophorese DNA (usually takes 1.5 days).
After these steps, the analysis/processing can be done offsite.
Comet assay equipment
A single experiment (one cell line, 4 radiation doses, triplicate samples) may involve ~50 irradiations.
Notes

## Slide 13
The chick embryo tumour model
Day 0
Day 3
Window
Day 7
Implant cells
Day 10
Drug
Day 11
Irradiate
Dissect
Day 14
Very good preclinical tumour model (3Rs).
Needs specialist laboratory, equipment and technical expertise.
Chick embryos are very sensitive to the environment (~30 % embryos survival from start to finish).
Very labour intensive (needing ~2-3 million tumour cells per implant).
Notes

## Slide 14
Take home messages
Key equipment needed (class II safety cabinet, CO2 incubators, pipettes, pipette fillers, plastic consumables etc).
Key infrastructure needed (CO2 for incubators, CO2/N2/compressed air for hypoxia workstations, bench area, sink).
Waste disposal (generating biological waste that needs specialist route).
Some techniques are time intensive, needing dedicated space in class II safety cabinet (ideally need multiple), and/or bench space.