## Slide 1
Katsuya Yonehara
NBI 2022, Abingdon, UK
September 19, 2022
Recent Fermilab Neutrino beam operations
(Booster Neutrino Beam and Neutrinos at the Main Injector)

## Slide 2: Fermilab Accelerator Complex and Neutrino lines
Tevatron (collider program) shut down in 2011
Proton-Improvement-Plan (PIP) has begun since 2011 to reprogram 8 GeV proton beam system for Muon campus (g-2 & Mu2e) and Booster Neutrino Beamline (BNB), and 120 GeV/c proton beam system for NuMI and Fermilab Test Beam Facility
Refurbish Linac and Booster for 15 Hz beam operation
Reoptimize Recycler ring and Main Injector
Accelerator Improvement Plan (AIP) issued since 2018 and ended 2022
Present available proton beam power 30 kW for BNB & 900 kW for NOvA

## Slide 3: Booster Neutrino Beam (Utilize 8 GeV protons)
Up to ~30 kW of beam (5e12 ppp)
Anticipate to complete run in FY27
  Future running TBD
Chart: Protons Delivered BNB
| FY2017 | FY2018 | FY2019 | FY2020 | FY2021 | FY2022
desgin | 4.3e+20 | 3.25e+20 | 3.5e+20 | 2.9e+20 | 2.9e+20 | 3.45e+20
delivered | 3.3e+20 | 3.25e+20 | 3.65e+20 | 1.95e+20 | 2.15e+20 | 3.24e+20
base | 3e+20 | 2.15e+20 | 2.45e+20 | 1.8e+20 | 1.95e+20 | 2.4e+20
Phys.Rev.D 105 (2022)
11, 112005
M.Ross-Lonergan

## Slide 4: LArTPC detectors in BNB
Physics data with full CRT
begun June 2022
Collected data from 2015 to 2020
Largest sample of n in LAr
Start from late 2023
SBND-PRISM similar as DUNE ND
M.Ross-Lonergan

## Slide 5
Low-energy excess researches and other exotic BSM physics
Improving our understanding n-Ar interactions
LArTPC hardware and software R&D
M.Ross-Lonergan

## Slide 6: BNB target system
Two target/horn assemblies have been replaced (water)
  2nd horn lasted ten years and > 400M pulses Design lifetime was about one year and 100M pulses
  Requires to redesign and replace adjustor platform and horn extraction mechanism (corrosion)
3rd horn installed 2015 –still operating
4th horn complete and tested, undergoing minor upgrades
5th horn fabrication in progress
8 GeV proton beam

## Slide 7: BNB Upgrades
Complete
  Horn Charging Supply has been upgraded to charge at 20 Hz, in anticipation of PIP-II era.
  Average repetition rate will remain at 5 Hz. Limit is joule heating in stripline.
  Protons limits (per pulse, hourly, yearly) have not been revised. This would require a detailed study of the target.
In progress
  “New” target multiwire
    1st wire worked well, 2nd and 3rd gens did not work well, thus it is back to the original design
  Remote disconnect for target BPM cables
    New design includes a “carrier pipe” for coax connecting BPM to front-plate of horn box. Allows for replacement of entire coax assembly.
T. Kobilarcik

## Slide 8: NuMI Neutrino Beam to NOvA (utilize 120 GeV/c p)
NuMI (Neutrinos at the Main Injector) provides a high-quality neutrino beam to the NOvA (NuMI Off-axis ne Appearance) Near/Far Detectors (ND/FD)
Mission is creating high statistic and low systematic accelerator neutrino events in NOvA ND/FD
Anticipate to operate until FY27
K. ENGMAN/SCIENCE 345, 6204
J. Wolcott, FNAL JETP Seminar Sept. 18, 2020

## Slide 9: NOvA Neutrino Detectors
Same type of detectors used at ND and FD to mitigate systematics for oscillation measurements
ND also contributes to study the two nm CC X-section measurement
J. Wolcott

## Slide 10: NuMI Accelerator Improvement Plan
Main injector
Target
Absorber
Layout of NuMI target system
NuMI beam parameter
Present target goal
Present NuMI beam record 895 kW in July 2022

## Slide 11: Integrated POT
400 kW
700 kW
900+ kW

## Slide 12: After 2013 Upgrade
“COVID 19”
700 kW TARGET
900+ kW TARGET
MET02
(POT 1.18E21)
MET01
(POT 1.01E21)
MET03
(POT 0.56E21)
MET05
(POT 1.23E21)

## Slide 13: Inventory of NuMI target system
MET-05: Total POT 1.23e21 for 3-years operation, no issue
MET-06: Installed in the 2022 summer shutdown
MET-07: Fabrication in progress
PH1-03: Total POT 2.36e21 for 5-years operation, replaced in 2020 to upgrade 1-MW capable horn
PH1-04: spare, 700 kW capable
PH1-05: 1-MW horn using now, Total POT 1e21 for 2-years operation
PH1-06: spare
PH2-02: Total POT > 5e21 for 12-years operation, replaced in 2020 due to water leak
PH2-04: use now, total POT 1e21 for 2-years operation
PH2-03: spare

## Slide 14: 1-MW horn
Downstream end
Peak horn current 200 kA, 2.3 ms (half sin wave)
Convectional air flow on a stripline for 1-MW through air-diverter
Air diverter
Air flow
Beam

## Slide 15: Tune NuMI beam optics
Study 900+ kW beam lattice in the NuMI beam transport line
  Enlarge RMS beam spot size at the NuMI target from 1.2 to 1.4 mm to mitigate thermal impact on the system including target fin, pretarget Beryllium window, and DS Beryllium window
Beam position
Pretarget window
NuMI target
DS Be window

## Slide 16: NuMI beam transport line (from MI to Target)
Deliver 120 GeV/c protons from MI every 1.2 second by fast extraction
Each beam spill contains 6 batches in 10 msec
Maximum average beam power 896 kW (5.6e13 protons/spill)
Total length of the transport line is 360 m
  17 dipole magnets
  21 quadrupole magnets
  19 steering magnets
Beam directs downward by 58 mrad at the target

## Slide 17: NuMI beam transport line
Extraction
Bending downward by 156 mrad
Carrier tunnel
MI
NuMI
RR
Bending beam to the correct vertical angle 58 mrad
proton
proton
proton
proton

## Slide 18: Beam lattice
Matching
FODO
Collins insert
Final focusing
Matching: Match the beam into the straight line
FODO+Insert: Prepare beam for the final focusing
Final Focusing: Low dispersion and beta at the target

## Slide 19: Proposed optics (Simulation)
Quad current list (unit Amp)
Vertical b, Disp.
Horizontal b, Disp.
Red: Present
Blue: Option2
QF: Quadrupole Focusing in horizontal plane
QD: Quadrupole Defocusing in horizontal plane
Number: Location (bigger is closer to the NuMI target)
Option 1 is lower current strength but dispersion at the target is non-zero
Option 2 is higher current but dispersion at the target is close to zero

## Slide 20: Observed Horizontal Beam spot size at PM121 and PMTGT
PM121 (z=20 m)
PMTGT (z=10 m)
TGT (z=0 m)
beam
present
option 2
option 1
Horizontal beam spot size (mm)
PM121
PMTGT
Measurement shows that the beam spot size is enlarged with both options

## Slide 21: Observed Vertical Beam spot size at PM121 and PMTGT
present
option 2
option 1
Vertical beam spot size (mm)
PM121
PMTGT
Measurement shows that the beam spot size is enlarged with both options
Beam diverging larger with option 1 than option 2
option 2 is more preferrable than option 1

## Slide 22: Strategic plan for NuMI beam commisioning
When do we apply the new optics?
  Prefer to use the present optics for the target scan since the resolution of target scan is better by using smaller spot size beam
  Prefer to use option 2 at the beginning of HEP beam operation
    Need to make sure that Quads and PSs are stable at high current operation
Target system is ready for 900+ kW operation in FY23!
  I heard that the MI group is ready for the 900+ kW beam operation, too
    Beam intensity will exceed 5.6e13 (until 6.2e13 (1-MW))

## Slide 23: Future beam power upgrade plan
PIP-II SRF Linac + 20 Hz Booster for 1.2 MW (2025? -)
PIP-II SRF Linac + New accelerator system (SRF Linac or Fast ramp RCS) for 2.4+ MW (203X -)
PIP-II SRF linac
Booster
PIP-III SRF linac
PIP-III RCS

## Slide 24: Fast Ramping RCS at Fermilab
Integrable optics has a potential to compensate a space charge: The concept has been tested at Fermilab Accelerator Science and Technology (FAST)
If success, we will have a solution to accelerate a 5-MW scale beam in PIP-III RCS
Integrable optics magnet in FAST
Demonstrate prototype fast
ramp HTS at Fermilab (12 T/s)
H. Piekarz, NIMA 162490 2019
IOTA/FAST https://fast.fnal.gov/?p=papers

## Slide 25: Summary
Fermilab has successfully operated BNB and NuMI beams for neutrino programs
BNB and NuMI beam elements have been upgraded continuously
Highest NuMI beam power record 895 kW
Future prospect for higher beam power operation
  Optimize NuMI beam optics
  Understand radiation damage on beam element
  Apply AI for beam permit and target anomaly detection
  Study new muon monitor to extract further neutrino information
In this talk
RaDIATE
Yiding on Tue