## Slide 1
Target and horn pulsed effects and vibration issues
Peter Loveridge
STFC Rutherford Appleton Laboratory
NBI Workshop, September 2022

## Slide 2
Question:
“Could the LBNF target lifetime be impacted by dynamic loading coming from the horn?”
In this talk I will discuss ongoing efforts to quantify / mitigate this issue through design, simulation and measurements
Motivation

## Slide 3: Target / Horn Mechanical Coupling
Close mechanical coupling between LBNF target and horn is a departure from NuMI & T2K operating experience
Target and horn attached to common support frame
T2K
Target and horn supported from separate modules
NuMI
LBNF

## Slide 4: So What’s the Problem..?
Horn “rings like a bell” … … potential for dynamic excitation of nearby structures
T2K horn test firing
NuMI horn test firing

## Slide 5: LBNF Project Outlook
Combined horn + target pulse test planned in ~2-3 yrs time
In the mean time: focus on simulation efforts to inform target mounting design and potential mitigation measures
  Need FE models of horn and target
  Need to capture how they are coupled together
  Horn pulsing is relatively complex simulation challenge! (see right)

## Slide 6: Horn Vibration Modelling Trick #1: Joule Heating
Inner conductor as a thin-walled tube:
r
w
Half sine-wave shaped current pulse:
0
Imax = 300kA
0
τ=0.8ms
0°C
1.9°C
Volumetric heating
Ohm’s Law
Temperature rise in conductor simply varies as a function of
No need to model electric current flow…
… directly apply temperature rise as a function of position in mechanical simulation

## Slide 7: Horn Vibration Modelling Trick #2: Magnetic Forces
Inside the magnetic volume the field Varies with r according to:
And from the previous slide the current density is:
It is convenient to express the magnetic force acting on the horn conductor as a “pressure”
The total longitudinal force is found from
Field near a current-carrying wire
0 MPa
1 MPa
“Pressure” on conductor simply varies as a function of
More than 1 tonne longitudinal repelling force between two ends while current flows
No need to model magnetic field…
… directly apply pressure load as a function of position in mechanical simulation

## Slide 8: Does the Model Work..? Yes!
Point #7
Point #2
Max vibration amplitude at various locations – T. Sekiguchi, KEK

## Slide 9: LDV Interpretation: Modes
Signal differentiated to give acceleration
FFT carried out on acceleration- this gives more pronounced peaks as there is a low frequency decay in the displacement
200Hz
Inner Conductor “Violin Mode”
800Hz
Longitudinal Mode
Ben Suitters, RAL

## Slide 10: LDV Interpretation: Damping
Can estimate “damping ratio” (% of critical damping) from the initial ~800Hz response component in the LDV data
Expect inherently low levels of damping
  Metal structure, Bolted joints
Damping ratio is important dynamic characteristic:
  i.e. how many stress/strain cycles per pulse?

## Slide 11: LBNF Target Vibration?
LBNF Horn-A FE model (Loveridge)
  Simulated horn response to electric current pulse
  Observed axial vibration mode at target mounting flange
Axial vibrations transmitted
from horn to target mount
(Peak applied acceleration ≈20g)
Axial vibrations observed at target mounting flange
LBNF Target FE model (Wilcox)
  Input frequency/amplitude at mounting positions
  Observed potentially large deflection/stress response in target
  How to mitigate this?
Response as a function of stripline mass

## Slide 12: Different Mounting Variants Investigated
Used “Sine-Sweep” method to investigate various mounting design variants
Predicts target response to constant amplitude sinusoid across a range of frequencies
Potential driving frequency range (yellow zone)
Baseline Geometry
(Aluminium Plate)
Steel Plate
(Stiffer)
2 thin plates (Axially Compliant)
Stress Criterion
Dan Wilcox, RAL

## Slide 13: Present Modelling Effort: “Full Transient”
Combined target + horn model
Full transient
Two-way dynamic coupling
Driving frequency (axial deformation at the horn flange) is ~640Hz
Similar response frequency in target, but direction is lateral
On the limits of what we can solve with available computational fire-power!
Gauge point is on target titanium flow-divider (location of peak stress)

## Slide 14: Future Thoughts and Plans
Project schedule enables us to construct and then install a prototype target in the prototype horn for pulse testing, prior to construction of the first operating target
If issues identified during pulse test then strategy is to modify the (green) support plate i.e. do not need to re-design target
Double-plate concept appears promising at this stage. May be “tuneable” – plate spacing, thickness, etc.
Tuneable Target Mounting Plate
Forcing Function
2x 6mm thick plates, with 58mm spacing between
Gravity Sag
Cantilever target