## Slide 1
Meredith Lee
Accelerator Division/Target Systems Department
9/20/2022
Fermilab Horns Operational Experience

## Slide 2: Agenda
Overview
PH2-02 – Leaking Water
SLB-08 – Ground Fault
PH1-04 – Stripline Failure
PH2-01 – Stripline Failure
PH1-03 – Hanger Water Leak
PH1-01 – Broken Suction Line
Summary
1 MW Horn PH1-05 being installed in 2020 shutdown

## Slide 3: Overview
Running NuMI horns since 2005
Initially designed for 400 kW
  Upgraded for 700 kW, then 1 MW operation
Designed for 100 M pulse lifetime
Annual shutdowns is key for horn and target-related maintenance to prolong operations
  Replace horns or supporting systems if necessary
  1 MW upgrade in 2020
Horn | Lifetime Pulses
PH1-01 | 24,200,000
PH1-02 | 45,900,000
PH1-03 | 26,960,000
PH1-04 | 52,390,424
PH2-01 | 28,100,000
PH2-02 | 125,250,424
1 MW Horn PH1-05
Lifetimes of horns no longer in operation

## Slide 4: Overview – History
Several significant horn events during 17 years of NuMI running that have required horn replacement
Some root causes of horn failures have been practicalities of operation
  Hard to predict
  Not necessarily due to ineffective design, assembly, testing, or install
Same failure has not happened twice
  Thorough troubleshooting and resolution of problems

## Slide 5: PH2-02 – Leaking Water
PH2-02 leaking water from beam left Bdot
  Device used to measure magnetic field
  At neck of the horn
Removed during 2020 summer shutdown
  Leaking water for ~1 year
  4-5 gallons per day
PH2-02 during removal from target hall
Horn 2 Bdot location
Bdot

## Slide 6: PH2-02 – Leaking Water
Water leak evidenced by corrosion near Bdot
Twelve year lifetime
  125,250,424 pulses
Have not used Bdots on subsequent horns
  Capped off flange prior to install
PH2-02 during removal from target hall
PH2-02 during removal from target hall
Corrosion visible at Bdot

## Slide 7: SLB-08 – Ground Fault
Stripline blocks connect power supply stripline to horn stripline
  Interior aluminum stripline shielded via thick steel panels
Replaced both NuMI horns and accompanying stripline blocks in 2020 shutdown
  1 MW upgrade
Ground fault in the horn system discovered shortly after
Traced to loose washer in the stripline block SLB-08
  Shorting current from one of the outermost stripline layers
NuMI stripline block
Borescope image of loose washer
2020

## Slide 8: SLB-08 – Ground Fault
Disassembled and removed stripline block covers
One stud found with missing and loose hardware on one end
  Other notable anomalies
Recorded breakaway torque for all nuts on rest of stripline
  Several lower than 40 ft-lbs torque spec
Root cause: stripline bolts not torqued to 40 ft-lbs torque spec
2020
Missing nut and washer; loose ceramic
Breakaway torque results

## Slide 9: PH1-03 – Hanger Water Leak
Cooling circuit to cool hanger
  Minimize thermal expansion
    Minimize movement of horn
Leaking 20 gallons of water per day
Attributed to weld porosity
Performed weld spot repair
Ran until 2020 until it was replaced with PH1-05 for 1 MW upgrade
Location of leak on PH1-03
Location of leak on spare horn
2018

## Slide 10: PH1-04 – Stripline Failure
PH1-04 had new open style stripline
  Improved cooling of stripline flags
  Ran fine at 400 kW
  First stripline to operate at 700 kW
Horn current imbalance identified after 2 years of operation
Borescope image showed crack in stripline
27M pulses before failure
2015
NuMI Horn 1 compact (original) and open stripline
Crack in PH1-04 stripline

## Slide 11: PH1-04 – Stripline Failure
Vibration tests showed lightly damped modes on lower stripline flag
  Large displacements
Additional cycles from ringdown contributed to high cycle fatigue
Stress concentration from bolts in region contributed to fracture
2015
Waterfall plot for comparison of mode damping

## Slide 12: PH2-01 – Stripline Failure
Hydrogen embrittlement of high strength steel washer
Stripline fractured due to lack of clamping force
Solution: use lower strength SS washers
2008
Notes: Higher tensile strength correlated with greater susceptibility to hydrogen embrittlement

## Slide 13: PH1-01 – Broken Suction Line
Suction lines were Kovar to ceramic brazed assemblies
Suction line broke at electrical insulator
Solution:
  Used thicker layer of steel at transition to insulator
  Shrink fit assembly
2008
Example of suction line failure
Shrink fitting currently used assembly

## Slide 14: Summary
NuMI horns have been running for 17 years
All horns have achieved at least 2 year lifetime
Several failures due to practicalities of target hall environment
All failures and lessons learned are invaluable for LBNF
  Large influence on design, assembly, and fabrication

## Slide 15: Acknowledgements
Jim Hylen
Kris Anderson
Katsuya Yonehara
Marty Murphy