## Slide 1: Horn Construction at CU Boulder
Michael Reh
for

## Slide 2
Content
T2K horns
Updates to design
Recent construction

## Slide 3
T2K Horns
T2K uses 3 aluminum focusing horns
  Beam target sits inside first horn
  Two more horns downstream help to direct the beam towards the near and far detectors
Suspended in a helium chamber, cooled by water from spray nozzles mounted on outer conductor
Horn 1
Horn 2
Horn 3
Target
Helium chamber
Water sprayed from outer conductor onto inner conductor
Beam
Notes: 3 horns, get sequentially larger
First horn houses beam target
Cooling: Beam would melt the horn if no cooling. Minor heating leads to thermal expansion which can hurt horn alignment

## Slide 4
T2K Horn History
Generation | Horn 1 | Horn 2 | Horn 3
1 | Japan (2009-2013) | CU (2009-2013) | Japan (2009-2013)
2 | Japan (2014-2022) | CU (2014-2022) | Japan (2014-present)
3 | CU (2023-?) | CU (2023-?) | -
4 | CU (Spare) | - | -
Most recent production at CU
Starting production soon!
Notes: Horns are replaced as a precaution
No T2K has failed thus far
Recent replacements will help with the beamline upgrade challenges

## Slide 5
Past CU Horn Production Teams
2007-2008, Horn 2
2012-2013, First Replacement Horn 2
2014-2019, Second Replacement Horn 1

## Slide 6: What’s New with Horn 2?

## Slide 7
Design Updates to Horn 2
Motivation:
  Upgrading beam power (500 kW -> 1.3 MW)
  Upgrading horn current (250 kA -> 320 kA)
  Other ease of production upgrades
Notes: More current should increase beam flux 10%
More power also increases beam flux (more protons coming in)

## Slide 8
Design Updates to Horn 2
Upstream cooling lines to handle higher power beam & higher current (made in Japan)
  Cooling lines embedded in the upstream flange and strip lines
  Water lines electrically isolated using ceramic buffers
Flange Cooling
Strip Line Cooling

## Slide 9
Design Updates to Horn 2
Added ribs to the inner conductor to improve resistance to magnetic and thermal warping
  The previous horn 2 had a large tympanic vibration -> ribs will help reduce fatigue

## Slide 10
Design Updates to Horn 2
Replaced steel and aluminum bolts with titanium in several places (cooling nozzles, helium ports, threaded rods holding inner/outer conductors together)
  Previously, would torque with steel screws to crush seals, then replace 1:1 with aluminum screws
  Now, use titanium screws from the start
Notes: Ti has higher Z (more impacted by beam), but also stronger and so less failure prone than Al

## Slide 11
Design Updates to Horn 2
Changed the design of drain bellows
  Previously welded directly to the drain tank
  Now can be more easily moved as needed; easier to crush seals
  Flange bolt size increased for stronger seal
Previously welded to the drain tank
No longer pre-welded; easier to install due to being unconstrained
Notes: Previously had to crush seals on top of the drain tank
Now have more flexibility for assembly

## Slide 12: T2K Horn 2 Construction at CU (2021-2022)

## Slide 13
Challenging Times
Slow part procurement & production due to worldwide supply chain issues (COVID)
Had to change vendors for several parts
Over-reliance on local machining due to difficulty working with external vendors

## Slide 14
Delivery of Major Pieces (2021)
Received major pieces in early 2021
  Top frame from GETT Industries (February 2021)
Notes: Left in its crate since it goes on late in production

## Slide 15
Received major pieces in early 2021
  Top frame from GETT Industries (February 2021)
  Outer conductor from Japan (February 2021)
Delivery of Major Pieces (2021)
Rotating Fixture
Notes: Mounted in rotating fixture for later

## Slide 16
Received major pieces in early 2021
  Top frame from GETT Industries (February 2021)
  Outer conductor from Japan (February 2021)
  Frame columns from Boston University shop (March 2021)
Delivery of Major Pieces (2021)
Grout-leveled plate
Notes: BU shop did a great job, think we will be working with them more in the future

## Slide 17
Received major pieces in early 2021
  Top frame from GETT Industries (February 2021)
  Outer conductor from Japan (February 2021)
  Frame columns from Boston University shop (March 2021)
  Drain tank from Bright Light Welding (April 2021)
Delivery of Major Pieces (2021)
Notes: Installed among the frame columns

## Slide 18
Received major pieces in early 2021
  Top frame from GETT Industries (February 2021)
  Outer conductor from Japan (February 2021)
  Frame columns from Boston University shop (March 2021)
  Drain tank from Bright Light Welding (April 2021)
  Inner conductor from Japan (April 2021)
Delivery of Major Pieces (2021)

## Slide 19
Installing the Inner Conductor
Lifted inner conductor using eye bolts (no extra support required)
A soft aluminum seal gets crushed between conductor flanges
Notes: Larry did a deflection test to show that no extra support was needed for I.C. (would not buckle)
Soft aluminum seal flows under pressure, filling in gaps between flanges

## Slide 20
Installing the Inner Conductor
Centered inner conductor to within 0.2 mm!
Tighten in “star” pattern (uniformly crush seal)
Feeler gauge
Notes: Feeler gauge all around to ensure centering
Tightened nuts in a star pattern to uniformly crush the seal
Spiralock nuts do a great job of holding, but were a huge pain to order

## Slide 21
Upstream Ceramic
Conductors isolated by ceramic ring on upstream end
Ceramic Ring
“Spider” lifting fixture
Teflon contacts grip the ceramic ring
Notes: Ceramic requires special “spider” lifting fixture -> too fragile to sustain its own weight

## Slide 22
Upstream Flange
Must transfer depth measurements to flange to get a good fit
Depth gauge locates ceramic ring and conductor
Transfer punches locate the clocking on the flange
Notes: Flange must be machined to match depth of I.C. and ceramic all the way around
  Don’t know the exact depths and clocking until the test-fit
Machining was outsourced (can’t remember where)

## Slide 23
Installing Upstream Flange
Sent the flange for machining, then installed it on upstream end
Notes: Flange had to be redone because the first job didn’t go so well

## Slide 24
Installing Upstream Flange
Ceramic tubes isolate threaded rods from flange
Spiralock nuts hold flange to the outer conductor
Tightened w/ star pattern to uniformly crush seals!
Notes: Kapton on threaded rods to prevent rods from scratching ceramic
Flange in electric contact with I.C.; isolated from O.C.

## Slide 25
Leak Testing
Check the performance of the seal
Red food coloring + kimwipes make leaks easy to identify
Tests performed for both upstream and downstream ends
No leaks after 24 hrs!
Notes: Both upstream and downstream seals were tested in this way
Used a siphon to get liquid in and out

## Slide 26
Moving Conductors into Frame
Horn connected to columns with ceramic isolation blocks

## Slide 27
Installing the Top Frame
Moved the top frame onto the columns
Use a laser to align top frame to outer conductor
Aligned frame to within the guide laser’s precision (1 mm)

## Slide 28
Seal Crushing
Use helicoflex seals between ceramics and stainless steel parts
  Quite tough to crush
  Need to ensure good ceramic-steel interface
  Use a custom jig to do the crushing
Helicoflex between SS and ceramic
Get extra crushing power from external plates
Notes: Helicoflex seals are tough to crush, so need extra power from external jig
24 spray nozzles, made in this way

## Slide 29
Similar process for other seal crushing
Seal Crushing
Custom Clamp
Hold ceramic + steel flange
Crush using external plate
Drain bellows seal crushing:
Notes: Uses another unique clamp to hold pieces in place, but the main steps are the same.

## Slide 30
Light gap re-opens after removing crushing plates (gap between ceramic and steel)
  Tried tightening bolts past torque specs
  Added grease under bolt heads to reduce torque loss to friction
  Tried newer seals
Bellows clamp leaves metal marks on the ceramic
  Will have to modify the clamp in the future so it only contacts the steel flange
Seal Crushing Problems
Notes: Most of the helicoflex seals used here were leftovers from previous horns
Have to hope that the light gap does not translate to water leaks
Bellows flange is thinner than it used to be, so the normal clamp is now too big

## Slide 31
Plumbing
Attached water cooling nozzles using titanium bolts
Cleaned and installed water manifolds
Bent tubes connect nozzles to supply manifolds and drain tank
Tube shape allows for some flexibility, but the fits are still very tight
Notes: Had to manually bend one of the tubes to make it fit
Auxiliary drains prevent corrosion of SS nozzles
  (lesson from MiniBoone horns)

## Slide 32
Pressure Test
Pressurized to +14 psi with compressed air
Fell to 10 psi in 20 hours
  Main source of leaks was temporary Viton seals on helium ports
Spot-checked all joints with snoop and tightened any visible leaks
Tighten the leaky joints
Notes: At this point, the horn is not complete; several temporary seals in place
Viton seals were the main source of leaks
  Being replaced later anyways, so no big deal
Tightened up any Swagelok connections that might be leaky

## Slide 33
Shipping
Shipping fixture helps to reduce horn motion in transit
  Protects the ceramic blocks that hold the conductors
Braces fix conductor ribs to frame
Held together by long threaded rods
Brackets too big to lift by hand
Connect upstream and downstream ribs; tight fit
Notes: Shipping fixture is a pain to install due to constraints
Helps support conductors and take stress off ceramic blocks

## Slide 34
Shipping
Same crating company used for all horns built at CU
  Craters & Freighters
3 meter cube!
Protecting the flange ceramics

## Slide 35
Shipping
Military vehicle on our shipping truck
Horn in crate
?!?
Notes: Surprise guest riding on our delivery truck
Military vehicle followed by huge black tarp box -> very suspicious on highway

## Slide 36
Shipping
Tight fit trying to extract horn crate from the CU lab
Notes: Driven from CU to LAX, flown in a 747 to Japan
Military vehicle followed by huge black tarp box -> very suspicious on highway

## Slide 37
Work in Japan
Stephen Coleman and I travelled to J-PARC to work with Tetsuro Sekiguchi-san on the remainder of the horn
Installed plumbing for frame cooling, flange cooling, and helium

## Slide 38
Work in Japan
Problems with parts
  Some changes in plumbing design didn’t make it to production drawings
  Flex hoses for water draining had to be reinforced on the fly after seeing previous hoses break
Flex hoses for water return were destroyed during removal of the old horn.
Reinforced for the future.
Notes: Some parts the wrong size, wrong fits due to not having all of our production drawings ready
  E.g. ordering of water return lines was changed
Some modifications had to be made on the fly, e.g. the reinforcement of flex hoses

## Slide 39
Work in Japan
Last bit of plumbing, and strip lines were installed by Sekiguchi-san, completing the horn
Successfully installed in the helium vessel as of September 1!

## Slide 40
New T2K spare horn 1 production to begin soon
CU is committed to building the next Horn 1 for T2K, and more horns in the future!
Upcoming Production
Notes: Want to get top frame & columns this FY, rest of production next FY

## Slide 41
Thank you!
M. Reh
S. Coleman
T. Sekiguchi
K. Allison
B. Rumberger
A. Cudd
L. Bartoszek
E. Zimmerman

## Slide 42: Backup
Notes: Want to get top frame & columns this FY, rest of production next FY

## Slide 43
T2K Horns
Design produces a toroidal field that can focus or de-focus either positive or negative charges to give a neutrino or anti-neutrino beam depending on horn current direction
  Pulses every 2.48 s @ 250 kA for ~2.1 T field
Cross section cartoon of horn 2
Notes: Current direction drives particle selection

## Slide 44
Cleaning Parts
Simple Green and isopropyl alcohol go a long way
Outer conductor
Inner conductor
Soft aluminum seals
Have to edge off waterjet burrs with stone
Notes: Had to edge water jet burrs off the aluminum seals using sharpening stones

## Slide 45
Rotating the Conductors
To ensure the inner conductor does not bend while rotating the fixture, installed steel braces to hold it in place

## Slide 46
Leveling Columns
Uneven frames make horn alignment uncertain
Largest difference between column levels = 3/128” (acceptable)
Notes: Leveling is a testament to the quality from the BU shop

## Slide 47
Frame Cooling
U-shaped water lines go into each column to reduce thermal expansion
Held into place with dozens of aluminum blocks
  Had to hand-tap all ~100 of them 
U-channel
Holding Blocks
Special tool for locating blocks

## Slide 48
Installing the Inner Conductor
Drilling and tapping holes for the lifting eye bolts

## Slide 49
Installing the Top Frame
Re-mounted laser because previous floor threads were unusable
Guide laser could not easily reach all score marks
  Had to custom-mount the laser
Laser had to be mounted with duct tape for it to line up correctly
Drilling new holes for laser mount

## Slide 50
Plumbing
Water drain pipes had some trouble with clamping
Clamp holes
Bracket holes
Bracket too wide!
Had to pivot to U-bolts

## Slide 51
Seal Crushing
1. Place nozzle in clamp
Custom vise clamp
Steel spray nozzle
Notes: 24 spray nozzles to make

## Slide 52
1. Place nozzle in clamp
2. Add helicoflex seal
Seal Crushing
Seal to be crushed

## Slide 53
1. Place nozzle in clamp
2. Add aluminum seal
3. Cover seal with ceramic piece
Seal Crushing

## Slide 54
1. Place nozzle in clamp
2. Add aluminum seal
3. Cover seal with ceramic piece
4. Prepare bolts
Seal Crushing
Finger loose during crushing!

## Slide 55
1. Place nozzle in clamp
2. Add aluminum seal
3. Cover seal with ceramic piece
4. Prepare bolts
5. Add top crushing plate & crush seal by tightening nuts
Seal Crushing
Crush until no light gap here
Bring bolts up to torque after seal is crushed
Notes: Crush seal by tightening bolts sequentially (want seal to crush uniformly).
Tighten until no light can be seen coming between ceramic and aluminum.
Once seal is crushed, tighten bolts up to spec.
Pre-crushing the seal reduces the likelihood of failure from bolt pressure points

## Slide 56
Nozzle Problems
Welding nozzles from the outside results in warping
  If the flange surface does not lie flat, it may break the ceramic during seal crushing

## Slide 57
Plumbing
Attached steel bellows to drain tank (had to get these redone due to bolt holes being misaligned)
Misalignment
Fixed!